## Slide 1
Manipulation of (radioactive) ions for laser spectroscopy
Vladimir Manea
IJCLab, Orsay, France

## Slide 2: Outline
Brief overview of laser spectroscopy at accelerator facilities
  Collinear laser spectroscopy
  Hot-cavity and gas-cell laser spectroscopy
Gas-jet laser spectroscopy
  Main concepts
  Improving extraction time and neutralization efficiency
Trap-assisted laser spectroscopy

## Slide 3: Laser spectroscopy of exotic nuclei
I, µ, Q
Ion/photon number
l
Wavenumber
e–
I
J
F
<r2>
Key parameters when working with rare isotopes:
  Resolution
  Efficiency
  Sensitivity
Exploits the hyperfine interaction to extract nuclear observables

## Slide 4: Laser spectroscopy of exotic nuclei
Collinear laser spectroscopy:
  Resolution:
    > 30 keV acceleration: ~ 10 MHz
  Sensitivity:
    ≈103 pps for fluorescence
    ≈10 pps for RIS
Accelerator
light projectiles
heavy projectiles
Thick target
(ISOLDE, ISAC)
Thin target in gas cell
(IGISOL)
Thin target in flight
(NSCL)
In-flight separator
High resolution separator
>30 keV beam
Cooler-buncher
Neutralization
vapor cell
Collinear laser spectroscopy (fluorescence, RIS)
Photomultipliers
MCP
ions
ions
He
He
atoms
X. F. Yang et al., Prog. Part. Nucl. Phys., 129, 104005 (2023)

## Slide 5: Laser (spectroscopy) ion sources
The most direct form of laser spectroscopy, but broadening mechanisms:
  Doppler broadening
  Collisional broadening
Accelerator
light projectiles
heavy projectiles
Thick target
(ISOLDE, ISAC, IRIS)
Thin target in gas cell
(IGISOL, LISOL)
High resolution separator
>30 keV beam
He
V. N. Fedosseev et al., Phys. Scr. 85, 058104 (2012)
B. A. Marsh et al., NIM B 317, 550–556 (2013)
63Cu
λ = 327 nm
Talk by Klaus Wendt

## Slide 6: In-gas-jet laser spectroscopy at LISOL
Probing in the supersonic gas jet
Low temperature and density
Resolution 400-600 MHz
R. Ferrer, Nature Comm. 8 14520 (2017)
C. Granados et al., Phys. Rev. C 96, 054331 (2017)
A. Zadvornaya et al. Phys. Rev. X 8, 041008 (2018)
Louvain-la-Neuve facility

## Slide 7: Gas-cell laser spectroscopy setups
T. Sonoda et al., NIMB 295, 1-10 (2013)
Y. Hirayama et al., NIMB 412, 11–18 (2017)
S. Raeder et al., NIM B 463, 272-276 (2020)
A. Zadvornaya et al., NIM B 539, 33-42 (2023)
A. Ajayakumar et al., NIMB 539, 102–107 (2023)
S3-LEB
MARA-LEB
JETRIS
PALIS
KISS
M. Laatiaoui et al., Nature 538, 495–498 (2016)
RADRIS

## Slide 8: A dedicated design for fusion-evaporation products
Critical performance criteria :
  Chemical survival/neutralization efficiency
  Stopping efficiency
  Extraction efficiency and time
Radioactive nuclei
Buffer gas at 100-500 mbar
Stopping, thermalization
and neutralization
Supersonic jet
Extraction by gas flow only
Decoupling of laser axis from spectrometer axis
Shown is S3-LEB/MARA-LEB geometry
Gas cell laser probing
Gas jet laser probing
Thin window
Talks by Jorge Moreno and Nathalie Lecesne
E< 1 MeV/u

## Slide 9: A dedicated design for fusion-evaporation products
Radioactive nuclei
Ar at 100-500 mbar
Supersonic jet
Critical performance criteria :
  Chemical survival/neutralization efficiency
Chemistry is a loss mechanism:
 ultrapure buffer gas needed
Resonance-ionization spectroscopy:
    neutral atom highly preferable
    use Ar as buffer gas
After thermalization charge exchange not possible
Ion stopping generates plasma
A fraction of the ions will charge exchange while being slowed down.
Gas jet laser probing

## Slide 10: A dedicated design for fusion-evaporation products
Radioactive nuclei
Ar at 100-500 mbar
Supersonic jet
Critical performance criteria :
  Chemical survival/neutralization efficiency
Chemistry is a loss mechanism:
 ultrapure buffer gas needed
Resonance-ionization spectroscopy:
    neutral atom highly preferable
    use Ar as buffer gas
After thermalization charge exchange not possible
Three-body recombination
Dissociative recombination
Ion stopping generates plasma
A fraction of the ions will charge exchange while being slowed down.
Gas jet laser probing
Strong dependence on ion beam intensity
No electrical field in neutralization area.

## Slide 11: A dedicated design for fusion-evaporation products
Radioactive nuclei
Ar at 100-500 mbar
Supersonic jet
Gas jet laser probing
S3 beam size in convergent mode
Critical performance criteria :
  Chemical survival/neutralization efficiency
  Stopping efficiency
  Extraction efficiency and time
No electrical field
  Extraction velocity is gas velocity
  Minimize volume  reduce extraction time
  Increase pressure (≈ 500 mbar)
     increase stopping power,
     reduce diffusion effect
Stopping efficiency 100% (for fusion-evaporation products)
Extraction efficiencies > 50 % for 500 mbar pressure (depending on diffusion coefficient)
Nozzle diameter | Extraction time
d=1 mm | 630 ms
d=1.5 mm | 280 ms
Optimization of the geometry performed in COMSOL (E. Mogilevsky et al., KU Leuven)

## Slide 12: Super/hypersonic gas-jet optimization
Mach number:
Super/hypersonic jet = cold jet  low Doppler broadening
Radial distance (mm)
R. Ferrer et al., Phys. Rev. Res 3, 043041 (2021)
Color code: Doppler FWHM (MHz)
M = 8.1 de Laval nozzle

## Slide 13: Super/hypersonic gas-jet optimization
Mach number:
Super/hypersonic jet = cold jet  low Doppler broadening
Homogeneous jet  no Doppler smearing
But requires pressure matching
Radial distance (mm)
Yu. Kudryavtsev et al., NIMB 297, 7–22 (2013)
S3-LEB limited to 1.5 mm for Ar
M = 8.1 de Laval nozzle

## Slide 14: Further reduce gas-cell extraction time
Extraction time is a limitation for short-lived isotopes
Most time is “lost” in the stopping region which is far from the exit
≈ 400 ms
≈ 250 ms
≈ 25 ms
Radioactive nuclei
Ar, 500 mbar
Have exit closer to stopping volume: simulated limit 130 ms for 1 mm exit hole
Challenging stopping volume
Gas-cell spectroscopy difficult
High-power probing only transversal

## Slide 15: Further reduce gas-cell extraction time
Extraction time is a limitation for short-lived isotopes
Most time is “lost” in the stopping region which is far from the exit
≈ 400 ms
≈ 250 ms
≈ 25 ms
Radioactive nuclei
Ar, 500 mbar
Have exit closer to stopping volume: simulated limit 130 ms for 1 mm exit hole
Challenging stopping volume
Gas-cell spectroscopy difficult
High-power probing only transversal
Boost extraction from slow volume by electrical field
E
Neutralization becomes a challenge

## Slide 16: Further reduce gas-cell extraction time
Extract ions quickly from stopping volume by electrical gradient
Neutralize in fast flow near exit
Fast gas flow
E
Electrons are removed from stopping volume by electrical field
Transfer ions to a region without electrical field
Extract by gas flow

## Slide 17: The RADRIS/JETRIS approach
Laser spectroscopy on superheavy elements at GSI/SHIP:
JETRIS setup: attract beam on filament for neutralization, re-evaporate and extract by flow in gas jet
H. Backe et al., Eur. Phys. J. D 45, 99 (2007)
F. Lautenschläger et al., NIMB 383, 115 (2016)
M. Laatiaoui et al., Nature 538, 495–498 (2016)
J. Warbinek et al., Atoms 10, 41 (2022)
RADRIS: using filament for collection and neutralization in the gas cell, followed by re-evaporation
S. Raeder et al., NIM B 463, 272-276 (2020)
First on-line in-jet spectroscopy
Critical filament focusing and trade-off of efficiency with extraction time
Talks by Danny Münzberg, Rafael Ferrer and Sebastian Raeder
Talk by Fedor Ivandikov

## Slide 18: Exploring other neutralization approaches
Other approaches can aim to induce neutralization in the free flow, without collection.
Fast gas flow
E
Hot filament
Beta source
Intense electron source
Impurities
Transfer from electrical region to flow is not trivial
Time scale of neutralization process will limit the total extraction time.
FRIENDS3 project at IJCLab/GANIL: construct a demonstrator for systematically studying the relevant phenomena
Talk by Wenling Dong
R. Ferrer et al., Nucl. Instr. Meth. B 317, 570-581 (2013)

## Slide 19: Exploring other approaches: ion chromatography
New project to perform laser resonance chromatography (LRC):
  Optically pump ions into metastable state
  Detect laser resonance via ion chromatography
  (= change in mobility when in metastable state)
  A single laser is required
M. Laatiaoui et al., PRL 125, 023002 (2020)
E. Romero Romero et al., Atoms 10, 87 (2022)
Sc+

## Slide 20: Ion traps for laser spectroscopy
U
B
Penning trap
Multi-reflection time-of-flight mass spectrometer
S. Eliseev et al., PRL 110, 082501 (2013)
101In+
82Sr19F+
M. Mougeot et al., Nature Physics 17, 1099–1103 (2021)
Phase-imaging ion-cyclotron resonance (PI-ICR)
Time-of-flight ion-cyclotron resonance (TOF-ICR)
Ion traps can be very useful tools for mass-tagged ion counting

## Slide 21: Decay and trap assisted laser spectroscopy
Combination of MR-TOF MS and decay station used at ISOLDE for in-source laser spectroscopy of heavy nuclei
With current resolution of MR-TOF MS, isomeric separation is also be possible
R. N. Wolf et al., Int. J. Mass Spectrom. 349-350, 123-133 (2013)
S. Sels et al., Phys. Rev. C 99, 044306 (2019)
T. Day Goodacre et al., Phys. Rev. Lett. 126, 032502 (2021)
T. Day Goodacre et al., Phys. Rev. C 104, 054322 (2021)

## Slide 22: Penning-trap assisted laser spectroscopy
Penning traps can also be used for high-resolution mass tagging either in PI-ICR or TOF-ICR mode.
The linearity of counting can be a limitation especially in PI-ICR mode (but also high-resolution MR-TOF mode).
Early (failed) attempt of in-source laser spectroscopy with PI-ICR detection at ISOLTRAP

## Slide 23: Penning-trap assisted laser spectroscopy
Penning traps can also be used for high-resolution mass tagging either in PI-ICR or TOF-ICR mode.
For TOF-ICR, one needs to convert the ICR data in count-rate separation.
Kinetic energy
Ions excited on resonance
Ions excited off resonance

## Slide 24: Penning-trap assisted laser spectroscopy
Penning traps can also be used for high-resolution mass tagging either in PI-ICR or TOF-ICR mode.
For TOF-ICR, one needs to convert the ICR data in count-rate separation.
Kinetic energy
Ions excited on resonance
Ions excited off resonance

## Slide 25: Penning-trap assisted laser spectroscopy
Penning traps can also be used for high-resolution mass tagging either in PI-ICR or TOF-ICR mode.
For TOF-ICR, one needs to convert the ICR data in count-rate separation.
Kinetic energy
201mBi
201gBi
201mBi
Excite this frequency
In-source laser spectroscopy of the 1/2+ isomer in 201Bi while blocking away the ground state (306.8 nm).
Pile-up effect less problematic because of large TOF distribution.

## Slide 26: PI-ICR assisted laser spectroscopy
M. Reponen, M., R.P. de Groote, et al. Nat Commun 12, 4596 (2021)
Use of the PI-ICR technique for in-source laser spectroscopy of neutron-deficient Ag at IGISOL.
Determining the charge radii of Ag isotopes below the N = 50 shell closure.
Talk by Mikael Reponen

## Slide 27: Collinear spectroscopy line at intermediate energy
Buncher
MR-TOF MS
Penning Traps
CRIS technique
RAPTOR: “RIS And Purification Traps for Optimised spectroscopy”:
  Neutralization in charge-exchange cell
  Collinear laser resonance ionization spectroscopy with few keV beams
  ≈ 100 MHz resolution
Coupling to ion traps for mass tagging
Talk by Mikael Reponen
Slide courtesy of Ruben de Groote

## Slide 28: Conclusions
Gas-jet laser spectroscopy is a promising emerging technique at various accelerator facilities.
  Different geometries and approaches are being used, commissioned or developed
  Extraction time and (neutralization) efficiency are important topics of development
Ion traps greatly increase sensitivity of laser spectroscopy across the nuclear chart.
  Several in-source/in-gas laser spectroscopy facilities start exploiting or implementing them
Other approaches being developped (e.g. in-trap laser spectroscopy, ion cooling  MIRACLS project)
Talk by Stephan Ettenauer
S. Sels, F. M. Maier et al., Phys. Rev. Research 4, 033229 (2022)