## Slide 1
The N = 126 Factory
Maxime Brodeur
University of Notre Dame

## Slide 2: What is known?
208Pb
Fission peaks
252Cf
238U
Actanides
N = 126

## Slide 3: Cross-sections…
Fragmentation
MNT reactions
(calculation)
MNT reactions
(measurement)
Fragmentation
136Xe + 198Pt at 10 MeV/u
(best multi-nucleon transfer (MNT) reaction)
Hirayama et al., EPJ Web Conferences 109, 08001 (2016)
208Pb + 9Be at 1 GeV/u
(fragmentation reaction with best cross-sections for N = 126)

## Slide 4: Production of N = 126 nuclei
Calculations by James Kelly done using:
http://nrv.jinr.ru/nrv/webnrv/grazing/

## Slide 5: Near the heavy fission peak
Er
Dy
Gd
Yb
Sm
Nd
136Xe +164Dy
Done at JYFLTRAP/CPT
AME16
M. Vilen et al., PRL 120, 262701 (2018)
Calculations done using:
http://nrv.jinr.ru/nrv/webnrv/grazing/

## Slide 6: From Mg to Cf
5 pmA 136Xe at 9 MeV/u on different targets (26Mg to 252Cf)
Target thickness 10 mg/cm2 or 50 mCi/cm2 limit.
Red lines: AME20 known masses
Calculations by Biying Liu done using:
http://nrv.jinr.ru/nrv/webnrv/grazing/

## Slide 7: The N = 126 factory
G. Savard et al., NIM B 463, 330 (2020)

## Slide 8: Area 126
Gas cell
Gas cell
Gas cell
Dipole magnet
RFQ cooler-buncher

## Slide 9: The stubby catcher
Stubby catcher of large angle MNT reaction products
Thermalize in 50-100 mbar helium
Transported with DC + RF and extracted by gas flow
orifice

## Slide 10: The stubby catcher guts
Thermalize MNT reaction products

## Slide 11: The curved RFQ
90 degrees curved RFQ ion guide.
Accelerating section.

## Slide 12: The N = 126 beam factory: Magnet
Dipole magnet with R~1,500 to separate non-isobars

## Slide 13: The cooler-buncher
Cool and bunch the RIBs
FRIB EBIT cooler-buncher design. Other copies for BearTrap and St. Benedict at ND (see R. Zite talk)
Separate cooling & bunching sections
A.A Valverde et al., NIM B 463, 330 (2020)

## Slide 14: The N = 126 Factory RFQ
Flared entrance section for larger acceptance
High-power RF applied on backbone
Cross-cut DC electrodes

## Slide 15: The MRTOF
Separate contaminants by their TOF between electrostatic mirrors
Could also be used for mass measurements

## Slide 16: The MRTOF test setup
Assembled and tested at Notre Dame.
B.E. Schultz et al., NIM B 376, 251 (2016)
J. Kelly et al., NIM B 463, 485 (2020)

## Slide 17: Off-line test setup

## Slide 18: Resolving power and efficiency
400 loops
FWHM = 75 ns
Overlapping 85,87Rb
Most losses occur in the first 5 loops.
Efficiency limited by acceptance of large angular spread BNG-produced bunches.
Resolving power limited by power supply stability and possibly bunch-production method.
B. Liu et al., NIM A 985, 164679 (2021)

## Slide 19: MR-TOF optimization
Optimized ion optics for MR-TOF using beams from cooler buncher at N=126 Factory using a particle swarm code.
Resolving power reaching 100,000 can be obtained.
B. Liu
Cooler-buncher
MRTOF
beam
CPT

## Slide 20: Experiments
CPT will be the 1st experiment to receive N=126 Factory beams
Also plans to have the Xarray decay station coupled to it
Open to suggestions/ideas from the community

## Slide 21: Status of CPT
CPT is undergoing its 3rd move.
To make room for nuCARIBU upgrade (J. Clark talk) and use at N=126 Factory.

## Slide 22: Conclusion
The ANL N = 126 Factory aim to produce nuclei of importance for the r-process that are difficult of access: N = 126 shell, after fission peaks, and actinides.
Features a stubby catcher to thermalize large-angle MNT products. Electrodes all assembled. Cask in place in N126 room.
Followed by 90 degrees-curved RFQ ion guide and acceleration section. Electrodes all assembled.
RFQ cooler-buncher based on design from FRIB EBIT cooler-buncher. Installed in the N=126 Factory beam line.
The MR-ToF has been commissioned off-line at Notre Dame and mass resolving powers reaching 70,000 has been observed. Installed in the after BearTrap cooler-buncher for on-line commissioning.
CPT is out of CARIBU room and will be installed in N126 room Fall 2023.
First beams expected late 2023.

## Slide 23: Acknowledgements
K.S. Sharma
D.P. Burdette,
J.A. Clark,
R. Knaack,
G. Savard,
L. Varriano,
B.J. Zabransky,
A.A. Valverde
M. Brodeur,
A. Houff,
B. Liu,
S. Porter,
F. Rivero,
R. Zite