## Slide 1: Development of a Hot Cavity Catcher Laser Ion Source
Docent Mikael Reponen – SMI, Gießen, Germany , 2023

## Slide 2: Outline
JYFL-ACCLAB
  IGISOL
    The IGISOL method
Laser setups and laser spectroscopy
Motivation
History
Recent results
Outlook

## Slide 3: University of Jyväskylä Accelerator Laboratory

## Slide 4: JYFL-ACCLAB
K130:
Emax= 130 (q2/A ) MeV
Beams from p to Au
Annual use: 6500-7000 h/year
Ion sources
ECR: (6.5 GHz, 14 GHz, 18 GHz )
Multicusp: (H-,D-)
RADEF
Radiation effects
Microfilters
Accelerator based material physics
ToF-ERDA/RBS/PIXE
Ion source development (Lasers + Cs sputtering)
MCC30
Emax=30 MeV
Pelletron
EMAX=1. 7 MeV
C-Linac
LSC
Nuclear reactions
RITU/MARA/ MARA-LEB
Nuclear spectroscopy
(Optical spectroscopy)
IGISOL
Optical spectroscopy
Atomic masses
Decay spectroscopy

## Slide 5
IGISOL
Fast and chemically non-selective way to produce radioactive nuclei.
FURIOS
(The Fast Universal ResonantIOn Source)
A 10 kHz pulsed solid-state Titanium:sapphire laser system‌
Provides high-power laser beams for very sensitive resonance ionization spectroscopy (RIS).
Atom Trap
Goal: Producing coherent gamma radiation via isomeric decay of 135mCs in a Bose-Einstein condensate.
Dipole magnet
Offline ion source
Spectroscopy beamline
Diagnostics
Nuclear decay spectroscopy
Instrument development
MORA
(Matter's Origin from the RadioActivity of trapped andoriented ions)
Looking for CP violation in nuclear beta-decay via D correlation measurement.
MR-ToF
200 000 MRP so far
RFQ Cooler-Buncher
Collinear laser spectroscopy
RAPTOR
(Resonance ionization spectroscopy And Purification Traps for spectRoscopy)
JYFLTRAP
(Penning trap mass spectrometer)

## Slide 6: HCLIS motivation – 94Ag
Measurement of 92Rh, 94Pd mass with JYFLTRAP at IGISOL
  94Ag mass
  1 proton and 2 proton separation energy
A. Kankainen et al., Phys. Rev. Lett. 101 (2008) 142503
Two-proton separation energy
and two-proton decay data
[6] I. Muhka et al., Nature 439, 298 (2006)
[23] D. Kast et al., Z. Phys A 356, 363 (1997)
One-proton separation energy
and one-proton decay data
[24] G. Audi et al., Nucl. Phys A 729, 3 (2003)
D. G. Jenkins, Phys. Rev. C 80 (2009) 054303
AME 2003 Ex = 6500(2000)# keV (21+)
AME 2021 Ex = 6500(550)# keV (21+)
AME 2021 Ex = 1350(400)# keV (7+)

## Slide 7: Hot cavity ion source origins
GSI Catcher-Ion-Source-System
  FEBIAD
  Surface ionization
Used to produce a lot of isotopes in the immediate region below tin-100
  Very efficient!
  Very fast
Some laser ion source work done already
101Sn: Z Janas et al 1995 Phys. Scr. 262 (1995)
100In: W. Kurcewicz, Z. Phys. A - Atoms and Nuclei 308, 21-31 (1982)
97Cd: K. Schmidt, Nuclear Physics A 624 185-209 (1997)
94Ag: I. Mukha, Nature volume 439, 298–302 (2006)
93Pd: K. Schmidt, Eur. Phys. J. A 8, 303–306 (2000)
R. Kirchner et al. Ion sources for the GSI on-line separator NIM 186, 1–2, (1981)
Notes: Foreced electron beam arch discharge

## Slide 8: Ionization method: Laser resonance ionization
Each element have their unique atomic structure - “fingerprint”.
Multiple laser beams overlapped with atoms to stepwise excite and ionize
  Efficient! As high as >50%, typically a few %
A great method for sensitive laser spectroscopy
  Resolution highly environment dependent.
λ1
λ2
0 eV
1st excited state
2nd excited state
Ionization potential
Rydberg states
Continuum
Autoionizing state
Ground state
~5-9 eV
e-
σR~ 10-12 cm2
σI~ 10-17 cm2
λ3
  We chose resonance ionization to gain a huge improvement in selectivity!

## Slide 9: Hot Cavity Catcher at IGISOL ver 0.
The hot cavity project at IGISOL started in 2007.
  First iterations were primary-beam heated catchers
T. Kessler, I.D Moore
“PRIMARY BEAM HEATED CATCHER
The first tests of a hot cavity involved direct heating of a graphite catcher using a 40Ca8+ primary beam. A beam intensity of 125 pnA provided a heating power of ~19 W on the catcher.

## Slide 10: Hot Cavity Catcher at IGISOL ver 1.
Two FEBIAD ion sources acquired from GSI in 2008-2009
  We had difficulties in achieving a stable operation
  Multiple melted components!
  First offline RIS results
Dipole mass scans over stable 107,109Ag
107Ag first step wavelength
scan as function of oven temperature
Laser ionized 107Ag signal in crossed-beam geometry
M. Reponen et al., Eur. Phys. J. A 42, 509–515 (2009)
Notes: Promise to make 94Ag that

## Slide 11: Inductively Heated Hot Cavity Cather Laser Ion Source Ver. 3
Made in collaboration with JYFL ACCLAB ion source team
Focus was to address the stability issues of FEBIAD and provide a better laser ionization geometry.
  The first iteration was without a specific laser interaction region.
  Laser ionization between the coil caused huge energy spread
  Poor efficiency
  Laser scan over the first resonant step. The FWHM
  of the scan is 8.2 GHZ.
  Catcher temperature as a function of the power drawn by
  the RF supply.

## Slide 12: Inductively Heated Hot Cavity Cather Laser Ion Source Ver. 4
Included a transfer tube for laser ionization
  Inductively heated
Demonstrated the fast extraction of silver
M. Reponen et al., Rev. Sci. Instrum. 86, 123501 (2015)
1. SPIG entrance, 2. Ta transfer tube,
3. Water-cooled heat shield, 4. Copper coil, 5. Graphite catcher, 6. Ta window, 7. Hot cavity, 8. Mo crucible, 9. Ni degrader foil.
The mean delay time τ acquired via a fit for different catcher temperatures (measured at the window) and implantation depths. The error bars indicate one standard deviation of the implantation depth distribution. Errors associated with the delay time are within the data points.

## Slide 13: Inductively Heated Hot Cavity Cather Laser Ion Source ver 5.
Separate heating for catcher and the transfer tube
  Current flow through the whole crucible
  Full Mo crucibles hard to manufacture
    Deformation under heating an issues
First extraction of radioactive silver!
  99Ag observed
  Lasers scanning and ion detection arrangement was deemed poor.
Beam out
Laser in
Primary beam
Catcher
99Ag gamma

## Slide 14: Inductively Heated Hot Cavity Cather Laser Ion Source ver 5. - Combined PI-ICR and Dual Etalon lasers
M. Reponen et al., Nat. Comm. 12 (2021)

## Slide 15: Inductively Heated Hot Cavity Cather Laser Ion Source ver 6.
A target ion source system for fusion-evaporation products
  Efficient: 1 % for Ag and Pd
  Fast: <20 ms for Ag, less than 90 ms for Pd
14N + nat./92Mo
40Ca + 58/60Ni
Notes: The graphite transfer tube was replaced with sigradur.

## Slide 16: PI-ICR Assisted RIS and mass measurements beyond N=50
Preliminary!
Z. Ge, M. Reponen, in preparation
M. Reponen, in preparation

## Slide 18: Latest results
26.4-10.5 mass spectrometry of 94Ag
  A 205 MeV 40Ca
  2.2 mg/cm2 58Ni rotating target
  1, 2, 3, 4 µm Mo degrader set
95Ag clearly seen with MR-ToF
Two states clearly observed at mass 94
Laser wavelength set to 984.494 nm (JUN45 based estimate for 7+!)
Laser wavelength set to 984.525 nm (JUN45 based estimate for 21+ !)
  Mass peaks responds to lasers on/off and delays and first step laser frequency.
Preliminary!
Preliminary!
Preliminary!
1st step: 328 nm
Ionizing step: ~750-770 nm
Notes: Encouraged by recent successes on 96, 95Ag in JYFLTRAP Penning trap.
21+: ~70 nbarn
50+: ~580 nbarn

## Slide 19: Summary and Outlook
Hot cavity + mass filters
  Access to N=Z line!
    94Ag produced via 40Ca+58Ni!
    MNT reactions possible pathway for Sn and In?
Research opportunities in the region below tin-100:
  Laser spectroscopy
    94Ag will be next
  Further mass measurements
    1 % HCLIS efficiency shown for Pd!
  Decay spectroscopy with pure isomeric beams?
Hot cavity future activities
  Characterize the latest catcher properly!
  Improve efficiency
    Now factor or 20-30 away from GSI
21+
Notes: 21+ cross section very similar to tin-100 cross-section. 70 nbarn vs 30 nbarn.

## Slide 20
Thank you for listening!
JYFL-ACCLAB: T. Eronen, A. Jaries, A. Kankainen, S. Kujanpää I. D. Moore, S. Nikas, I. Pohjalainen, A. Raggio, J. Ruotsalainen, M. Stryjczyk, V. Virtanen,
and the IGISOL group!
GANIL: L. Caceres
Giessen: G. Kripko-Koncz
KU Leuven: R. P. de Groote
GSI: Z. Ge