## Slide 1: Beam Stopping Facility at FRIB
Chandana Sumithrarachchi
Ryan Ringle

## Slide 2: Outline
Overview of the stopped beam facilities
Stopped beam operational demands
Scheme for beam stopping of isotopes produced by projectile fragmentation
Instrumentation for high energy beam preparation
Beam stopping devices, operation, and challenges
BMIS
Summary

## Slide 3: Overview of Stopped Beam Facilities Successfully Operated Since 2002
Stopped beam facilities are scheduled for 35-40% of FRIB beam time for user experiments (PAC1+PAC2)
History of beam stopping at NSCL/FRIB
  First generation gas cell – 2002-2010
    Beams to mass measurements (LEBIT)
  ANL room temperature gas cell (RTGC) since 2011
  Advance Cryogenic Gas Stopper (ACGS) since 2017
  Cyclotron stopper; commissioned – still to be connected to beamline distribution
Wide range of stopped rare isotope beams delivered since 2011
  More than 30 elements from Z=8 to Z=40 used in stopped beam or reaccelerated beam experiments
  More than 90 different isotopes
Addition of Batch Mode Ion source (BMIS) in 2021
  Stand-alone beam operation during transition from NSCL CCF to FRIB
Mass analyzer

## Slide 4: Stopped Beam Operational Demands From User Experiments
Stopped beam facilities provide beams to following experimental areas, where beam requirements are specific
  LEBIT (mass measurements) – High purity beams, can handle low rates
  BECOLA (laser spectroscopy) – Moderate rates, mostly singly charged atomic ions, specific molecular beams
  Experiments at the two general purpose beamlines in stopped beam area – High purity and high rates
  Beams for reacceleration – High rates and moderate purity
    SECAR (recoil separator for astrophysics) in ReA3 area
    Two general purpose beamlines in ReA3 area
    SOLARIS (dual-mode solenoidal spectrometer for reaction studies) in ReA6 area
    One general purpose beamline in ReA6 area
Operational objectives to meet demands
  High energy beam properties that maximize the gas stopping of desired isotope
  Optimized beam extraction under the given gas cell condition, satisfying experiment requirements
  Identified molecular fragments of desired isotope and optimized beam purity
  High total transmission efficiency from ARIS to the experiment

## Slide 5
Scheme for Beam Stopping of Isotopes Produced by Projectile Fragmentation
Production of fragments from high energy beam
  Large momentum spread due to reaction mechanism (projectile fragmentation) and production target
Br and DE separation to select desired isotope
  ARIS spectrometer (High acceptance: ~5 % Dp/p), achromatic wedges
Momentum compression for efficient beam stopping
  Narrow momentum spread beams lead to high stopping efficiency
  Narrow momentum is achieved by degrading the beam at the object point and utilize a wedge at the dispersive focal plane
Beam stopping in gas cells
  Ions collect and come nearly to rest in helium filled gas cell
  Transport in gas cell with DC, RF fields
  Extraction with electric fields and gas flow
Electrostatic, low-energy transport with magnetic mass separation
~ 200 MeV/u

## Slide 6: High-energy Beam Preparation for Stopping Momentum Compression with Careful Selection of Degraders and Wedges
Two momentum compressed beamlines operational since 2011
Degraders (aluminum): Fine adjustments to degrade the beam energy by varying the angle with respect to the beam
  Each object point has a degrader
  Each gas cell has two large degraders in front of it to accommodate large beam size
Wedges (aluminum): Wedge angle is critical for dispersion matching. Can use either
  Fixed-angle wedges
  Rotary wedges (variable angle, based on GSI design)
Degrader drive
Rotary wedge

## Slide 7: Rotary Wedge System Stopping efficiency can be increased by having tunable wedge system
Tunable wedge system installed recently.
Two fused silica wedges rotate opposite direction to get the desired angle
Angle per wedge = 2.5 mrad; middle thickness = 0.5 mm; Max wedge angle = 5 mrad
Tested with 75Ga beam

## Slide 8: Beam Stopping Devices Two Gas Cells Provide Beams to Experiments
Room Temperature Gas Cell (RTGC) - reliable workhorse since 2011
  Large linear gas catcher developed and built by Argonne National Lab
  120 cm long gas catcher operates at pressure of 70 Torr and temperature of -10 0C
  Operates with Radio-frequency (RF) + DC voltage gradient
Advanced Cryogenic Gas Stopper (ACGS) provides improved performance since 2017
  Novel geometry reduces space charge effects (>10x higher beam rate capability)
  Ion surfing technique for fast extraction (2x faster)
  Cryogenic operation for cleaner beams (in-situ gas purification)
  Features
    1.2 m (9 segments) wire carpet operated with 4 phase-RF creating a traveling wave
    Each segment has 276 CuBe wires 50 μm diameter
Two gas stoppers provide redundancy

## Slide 9: Beam Stopping Devices ACGS – Improved Extraction Scheme Implemented
New extraction carpet for easier operation and higher currents
Original design had a funnel to guide surfing ions onto a mini-carpet
  Precision of funnel assembly positioning above and below carpets was critical as well as its voltage
Particle-in-Cell simulations showed that a large extraction carpet is less sensitive and allows higher currents to be extracted
Tests with internal alkali ion source showed ~100% transmission for nanoamps currents

## Slide 10: PIC Simulations Have Been Developed to Study Ion Transport and Extraction Efficiencies
Total electric field at the surface of the wire RF carpet
  Each stopped rare isotope generates ~ 106 He+/e- pairs
  Slow He+ ion removal increases space charge in ACGS body, reducing transport efficiency
  Increase He+/e- collection speed
Charge capacity of extraction carpet and orifice
  Charge exchange and/or direct ionization of impurities in He buffer gas generates beams of stable molecules
  Extraction efficiency can be compromised by large stable beam currents
  Increase charge throughput

## Slide 11: Ionization of He Buffer Gas Creates Additional Electric Fields
PIC 3D Cartesian geometry
Energy deposition from LISE++
He+ and e- included
SDS gas collision model1
P = 20 Torr @ 50 K
e-
He+
energy
deposition
total electric field strength at RF carpet surface2
108 pps
Epush = 10 V/cm
1A.D. Appelhans & D. A. Dahl, Int J Mass Spectrom 244, 1–14 (2005)
2Ringle, R. et al., NIMB 496, 61–70 (2021)
rf carpet
He buffer gas
, Slide 11

## Slide 12: IonCool Accurately Calculates Ion Transport Efficiency Across ACGS RF Carpet
Need to determine ion transport efficiency as a function of Epush
  Using ACGS, ion transport efficiency of 39K+ was measured
  Multiple pressures at T=50K.
  IonCool1 simulation results show good agreement with experiment
  Confident in IonCool results to make broader predictions
1Schwarz, S. NIMA 566, 233–243 (2006)

## Slide 13: Total RF Carpet Transport Efficiency Can Be Calculated Using PIC and IonCool
Combine IonCool and PIC results to calculate total transport efficiency
  Stopped rare isotope distribution obtained from LISE++
  Monte-Carlo approach used to calculate transport efficiency
  Folding in stopping efficiency determines optimum total efficiency that is rate dependent1
1R. Ringle. et al., NIM B 496, 61–70 (2021).

## Slide 14: PIC Simulations of ACGS Extraction System Yield Efficiency Improvements
orifice
cone
RF carpet
2D cylindrical RZ geometry
Gas flow calculated with COMSOL
Traveling wave transport across RF carpet1,2
Compared original ACGS “nozzle” extraction to a simple hole
Simulations accurately predicted significant gain in throughput for the hole vs. nozzle
1G. Bollen, Int J Mass Spectrom 299, 131–138 (2011)
2M. Brodeur et al., Int J Mass Spectrom 336, 53–60 (2013)
nozzle
Hole
natK+

## Slide 15: Contaminant Ions Can Have a Significant Impact on Extraction of Rare Isotope Beams
P = 10 torr
I = 1 nA O2+
Orifice @ 6V
P = 15 torr
I = 5 nA O2+
Orifice @ 9V
Scan potential applied to orifice and vary the incident O2+ current
Once steady state is reached, create tracer particles for rare isotopes (40Cl+ and 80Ge+)
O2+ current can have a significant impact on extraction efficiency of rare isotopes
Many studies complete and underway to optimize performance

## Slide 16: Beam Stopping Operation Multi-step Selection Process
Isotope production and separation, identification and delivery to gas cell through momentum compression beam line
Range selection in the gas cell and extraction (angle scan)
  Varying degrader angle and measure the electron current during the ionization, positive current extracted, and beta decay of the extracted radioisotopes (Example -31S fragment)
Selection of desired isotope or corresponding radioactive molecule before delivery to experiment
  Varying mass (mass analyzer magnet field) and measure radioactive and stable ion current (Example -31S fragment)
PID of ARIS beam

## Slide 17: Beam Stopping Devices Highest Z isotopes delivered by ACGS are Zirconium (Z =40)
83Zr cocktail beam delivered from A1900. –Purity of 83Zr : 9%
ACGS has a capability to measure electrons generated from beam stopping at segmented push plates regions – Stopping profile
Zr beams come with lots of impurities.
ACGS has a way to see the stopping profile with push plate electron current.
83Zr angle scan and electron current from different segments- manipulate the stopping closer to extraction when needed for low rate incoming beam.
Zr came as only 2+ & 1+, not other molecules
ACGS has delivered 80-83Zr for mass measurement1, purity of 80Zr is 0.1%
83Zr
A1900 PID
83Zr2+
83Zr1+
1Hamaker, A. et al., Nat Phys 17, 1408 (2021)

## Slide 18: Beam Stopping Devices Having ACGS and RTGC provide choice of beam delivery
RTGC provides several molecular adducts for most of beams and it may have high rates for one of the molecular ion –rate choice
ACGS mostly provides 1+ and 2+ bare ions at similar rates and has a choice between purity and high rates
ACGS
RTGC
Highest rate measured from ACGS : 1E6 pps of Br-85

## Slide 19: Gas Stopping Challenges Quality of High Energy Beam Impacts Efficiency
Large impurities in high energy beam increase space charge in gas cell and reduce extraction efficiency
  Wedges open secondary reaction channels and produce additional fragments
New challenge for heavier beams are multiple charge states
  Multiple charge states in high-Z beams leads to decreased incoming beam rates
37K – Fragment of interest; contaminants due to secondary reactions with wedge
106Sn beam charge states
Example of gas cell saturation (RTGC)
TOF (ns)
DE (MeV)
37K

## Slide 20: Gas Stopping Challenges Radioactive molecules and Stable Beam Contaminations
Radioactive molecules formed between stopped rare isotope and gas impurities
  Fractionation of ions that can be delivered to experiments if more than one molecule
Stable ion contamination from ionization of gas impurities by incoming beam
  Can overwhelm experiments that can’t take high beam rate if A/Q is same as ion of interest
Image of MCP located after the mass analyzer (mass =29 was selected)
29P activity on the left
Radioactive and stable masses at A=29 (e.g.. CHO+)

## Slide 21: Batch Mode Ion Source (BMIS) Successful Stand-alone Operation During Transition to FRIB
BMIS provides beams of stable and long-lived isotopes for stopped and reaccelerated beams experiments; realized in collaboration with ISOLDE
  Based on ISOLDE target/ion source modules and front-end design
  Samples of long-lived isotopes placed in target container
Together with FRIB radiochemists a variety of beams were developed. Examples:
  Be-10 (T1/2 = 1.5E+6 y) and Be-7 (T1/2 = 53 d)
    NF3 as a reaction gas to create BeF2+ in-situ, working temperature around 1,000 C
  Si-32 (T1/2 = 153 y)
    Extracted as SiO+ at about 700 C.
  Al-26 (T1/2 = 7.2 y)
    Al2(SO4)3 combined with NF3 in-situ for extracting AlF at about 1,000 C
Stable beams of Cr-50, Fe-58, Kr-86 and Sn-120 were produced
BMIS will continue to deliver beam for stand-alone operation; also planned to be used for solid-stopper demonstration
Radioactive sample

## Slide 22: Summary
Stopped beam operational demands are identified
Beam stopping of isotopes produced by projectile fragmentation at MSU since 2002
High energy beam momentum compression is key to efficient stopping
Two gas cells are operational and provide stopped beams to experiments successfully
BMIS provides stable and long-lived radioactive beams to stopped beam area
Gas stopping challenges
  Quality of high energy beam impacts efficiency
  Radioactive molecules and stable beam contaminations

## Slide 23: Acknowledgements
Collaborators
Georg Bollen, Kasey Lund, Dave Morrissey, Ryan Ringle, Stefan Schwarz, Antonio Villari