## Slide 1: Monte Carlo Transport Simulation
Panda Computing Week 2012, Torino

## Slide 2: What is a Monte-Carlo simulation?
The expression "Monte Carlo method" is actually very general. Monte Carlo (MC) methods are stochastic techniques, meaning they are based on the use of random numbers and probability statistics to investigate a problem
A Monte Carlo method is a technique that involves using random numbers and probability to solve problems. The term Monte Carlo Method was coined by S. Ulam and Nicholas Metropolis in reference to games of chance, a popular attraction in Monte Carlo, Monaco

## Slide 3: What is a MC transport simulation?
A Monte Carlo transport simulation is a program which simulates the passage of elementary particles through matter. [Geant3 User’s Guide]
In consists of the following parts:
  Geometry package
  Transport package
  Visualization package
  Detector response package
  User Code

## Slide 4: How does a MC simulation work?
Initialization
  Create geometry
    Define materials and media
    Create the geometrical setup of the experiment
    Define active sensitive volumes in the setup
  Define/Create particles and their physics properties
Event processing
  Read one event from event generator
  Transport one event through the setup
  Cleanup to be ready for the next event
Final Cleanup
  Write data to file

## Slide 5: How does a MC simulation work?
Quite complex dependencies
User code implemented “inside” the MC framework
Complete rewrite needed for new MC framework

## Slide 6: How does VMC work?
Use interfaces which decouple the user code and
the concrete Monte Carlo
Use different Monte Carlo’s with same user code

## Slide 7: MC transport in detail (1)
Silicon detector
Gold Target
Particle
Initialization done
Transport package read event kinematics
One particle at position (x, y, z) with momentum (Px, Py, Pz)
Transport package get from geometry package the distance to the next boundary in direction of particle track
Transport package get from physics package the distance where the next interaction in the medium happens
Depending on the medium, the particle and the physical settings there are several physical processes to be taken into account

## Slide 8: MC transport in detail (2)
Silicon detector
Gold Target
Assume particle is in vacuum, so no interaction
Transport moves particle on the next boundary to be crossed

## Slide 9: MC transport in detail (3)
Silicon detector
Gold Target
Assume particle is in vacuum, so no interaction
Transport moves particle on the next boundary to be crossed
If one looks much closer, one can see that the particle is moved slightly inside the new volume
Now the transport again checks for distance to next boundary and physical interaction
Particle has an interaction inside the target (scattering) so the kinematic properties of the particle are updated
Particle leave target without any further interaction.
Medium 1
Medium 2
Boundary
ε

## Slide 10: MC transport in detail (4)
Silicon detector
Gold Target
Since particle is in vacuum again, it is moved across the next boundary
This time we are in a detector (active medium)
Detector response function is called for every step inside the detector which has access to the following information
  Position
  Momentum
  Energy loss
  PID
  Track length
  Time of flight

## Slide 11: MC transport in detail (5)
Sensitive Volume
1
2
Geant 3
1: entering
1: exiting
2: entering
2: exiting
Geant4/Fluka
1: entering
1: disappeared
2: entering
2: exiting
1: entering
1:exiting
2 MC points 3 MC points
Tracks are transported sequentially
Two possible ways
  Put particle 1 on stack
  Put particle 2 on stack
Handled differently by different MC
In CbmRoot
  Save info when particle is entering a sensitive volume
  Sum up energy loss while inside sensitive volume
  Write complete MCPoint to output when particle leave sensitive volume
 Only one MCPoint
Second case handled wrong