## Slide 1: The CBM experiment at FAIR  Overview of detector and technologies 
Facility for Antiproton and Ion Research
Compressed Baryonic Matter Experiment
Johann M. Heuser, GSI, Darmstadt
J-PARC Heavy-Ion Seminar – November 10, 2022

## Slide 2
Outline
very brief reminder of the physics aim of CBM
out of which the proposed experiment structure follows
and the chosen detectors and technologies
before we then overview those, a brief look at the status of FAIR and the site construction
finally, a short selected look at the demonstrator setup mCBM is made
… all sticking to a personal selection and depth of the matter, as the topics are quite extensive …

## Slide 3: Physics aim
Systematic exploration of QCD matter at large baryon densities, with high accuracy and (rare) probes.
Equation-of-state, phases
Hadron yields, collective flow, correlations, fluctuations
(Multi-)strange hyperons (K, Λ, Σ, Ξ, Ω)
production at (sub)threshold energies
Chiral symmetry
In-medium modifications of light vector mesons
ρ, ω, φ → e++e- (μ++μ-) via dilepton measurements
Hypernuclei
Charm production
Excitation function in p+A collisions (J/ψ, D0, D)
Charmonium suppression in cold nuclear matter

## Slide 4: Physics aim
Systematic exploration of QCD matter at large baryon densities, with high accuracy and (rare) probes.

## Slide 5: CBM and HADES experiments at SIS100
HADES SIS18  SIS100
CBM
forward spectrometer
polar angular acceptance 2.5 < Θ < 25 
full azimuthal coverage
configurations:
Hadron-Electron
Hadron-only
Muon
core functionality in all:
silicon tracking in dipole magnetic field
components laid out for
heavy systems (like Au+Au)
full event reconstruction up to (peak) interaction rate 107/s
CBM-HADES
sharing of same beamline
different target positions
different running times (HADES beam dump between CBM and HADES)

## Slide 6: FAIR and CBM sites under construction
CBM building
CBM cave
Fall 2022
SIS100 tunnel
beams to CBM: GeV 2-29 GeV (p), 2-14 AGeV (Ca), 2-11 AGeV (Au)
up to 109 ions/s on target

## Slide 7: FAIR and CBM sites under construction
CBM building
CBM cave
Fall 2022
SIS100 tunnel
beams to CBM: GeV 2-29 GeV (p), 2-14 AGeV (Ca), 2-11 AGeV (Au)
up to 109 ions/s on target
Civil construction proceeds well:
SIS 100 tunnel completed
transfer building
CBM building
NUSTAR sites …
further installations open
Accelerator components:
many available (SIS100 dipole magnets)
others (quadrupoles, …) impacted by sanctions due to Russia’s war on Ukraine
News, next steps: Scientific Review report, FAIR Council 12/2022

## Slide 8: A walk through the detector systems
Micro Vertex Detector (MVD)
Silicon Tracking Systen (STS)
Ring Imaging Cerenkov Counter (RICH)
Transistion Radiation Detector (TRD)
Muon Chambers (MUCH)
Time-of-Flight system (TOF)
Projectile Spectator Detector (PSD)
Data Acquisition System (DAQ)
configurations:
Hadron-Electron MVD, STS, RICH, TRD, TOF, PSD
Hadron-only
Muon
STS
MVD
RICH
TRD
TOF
PSD
MUCH (park position)
SC Dipole Magnet
beam dump
target
HADES
DAQ
~ 20 m

## Slide 9: A walk through the detector systems
configurations:
Hadron-Electron
Hadron-only STS, RICH, TRD, TOF
Muon
STS
MVD
RICH
TRD
TOF
PSD
MUCH (park position)
SC Dipole Magnet
beam dump
target
HADES
DAQ
~ 20 m
Micro Vertex Detector (MVD)
Silicon Tracking Systen (STS)
Ring Imaging Cerenkov Counter (RICH)
Transistion Radiation Detector (TRD)
Muon Chambers (MUCH)
Time-of-Flight system (TOF)
Projectile Spectator Detector (PSD)
Data Acquisition System (DAQ)

## Slide 10: A walk through the detector systems
configurations:
Hadron-Electron
Hadron-only
Muon STS, MUCH, TRD, TOF, PSD
STS
MVD
MUCH
TRD
TOF
PSD
RICH (park position)
SC Dipole Magnet
beam dump
target
HADES
DAQ
~ 20 m
Micro Vertex Detector (MVD)
Silicon Tracking Systen (STS)
Ring Imaging Cerenkov Counter (RICH)
Transistion Radiation Detector (TRD)
Muon Chambers (MUCH)
Time-of-Flight system (TOF)
Projectile Spectator Detector (PSD)
Data Acquisition System (DAQ)

## Slide 11: Silicon Tracking System
Main CBM detector for charged particle measurement incl. momentum determination.
track point measurement in high-rate collision environment: 105  107/s (A+A), up to 109/s (p+A)
physics aperture, position in dipole magnet:
   2.5    25, 0.2 m  z  1.1 m
  first four stations wider for better low-momentum particle detection (e.g. di-lepton program)
8 tracking stations
  radiation hard for several years of operation
  double-sided silicon microstrip sensors
  hit spatial resolution  (x) 15 µm, (y) 110 µm
self-triggering front-end electronics
  time-stamp resolution  5 ns
material budget:  0.3% – 1.5% X0 per station
  p/p < 2% (p > 1 GeV/c, 1 Tm field integral)
target
beam pipe
2.5
25
MVD
STS
p+C, 29 GeV
central Au+Au, 8 AGeV
UrQMD + GEANT + CbmRoot
in-STS decay, Au+Au, 10 AGeV
Dipole magnet: H-shape, 320 t, warm iron yoke/poles, cylindrical super-conducting coils in two separate cryostats with LHe cooling
opening: 144 cm (H), 300 cm (W),  120 cm (L)
coils: Nb-Ti filaments in copper matrix; 1749 turns
operating current 686 A, max. magnetic field in coils 3.25 T

## Slide 12: Environmental conditions for STS
Non-ionizing dose (FLUKA)
Sensors: < 1014 1 MeV neq over lifetime  cooling to -10 C
25 GeV/u Au+Au collisions; SIS300, CBM experiment in muon configuration.
1 month of “standard” running
corresponds to 109 Au ions/s on a 250 µm Au target yielding 2.6 x 1013 interactions
in its 1% nuclear interaction length.
Electronics:
< 1 Mrad over lifetime
 locate at detector periphery
25 GeV/u Au+Au collisions; SIS300, CBM experiment in muon configuration.
5 x 1013 interactions; Delta electrons produced at the target not included.
Total ionizing dose (UrQMD/CBMRoot/GEANT3)

## Slide 13: STS breakdown
front-end electronics board in cooling shelves
876 modules
in 132 variants
8 tracking stations
18 mechanical half-units
ultra-thin r/o cables (“micro cables”)
sensor
read-out + power electronics
106 ladders in 41 variants
material budget/station [%X0]
8/10 modules on CF support
system integrated in thermal enclosure
sensors at T ~-10 C (gas cooling)
electronics cooling through thermal interfaces (liquid NOVEC, T > -40 C)
services/ massive materials located at the periphery
includes target box, beam pipe
    module:
    2 x FEBs à 8 r/o ASICs/128 ch.
    2 x 8 ultra-thin read-out cable stacks
    double-sided silicon micro-strip sensor, 1024 strips per side
    system:
    ~ 1.8 million read-out channels
    ~ 14 000 r/o ASICs “STS-XYTER”
    ~ 40 kW power dissipation incl. all r/o + power electronics
front-end electronics
1.4 m
2.3 m
1.0 m
C-frame
many components of unique design, precisely matching their specific location
FEE

## Slide 14: Sensor, FEE, microcables, assembly
vendor (~25 C)
GSI (~22 C)
TAB bonding
microcables: Al-polyimide, 2× 14+10 µm thick
SMX2.2, a 128 Channel, Event-Driven Tracking Chip for Silicon and Gaseous Detectors
radiation hardness
fast path: timing 3.125 ns
slow path: amplitude measurement 0-12 fC, 8bit ADC
P=8.5-10 mW/channel (incl. logic)
data rate: 9.41 – 47 Mhit/s/ASIC
UMC 180 nm
module, pre-series assembly
ladder
Al traces 20 µm wide, at 166 µm pitch
ASIC
sensor
wire bonding
wedge tool
Al wire (typ. 25 µm  )
Delvotec G5
microcables + chip
FEB
Hamamatsu
  type n, 320  15 µm
  resistivity < 8 kOhm·cm
  double-sided, 0/7.5 strip angle
  p-side with 2nd metal routing
  1024 channels/side , 6 cm wide
  strip pitch 58 µm; AC read-out
  strip lengths: 2/4/6/12 cm
tab tool
arXiv:1506.05168

## Slide 15: STS – performance simulations
Bx,y [T]
z [cm]
0
40
20
60
80
-20
-40
STS top view – MC hits
position in magnetic field
target
primary-track efficiency
momentum resolution
Au+Au, 12 AGeV/c, 1 T
> 97%
GEANT model with active and passive materials (v21e)
Au+Au, 12 AGeV/c, 1 T
pT – y coverage

## Slide 16: Micro Vertex Detector
MIMOSIS 1: full-scale prototype
state-of-the-art MAPS technology
CVD diamond / TPG carrier for heat evacuation to heat sink
Material budget:
  O(0.5 %) (x/X0) /station
  First station in VX: O(0.3 %) (x/X0)
~300 CMOS sensor chips
extends momentum reconstruction for charged particles down to about 300 MeV/c
enables secondary vertex reconstruction for weak decays of charmed hadrons, precision significantly better than 100 μm for decay products with plab > 1 GeV/c, benchmarked by the D mesons (lab) life time.
Monolithic Active Pixel Sensors operating in target box vacuum ∼ 10−4 mbar
Radiation hardness > 7 × 1013 n/cm2, > 1 Mrad (back/top biasing)
Operation temperature -10 C  liquid NOVEC cooling
 5 µm spat. resol.
 150 W total
 ~ 105coll./s
from standard MAPS
to modified with gap

## Slide 17: Ring Imaging Cherenkov Detector
CO2 radiator gas, vessel volume 2.2 × 6 × 5.06 m3 (l × w × h) = 67 m3
  p-threshold 4.65 GeV/c, n=1.00045, UV cutoff 180 nm
13 m2 segmented glass mirrors with reflective Al and protective MgF2 coating 80 tiles, 6 mm thick, R=3m, focal length 1.5m
photo detector planes:
  MAPMT (H12700) readout (1000 pcs), 64k ch,
  DIRICH readout chain: quasi free-streaming FPGA-TDC readout, leading trailing + edge time measurement
special challenge: B-shield down to 2-3 mT
Cherenkov Radiation: Charged particle travelling faster than speed of light in the respective medium radiates light at Cos(Θ) = 1/(n ) = vl/vp  threshold Cherenkov
emitted light may be focussed onto a circle with rcirc~ Cos(Θ) ~ 1/vp
RICH signature + momentum reveals particle type
CBM MAPMTs in HADES RICH
hadron suppression ~ 104
DIRICH readout modules
 di-electron + hadron programs

## Slide 18: Transition Radiation Detector
electron identification at high momenta (p ≳ 6 GeV/c) where RICH alone is not longer effective  pion suppression factor of 10 − 20 (SIS100)  RICH + TRD (+ TOF): > O(104)
identification of fragments (e.g. d ⟷ 4He) via specific energy loss measurement (dE/dx) → resolution ~30 %
four-layer TRD adds tracking capability:
  Tracking between STS and TOF detectors  good space point resolution of ~ 300 μm
  Works at high interaction rates (up to 10 MHz)  r/o ASIC SPADIC (Self-triggered Pulse Amplification and Digitization ASIC)
Sudden change of ratio:
⇒ emission of e.m. radiation ⇒ change of n: TR
entrance window
cathode pad plane
25 µm Kapton + 50 nm Al
– Al coating is drift cathode, also moisture barrier
– TR absorption trough Al, 5 keV in 50 nm Al: 99,7% transmission
mTRD demonstrator
electrons: dE/dx + TR
rest (pions): dE/dx
pads read-out by independent channels
TRD2D variant demonstrated: triangular pad read-out and
paired signal amplification
(short)
counting gas mixture:
Xe/CO2 (85/15) (optionally Ar/CO2 (80/20)
high absorption cross section for photons in the TR spectral range
PE foam/ fibers/ foils

## Slide 19: Muon Chambers
track, vertex and momentum reconstruction
muon identification
global tracking
particle identification via time measurement
Silicon Tracking System (STS)
Muon Absorber and Chamber System (MUCH)
Transition Radiation Detector (TRD)
Time of Flight Detector (TOF)
instrumented hadron absorber
muon: heavy lepton, mass 106 MeV
  little multiple scattering + Bremsstrahlung
  very long absorption length in matter
separate muons from hadronic (strongly interacting) background
energy dependence  energy filter for Muons
Each station with three tracking layers.
GEM detector technology
Trigger RPCs MUCH 3 and 4
robust
low-cost
fast
~ 1 ns single-gap
~50 ps for multi-gap
MUCH-XYTER based readout
Ar+CO2 70:30

## Slide 20: Time-of-Flight
ToF Requirements
Full system time resolution σT ~ 80 ps
Efficiency > 95%
Rate capability  50 kHz/cm2
Polar angular range 2.5° – 25°
Active area of 120 m2
Occupancy < 5%
Low power electronics (~120.000 chs)
Free streaming data acquisition
Inner
wall
Outer wall
Charged particle flux at L = 8 m from target
FLUKA Au+Au at Ekin = 11A GeV, 107/s
X [cm]
Y [cm]
flux [Hz/cm2]
Detectors with different rate capabilities and granularities needed as function of polar angle.
Inner wall: MSMGRPCs
highest counting rate
highest granularity
~15 m2 active area (up to Θ 11°)
modular architecture
  12 modules, 4 types
Symmetric structure: 5 gaps × 2 stacks
Gas gap thickness: 200 μm
Active area 60/100/200 mm × 300 mm
Resistive electrodes: ~1010 Ωcm, 0.7 mm Chinese glass
Strip structure for Readout & HV electrodes
Differential readout
σT = 67 ps
90%C2H2F4 + 5%SF6 + 5%iso­C4H10
NINO FEE (ALICE Coll.) + CAEN TDCs
charged hadron identification through Time-of-Flight measurement
tToF = tsp – tst – offset(s)
(CBM: L = 6 m)
p
K

T0 (tstart) concepts
in beam:
  diamond counter   30 – 40 ps , 100 kHz rate limit
  LGADs alternative for light systems
software solution
  fast particles in (semi) central collisions
fragment counter surrounding beam pipe
Multi-gap Resistive Plate Chambers
TRPC  40ps
various variants for CBM:
# gaps, glass type + thickness, strip lengths + pitch, outer dimensions, impedance
eTOF @ STAR
cosmics test stand

## Slide 21: Projectile Spectator Detector
Nspec = Aproj +Atarg −Npart
N produced particles ~ Npart "wounded nucleon"
determination of centrality and even plane of the collisions
Wanted: "reaction plane"
defined by vectors of beam direction and impact parameter
no direct measurement possible.
Instead: “event plane”
determination with a “Forward Wall Detector”
compensating sampling calorimeter
sandwich Pb/Scint ratio 4:1
44 modules, aperture 0.21° < Θ < 5.7°
6.5 l, good energy resolution ~55%/√E
light readout from a section through
WLS fibers by photodiodes
20 × 20cm beam hole in the center, reducing radiation damage
total 22 tons of weight on a platform movable in 3 dimensions
PSD as proposed in TDR
Many physics variables are highly dependent on the centrality: kinetic freeze-out temperature, multiplicity of produced particles, flow...
scintillators BC408 + SIPMs
CBM hadron setup with PSD replaced by a FWALL?

## Slide 22: mCBM @ SIS18
CBM full-system test-setup,
a slice in  of CBM detector systems, Θ = 2.5 – 25
set up from 2017/18 at HTD detector test area of SIS18
commission and optimize the complex interplay of the different detector systems with the trigger-less streaming data acquisition and the fast online event reconstruction and selection.
test detector and electronics components developed for CBM, as well as the corresponding online/offline software
under realistic experiment conditions up to the top CBM interaction rates of 10 MHz.
beam on target

## Slide 23: mCBM @ SIS18
high-rate tests with TOF – RPCs (2021)
mSTS demonstrator (2021)
O+Ni at 2 AGeV, 1010 ions per spill, ~ 500 kHz int. rate
2 tracking stations
4 mechanical units
11 modules (various prototype component versions, 2017 – 2021)
mounted on 5 detector ladders with carbon-fiber support frames
2 AGeV 16O beam, 10 s spills
4 mm Ni target
108 – 1010 beam particles/s
208Pb+Au at 1MHz
offsets corrected
time correlation and stability of subsystems (2020)
a look at few of the many results
[ps]

## Slide 24: mSTS performance (2021)
Operational!
Just few r/o ASICs not read-out, few individual channels missing/masked
3D hits maps, projections onto tracking layers
Charge calibration: MIPs clearly in range
YY
XX
inside time window (-100, +100) ns
Correlations of hit pairs STS1:STS2 (hit time resolution 5 ns)
Fraction of correlated hits as function of r/o threshold
Target extrapolation STS1:STS2 with simplified alignment
Correlation mSTS0:TOF
first performance results match expectation
much more to come … analysis of mCBM campaign 2022
 = 0.028 cm
YY0 = 0.0655 cm
YY1 = 0.1099 cm
fits with simulation

## Slide 25: Summary
Acknowledgements
Much input and material used from my CBM colleagues, without explicit mentioning.
It’s a great pleasure, and trust in CBM, that STS modules from the pre-series production, and read-out components, will be used in the ongoing upgrade of J-PARC E16.
CBM requires detectors, as well as data transport, processing and analysis, capable of registering the imprints of high-rate nuclear collisions beyond example in heavy-ion physics.
Suitable state-of-the art techniques have been chosen in CBM-specific adaptations.
Prototypes detectors have been developed, performance tests made, showing the CBM requirements reached / in reach soon.
Construction of many systems is to start shortly, the site infrastructure is far advanced.
For deeper insight, refer to e.g. the Technical Design Reports as pointed to in the References.
Due to sanctions in response to Russia’s war on Ukraine, several components from Russia have become unavailable to the CBM project, entire teams are suspended from the Collaboration. E.g. the superconducting dipole magnet - efforts on replacement are being made.

## Slide 26
CBM-STSモジュールを楽しみにしています 2023年春のJ-PARC E16実験で

## Slide 27: References
CBM Collaboration: https://www.cbm.gsi.de
Status and Perspectives of the CBM experiment at FAIR N. Herrmann, Proc. SQM 2021 EPJ Web of Conferences 259, 09001 (2022) https://doi.org/10.1051/epjconf/202225909001
CBM Progress Report 2021: https://repository.gsi.de/record/246663
CBM Technical Design Reports: https://www.cbm.gsi.de/documents