## Slide 1
A SHOT ON NArCoS
THE NEW NEUTRON HODOSCOPE
PAGANO EMANUELE VINCENZO
(LNS-INFN)

## Slide 2
Idea for a new Neutron Hodoscope
6.4 cm
6.4 cm
300 μm
32 strip front
32 strip back
Δstrip = 2 mm
Interstrip = 0.1 mm
T
DSSSD 32x32
300 μm
NArCoS
≈ 12 cm
CP
n
100/150 cm
50/75 cm
3x3x3cm3
SiPD
EJ276G
To realize a prototype of detector able to detect at the same time charged particles and neutrons with high energy and angular resolution for reaction studies and applications
Candidate: The plastic scintillator EJ276-Green Type (ex EJ299-33) (3x3x3cm3)
1 cluster: 4 consecutively cubes -> 3x3x12 cm3
Neutron detection efficiency ≈ 50% for the prototype
Reading the light signal: Si-PM and digitalization
Modular, reconfigurable (in mechanic and electronic)
Discrimination of n/γ from PSD (but also light charged particles)
Energy measurement from ToF (Δt≤0.5 ns with LToF≈1÷1.5m)
TOF measured using the RF of the CS or with an ancillary MCP (low intensity exotic beams)
NArCoS (Neutron Array for Correlation Studies)
Neutron-particles correlations (HBT)
Reaction Dynamics and time scale
Symmetry Energy in EoS of nuclear matter
Nuclear structure of unbound exotic nuclei
In medium nuclear interaction
Nuclear astrophysics (neutron stars and nucleosynthesis processes)
Medical application (neutron production cross section, differential cross sections)
Detector
Physic cases
  NuSym23 – GSI Darmstadt, Germany - 22 September 2023
E. V. Pagano. LNS-INFN
1

## Slide 3
PSD studies using sources
Detector | FoM
i-Spector + EJ-276 | 0.98
i-Spector + EJ-276G | 1.47
PMT + EJ-276G | 1.03
EJ-276 + i-Spector
EJ-276G + i-Spector
E.V.Pagano, G. Politi, A. Simancas et al., in preparation
Detector Configurations:
  EJ-276G + PMT
  EJ-276 + i-Spector
  EJ-276G + i-Spector
Lab measurements with radioactive sources:
  Vacuum Chamber
  Pb shield
  Gamma sources: 133Ba, 137Cs, 60Co, 152Eu
  Alpha source: 241Am
  Digitizer from CAEN
Example of signal and integration windows
Results
Pagano E.V. et al., N.S., Nucl. Instrum. Methods A, 889 (2018) 83-88
Pagano E.V. et al., N.S., Nucl. Instrum. Methods A, 905 (2018) 47-52
Pagano E.V. et al., IL NUOVO CIMENTO 41 C (2018) 181
Pagano E.V. et al., JPS Conf. Proc. 32, 010096 (2020)
Pagano E.V. et al., IL NUOVO CIMENTO 43 C (2020) 12
Pagano E.V. et al., J. Phys.: Conf. Ser. 1643 (2020) 012037
Pagano E.V. et al., IL NUOVO CIMENTO 45 C (2022) 64
Particle Identification Paramenter
  NuSym23 – GSI Darmstadt, Germany - 22 September 2023
E. V. Pagano. LNS-INFN
2