## Slide 1: HTS beam transfer magnet
T. Winkler, C. Mühle, C. Roux, P. Spiller, K. Sugita

## Slide 2: Motivation
Beam transfer magnets at GSI:
DC and fast switching between shots
superferric H-Frame magnets
High energy consumption
(almost) Ideal geometry for pancake coils

## Slide 3: Magnet parameters
Change of infrastructure to be minimized, e.g. same power converter
Coil parameters:
  2x 100 turns
  535 A, 85.4 V
  387.4 mH
  DC power: 45.7 kW
Magnet parameters
  1.6 T
  1 T/s
  12.5° at 8 ¼ m radius
Cycle duration
  From sec to hours
mainly inductive load
  130 V @ 334 A/s (1 T/s)
  55.4 kJ

## Slide 4
Idea: “drop-in” replacement of copper coil
High current density in HTS tapes
  => coil will be smaller
  Free space can be used for cryostat and cooling
Magnet layout

## Slide 5
AC loss
  Coil layout (cross-section)
  Coil position in yoke
Thermo-Mechanical Design
  Thermal design for coil and cryostat
  Mechanical design for coil and cryostat
  Cooler-choice
Ongoing Studies
S-FRS Dipole FoS

## Slide 6
JC(T,B,θ) for Theva ProLine tapes
AC loss estimate with high field approximation from last yesterday:
Coil split in two regions:
  In yoke
  Outside of yoke
Sum: ~1 kJ/cycle
AC loss

## Slide 7
Thank you very much for your attention.
Question?
HTS beam transfer magnet