## Slide 1
MATerials Research
(FAIR Phase 0, ES, FS, FS+, FS++...)
María Eugenia Toimil-Molares – Research Retreat – July 2023

## Slide 2
Functional Isoporous membranes
Single-nanochannel sensors
Size-dependent properties of nanowires
Nanowire assemblies
for energy applications
Materials Research with Swift Heavy Ions
I. Ion-Track Nanotechnology
Activities included in POF – Matter – MML – RT2 (Complex and functional materials, quantum materials)

## Slide 3
Functional Isoporous membranes
Single-nanochannel sensors
Size-dependent properties of nanowires
Nanowire assemblies
for energy applications
ions
Materials Research with Swift Heavy Ions
I. Ion-Track Nanotechnology
II. Heavy-Ion-induced modifications
Activities included in POF – Matter – MML – RT2 (Complex and functional materials, quantum materials)
Functional materials
Space electronics
Nanomaterials
Molecules
from
bulk
to
nano

## Slide 4
Ion penetration range
Pressures of up to ~50 GPa
Energy loss
Functional Isoporous membranes
Single-nanochannel sensors
Radiation hardness of functional materials
High-pressure irradiation
Size-dependent properties of nanowires
Nanowire assemblies
for energy applications
ions
Materials Research with Swift Heavy Ions
I. Ion-Track Nanotechnology
II. Heavy-Ion-induced modifications
III. Materials under Extreme Conditions
Temperature
High Pressure
Activities included in POF – Matter – MML – RT2 (Complex and functional materials, quantum materials)
Functional materials
Space electronics
Nanomaterials
Molecules
from
bulk
to
nano
Ion Irradiation

## Slide 5
Ion penetration range
Pressures of up to ~50 GPa
Energy loss
Radiation hardness of functional materials
High-pressure irradiation
Functional Isoporous membranes
Single-nanochannel sensors
Functional materials
Space electronics
Nanomaterials
Molecules
Size-dependent properties of nanowires
Nanowire assemblies
for energy applications
from
bulk
to
nano
ions
Materials Research with Swift Heavy Ions
I. Ion-Track Nanotechnology
II. Heavy-Ion-induced modifications
III. Materials under Extreme Conditions
MAT-program at existing facilities
Cave A  APPA Cave
Temperature
High Pressure
Ion Irradiation

## Slide 6
UNILAC
SIS18
SIS18
SIS100
Super-FRS
CBM
NUSTAR HEB
UNILAC
MAT@CRYRING
Cave A
M-branch
X0
UNILAC (3-11.4 MeV/u)
Ion range up to 100 µm
SIS18 (80-1000 Mev/u)
Ion range ~mm-cm
High energy / ion range
tests of space electronics and materials
irradiations at high-pressures
radiation hardness of materials
ion-track nanotechnology
ion-induced materials modifications
astrochemistry
Highest ion energy loss
CRYRING: Highly charged ions
at low kinetic energies
Science at existing facilities
ion-surface interaction

## Slide 7: Facilities
Important for MAT collaboration:
flexible beam conditions
various ion species, energies, fluxes….
versatile target stations
online and in-situ analysis
efficient sample irradiations
Highest ion energy loss
Large ion penetration range
Highly charged ions
at low kinetic energies
Higher intensities
Higher energies
Worldwide largest combination of swift heavy ion beams for Materials Research
MAT Collaboration:
~ 200 collaboration members from 27 countries
~ 40 groups served per beamtime
~ very interdisciplinary (materials science, chemistry, geology, biology, nanosciences,…)

## Slide 8: Materials under extreme conditions
High-pressure irradiation setups
Required beams
Higher ion flux > 1e9 U-ions/s
Higher ion energy
Multipurpose-target station with in-situ and online analytics
APPA cave
MAT stations
HED@FAIR
SPARC
BIOMAT beamline
SIS18
SIS100
Super-FRS
CBM
NUSTAR HEB
APPA cave
Development and testing with SIS-18 beams
Betriebsgenehmigung for all GSI caves *1e9 U-ions/s
High intensity pulsed beams
APPA cave
Cave A
yes
yes
yes
no*
?
no

## Slide 9: High-pressure irradiation setup I
Prototype setup with online Raman spectroscopy ready
Total space: ~ 2 x 3 m2
Further developments in 2023-2025 (collimation, automatic sample exchange system, remote control of motors …)
Ready for FAIR day-1 exp
Collimator
Raman Head
Optical fibers to spectrometer
DAC
Camera
Ion beam
Motorized axes
Laser table (1 x 1 m)
Mobile setup
Prof. B. Winkler, Bayarjargal, Liang, Merges, Schröck

## Slide 10: High-pressure irradiation setup II
2023-2025: design, collimation, positioning and cooling systems,…
Ready for FAIR-day 1 experiments
Paris-Edinburg Cell (PEC)
Sample size ~ mm2
Pressure up to ~12 Gpa
Tmax ~ 600 °C
Exchange magazine and positioning platform
Automatized exchange of inner pressure cell
Irradiation and in-situ analysis of up to 12 samples
Prof. L. Tacjmanova, Cionoiu, Glasmacher, Blum, Faller (Uni Heidelberg)

## Slide 11: Radiation hardness setup
APPA cave or intermediate locations:
New facility to study dynamic response of beam-facing materials on site
Fast extraction of high-intensity pulsed beams (intensities up to 1010 pps)
High energy – larger volumes of radiation damaged and thermally excited material
Monitoring of ion-pulse induced stress waves
Applications:
High-power accelerators: targets, collimators, beam windows and beam dumps
High temperature reactor materials
Space materials
Shock and Vibration (2021) 8884447
Multipurpose chamber:
Radiation resistant carbon fiber composite windows
Remote-controlled sample exchange system
In-situ analysis techniques
Space: 2 x 1 m2
BMBF VF application in 2024 (Univ. of Münster)

## Slide 12: Timeline
María Eugenia Toimil-Molares – Research Retreat – July 2023
2024
2026
> 2030
2025
2027
2028
2029
2030
Experimental program of MAT collaboration at existing facilities (UNILAC & HELIAC / SIS 18)
M-branch
X0
Microprobe
MAT @ CRYRING
Cave A
Preparation/ testing of new setups for APPA cave

## Slide 13: Timeline
María Eugenia Toimil-Molares – Research Retreat – July 2023
2024
2026
> 2030
2025
2027
2028
2029
2030
Experimental program of MAT collaboration at existing facilities (UNILAC & HELIAC / SIS 18)
SIS100  APPA Cave
M-branch
X0
Microprobe
MAT @ CRYRING
Cave A
Preparation/ testing of new setups for APPA cave

## Slide 14: Timeline
María Eugenia Toimil-Molares – Research Retreat – July 2023
2024
2026
> 2030
2025
2027
2028
2029
2030
Experimental program of MAT collaboration at existing facilities (UNILAC & HELIAC / SIS 18)
M-branch
X0
Microprobe
MAT @ CRYRING
Cave A
SIS18  SFRS  Ring branch
SIS100  SFRS  Ring branch
SIS100  CBM
SIS100  APPA Cave
Possibilities for BIOMAT presented to ECE and JSC last June
Preparation/ testing of new setups for APPA cave
limited intensity 

## Slide 15: Intermediate MAT locations in ES/FS/FS+
SIS18
SIS100
CBM
Ring-branch @S-FRS
APPA cave
MAT beam requests:
    intensities > 1e9 U-ions/s
heavy beams (Z ≥ Au, preferred U)
slow and fast extraction
energy range 180 - 500 MeV/u
“small” beam focus < 5 mm
Space: 2 x 3 m2
2 possible locations identified
Discussions with colleagues A. Senger, P. Gasik, S. Ratschow, H. Simon, and H. Weick are thankfully acknowledged.

## Slide 16: Early Science (ES) and FS at ring branch
Advantages for MAT:
high flux beam available
sufficient space available
MAT and BIO setups compatible
beam focus ~ few mm for 200-600 MeV/u U ions
access to SIS-18 and SIS-100 beams
More detailed plans in progress (ECE recommendation):
FLUKA calculations for MAT beam parameters  local shielding needed?
planning of common beamline for BIOMAT
access to site for sample exchange or other needs?
(it is a tunnel, not a cave…)
S-FRS
Ring branch
BIOMAT
María Eugenia Toimil-Molares – ECE Meeting - May 4th 2023
María Eugenia Toimil-Molares – Research Retreat – July 2023

## Slide 17: Early Science (ES) and FS at ring branch
Planning of common BIOMAT beamline until the next ECE in November 2023:
Ionoptic calculations
Design of BIOMAT beamline (beamline, diagnostic chambers, instrumentation…) such that they can be transferred to the APPA Cave once it becomes operational.
Cost estimate for beamline.
In-kind GSI contribution for BIOMAT in APPA Cave:
Target handling (1.3.5.2) + Control room (1.3.5.7) + Beamline instrumentation (1.3.5.8) → 531 k€ (in 2005 prices)
Diagnostic chambers (BIOMAT)
MAT Setup
Mobile
In preparation
BMBF ErUM funded
Beam dump
MAT Setup

## Slide 18: Intermediate location in CBM cave
MAT@CBM: explored as backup option if ring branch would not work
Advantages for MAT:
high flux beam available before FS++
sufficiently small focus at HADES target position for 400 MeV/u U ion beam.
Discussions ongoing:
FLUKA calculations to estimate MAT experimental conditions that do not affect CBM detector or electronics.
SIS100
CBM
HP setup
María Eugenia Toimil-Molares – ECE Meeting - May 4th 2023
2 x 2 m2
María Eugenia Toimil-Molares – Research Retreat – July 2023

## Slide 19: Beamtime requirements in 2026/27
María Eugenia Toimil-Molares – Research Retreat – July 2023
2024
2026
> 2030
2025
2027
2028
2029
2030
Continuation of experimental programs at MAT existing facilities (UNILAC / HELIAC / SIS 18)
M-branch
X0
Microprobe
MAT @ CRYRING
Cave A
SIS18  SFRS  Ring branch
SIS100  SFRS  Ring branch
SIS100  CBM
SIS100  APPA Cave
Possibilities for BIOMAT presented to ECE and JSC last June
Preparation/ testing of new setups for APPA cave

## Slide 20: Beamtime requirements in 2026/27
María Eugenia Toimil-Molares – Research Retreat – July 2023
2024
2026
> 2030
2025
2027
2028
2029
2030
Continuation of experimental programs at MAT existing facilities (UNILAC / HELIAC / SIS 18)
M-branch
X0
Microprobe
MAT @ CRYRING
Cave A
SIS18  SFRS  Ring branch
SIS100  SFRS  Ring branch
SIS100  CBM
SIS100  APPA Cave
Possibilities for BIOMAT presented to ECE and JSC last June
Preparation/ testing of new setups for APPA cave
More access to SIS18 beams to commission and test new setups, and support and enlarge the pillar III community.
UNILAC and CRYRING beams for continuation of experimental programs.
Sufficient beamtime for third-party funding projects, PhD students, young scientists, and users of the MAT collaboration.

## Slide 21: MAT & HELIAC
María Eugenia Toimil-Molares – Research Retreat – July 2023
MAT activities would profit from access to HELIAC: stable beam, higher efficiency.
MAT research activities at HELIAC at ~ 7 MeV/u.
Opportunity for technology transfer:
  - nanotechnology
  - heavy ion microprobe for nanostructuring, electronics and detectors tests,…
https://www.it4ip.be
Interest in roll production of etched ion-track membranes at GSI expressed by:
Roll irradiation device
@ GANIL
Jon de Tech pilot line for nanowire plating in Hofstetter PCB Plating in Herrenberg.

## Slide 22: Summary
María Eugenia Toimil-Molares – Research Retreat – July 2023
Materials under extreme conditions experiments require higher ion fluxes than currently available in cave A.
    In Cave A: limited flux, high-intensity pulsed beams for radiation hardness not possible, and high-pressure irradiations are very inefficient (very long times for fluence accumulation)
Temporal locations for MAT prior to APPA cave: Ring branch at S-FRS and CBM cave.
Diagnostics and setups for BIOMAT to be transfered to APPA cave as soon as it is available.
Addtitional core personnel requested for installation and operation of new FAIR MAT facilities.
Very limited lab space. Labs in APPA cave won’t be accessible soon.
All MAT activities continue at the current facilities.
Activities will profit from access to HELIAC: stable beam, higher efficiency, and possible technology transfer.

## Slide 25: Summary
All MAT-stations will remain in operation as the large variety of ion species as well as a wide range of energies, beam intensities, and analytical tools are essential for the MAT collaboration.
Alternative locations for MAT-program in APPA Cave (Materials under extreme conditions):
Cave A (HTA):
    - Limited flux conditions (max. 1e9 ions/s) by the GSI Operating Permit.
                - High-intensity pulsed beams for radiation hardness tests not possible.
                - High-pressure irradiations very inefficient (very long times for fluence accumulation).
Ring-branch at S-FRS is a very suitable intermediate location.
CBM Cave is an alternative in case ring-branch would not work. Ionoptics for E < 400 MeV/u needs to be clarified.
Both provide early access to high-flux beams for experiments under multiple extreme conditions.
Diagnostics and beamline shared by BIOMAT and covered by in-kind GSI contribution to BIOMAT in APPA cave.
Designed to be transferred to APPA cave once it is operational.

## Slide 26
Coupling extreme conditions
High static pressures
Up to 100 GPa
Diamond anvil cells
Pressures of up to ~100 GPa
Ion fluence up to 1013 i/cm2
Penetration depth (mm)
Ion Irradiation
Energy density ~ eV/atom
GeV heavy ions deposit enormous amount of energy in very localized volumes and in very short times
Temperature
High pressure
Ion Irradiation
Formation and stabilization of high-pressure phases - new properties!
Study of phases in Earth’s & rocky planet’s interiors
New thermodynamic paths for phase-transitions of bulk materials and nanomaterials
PRL (2006)
Nature Materials (2009)

## Slide 27: MAT Beamtime 2024 / 2025
UNILAC, M-branch and X0 beamline:
Sample irradiations for internal and external user groups
ion species: any ions between ~Ca and U
3.6 – 11.4 MeV/u
long pulses (1-4 ms) preferred
duty cycle (5 – 50 Hz)
Parallel operation of UNILAC beamlines

## Slide 28: High-pressure irradiation setup I
beam
collimator
250 µm aperture
200-500 MeV/u ions
goniometer
Raman spectrometer
Setup for irradiation of DACs
(diamond anvil cells)
Beam stops in sample
Beamtime 2022
Cave A
Ion-induced BI-BII phase transformation of 35 nm diameter Bi nanowires
New nanomaterials properties expected