## Slide 1: BIOPHYSICS status report
Research retreat
19.7.23
Marco Durante

## Slide 2: 1. Biophysics in FAIR-phase-0
1998 2022
Particle therapy
Space radiation protection
ESA reference facility for ground-based space radiation protection studies
Current ESA-supported programs ongoing: IBER/IRES/ROSSINI/GCRsim
ESA/FAIR Summer School in Darmstadt
EU programs: RADNEXT-HEARTS
First European center to treat patients with high energy 12C-ions (440 patients treated on site)
Now extensive research program in particle therapy covering from nuclear physics to molecular biology
Work supported by BMBF, EU (INSPIRE, HITRI, ERC AdG), NIH

## Slide 3: Biophysics at present facilities
Cave A
Cave M

## Slide 4
RIBs at GSI-FAIR
FRS-Cave M branch for RIB in biology & medicine
SIS18
FRS
Cave M
Commissioning of FRS-CAVE M (medical cave) beam line:
oxygen beams (June 2021):
Transmission FRS-Cave M 15O: 6%
15O in Cave M per 16O in SIS18: 6e-4
RIBs candidates at FRagment Separator (FRS):
Isotope | 12C | 11C | 10C | 16O | 15O | 14O
Half-life, min | stable | 20.4 | 0.32 | stable | 2 | 1.17
Intensities | ~ 106–109 particles per spill |  |  |  |  | 
Haettner et al., NIM-A, 2023

## Slide 5: Bio-PAC Beam Time Request (June 2022 – beamtime available in 2024-2025)
Year | Proposals (approved) | External (%) | Shifts | SIS18/ UNILAC (%) | Available (% of requests)
2017 | 12 (12=100%) | 5 (40%) | 77,8 | 91% | 29,8 (38%)
2020 | 27 (21=77%) | 16 (60%) | 118,5 | 90% | 50,7 (42%)
2022 | 28 (10=35%) | 16 (57%) | 81,4 | 98% | 23 (28%)
“Basic” beam request is 12C and 56Fe at 0.15-1 GeV/n
Notes: Proposals asking for UNILAC and for SIS beam are counted as one.

## Slide 6: 2. Biophysics Collaboration in ES/FS
BIOMAT

## Slide 7: Biophysics @S-FRS: the science case
The ERC AdG BARB elicited a large interest in exploitation of RIB in biology and medicine
BARB results show that 10C would provide the best range resolution, but its intensity at FRS-Cave M is too low for experiments
Institut Curie in the Biophysics Collaboration has proposed the use of RIB for minibeam radiotherapy
Recently, collaborators form the University of Strasbourg published a simulation on potential enhancement of biological effects using short-lived 8Li or 8He-ions
0.04 mm
0.7 mm
1.4 mm
4 spills, 19 s (Kostyleva et al., Phys. Med. Biol. 2023)
119 ms
837 ms
Synergy with NuSTAR tetraneutron experiment

## Slide 8: BIOMAT setup at ring branch tunnel
main separator
ring branch
HEB/LEB
Beam pipe
Diagnostic chamber 1
Diagnostic chamber 2
Valve (reference point)
Robotic arm with magazine
Beam dump
BIOMAT@S-FRS: beamline with exit window + 2 diagnostic chambers (originally planned for APPA) + BIO & MAT setups

## Slide 9: 3. Biophysics Collaboration in FS+

## Slide 10: Human exploration program
Artemis 1
Launch: 16.11.2022
Splashdown: 15.12.2022
Artemis 2: November 2024
Artemis 3: December 2025

## Slide 12: Galactic cosmic radiation: a potential showstopper for exploration
Durante & Cucinotta, Rev. Mod. Phys. 2011

## Slide 13: The NASA GCR simulator
Simonsen et al., PLoS Biol. 2020
33 beams
150 min/Gy

## Slide 14: The GSI GCRsim
Schuy et al., Front. Phys. 2020

## Slide 15: Energies >1 GeV/n
Durante et al., Phys. Rep. 2019
The GSI range modulator with the 10 GeV/n 56Fe-ion beam will set a world record in GCR simulation quality

## Slide 16: BIOMAT setup at the CBM cave
Irradiated targets
GCR simulator

## Slide 17: FLUKA simulations (courtesy of Anna Senger)
STS (inner Si-tracker

## Slide 18: Conclusions –(FAIR-phase-0)
The Biophysics Collaboration suffers from insufficient beamtime
It will be very important to have enough beamtime in 26-27 also to fulfill the many commitments in third-party projects
With the current outlook, a Bio-PAC is not necessary

## Slide 19: Conclusions –(ES/FS)
The Biophysics Collaboration has a strong scientific motivation in using S-FRS, which allows tests with very exotic beams whose intensity is too low at the FRS-Cave M beamline
Along with MAT, support can come from the already planned GSI in-kind contribution for the APPA cave + external funds (HI-Acts)
Setup is simple but new TDR can be prepared and submitted

## Slide 20: Conclusions – II (FS+)
The space radiation research program needs access to the maximum energy of SIS100 heavy ion beam
SIS100 energy will set a world record in GCR simulator quality
Support comes mostly from ESA and EU-HEARTS contracts
Setup is simple but new TDR can be prepared and submitted

## Slide 21: Thank you very much!
www.gsi.de/bio-coll

## Slide 22: 4. Resources for FAIR2028

## Slide 23: Cost-matrix APPA cave
531 k€
for BIO+MAT
Entirely already in the APPA budget

## Slide 24: TDR

## Slide 25: Additional funding for FS+/CBM cave