## Slide 1: A VHE ion beam irradiation facility at CERN (CHIMERA/HEARTS)
E. Johnson (SY-ABT-BTP)
With thanks to M. Fraser, P. Arrutia, M. Delrieux, R. Taylor, B. Mikulec, F. Velotti, D. Banerjee, D. Cotte, R. Garcia Alia, F. Ravotti, J. Mccarthy, S. Danzeca, M. Coly and many others
5th Slow Extraction Workshop at MedAustron, Wiener Neustadt, Austria
Monday 12th February 2024

## Slide 2: Outline
What is CHIMERA / HEARTS
Facility Overview
Slow extraction and technical aspects

## Slide 3: CHIMERA / HEARTS
Ion irradiation activities at CERN
  CHIMERA funded by ESA
  HEARTS funded by the EU
    High-Energy Accelerators for Radiation Testing and Shielding
    Objective: Accessible and available VHE ion beams to enable breakthrough space applications
      SEE testing to qualify electronic components for radiation hardness assurance
      Shielding and radiobiology studies for human spaceflight missions to the moon and mars

## Slide 4: Why High-energy heavy ions ?
Space agencies and industry wish to test non-de-lidded chips
  Requirement: High penetration range
Ideal solution: Pb82+ high range (>1mm in Si), high LET
Lower LET ions are of interest but only if able to quick swap
  Use case: test components sensitive to the lowest LET achievable with Pb82+, around 10 MeV·cm2/mg
  Idea: decelerate protons to 500 MeV as a bonus offer during irradiation
72 MeV/u
https://polymerinnovationblog.com/polymer-challenges-in-electronic-packaging-overview/

## Slide 5: Why CERN ?
Other labs
  Very scarce number of infrastructures that offer high-energy heavy ions for electronics testing
  Whereas the demand is increasing rapidly
CERN PS
  Transfer line from PS to East Area (F61 + T8) available which allow different optics
  Existing irradiation infrastructure
    IRRAD
    CHARM
  Large energy range (72 MeV/n – 5.4 GeV/n)
  Flux tuning through slow extraction

## Slide 6: Timeline
2021
1-day Pb run
(efficiency, ion charge state, beam instrumentation)
2022
5 days Pb run
(variable energy, intensity, beam size)
2023
HEARTS kick-off meeting
15 days Pb run
2024
First external users at CHARM
2025
TRL 6-7 for electronics testing at CERN and GSI
2026
Routine access for external users at CERN and FAIR
Deliverables 5/31
Milestones 6/23

## Slide 7: Facility overview
LINAC 3
LEIR
PS
East Area

## Slide 8
PS
F61
T08
IRRAD
CHARM
East Area

## Slide 9
East area – F61 transfer line
Dump Bending Dipole
F61

## Slide 10: East Dump
Extremely useful for parallel optics measurements
  Quadrupole scans and beam size measurements using BTV
  Initial parameter reconstruction
  Spill improvements
  Slow extraction studies

## Slide 11
CHARM
DUT

## Slide 12: Mechanical & electrical integration
MONTRAC
Diode
Preamplifier
Diode setup ready on the movable table
Diode on the movable table inside CHARM
Movable table
on MONTRAC
Cable chain
https://indico.cern.ch/event/1211404/

## Slide 13: Air scattering
Transfer line to IRRAD/CHARM has large air regions
The transfer line is scaled with energy but does not account for straggling effect (i.e. energy loss)
Increase of beam size through Multi-Coulomb Scattering
Transmission difficulty of low energy beam
Thanks Gianni and Frederik for Xsuite example ! 😊

## Slide 14
IRRAD
Move from CHARM to IRRAD Table 1

## Slide 15: Slow Extraction and technique
Uses magnetic septum SMH57 and SMH61
Bypass SEH23 (used only for p+)
  Windows would fully strip the beam
Amplitude growth done with third order integer resonance and SX

## Slide 16: Iteration on SX
Change tune Q with PFW, QSE, LEQ
  OK for high energy beams (5.3 GeV/u)
  ≤ 2 GeV/u no PFW
  Bunch rotation
  Flat QSE under resonance
  Ramp tune with LEQ
RF Knock-Out (RFKO)
  Constant extracted beam optics
  RF Excitation with transverse damper
  No bunch rotation (small dp/p)
  More stable at different energy (no PFW and chirp on damper excitation freq)
  Easier control of the beam intensity
Bare machine tune
Extraction
[1]
L. Badano et al., “Proton-Ion Medical Machine Study (PIMMS), 1,” CERN Document Server. Accessed: Dec. 16, 2022. [Online]. Available: https://cds.cern.ch/record/385378

## Slide 17: Intensity PS
Extracted intensity modulated with RFKO gain
Equation to apply to the TFB to keep the intensity uniform as a function of time → Idea for next run to have PID controller
Spill structure: 1kHz (RFKO) and 130kHz (frev/3)

## Slide 18: Degrader + Mask system
Degrader system
  Used to lower beam energy
  Measure the Bragg Peak
Mask system
  Shape beam into uniform regions
  Cheaper and easier than octupoles or rastering

## Slide 19: 2024 timeline
Beam and FLUKA studies
Experimental area integration studies (cables for ext. users)
Design and manufacturing of remotely movable degrader/mask system
Activity scheduling
Ions in PS
Cryostat installation in IRRAD
Start of run
End of run
Beam development and commissioning to T8
Beam development and commissioning to East Dump
2024 HEARTS@CERN run, including commissioning completion and beam characterization
Analysis, reporting…
T8 commissioning could be extended through upstream move and compatibility with IRRAD cryostat
MDs:
Priority preparation of user Pb run
IRRAD optics
RFKO MDs
Decelerate protons
Magnesium ?
2024
Jan
Aug
Sept
Oct
Nov

## Slide 20: Conclusion
CERN has a Very High Energy Ion irradiation campaign called HEARTS
  Sending Pb ion beam during two-weeks in November each year
  Offers wide range of energy at different intensities
  Available for external user
  Close collaboration with GSI such as to be two interchangeable facilities

## Slide 22: Extra

## Slide 23: Spill structure
Slow and fast frequencies time structure
Slow because of RFKO technique
  Software limitation to max chirp rep rate of 1 ms intervals
  1 kHz
  Could exploit low-pass filter effect of beam (transit time) by exciting at higher frequencies

## Slide 24: Spill structure
Fast spill structure at the fractional tune of third integer
  Frev/3
  ~ 130 kHz
  (beam still bunched and debunching during extraction)
650 MeV/n

## Slide 25: Beam profile
Optics model of the line
  Different beam sizes
MAD-X
  used for optimization
FLUKA
  for a more in-depth study

## Slide 26
Energy / momentum straggling
Courtesy: Andreas Waets
Air region in cyan
Non-linear straggling effect
Installation of vacuum chamber could become necessary

## Slide 27
Energy / momentum straggling
Courtesy: Andreas Waets
Air region in cyan
Non-linear straggling effect
Installation of vacuum chamber could become necessary
IRRAD Table 1
CHARM
BTV035

## Slide 28: RFKO
Emittance increase through RF excitation
Transverse Damper used as exciter
Notes: Chromaticity: tune dependence on momentum

## Slide 29: Comparison between gain
Intensity gain
Reproducible shape per gain
Peak shifts with gain
  Dynamic effect
  True for range of gains
  Amplitude Modulation with feedback

## Slide 30: Spill time profile
> 7 instruments to measure spill time profile
Gas scintillator (BCGAA/BXSCINT)
XSEC 23/70/94
XION 71/94
Diode
(BLM, SRAM, …)
BCGAA023
XSEC023

## Slide 31: Spill profile
Time resolution:
  20 ms for XION, XSEC
  2-3 ms for Diode
  0.5 ms for BXSCINT
  Finer sampling possible with BXSCAL (0.3-0.04 ms) and white rabbit (not logged) in F61 and Diode up to 0.5 µs
Notes: Mention that this is for a single gain and energy

## Slide 32: Spill time profile
Average time 360 ms
Longer spill time (~1000 ms) could be tested if needed
  Long flat top
  No bunch rotation
  Only GRPOS tune shift

## Slide 33: R&D
Signal generator
Exploit low-pass filter effect of beam (transit time) by exciting at higher freq
Variable gain during spill
Transit time (10-100 turns)
Remote app
  Send python commands
  Continuous chirp

## Slide 34: RFKO amplitude control
RFKO Turn ON and OFF

## Slide 35: Magnetic rastering
Horizontal and vertical deflection using dipole magnets
  Spiral inwards/outwards
  TBD requirement on
    Sample size
    Uniformity (+- 5% ?)
Drawback
  Constant intensity needed
  Constant optics during the spill
  Complexity of the power converter to pulse at positive and negative current
Optics TBD
  Beam size for painting

## Slide 36: Beam energy and flux operator GUI

## Slide 37: Duty Factor

## Slide 38: Octupoles
Use of octupoles at NASA Space Radiation Laboratory (NSRL)
  Third order magnetic optics
Uniform beam of 10x10 to 20x20 cm^2
Clean and simple process
  No collimation or interaction with matter
Requirement: gaussian distributed beam
Jang, Ji-Ho, Hyeok Jung Kwon, Yong Sub Cho, and Wha Ryun Lee. 2011. “Uniform Irradiation in a PEFP 100-MeV Beam Line with Octupole Magnets.” Journal of the Korean Physical Society 59 (2(2)): 604–9. https://doi.org/10.3938/jkps.59.604.
Tsoupas, N., L. Ahrens, S. Bellavia, R. Bonati, K. A. Brown, I-Hung Chiang, C. J. Gardner, et al. 2007. “Uniform Beam Distributions at the Target of the NASA Space Radiation Laboratory’s Beam Line.” Physical Review Special Topics - Accelerators and Beams 10 (2): 024701. https://doi.org/10.1103/PhysRevSTAB.10.024701.
Tsoupas, N, L Ahrens, and K A Brown. 2007. “Uniform Beam Distributions at the Target of the NSRL Beam Transfer Line,” 3.
Tsoupas, N, S Bellavia, R Bonati, K Brown, I-Hung Chiang, C J Gardner, S Jao, et al. n.d. “Uniform Beam Distributions at the Target of the NSRL Beam Transfer Line,” 23.