## Slide 1: Crystal assisted slow extraction in the SPS – focus on latest progress
F. M. Velotti, L.S. Esposito, M. Fraser, P. Arrutia, S. Gilardoni, B. Goddard, V. Kain, E. Matheson, S. Solis Paiva, R. Seidenbinder
Seidenbinder

## Slide 2: Routine operation with local shadowing
Since 2021, TECS (local crystal) in operation in VR with intensities [1e13, 4e13] protons per extraction
Consistent ~30% loss reduction: crystal 2/3 and new ZS 1/3
  Cannot use crystal in channeling as beamlet lot in transfer line to targets
Clearly visible in residual activation measurements of the area

## Slide 3: Non-local shadowing machine results
Simulations agree very well with data (needed some iterations though)
Still to explore fully the combination of 2 crystals: one local and one non-local  first results in the machine were rather good
  Almost x3 loss reduction wrt 2018 losses at ZS
Data
Simulations
No crystals
TECA
TECA + TECS

## Slide 4: Non-local shadowing machine results
Clearly seen local loss reduction and no increase elsewhere (except at the crystal, as expected)
Non-local
crystal
ES
Transfer line + extraction region
SPS

## Slide 5: Practical problems
Design:
Large parameter space and simulations are rather lengthy – need to simulate SX process
  Crystal widths, bending angle, (angle, position), number of crystals…
Operation:
SPS closed orbit changes in time – hysteresis, magnets variations, non-ideality of converters, etc.
  Pulsed machine inherently less stable than a coasting one
TECS and TECA suffer of backlash
  Active backlash compensation already hidden in the low-level controls, but still error between CTRL and LVDT changes in time (depending on history of movement also)
  Resolution of movement lower than loss reduction acceptance
Crystals have small acceptances
  For shadowing, this a 2D problem: angle and position wrt ZS  scans are too slow
  Wrong settings of crystal can deflect beamlet on ZS or SPS aperture and cause losses/damages  need low intensity for setting up

## Slide 6: Design

## Slide 7: Crystal parameter optimization
Relatively large parameter space to explore  for each configuration, need to find optimum angle and position for shadowing
It gets rather complicated for MVRA – also need to optimize for relative alignment of each crystal of the MVRA
Bayesian optimization is the perfect tool for this: derivative-free optimization, designed to be optimal for noisy objective function, can include prior knowledge easily
  Extensively used in ML for hyper-parameter optimization
  Extensively used in industry for complex system design
We used both simple BO and multi-fidelity Bayesian optimization
  MFBO help to significantly reduce the time needed for optimisation  also leads to better accuracy (just because longer exploration possible/feasible)

## Slide 8: Crystal parameter optimization
Accurate simulation take ~ 10 min  just a waste of time/resources to run a full grid scan in a 6D space
Made cheap surrogate (NN) with a few low-particles simulations
Run multi-fidelity optimization to get optimal configuration for MVRA
  Basically, optimization done on simulations with very large number of particles as only run a few times
Direction | Angle (urad) | Position (mm) | Width (mm) | Relative angle (urad) | N. Crystals (1)
VR to inside | -789 | -16.03 | 1.4 | -7 | 5
VR to outside | -562 | -15.96 | 1.3 | -9 | 5
parameters
Add low or high-fidelity data to dataset
Update surrogate model
Get next point: low or high fidelity
ZS losses
MVRA parameters

## Slide 9: Commissioning

## Slide 10: Control crystal in LVDT “settings”
High level controller (simple PID) developed and tested in the SPS
  We could control the TECA using its LVDT (absolute position and angle measurement) instead of motor control  not affected anymore by non-reproducibility of position and angle of the crystal
  It allows to properly use numerical optimizers

## Slide 11: Optimum acceptance for shadowing
The main complexity to deploy shadowing in operation is given by the small optimum acceptance
For the SX shadowing, this is true both in angle and position
Easier when working in full VR, as for the local crystal  ~160 urad acceptance
  For the non-local one, it goes down to ~10 urad (this NOT channeling!!)
TECS
TECA
Acceptance for loss reduction

## Slide 12: Crystal setting up
For shadowing, we need to optimize 2 parameters: angle and position
  Can do with scans, but rather lengthy – SPS cycles are expensive!
  Need to low intensity – in some configurations, higher losses on ZS
Prepared NN to emulate simulations:
  NN(angle, position) = Loss at ZS
Bayesian optimization clearly best algorithm to use
Real machine data (TECA)

## Slide 13: Operation

## Slide 14: Operational test with nominal intensity
Operational test carried out  very important results:
  TECA can reduce losses x2 in this configuration also with high intensity
  Loss reduction is not resilient to machine stops or changes
    Major difference before and after long stop for MKDH cable replacement
    The good news is that the beam “drifts away”, hence we could catch this with “simple” feed-forward controller!
Drift from nominal loss reduction

## Slide 15: Continuous controller
Local shadowing with the TECS in VR has been working rather OK since re-start after LS2
  Angular acceptance is rather large, hence only once a month re-alignment needed: can do with numerical optimizer
Non-local shadowing with TECA has a very tiny angular acceptance: ~10 urad
  Showed already that cannot maintain loss reduction without adjusting for standard orbit drifts
Clearly seen the orbit drifting  change in loss reduction at the ZS

## Slide 16: CO distribution along the years
The CO seems the main contributor to the loss of shadowing during operation
The orbit seems to change quite a lot during the years and not possible to fully correct for it
  Only thing we could do is to flatten the extraction…but it is rather lengthy process  need to reduce intensity, remove extraction bump, stop extraction and then correct
  Not really feasible to do this often in operation

## Slide 17: Continuous control: models
The control problem is complex  no obvious way to know the direction in (angle, position) space of the optimum
The idea then is to use the BPMs in extraction regions (LSS4 and LSS2), ZS girder angle and to fit a model to predict optimal crystal alignment
  Gaussian process/Gradient Boosting/NN used for TECA: very high accuracy and uncertainty estimation
    + LVDT very accurate, + many points in separated in time of optimum, - small acceptance, - small dataset, - motor resolution
  NN for TECS: much more complicated due to the non-unicity of the solution (VR plateau)
    + loads of data, + large acceptance, - non-injective response, - very large LVDT noise

## Slide 18: Continuous control: models
TECA
Solved with a NN and partially with Gaussian Process and Gradient Boosting  NN better at finding good estimation far from training data
  GB tested in MD and first results very successful  expected NN to be better!
  Need to collect more data to make it robust – so far tested only in 1 MD
TECS
Needed quite large NN – finally had to compromise on output
  Robust solution seems to predict position of crystal and the estimate angle – pretty much linear relation
  Not so critical as TECA but still would be good to have
TECA

## Slide 19: Continuous control: models
TECA
TECS
TECA
Solved with a NN and partially with Gaussian Process and Gradient Boosting  NN better at finding good estimation far from training data
  GB tested in MD and first results very successful  expected NN to be better!
  Need to collect more data to make it robust – so far tested only in 1 MD
TECS
Needed quite large NN – finally had to compromise on output
  Robust solution seems to predict position of crystal and the estimate angle – pretty much linear relation
  Not so critical as TECA but still would be good to have

## Slide 20: Next steps
Keep improving f(BPMs, ZS)  TECS/A model:
  Need to test a few more models and methods to ensure high accuracy
  VAE to reduce dimensionality of BPMs for final model fitting
  Different NN architecture
  Collect data with deliberate orbit change (trim on orthogonal knobs in LSS4 and LSS2, change radial position at flat top) and find new crystal optima (next MD on shadowing)
Test MPC fitting NN on: f(BPMs, ZS, TECS/A)  losses
  It should be more robust  less sensitive to NN errors
  Data available should be enough
  Make a simple simulation model and test this approach
Test model on TECS and TECA

## Slide 21: Summary and outlook
Crystal shadowing offered many application for automation, advanced numerical optimization and machine learning
Used for both design stage and deployment in operation
Main issue so far is to deal with change over time of SPS closed orbit
  Fast numerical optimization models to quickly set up the crystal in shadowing  mostly operational, but more work ongoing to push performance
  Predictive models to build live controllers for both TECA and TECS on the way  first PoC done, but still quite some work to make them work consistently for long period of time
Aim to have online controller working this year and be able to test for long periods next year

## Slide 22: Thank you!

## Slide 23: Non-local shadowing machine results
Dedicated measurements with non-local crystal (TECA) started in 2022
Shadowing angle found rather quickly  55% loss reduction!!
Shadowing position clearly visible in AM scan  NOT channelling but only VR!
Configuration very reproducible using LVDT measurements of position and angle of the crystal
2022
33.5 mm

## Slide 24: Non-local shadowing - simulations
Optimal configuration for single crystal: 1.25 mm crystal with > 100 urad bend
Main advantage is that we exploit VR, hence easier to transport beam in transfer line
  Today we struggle to transport channelled beamlet to target in case of local shadowing
To reduce losses further, need to use Multi Volume Reflection Array (MVRA) crystals (see last workshop slides)
  Further simulations ongoing to evaluate the best configuration also considering local crystal
  Up to x10 loss reduction with 4-5 MVRA oriented (CH) towards the outside of the ring

## Slide 25: Introduction to crystal shadowing
SPS main physics users served with 4.8 s spill via 3rd integer resonant slow extraction
  About 3% of the beam lost on the ES
  Loss  activation  limit to the max proton on target (POT)
Crystal shadowing very promising
  Shadow the ES with thin bent crystal
  Already very good results obtained with local shadowing  x2 loss reduction in MDs and 20% reduction during physics (see later)
New facilities (hidden sector physics, Kaon physics…) require much larger POT than today  ~x4
Goal > Run 3

## Slide 26: Non-local shadowing - simulations
From normal slow extraction to crystal shadowing
From local shadowing to non-local shadowing
  Non-local shadowing concept developed in simulations [1]
Gain in efficiency using volume reflection (~98% vs ~45%) and exploit amplitude dependent phase-advance
  Extraction sextupole in between

## Slide 27: Today in the SPS
Installed crystal for non-local shadowing in LSS4: TECA
  Same crystal as in LSS2: 0.8 mm width with 160 urad bending angle
Goniometer differences LSS2 vs LSS4:
  Actuating from the inside of the SPS
  Crystal oriented towards the inside
  Space for 2 crystals but only one used
Both crystals can only be reached with a closed orbit bump at high energy
  Enough aperture for injected beam
TECA
TECS

## Slide 28: Faster alignment – meta-Bayesian optimisation
RGPE Bayesian optimisation for TECS alignment tested in simulations
  Promising x2 speed up to find channelling (~10 urad large minimum)
During machine tests, showed we can align TECA via BO in ~50 cycles
  Very reproducible and robust
  Only issue is the minimum step size the crystal can do
Test RGPE on machine  this year!
Real machine data (TECA)
Simulations (TECS)

## Slide 29: Faster crystal alignment: can we do better?
Alignment with BO demonstrated with local and non-local installation in 40-60 machine cycles…can we do better?
  This can be between 20 and 50 minutes, depending on machine configuration
Crystal alignment  very accurate model (from tracking)
Uncertainty on absolute value of input parameters (angle and position): it could be shifted, scaled…

## Slide 30: Faster alignment – meta-Bayesian optimisation
Rank-Weighted GP-Ensemble [2]
Usage of multiple Gaussian Process (GP) models to represent the underlying function
Each GP represents the target function with a give difference (shift, scale, rotation…)
The final prediction is made by combining the predictions of all the GPs using a weighting scheme that considers the quality of the predictions of each GP

## Slide 31: Faster alignment – meta-Bayesian optimisation
We can make many surrogates of our simulations
Select a target function to optimize
Original  shift and scale inputs to get the “base” models
We can then make Bayesian optimisation on a model that ranks the predictions from the different base models

## Slide 32: Summary
SPS operated with crystal in VR with ~30% loss reduction for the last 3 years
  Intensity extracted from 1e12 to 4e13 ppp
Loss reduction of x2 are within reach for operational beams
  x2 loss reduction demonstrated with non-local installation in LSS4 in physics conditions
    Need controller to be able to operate in this regime for long
Proposed method to align crystals in ~30 machine cycles
  RGPE ready to be tested in the machine
Simulations improved to properly reproduce results and extrapolate:
  Performance reach with single crystal seems between x2 and x3 (and not the hopped x4)…need something more to get to x4 target!

## Slide 33: Example of orbit drift
Loss reduction with TECS
Operational test carried out  very important results:
  TECA can reduce losses x2 in this configuration also with high intensity
  Loss reduction is not resilient to machine stops or changes
    Major difference before and after long stop for MKDH cable replacement
    The good news is that the beam “drifts away”, hence we could catch this with “simple” feed-forward controller!

## Slide 34: Operational test with nominal intensity
Operational test carried out  very important results:
  TECA can reduce losses x2 in this configuration also with high intensity
  Loss reduction is not resilient to machine stops or changes
    Major difference before and after long stop for MKDH cable replacement
    The good news is that the beam “drifts away”, hence we could catch this with “simple” feed-forward controller!
TECA setting up

## Slide 35: Operational test with nominal intensity
Operational test carried out  very important results:
  TECA can reduce losses x2 in this configuration also with high intensity
  Loss reduction is not resilient to machine stops or changes
    Major difference before and after long stop for MKDH cable replacement
    The good news is that the beam “drifts away”, hence we could catch this with “simple” feed-forward controller!
TECA in shadowing with HI beam

## Slide 36: Operational test with nominal intensity
Operational test carried out  very important results:
  TECA can reduce losses x2 in this configuration also with high intensity
  Loss reduction is not resilient to machine stops or changes
    Major difference before and after long stop for MKDH cable replacement
    The good news is that the beam “drifts away”, hence we could catch this with “simple” feed-forward controller!
Long machine stop

## Slide 37: Operational test with nominal intensity
Operational test carried out  very important results:
  TECA can reduce losses x2 in this configuration also with high intensity
  Loss reduction is not resilient to machine stops or changes
    Major difference before and after long stop for MKDH cable replacement
    The good news is that the beam “drifts away”, hence we could catch this with “simple” feed-forward controller!
Re-start and beam slowly drifting away

## Slide 38: Operational test with nominal intensity
Operational test carried out  very important results:
  TECA can reduce losses x2 in this configuration also with high intensity
  Loss reduction is not resilient to machine stops or changes
    Major difference before and after long stop for MKDH cable replacement
    The good news is that the beam “drifts away”, hence we could catch this with “simple” feed-forward controller!
Shadowing lost – TECA in AM

## Slide 39: Operational test with nominal intensity
Operational test carried out  very important results:
  TECA can reduce losses x2 in this configuration also with high intensity
  Loss reduction is not resilient to machine stops or changes
    Major difference before and after long stop for MKDH cable replacement
    The good news is that the beam “drifts away”, hence we could catch this with “simple” feed-forward controller!
Shadowing lost – TECA in AM

## Slide 40: Operational test with nominal intensity
Operational test carried out  very important results:
  TECA can reduce losses x2 in this configuration also with high intensity
  Loss reduction is not resilient to machine stops or changes
    Major difference before and after long stop for MKDH cable replacement
    The good news is that the beam “drifts away”, hence we could catch this with “simple” feed-forward controller!
Attempt to re-optimize but TECA blocked due to motor inaccuracy