## Slide 1: Development of an RF system
Slow Extraction Signal Generation and Measurement

## Slide 2: The story Behind the DeveloPment
New project in the middle east in need of RF cavity and beam regulation
End of Life notifications for old LLRF systems
Multiple designs with different interfaces to the MedAustron Control System
    A new LLRF design is needed!

## Slide 3: Wishlist
One LLRF to rule them all
Off the Shelf Hardware
Increased Diagnostic Capabilities
Injector
Cavity Regulation at 216MHz
Reflected power Interlock
Cavity Tuning Control
Synchrotron
Cavity Regulation at 400kHz – 10MHz
Beam Control (phase loop, radial loop)
RF Knockout
Signal generation close to the Tune frequency
Modulation schemes
AM, FM, PM
Cavity regulation?
Intensity modulation/regulation?
Beam Diagnostic
Injection Energy (Time of Flight)
Synchrotron Longitudinal Phase
Synchrotron Beam Position
Schottky Measurements?
Synchrotron Beam Tomography?

## Slide 4: What we came up with

## Slide 5: Hardware
Off the Shelf Vadatech mTCA based
  AMC560 Carrier Boards
    Zynq Ultrascale+ SOC
  FMC231 AD/DA conversion boards
    4 Channel 1GSps ADC
    4 Channel 2.5GSps DAC
  FMC155/FMC105 communication boards
    SFP/SFP+
    GPIO/LVDS
    RS485/Modbus

## Slide 6: System architecture Implemented together with Instrumentation Technologies

## Slide 7: Signal Sampling / Generation
Direct Sampling, Direct Digital Synthesis
NCO Based Frequency Generation
  Multiple Harmonics available for each NCO
I/Q Modulation/Demodulation for Baseband Signal treatment
  Translated to Amplitude and Phase for the User
Sequencers / Function Generators available for all modulation inputs (frequency, amplitude, phase)
  Update rates up to 10MSps for the Function Generators
Scaling and adjustment of modulation inputs available (e.g. frequency adjustment from the radial loop)
PI Controllers for Cavity, Beam Phase and Radial Position regulation

## Slide 8: Time of Flight – Beam Energy measurement

## Slide 9: Position Measurement

## Slide 10: Schottky Measurement

## Slide 11: RF Knockout Modulation Examples
Pseudo Random Phase Shift Keying
  Base Frequency 1MHz
  Feed Forward signal generation
  Function Generator „randomly“ updates the phase to ±90° at a 2kHz update rate

## Slide 12: RF Knockout Modulation Examples

## Slide 13: RF Knockout Modulation Examples
Dual Frequency Modulation
  Base Frequency 1MHz
  Feed Forward signal generation with fixed amplitudes and phases
  1 Function Generator generates a frequency sweep from 0.995 to 1.005 MHz
  1 Function Generator generates a frequency sweep from 1.005 to 0.995 MHz
  Signals are digitally added and sent out to one DAC

## Slide 14: RF Knockout Modulation Examples

## Slide 15: Questions to the Audience
Which modulation signals do you actually want?
I am especially interested in crazy ideas!