## Slide 1: R&D on MPGD technologies at GSI
P. Gasik

## Slide 2: MPGD R&D at GSI
A test bench for R&D with MPGD structures
  New prototypes (resistive MPGDs, Spark-Less Amplification Microstructures, new electrode materials)
  Multi-MPGD, hybrid structures
  Focus on working point optimisation (energy resolution, IBF, discharge stability) for TPCs and photon detectors
Currently, ongoing collaboration with TU Munich and TU Darmstadt
In the following: possible/ongoing R&D topics at GSI, without prioritisation

## Slide 3: Recent activities (collaboration with TUM)
H. Fribert, PG et al. JINST 18 (2023) C06015 + RD51 Coll. Meeting
PG, T. Waldmann et al.
JINST 18 (2023) C06011
MMG
PG, L. Lautner et al., NIM A 1047 (2023) 167730
THGEM+GEM
LPI density

## Slide 4: GSI R&D bench
Standard lab equipment (+ more) available
Gas lines, gas mixing unit
Oxygen meter
PC controlled:
  HV system
  HV pA-meter (ALICE TPC upgrade) – 24 ch
  Keithley
  ARDUINO controllers
Pre-amp + AMP readout
ADC, Scope
(thanks to C.J. Schmidt, M. Kiš, J. Hehner, M. Traeger for invaluable help in organising the R&D bench)
Contamination test

## Slide 5: Resistive layers
Dedicated studies on resistive MPGDs launched at GSI DetLab Goal: characterise primary and secondary discharge stability of resistive DLC (TH)GEMs and micro-RWELL
An attractive option for future upgrades of, e.g. CBM MuCh system
DLC THGEM: clear quenching mechanism observed, no discharges recorded at the gains where 100% probability is expected from standard THGEM studies
Gain saturation was not observed, though!
DLC THGEM
Ar-CO2 (90-10)
DLC THGEM
∼20 MΩ/□
Diamond-Like Carbon
@GSI

## Slide 6: New structures: micro-RWELL
Single-sided Gaseous Electron Multiplier (GEM) coupled to the readout anode through the material of high surface resistivity
Single amplification stage ➙ material budget, simplicity, industrialization, costs!
Resistive layer ➙ suppression of the transition from streamer to spark, with a consequent reduction of the spark amplitude.
G. Bencivenni et al., JINST 10 (2015) P02008
GEM
μ-RWELL
Starting soon @ GSI All components arrived!

## Slide 7: New electrode materials
Mo layers promising in terms of secondary discharge stability
If confirmed, possible application in stacks using extreme HV settings
First, full-scale Mo-THGEM was produced and characterized
The preliminary results with the Mo-THGEM but also gold-coated standard THGEM point to the surface quality as a possible driving factor for enhanced secondary discharge probability (TUM + soon GSI).
Surface studies in preparation (profilometer at CERN, AFM in Pisa)
Single-hole THGEMs
B. Ulukutlu, PG, et al. A 1019 (2021) 165829
Mo-THGEM @ TU München
Collaboration with TUM

## Slide 8: MPGDs in self-quenched-streamer mode?
Discharge probability could be reduced if a radial shape E-field is formed in the MPGD avalanche gap
Both simulation and R&D effort. Still need for optimization, but ideas on the market!
RD51 Common Project: Spark-Less Amplification Microstructures, V. Peskov, PG (2020-2023) – produced at CERN, measurements at GSI!
P. Fonte, “Simulations of discharge phenomena”, RD51 Meeting, TU Munich 2018 (link)
Needle + InGrid
Cathodeless CAT
T. Waldmann, PG et al. JINST 18 (2023) C07009
Collaboration with TUM, CERN
W-SLAM
S-SLAM
Measurements at GSI and TUM
W-SLAM
Soon available

## Slide 9: MPGD stacks
Study MPGD (hybrid) stacks focusing on the working point optimisation: energy resolution, IBF, gain, discharge stability
Wide dynamic range operation (e.g. Active Target TPCs)
Challenges wrt. loads and performance (e.g. low IBF)
Highly ionizing fragments – stability
Low/high pressure (see eg. Hyper-PUMA, operation in LP H2  backup)
Stable operation of MPGD-based photon detectors (low-IBF for photocathode longevity)
Hybrid stacks for photo-detectors and TPCs
GEM + (R-)MMG (e.g. HYDRA)
GEM + μRWELL
(R)THGEM–based
Hybrids with SLAM
Other structures?
22/13/128
25/15/128
45/18/125
80/30/200
HYDRA FC
W-SLAM
CsI THGEM

## Slide 10: Connection to ECFA

## Slide 11: Connection to DRD1 Working Groups and Work Packages
WGs
WPs

## Slide 12: Summary
MPGD R&D test bench available
Variety of topics - contribution to the worldwide effort/community within DRD1 structures
Blue-sky R&D and project-related R&D, e.g. input for various GSI projects
New structures, new stacks  attractive topics for BSc and MSc theses
HR needed! 

## Slide 13: BACKUP

## Slide 14: Low-pressure H2 (THGEM+MMG)
AT-TPC Collaboration basic performance evaluation studies in low-pressure He and H2
M. Cortesi et al., EPJ Web of Conf. 174 (2018) 01007
2-THGEM + MMG for stable operation, due to:
  the extended dimension of the THGEM holes, typically several times larger than the electron mean-free path even at low pressure;
  the confinement of the avalanche within the holes, resulting in smaller photon-mediated secondary effects
  the quenching effect of small amounts of impurities from natural outgassing of detector components - e.g. N2 acts as wavelength shifter suppressing UV-photons emitted during the avalanche.
For low MMG voltage – loss of electron collection efficiency and thus effective gain of the structure
High x-section for radiation less processes in H2 (excitation of vibrational and rotational levels)
Higher electric fields necessary for a substantial gas avalanche multiplication (resulting in e.g. field emission)
Higher voltages  higher discharge probability  lower max. achievable gain. Need R&D in HP H2

## Slide 15: Low-pressure H2 (WELL, THGEM and 2-THGEM)
Single THGEM (WELL) at low P – photon mediated secondary effects become relevant (lower maximum gain)
Double THGEM structure (charge/gain sharing) – improves stability
Instabilities at high pressures due to high absolute voltage
1-THGEM
2-THGEM
2-THGEM

## Slide 16: Humidity studies (TU Munich)
No major deteriorating effects of humidity were observed in the performance (gain, energy resolution, and charging-up)
Adding water vapour to the gas mixture improves the discharge stability at the highest voltages
  Reduction in the rate of spurious discharges related to electrode defects or charging-up of the insulating layers observed
  May also help with instabilities caused by ageing effects ➙ to be studied?
H. Fribert et al. JINST 18 (2023) C06015 + RD51 Coll. Meeting
23
No resistive layers!

## Slide 17: Micromegas studies
MMG1 - 22/13/128
  Wire distance: 22µm, Wire thickness: 13µm
  Amp. gap: 128µm, LPI: 730, Toptical = 39,5%
MMG2 - 25/15/128
  Wire distance: 25µm, Wire thickness: 15µm
  Amp. gap: 128µm, LPI: 640, Toptical = 39%
MMG3 - 45/18/125
  Wire distance: 45µm, Wire thickness: 18µm
  Amp. gap: 125µm, LPI: 400, Toptical = 51%
MMG4 - 80/30/200
  Wire distance: 80µm, Wire thickness: 30µm
  Amp. gap: 200µm, LPI: 230, Toptical = 52%

## Slide 18: What would be good to have/answer?
Simulation model describing secondary (propagated, delayed) discharges developing in the gaps between subsequent foils in a stack.
  Mechanism ➙ still a topic of a debate.
  Need to understand the entire process and, if possible, to eliminate the cause of these violent events completely.
  Model development of a primary discharge in a GEM hole and its subsequent transition to a gap discharge, taking into account:
    Space-charge densities
    Drift and amplification of charges, ion bombardment
    Heating of the electrodes …
    … and thermionic emission from the latter.
NIM A 937 (2019) 168
NIM A 937 (2019) 168
JINST 14 (2019) P08024
NIM A 940 (2019) 262
NIM A 1019 (2021) 165829

## Slide 19: Secondary discharge formation
The transition between Townsend discharge and Streamer discharge?
  Dependence on gas (⍺ process) and cathode? (𝛾 process - feeding)
  Time lag O(10 μs) with a rapid full gap breakdown
Mixed discharge mechanism at below-critical fields
  Townsend mechanism initiated by electrons from a primary discharge;
  Secondary emission from the heated cathode;
  Space charge accumulation at the anode;
  Transition to a streamer.
B. Ulukutlu, et al. NIM A 1019 (2021) 165829

## Slide 20
THGEMs with new materials
Investigating the first Molybdenum coated full scale THGEM
Significant mitigation of the dangerous, delayed secondary discharges
Mesh geometry of Micromegas
Systematic studies of discharge formation in Micromegas
Using Garfield++ simulations to model discharge formation

## Slide 21: Secondary discharges in GEMs*
a) Primary discharge
b) Secondary discharge
* See pioneering studies by S. Bachmann et al. NIM A479 (2002) 294 & V. Peskov, P.Fonte (2009) arXiv:0911.0463
A. Deisting, C. Garabatos, PG, et al. NIM A 937 (2019) 168
Discharge in a transfer/induction gap
Full gap voltage breakdown – can be associated with a spark development
Appears O(μs) after the primary spark
Develops at the gap fields below the amplification region
Precursor current can be measured in between two discharges ➞ Secondary emission and streamer development in the gap?
Leading theory: heating of the cathode after the primary discharge
  A. Deisting C. Garabatos, PG, et al. NIM A 937 (2019) 168
  A. Utrobicic, et al. NIM A 940 (2019) 262
Mitigation strategies established
  L. Lautner, PG, et al. JINST 14 (2019) P08024
  A. Deisting, C. Garabatos, PG, et al. NIM A 937 (2019) 168
A. Utrobičić et al. MPGD 2019,
La Rochelle

## Slide 22: Secondary discharges with different materials
Secondary discharge probability
Material dependence observed!
  Molybdenum displays especially high stability
  Which material properties play a role?
Less stable
More stable
 | Conductivity [106 S/m] | Work function [eV] | Melting point [°C] | Boiling point [°C] | Thermal conductivity [W/m*K] | Density [g/cm3]
Al | 36.9 | 4.08 | 660 | 2470 | 237 | 2.702
W | 8.9 | 4.5 | 3422 | 5550 | 174 | 19.35
Cu | 58.7 | 4.7 | 1083 | 2575 | 386 | 8.96
Inox | 1.37 | 4.4 | 1510 | 2750* | 16.3 | 7.85
Ta | 7.6 | 4.22 | 3017 | 5365 | 57.5 | 16.65
Mo | 18.7 | 4.5 | 2623 | 4651 | 138 | 10.22
*for Fe
B. Ulukutlu, PG, et al. A 1019 (2021) 165829

## Slide 23: Investigating improved ways of operating MPGDs
Humidity studies
First systematic studies on effects of humidity contamination on performance of MPGDs (Micromegas, GEM & THGEM)
No drawbacks of humidifying the used Ar-CO2 (90-10) gas mixture & increased stability against spurious discharges observed
Increasing stability

## Slide 24: Discharge limits, high rates
Critical charge limits and max-gain rate dependency
Overlap of avalanches may further reduce the stability of the detector
Unlikely even at the highest rates and moderate gains (e.g. COMPASS, LHCb trackers)
Troublemakers:
Cathode excitation, electron jets, etc.
Highly Ionizing fragments (Nprim,α = 104 × Nprim,MIP), high neutron doses
Wide dynamic range operation (e.g. Active Target TPCs)
Challenges wrt. loads and performance (e.g. low IBF)
The stability of your system relies on the stability of a single amplification structure. Pin down the limits!
Plasma Sources Sci. Technol. 19 (2010) 034021
NIM A 422 (1999) 300
© LHCb GEM Tracker
© AT-TPC (link)

## Slide 25: Micromegas studies
MMG1 - 22/13/128
  Wire distance: 22µm, Wire thickness: 13µm
  Amp. gap: 128µm, LPI: 730, Toptical = 39,5%
MMG2 - 25/15/128
  Wire distance: 25µm, Wire thickness: 15µm
  Amp. gap: 128µm, LPI: 640, Toptical = 39%
MMG3 - 45/18/125
  Wire distance: 45µm, Wire thickness: 18µm
  Amp. gap: 125µm, LPI: 400, Toptical = 51%
MMG4 - 80/30/200
  Wire distance: 80µm, Wire thickness: 30µm
  Amp. gap: 200µm, LPI: 230, Toptical = 52%

## Slide 26: Photon detection with THGEMs
Combining a photosensitive material with a robust and low-cost device; THGEMs
  Studies ongoing with CsI and DLC coatings as photocathode layers on the THGEM surface
  Verification of the experimental setup successful
  First results from aging studies of used materials under operation

## Slide 27: 1st prototype
Copper readout strips
DLC coating 30 MΩ/□
Micro-Pattern Walls
  Thickness: 270 µm
  Height: 256 µm
  Pitch: 700 µm
Wires
  Diameter: 50 µm
  Pitch: 850-1000 µm
Photo of the prototype
Microscope image (100x magnification)
Produced at CERN EP-DT-DD Micropattern Structures laboratory

## Slide 28: Very 1st measurements
Maximum stable gain reached with setup ∼1500
With higher voltages (> 900 V) current spikes (corona?) observed
At ∼950 V and continuous discharge (glow?) triggered
Cleaning with sulphuric acid to dilute residual fibres ➙ measurements soon
Further SLAM optimisation
  Using pillars instead of walls
  Decrease wire pitch
  Decrease wire diameter
New geometries ➙ a strip-like SLAM
Source rate (Hz) | 1400
Primary current (nA) | 4.59E-05
Reached gain | 1,158.91