## Slide 1: FAIR Booster Mode
D. Ondreka, SYS
7th Beam Time Retreat, 11 July 2024

## Slide 2: Contents
Booster mode
  Definition
  Topics
Super-cycle development
Hysteresis effects
BD applications and booster mode
Status
Summary and outlook

## Slide 3: Booster Mode
Stacking scheme for RIB production
Goal: reach maximum intensity in SIS100
  Longitudinal filling by stacking four SIS18 cycles
  Two empty buckets as beam abort gap
  Used with any ion species
Fundamental requirements
  Fastest possible repetition rate
  Direct ramp-down to injection level
  Fast extraction only
Repetition rate
  Original value: 2.7 Hz for U28+ (reference)
    Cycle length 370 ms incompatible with 50 Hz
  Presently aiming for cycle length 380 ms (2.6 Hz)
  Cycle time longer for lighter ions to 18 Tm!
Common misconceptions:
  booster mode highest intensities of U28+
  fastest ramp rate (19 kA/s) booster mode
SIS18 and SIS100 cycles for RIB production
SIS18
SIS100

## Slide 4: Booster Mode: Topics
Beam physics
  Acceleration at max. possible ramp rate (19 kA/s)
  Strong eddy current effects
  Hysteresis effects due to special magnetic cycle
Hardware
  AEG power converters
    Reaching 19 kA/s on down ramp
    Decrease of rounding time: 32 ms  24 ms ?
  MA cavities for H=2
    Max. voltage, especially for lighter ions
Machine model
  Generation of booster mode cycles
  Smallest number of BPs: bunching in INJECTION
Control system
  BD applications handling booster mode properly
  Ramped front-ends: smaller min. BP length
  Coupling with new UNILAC timing system
  FAIR patterns: repetition of single booster cycle

## Slide 5: Super-Cycle Development
Preferred operation: n-fold repetition of same cycle
  May or may not be feasible
Version 1
  First successful test with beam (U28+, 2022)
  Drawback: completely different magnetic hysteresis for first cycle
Version 2
  Advantage: same hysteresis for every cycle
  Drawback: eddy currents different in first cycle due to UNILAC synchronization
  Successfully used (U28+, 2023; U73+, 2024)
Version 3
  Advantage: same hysteresis and eddy currents in every cycle
  2 failed test in 2024 (wrong timing graph?)
    Error analysis ongoing
    May wait for new UNILAC timing system
UNI sync
Injection
Injection
Injection
Injection
Version 2 (2023)
UNI sync
Injection
Injection
Injection
Injection
Version 1 (2022)
Version 3 (2024)
UNI sync
Injection
Injection
Injection
Injection

## Slide 6: Hysteresis Effects: General
Different magnetic cycle for booster
  Direct ramp-down to injection level to save time
  Hysteresis loop significantly smaller
Expected general effects
  Larger remnant field at injection
  Different shape of excitation curve
Impact on performance
    Degradation of injection performance
    Increased beam loss at start of ramp
    Measured with special U73+ booster cycle U73+
      Injection into 4/5 repetitions for same eddy currents
Small losses at start of ramp in standard cycle
High losses at start of ramp in booster cycles
Magnetic field in booster cycle (first injection omitted)
Injection
Injection
Injection
Injection
Magnetic field in standard cycle
Injection
UNI sync
UNI sync

## Slide 7: Hysteresis Effects: Dipoles
Larger remnant field at injection
  Shift of horizontal orbit towards center
  Compensation by adjusting B field at injection
Strong orbit motion at start of ramp
  Caused by different shape of B(I) curve
  Good news: cycles appear to behave identical!
Observation by monitoring orbit
  Orbit application can display all cycles
  Data can be exported in binary format
  Limitations of present software
    No comparison of different cycles
Cycle | ΔR set value
Booster | 8 mm
Standard | -2 mm
Difference | 10 mm
Radial position for same orbit at injection
Horizontal orbit evolution in standard cycle
Horizontal orbit evolution in booster cycles

## Slide 8: Hysteresis Effects: Quadrupoles
Larger remnant field at injection
  Tune shift, esp. large in vertical plane
  Compensation by adjusting set tunes
Strong tune motion at start of ramp
  Caused by different shape of B’(I) curve
  Good news: cycles appear to behave identical!
Observation difficult
  Displayed data: snapshots from video recorded on smart phone
  Limitations of present software
    No comparison of different cycles
    No saving data for different cycles
Cycle | Qh set value | Qv set value
Booster | 4.275 | 3.21
Standard | 4.305 | 3.315
Difference | -0.03 | -0.105
Injection tune set values for U73+ for same real tunes
Vertical tune in booster mode with U73+ for four successive cycles
#3
#4
#2
#1
Different Qv on flattop!
#3
#4
#2
#1
Horizontal tune in booster mode with U73+ for four successive cycles

## Slide 9: Hysteresis Compensation (I)
Short test during last week of beam time
  Made possible due to septum cable failure
  U73+ booster cycle with single injection used
  Goals: measure and demonstrate compensation
Measurement of hysteresis
  ‘Chimney’ used to change hysteresis loop
  Injection offsets compensated by set values
  Separately for dipoles and quadrupoles
  Data acquired, analysis ongoing
Injection
‘Chimney’
Booster cycle with ‘chimney’ used for hysteresis measurements
Effect of changing hysteresis loop for D-quadrupoles on vertical tune
Standard
B1L = -0.4T
B1L = -0.6T

## Slide 10: Hysteresis Compensation (II)
Demonstration of dynamic compensation
  Manual trims during ramp
    Dipole hysteresis  integral field B0L
    Quad hysteresis  vertical tune Qv
Manual correction trim to vertical tune
Measured vertical tune
uncompensated
compensated
Manual correction trim to integral dipole field
uncompensated
compensated
Measured horizontal orbit
Software tools required for routine operation
  Orbit correction on ramp
  Tune correction on ramp

## Slide 11: BD applications for booster mode
Non-uniform behavior of existing applications for displaying beam signals
  DCT and orbit application
    All cycles displayed on single time axis at end of super-cycle
  ACT and tune application
    Every cycle is displayed when it finishes, erasing the previous one
  Saving data of individual cycles may or may not be possible
Goals
  Allow operators to focus on and diagnose individual cycles
  Allow operators to compare individual cycles
  Allow machine physicists to save data of individual cycles
Considerations for implementation
  Requirements need to be clarified
  Present ‘booster mode light’ may not be identical to final solution
  Final booster mode structure will be part of FAIR pattern concept

## Slide 12: Status of Topics
Category | Topic | Demonstration | When | Status
Physics | Ramp rate 19 kA/s with U28+ | Reached 18.9 kA/s up, 17.6 kA/s down | 12/2023 | up: ok down: p.f.i.
Physics | Investigation of eddy current effects |  |  | open
Physics | Compensation of hysteresis effects | Manual compensation | 06/2024 | demo: ok tools: open
HW | Smaller rounding times for AEG |  |  | open
HW | Max. voltage for MA cavities to 42 kV |  |  | open
Model | Super-cycles with optimal hysteresis | Version 2 successful, version 3 failed | 2022+23 | p.f.i.
Model | Bunching in injection |  |  | open
CS | Adapt BI applications to booster |  |  | open
CS | Smaller min. BP length in FG |  |  | open
CS | Coupling with new UNILAC timing |  |  | open
CS | FAIR patterns: rep. of single cycle |  |  | open
p.f.i. = potential for improvement

## Slide 13: Comparison to FAIR Requirements
Present MA cavity voltage appears sufficient up to ~ 5∙1010 particles
Potential for reducing cycle time to 380 ms
  Increasing ramp down rate: 10 ms
  Reducing min. BP length from 16 ms to 12 ms: 4 ms
  Reducing rounding time from 32 ms to 24 ms: 16 ms
  Bunching in injection BP: 16 ms
Booster for U28+ | FAIR (50 Hz) | Present status
Ramp rate | 19 kA/s | 18.9 kA/s up, 17.6 kA/s down
Available MA voltage | 42 kV | 39 kV
Cycle time | 380 ms | 400 ms
Repetition rate | 2.63 Hz | 2.50 Hz
Stacking time | 1.14 s | 1.2 s
 FAIR design parameters for booster with U28+ well in reach

## Slide 14: Summary and Outlook
Booster mode machine development well advanced
  Demonstrated 2.5 Hz operation with U28+ (already in 2023)
  Hysteresis effects understood and manual compensation demonstrated
  Apparently four identical cycles possible with suitable super-cycle
Recommended next steps
  Activities in SYS
    Booster mode test with a lighter ion, e.g. Ar10+
    Investigation of eddy current effects
    Merging injection and bunching beam process to save time
    Development of hysteresis compensation tool
  Light-weight adaptation of BI applications to handle booster mode better