## Slide 1: Spill Optimization: SIS18 Micro Spill Cavity
Beam Time Retreat
K. Groß, RRF
11.07.2024
Acknowledgments: TRI, BAU, LRF, VAC, ARP, ATP, OPE, SIS100/SIS18, BEA, HADES, mCBM

## Slide 2: Current Status of Micro Spill Cavity in SIS18
Cavity installed in SIS18 in July 2023
Locally operated (BG 1.016)
Access SIS18 required to remove short-circuit
Impedance without shortcut about 500 kΩ Q 0 ≈ 5000
Frequency 80.3 to 81.6 MHz (sufficient for all energies with adjustment of harmonic number)
Gap voltage amplitude 1.5 kV without conditioning & warmup (up to 25 kV in test setup)
Conditioning required warming-up & cooling-down time

## Slide 3: Experimental Results from Operation with Beam
Dedicated MDE 29.11.2023
  Rev. freq. f0 = 904.8510 kHz
  h=4 fRF = 3.6194 MHz
  h=90 fRF = 81.4366 MHz
  Extraction: Quadrupole-driven 8 seconds
  Detector: HHD-CFD
Outline:
  Duty Factor
  Spectrum
  Arrival time with respect to RF
(MDE / Parasitic Operation) HADES 1. / 6.3.2024
  Rev. freq. f0 = 1.1661 MHz
  h=4 fRF = 4.664 MHz
  h=70 fRF = 81.6283 MHz
  Extraction: RF Knock Out with SOS 20 seconds (Noise / Noise++ / 3 Sines)
  Detector: multiplicity signal derived from HADES / HHDDI2P
Evaluation based on code by P. Niedermayer, data recorded by T. Milosic and ideas from P. Forck, R. Singh, S. Sorge and J. Yang → Thanks to all!

## Slide 4: Experimental Results from Operation with Beam
Dedicated MDE 29.11.2023
  Extraction: Quadrupole-driven (without SOS) 8 seconds
  Detector: HHD-CFD

## Slide 5: Experimental Results from Operation with Beam Dedicated MDE 29.11.2023
Bunched beam during extraction
Rebunching at h=90
Debunching at h=4

## Slide 6: Experimental Results from Operation with Beam Dedicated MDE 29.11.2023
Spill quality / weighted duty factor ( μs, ms)
167 spills, 16 voltages
Valid for μs
with in , in
Optimal voltage found at 2 kV is only valid for 14N7+ @ 300 MeV/u
Optimum synchrotron tune found at 2 kV is 0.0038
Meaning of optimal synchrotron tune → next MDE / next slide

## Slide 7: Experimental Results from Operation with Beam Dedicated MDE 29.11.2023 - Outlook
Next MDE – find optimal gap voltage amplitude:
  Assumption based on [1] and private communication
  Similar synchrotron tune → similar duty factor
  Strongest impact
    Transverse beam widths
    Momentum width
    Synchrotron tune
[1] S. Sorge et al, PR AB 26, 014402 (2023)

## Slide 8: Experimental Results from Operation with Beam Dedicated MDE 29.11.2023
Spill duty factor over time – up to 500 V
Spill duty factor increases with gap voltage

## Slide 9: Experimental Results from Operation with Beam Dedicated MDE 29.11.2023
Spill duty factor over time – 500 V to 4 kV
Optimum found at 2 kV
Second local max. for gap voltage > 2 kV

## Slide 10: Experimental Results from Operation with Beam Dedicated MDE 29.11.2023
Spill duty factor over time – 5 to 13 kV
Position of second local max. seems to depend on tune shift
Further evaluation necessary

## Slide 11: Experimental Results from Operation with Beam Dedicated MDE 29.11.2023
Spectrum of extracted beam
Improvement for all frequencies

## Slide 12: Experimental Results from Operation with Beam Dedicated MDE 29.11.2023
Arrival time with respect to RF phase (12.25 ns) - further evaluation needed
                1 kV
                13 kV

## Slide 13: Experimental Results from Operation with Beam
MDE - HADES 1.3.2024
  Extraction: RF Knock Out with SOS (Noise / Noise++) 20 seconds
  Detector: multiplicity signal with a jitter of several ns derived from HADES

## Slide 14: Experimental Results from Operation with Beam Parasitic Operation HADES Beam Time
Measurements performed by beam diagnostics department (BEA) on 1.3.2024
Best results found with spill optimization system AND micro spill cavity on
settings changed*
*) sextupole amplitude increased
tune adjusted

## Slide 15: Experimental Results from Operation with Beam Parasitic Operation HADES Beam Time
Measurements performed by beam diagnostics department (BEA) on 1.3.2024
Best results found with spill optimization system AND micro spill cavity on
settings changed*
*) sextupole amplitude increased
tune adjusted

## Slide 16: Experimental Results from Operation with Beam Parasitic Operation HADES Beam Time
Spill duty factor over time
„noise++“ vs. „noise++ with 2 kV“
„noise“ vs. „noise with 2 kV“

## Slide 17: Experimental Results from Operation with Beam Parasitic Operation HADES Beam Time
Fourier series
„noise++“ vs. „noise++ with 2 kV“
„noise“ vs. „noise with 2 kV“

## Slide 18: Experimental Results from Operation with Beam Parasitic Operation HADES Beam Time
Measurements performed on 1.3.2024
“noise++ with 2 kV”
multiplicity signal → over time → not “structured”
→ Washed-out due to multiplicity signal with a jitter of several ns
→ Structure (29.11.23) likely due to tune shift (quadrupole-driven extraction)

## Slide 19: Experimental Results from Operation with Beam
Parasitic Operation HADES 6.3.2024
  Extraction: RF Knock Out with SOS (3 Sines) 20 seconds
  Detector: HHDDI2P

## Slide 20: Experimental Results from Operation with Beam Parasitic Operation HADES Beam Time
Measurements performed by beam diagnostics group on 6.3.2024
3 Sines (“+++“) used instead of “noise++“ by SOS
HHDDI2P 107 ions / (20 s ∙ 81.63 MHz) = 0.006 ions
→ Structure (29.11.23) likely due to tune shift (quadrupole-driven extraction)
No further analysis due to different settings in the only measurement with cavity.

## Slide 21: Experimental Results from Operation with Beam Parasitic Operation HADES Beam Time (mCBM, Slow)
time difference TOF-T0 (diamond)
MQ based online analysis by Norbert Herrmann multivariate system of quadratic equations
The RF period of 12.25 ns could be measured at mCBM / HTD during quadrupole-driven slow extraction with cavity on at 1.5 kV

## Slide 22: Conclusion and Outlook
Significant improvement in spill quality due to micro spill cavity
Best results with combination of SOS and micro spill cavity
Several further machine experiments necessary
Work in progress to make the cavity usable with less RRF support
  Step 1: set amplitude for selected pattern, frequency fixed, read status
  Step 2: set frequency and amplitude, remote control (on, off, reset) remote short-circuit (if possible)
  Step 3: LSA-model includes results from upcoming MDEs, optimal operational parameters are set automatically
  Limited to 1.5 kV (2.25 W) for remote operation in all steps

## Slide 23: The End
Thanks
for your attention!
Questions?

## Slide 24: Acknowledgements
Development and Commissioning: Accelerator Radiation Protection, Atomic, Quantum & Fundamental Physics, Construction (B. Benz, J. Kalenda), Linac RF (B. Schlitt, G. Schreiber, W. Vinzenz, J. Zappai et al.), Ring RF (R. Balß, B. Breitkreutz, C. Christoph, O. Disser, M. Hardieck, H. Klingbeil, H.G. König, U. Laier, D.E.M. Lens, S. Lux, S. Schäfer, C. Thielmann, T. Winnefeld, B. Zipfel et al.), SIS100/SIS18 (P. Spiller, J. Stadlmann), Transport and Installation (D. Acker, K. Lück, M. Grenz-Gustafson, M. Diebel, K. Kalaitzidis et al.), Vacuum Systems (M.C. Bellachioma, E. Renz, G. Savino)
Spill Measurements: Accelerator Physics (S. Sorge), Beam Instrumentation (P. Boutachkov, O. Chorniy, P. Forck, T. Milosic, P. Niedermayer, R. Singh, J. Yang), SIS100/SIS18, HADES/mCBM (J. Pietraszko, C. Strum, M. Traxler)
Machine Operating and Discussions: (Accelerator) Operation(s) (R. Aßmann, A. Bloch-Späth, C. Böhm, V. Kamerdzhiev, H. Kummerfeldt, F. Lorenz, S. Reimann, Y. Valdau)

## Slide 25: Backup Slides
Cavity Development, Operation and Upgrade
Development
  Requirement on Frequency
  Gap Voltage Calibration
  RF Frequency and Harmonic Number
Operation
  Conditioning
  Temperature Development
  Vacuum
  High Beam Intensities
Upgrade
  Control System
  Short-

## Slide 26: Requirement on Frequency
J. Pietraszko, “The Hades/CBM physics case requirements”, oral presentation at Slow Extraction Workshop, Darmstadt, Germany, June 2016.

## Slide 27: Gap Voltage Calibration

## Slide 28: RF Frequency and Harmonic Number
One of several possibilities

## Slide 29: Conditioning
First conditioning in beam time can take 6 – 29 hours and require a power of up to 225 W (15 kV)

## Slide 30: Temperature Development
Properties of the ceramic gap

## Slide 31: Vacuum
Worst case „ conditioning“ limited in time and similar to high current operation
Vacuum (GS11VM1X) 1.5·10-10
Beam pipe tested as any other beam pipe
Heat out (up to now) limited to ceramic
Vacuum not influenced by operation at 1.5 kV
8. & 9.12.
13.-16.12.
29.11.
Only necessary for MDEs with high voltage requirements
Slow conditioning leady to lower peaks in the vacuum pressure

## Slide 32: Vacuum
Only the beam pipe is under vacuum

## Slide 33: High Beam Intensities
Additional test:
Successful acceleration of 1.5·1010 particles, 15 mA
Induced voltage was < 100 V

## Slide 34: Steps towards Operation from Main Control Room
Ramps and plunger control have to be integrated into control system
PLC for interlock handling to be integrated in control system
Limitation to 1.5 kV for standard operation without conditioning remains
New output- and directional coupler for lower power
Automatic short-circuit needed
  not cycle to cycle (impedance applies to all running virt. accel.)
  ambitious, evaluation of possibilities (new development of a plunger)

## Slide 35: Short Circuit
Construction of a new, small plunger

## Slide 36: Research on Current Limitations
Build up test environment / resonator to analyze the problems regarding …
  Conditioning / plasma discharge:
    Why was it not necessary in the test environment, but is necessary in SIS18?
    How does this need depend on the vacuum / environment?
    Coating, higher conductivity, better hided welds, …
  Temperature rise in the ceramic / dielectric losses:
    Measurement on Vacon-Temperature
    Measurements on Ceramic Probes
Decision on conditioning in SIS18

## Slide 37: Backup Slides
Experimental Results
Results not included in the presentation
  RF frequency variation
  Time structure of spill
  Selected frequencies
  Ions and energies
Details of the results included in the presentation
  Weighted duty factor for variation of tbin and tav
  max / mean duty factor
  Spectra
  Changed settings

## Slide 38: RF Frequency Variation
A shift of 100 Hz means a change in the harmonic number by 0.005 (marked with the bar in the figure – different setup simulation, calculation and measurement)
Chart: Mean and standard deviation
| 88 | 88.001000000000005 | 88.001999999999995 | 88.003 | 88.004000000000005 | 88.004999999999995 | 88.006 | 88.007000000000005 | 88.007999999999996 | 88.009 | 88.01 | 88.012 | 88.013999999999996 | 88.016000000000005 | 88.018000000000001 | 88.02 | 88.03 | 88.04 | 88.05 | 88.06 | 88.07 | 88.08 | 88.09 | 88.1 | 88.3 | 88.45 | 88.49 | 88.5 | 88.51 | 88.55 | 88.7 | 88.9 | 88.94 | 88.98 | 88.981999999999999 | 88.983999999999995 | 88.986000000000004 | 88.99 | 88.992000000000004 | 88.994 | 89
Standardabweichung | 102.125 | 104.9 | 113 | 126.8 | 142.1 | 161 | 180.4 | 204.3 | 228.6 | 249.334 | 269.4 | 299.316 | 320.634 | 323.488 | 319.125 | 318.7 | 243.952 | 186.883 | 160.937 | 152.8 | 151 | 148.5 | 146.9 | 145.16 | 143.89 | 143.9 | 141.709 | 113.666 | 144.737 | 143.672 | 144.309 | 146.754 | 159.2 | 313.4 | 320.2 | 325.3 | 317.963 | 266.6 | 221.8 | 179.5 | 101.74
Mittelwert | 2.92 | 22.29 | 45.03 | 65.48 | 86.91 | 105.4 | 130.7 | 160.1 | 172.7 | 183.271 | 189 | 178.357 | 166.914 | 137.116 | 117.094 | 107 | 45.6 | 20.8 | 7.86 | 5.354 | 8.882 | 8.743 | 1.907 | 6.53 | -1.57 | -0.92334 | -3.0513 | -3.25 | 2.7538 | -1.2515 | -0.02 | -5.44 | -12.51 | -103.1 | -116.9 | -144.7 | -170.795 | -196.2 | -170.6 | -132.1 | 0.91

## Slide 39: Experimental Results from Operation with Beam Time Structure of Spill
Spill structure – comparison between 0 kV and 2 kV ( μs)
Quadrupole-driven
„noise” (macro-spill feedback)
RF Knock Out with SOS
„noise++“

## Slide 40: Experimental Results from Operation with Beam Time Structure of Spill
Spill structure – comparison between 0 kV and 2 kV ( μs)
Quadrupole-driven
„noise” (macro-spill feedback)
RF Knock Out with SOS
„noise++“

## Slide 41: Experimental Results from Operation with Beam Particle inter-arrival-times
Particle inter-arrival-times – comparison between 0 kV and 2 kV
Quadrupole-driven
(80 MHz)
„noise” (macro-spill feedback)
RF Knock Out with SOS
„noise++“ (0.38, 0.76, 1.9 kHz)

## Slide 42: Experimental results from operation with beam Dedicated MDE 29.11.2023 (2 shifts)
No suppression of the dominant harmonics – rausnehmen!

## Slide 43: Ions and Energies

## Slide 44: Dedicated MDE 29.11.2023 Spill quality / weighted duty factor (14N7+ @ 300 MeV/u)
 | tbin=1 μs | tbin=10 μs | tbin=100 μs
tav=1 ms |  |  | 
tav=10 ms |  |  | 
tav=100 ms |  |  | 

## Slide 45: Dedicated MDE 29.11.2023 Spill quality / weighted duty factor (14N7+ @ 300 MeV/u)
 | tbin=5 μs | tbin=10 μs | tbin=20 μs
tav=5 ms |  |  | 
tav=10 ms |  |  | 
tav=20 ms |  |  | 

## Slide 46: Experimental Results from Operation with Beam Dedicated MDE 29.11.2023
Spill quality / weighted duty factor ( μs, ms)
167 spills, 16 voltages
Valid for μs
with in , in
Optimal voltage found at 2 kV is only valid for 14N7+ @ 300 MeV/u
Optimum synchrotron tune found at 2 kV is 0.0038

## Slide 47: Experimental Results from Operation with Beam Parasitic Operation HADES Beam Time
Measurements performed by beam diagnostics department (BEA) on 1.3.2024
Best results found with spill optimization system AND micro spill cavity on
settings changed*
*) sextupole amplitude increased
tune adjusted

## Slide 48: Experimental results from operation with beam Dedicated MDE 29.11.2023
Spectrum of extracted beam
Improvement for all frequencies

## Slide 49: Experimental results from operation with beam Dedicated MDE 29.11.2023
Spectrum of extracted beam
Improvement for all frequencies

## Slide 50: Experimental results from operation with beam Parasitic Operation HADES Beam Time
Fourier series – „noise ++“ vs. „noise ++ with 2 kV“

## Slide 51: Experimental results from operation with beam Parasitic Operation HADES Beam Time
Fourier series – „noise ++“ vs. „noise ++ with 2 kV“

## Slide 52: Experimental results from operation with beam Parasitic Operation HADES Beam Time
Fourier series – „noise“ vs. „noise with 2 kV“

## Slide 53: Experimental results from operation with beam Parasitic Operation HADES Beam Time
Fourier series – „noise“ vs. „noise with 2 kV“

## Slide 54: Experimental results from operation with beam Dedicated MDE 29.11.2023
Different Settings