## Slide 1: 7th Beam Time Retreat UNILAC – Lessons from the beam time 2024 and outlook to 2025
Hartmut Vormann – Machine Coordinator UNILAC
11th and 12th July 2024
@ Jagdschloß Kranichstein
BEM TIME RETREAT 2023
BEAM TIME RETREAT 2023

## Slide 2
Cables for experiments in EH new, due to measurement station removal
Farady Cup TK7DC3 (leak) replaced 20th October 2023 (Spare by BEA)
Farady Cup TK4DC3 (leak) replaced 18th October 2023 (Spare by BEA)
UT2MUX new coil installed end of September 2023
URMU1/ULMU1 new PS installed 15th January 2024
Shutdown 2023

## Slide 3
February
  Carbon from CH3, Titanium, Argon/ECR, Oxygen
March
  Gold from PIG (25 Hz) and from MeVVa,
  Easter-Service Period
April
  Iron PIG, Argon/ECR (36Ar HITRAP), Erbium (new!) HFS
  Argon Machine Experiments
May
  Nickel/VARIS, Chrome PIG (52Cr, not 54Cr ECR), Molybdenum (new!)
  Uranium exclusively
June
  Uranium exclusively (H2 gasstripper), Argon for UCW
Overview - main
Feb-15 Alvarez A4 pulse length 9 h
(X6, solved April 3rd)
Feb-22 EH Septa water dropping 24h
(X8, replaced Mar-28)
Feb-28 A4 instable 15h
Mar-18 EH Dipole PS UXAMU1 31h
PS water dropping (X0)
Apr-18 A2A Shortcut Transmitter 30 h
Apr-19/20 36Ar beam jitter at Tkend 15h
(QD11/Erbium )
May-8 beam loss X8, exp valve, 23h
May-31 TK4QD31 water loss, KS01 off 14h
Jun-11 IH1 tube socket shortcut 12 h

## Slide 4
February
  Carbon from CH3 (1 mA@UH1, 0.4 mA C4+/6+@TK7), Titanium (35 µA@UH1, 40 µA@Y7), Argon/ECR (130µA@UN3, 12 µA@X6, reduced), Oxygen (3 mA@UH1, 1.7 mA@TK7)
March
  Gold from PIG (25 Hz, 20-40 µA@UH1/UT1, source piano, Exp. reduced 5 µA) and from MeVVa (3 mA@UH1, 200/400µA@TK7),
  Easter - Service Period
April
  Iron PIG (120 µA@UH1, 50 µA@UT1), Argon/ECR (36Ar HITRAP, 120 µA@UN3, 40µA@X6), Erbium (new!, 170Er3+, 23+ Alv, 57+ TK; 1 mA UH1, 400-600 µA UH4, 250 µA TK7) HFS
  Argon Machine Experiments (4-5 mA @TK7)
May
  Nickel/VARIS (3 mA @UH1, 2 mA@UT1, 120 µA@TK7, reduced), Chrome PIG (52Cr, not 54Cr ECR --- 100µA@UL5DT8, 45-60/ 80 µA @UX8DT3), Molybdenum (new!, 400 µA Mo3+@UH1, 60 µA@TK7))
  Uranium exclusively
June
  Uranium exclusively (H2 gasstripper; 10 mA@UH1, 1.0/3.5mA U73+@TK7 – „multi charge“ beam), Argon for UCW
Overview - intensities

## Slide 5
Overview - more
Feb-07 A1 transm PS, 3h
Feb—11 IH1 crowbar several times, HV cable repl. 3.5h
fEB-12 UXAMU2 ICH card repl. 3 h X0
Feb-14 „door open“ 2h
Feb-16 HSI-RFQ Ignitron, HV cable 3.5 h
Feb-15 Quad Doublet UT1QD11 jitter long Y7,X6
Feb-22 Dipole Septa water dropping 24h X8 (replaced Mar-28)
Feb-15 Alvarez A4 pulse length (solved April 3rd), 9h X6
feb-25 gassstripper pressure drop, 3.5h
feb28 A4 springt, 15h
mar-15 stripper roots oil 3 h
March-18 UXAMU1 PS water dropping 27 h +4h (20.3.) (X0)
March -25 Gas stripper valve #1 replaced
apr11 timing profile grids x0, csco timing 15 h
april-18 A2A shortcut Transmitter (30 h)
Apr-19/20 36Ar jitter at Tkend, QD11/Erbium …15h
Apr-22 A4 dripping, 2.5h
may 7 gasstripper valve repl. 7h
may-8 beam loss X8, exp valve, 23h
May-19 IH2 transistor driver. repl. 3h
May-31 TK4QD31 water, KS01 off, 14 h
June-6 BB12 HV-cable 4.5+3 h
Jun-10 HSI-RFQ stressed, 2 h
jun-11 IH1 tube socket shortcut, 12 h
Jun-17 HSI-ICH-triplet water and mech. instable (

## Slide 6
16.2. HSI-RFQ Ignitron tausch , 3,5 h.
22.2.24: UT2MUX tröpfelt , eimer, später kamera…
22.2.24: UT1QD11 kann nicht Hub >0,5 Volt , strahl springt auf X6 vertik.-DG
22.2.24 A4 Pulsklnge gehtz nicht 1 ms, behoben durch Kainberger ab 3.4.24
20.3. UXAMU1 water leak Power supply
25.3.-28.3 Reparaturen Tunnelseptum Tausch 3. Spule X, Gasstripper Ventil Nr. 1 kaputt, wird getauscht.
Do, 18.4.2024, 09:14 Ausfall A2A, Kurzschluß Leitung Senderwagen zu Endstufe UG1, Reparatur dauert lange, bis Freitag 15 uhr.
18.4. A2A kaputt, senderwagen, (30 stunden, Do 0900 bis Fr 1500)
sa 20.4.24 Strahl 36Ar8+ wackelt am TK-Ende, Pulseung/Parallelbetrieb mit Erbium geht nicht gut (UT1QD11??)
20.4. TK2MU3 …wackelt. wie QD11...
31.5. TK4QD31 tröpfelt, rep. TRI (00:10 -14:10 h). KS01 fiel aus wg wasserverslust an TK4QD31 (viele sis geräte aus, ks01….)
Do 6.6. BB12 (viel-schalt-zu 1,5 h), 7.6. hochspannnungskabel röhrenkabinett gekürzt (3 h), Sa 8.12. ausfall-weiter ohne bb12 nur niedrige intensität verlangt, Mo 10.6. tausch kabel (3 h).
10.6. hsi rfq hustet, IZ aus, ein, ampl. 7,18 auf 7,08 riunter..(ebenso 3 x früher…)
nacht auf 11.6., 2 uhr IH1 , röhrentausch, röhrensockel kurzschluß, anodenkondensator (12 Std.), 1,3-1,8 MW, >200 kW rücklauf, Mi 12.6. ampl von 8,568 auf 8,403 Volt runtergesetzt.
17.6. hsi IH triplet uh3qt3 water loss and mech. instable, wobbeling, during SIS down (20-kV-filter AEG)
Remarkable events

## Slide 7
9th Feb: Interlock from ECR ion source microwave SPS
16th Feb: HSI-RFQ ignitron replaced, 3.5 h.
22nd Feb: UT2MUX water loss, automatic pumped bucket, monitored by camera
22nd Feb: Vertical beam jitter (X6 SEM grid), quadrupole UT1QD11 switch range >0,5 V…
22nd Feb: A4 beam pulse length 1 ms not possible (solved 3rd Apr)
Remarkable events February (C, Ti, Ar, O-beam)
UT2MUX, 22nd Feb
new spare part ready 26th Feb
UT1QD11 beam jitter

## Slide 8
20.3. Dipole magnet UXAMU1 power supply water leak (30 h loss for X0)
25.3.-28.3 Easter break:
  UT2MUX replaced
  Gas stripper valve #1 replaced
Remarkable events March (Gold beam)
Damaged UT2MUX, photos 10th April
UXAMU1 Power Supply,
water cooled transistor bank,
photos 18th March
Gas stripper section, photo 26th March

## Slide 9
18th Apr, 9 a.m., failure Alvarez A2A, short circuit of Grid-1 connection of RF tetrode, disassembly of amplifier and tube socket, repair lasts until 19th Apr, 3 p.m. (30 hours)
20th Apr, beam jittering at transfer channel end (36Ar8+), parallel operation with 170Erbium23+ problematic (UT1QD11?)
20th Apr, also TK2MU3 causes beam jittering (like QD11). Switching coil current from 330 A (Erbium) to 199 A (Ar) problematic.
Remarkable events April (Fe, Ar, Erbium-beam)
Power Supplies TK1MU1, MU2, TK2MU3 (photo 22nd Apr)
A2A short circuit Grid-1 connection of RF tetrode.
Photos courtesy G. Schreiber

## Slide 10
7th May: gas stripper valve #2 replaced (7 hours during planned interruption)
31st May („bridge day“, Corpus Christi): water loss TK4QD31, KS01 switch off (14 hours)
Remarkable events May (Ni, Cr, Molybdenum-beam)
leak copper pipe…, brazed, … insulated.
TK4 curve
11.25° dipole
MU41 QD31 QD32 QD4
… …MU42

## Slide 11
6th-10th Jun BB12
  needs multiple switching-on to re-start (1,5 h),
  7th Jun, high voltage cable to tube cabinet shortened (3 h),
  8th Jun, again failure, then operation without BB12 (only low beam intensity requested),
  10th Jun, high voltage cable and HV filter box feedthrough connectors replaced (3 h).
10th Jun (and 3x before), HSI-RFQ, Uranium routine operation: RF level failure, sparking (ion getter pumps switching off!), then: reduce voltage from 7.18 to 7.08 V.
11th Jun, night (2 a.m.), HSI-IH1 RF failure, tube replaced, tube socket short repaired, anode capacitor replaced (12 h). Increased RF power: 1.6 MW, >200 kW reflected!
12th Jun, voltage reduced from 8,568 to 8,403 V.
17th Jun, HSI Quadrupole Triplet UH3QT3 water loss and mechanically instable (wobbeling), provisionally fixed during SIS down (20-kV-filter AEG)
Remarkable events June (U-beam)
RF behaviour IH1
UH3QT3
Tube cabinet IH1
Fotos IH1 courtesy G. Schreiber

## Slide 12
2.2.24: IBN/Machine Exp, PIG 50 Ti (bis 6.2.), MUCIS CH3 (bis 21.2.), 40Ar EZR (bis 18.2.)
16.2. HSI-RFQ Ignitron tausch , 3,5 h.
22.2.-27.2. MUCIS 18O
22.2.24: UT2MUX tröpfelt , eimer, später kamera…
22.2.24: UT1QD11 kann nicht Hub >0,5 Volt , strahl springt auf X6 vertik.-DG
22.2.24 A4 Pulsklnge gehtz nicht 1 ms, behoben durch Kainberger ab 3.4.24
28.2.-24.3. PIG Au8+ 25 Hz, und MeVVa Au4+
20.3. UXAMU1 water leak Power supply
25.3.-28.3 Reparaturen Tunnelseptum Tausch 3. Spule X, Gasstripper Ventil Nr. 1 kaputt, wird getauscht.
Do, 18.4.2024, 09:14 Ausfall A2A, Kurzschluß Leitung Senderwagen zu Endstufe UG1, Reparatur dauert lange, bis Freitag 15 uhr.
cwlinac:\UNILAC\4_UNILAC_MK\BTR\2024\BTR 2024 UNILAC.pptx
Sammlung Beamtime 2024
BEAM TME RETREAT 2023
BEAM TIME RETREAT 2023

## Slide 13
18.4. A2A kaputt, senderwagen, (30 stunden, Do 0900 bis Fr 1500)
sa 20.4.24 Strahl 36Ar8+ wackelt am TK-Ende, Pulseung/Parallelbetrieb mit Erbium geht nicht gut (UT1QD11??)
20.4. TK2MU3 …wackelt. wie QD11...
uxads1hl endlage außen 25.4. wg. leck (2 hours)
31.5. TK4QD31 tröpfelt, rep. TRI (00:10 -14:10 h). KS01 fiel aus wg wasserverslust an TK4QD31 (viele sis geräte aus, ks01….)
Do 6.6. BB12 (viel-schalt-zu 1,5 h), 7.6. hochspannnungskabel röhrenkabinett gekürzt (3 h), Sa 8.12. ausfall-weiter ohne bb12 nur niedrige intensität verlangt, Mo 10.6. tausch kabel (3 h).
10.6. hsi rfq hustet, IZ aus, ein, ampl. 7,18 auf 7,08 riunter..(ebenso 3 x früher…)
nacht auf 11.6., 2 uhr IH1 , röhrentausch, röhrensockel kurzschluß, anodenkondensator (12 Std.), 1,3-1,8 MW, >200 kW rücklauf, Mi 12.6. ampl von 8,568 auf 8,403 Volt runtergesetzt.
17.6. hsi IH triplet uh3qt3 water loss and mech. instable, wobbeling, during SIS down (20-kV-filter AEG)
17.6. UH3QT3 tröpfelt und wackelt, fixiert, tröpfel rep. folgt im shutdown.
Slide Titel
BEAM TME RETREAT 2023
BEAM TIME RETREAT 2023

## Slide 14
Decisison before Christmas: pulsed stripper for beamtime 2024!
Oil services…
17th mar, roots failure, oil failure, 3 hours (2.5 litres re-filled).
25th-28th mar, easter shutdown, valve #1 replaced.
11th apr, valve #2 defective, permanent-open. Replaced 7th may, incl. oil service (7 hours)
from 8th may on: only valve #2, 550 mbar (=Cr optim., Ni 250, Mo 400 optim)
from 22nd may Uranium exclusively, (valve #2, 500 mbar N2, permanent-open - didn’t matter.
3rd-6th jun H2 stripping gas, valve #1, 6 bar.
5th jun: For PIG-Ar-beam to US3 additionally 5 Hz H2-Gas , vacuum pressure increases and bunchers BB3+4 switch off (vac–threshhold) – machine exp. postponed to N2 gas next day.
Gasstripper
BEAM TME RETREAT 2023
BEAM TIME RETREAT 2023

## Slide 15
A2QS105/106 (QS46/47) out of operation (DR105)
ER1 max 4,5 V, BB4 max. 5,3 V, BB6 max 6 V.
UN3DC2 sudden drive in beam (06th feb), IL µWave…
special regulations EH from rad. safety department, chains and locks…
Scada MCR no ion getter pump switching-on for normal operators.
from 11th apr on: (36Ar8+) HLI RFQ phase jitter, misleading displaying in the MCR RF application.
25th apr, Slit/blind UXADS1HL water dripping, provisionally fixed (2 h)
13th may, 52Cr14+ for X8 suddenly lost. Dipole UXAMU1?? – UX8VV2T leak (replaced 14th may)
Preconditons and Various
BEAM TME RETREAT 2023
BEAM TIME RETREAT 2023
EH Caves, locked, regulations
A2QS105+106 out of operation
UXADS1HL water loss

## Slide 16
Beam time was planned carefully!
Hardware failures, …some
  – minor influence
  – during planned intervention times
  – or repaired in short time
Less failures from RF department point of view
Summary / Conclusions

## Slide 17
UN5QT4, spare part in production,
  Dec. 2024 delivery date (then copper coating),
  Feb. 2025 beam operation 48Ca10+ with defective old QT4 (test!).
  Then replacement if resonable/necessary.
EH dipole chambers..
new power supplies UL/UR quadrupoles?? delivery…
Gas stripper pulsed (valves…) or not pulsed? (Uranium efficiency!)
54Chrome from PIG or ECR? (54Cr2+…)
A2DR105 replaced? (If QS105+106 in operation, then all QS in operation.)
Outlook to 2025
BEAM TME RETREAT 2023
BEAM TIME RETREAT 2023

## Slide 18
Thank you for your attention!