## Slide 1: Triplet Based Online Track Finding in the PANDA-STT

## Slide 2: Outline
  Introduction
    PANDA Detector
    Straw Tube Tracker (STT)
    Operating Conditions
  Online Tracking Scheme
    Concept
    Tracking Algorithms
  Triplet Finder
    Concept
    Processing of Axial and Skewed Straws
    Monte Carlo Benchmarking
    Results
    GPU Implementation
  Summary

## Slide 3: Future FAIR Facility in Darmstadt
Antiproton – Proton fixed target experiment in the charm mass energy region
PANDA

## Slide 4: PANDA Detector
Interaction point
Antiproton beam
Fixed proton target:
Pellet or cluster jet
13 m

## Slide 5: PANDA Detector
13 m
Micro Vertex Detector
  PANDA: Rare channels, high rates (2·107 evts/s)
  Similar topology of signal and background
  No simple event selection criteria with high suppression potential
Online event filter instead of traditional trigger
  Most signal channel selections require online tracking information
Straw Tube Tracker

## Slide 6: Straw Tube Tracker
  Straw = cylindrical drift chamber
  4636 straws in 20 – 27 layers
  Close packed axial layers
  Skewed layers (±3°) for z reconstruction
  Total weight: 15 kg
  Total radiation length: 1.2 %
84 cm
isochrones
tdrift = thit – t0
150 cm
1 cm

## Slide 7: PANDA Operating Conditions
  Gap estimate:
    Barrier Bucket: 80% Filling
    HESR length: 575 m
    Antiproton velocity: ~c
    Revolution time: 2000 ns
    Gap: 400 ns
    Fill/Gap ratio may vary
  Events per revolution  Burst:
    2·107/s·2 µs = 40

## Slide 8: Event Structure
Time based simulation by T. Stockmanns
2 · 107 events/s
Blue: MVD Hits
Red: STT Hits

## Slide 9: Online Tracking Scheme

## Slide 10: Online Tracking
Online Tracking
Tracks
Information Merging:
PID, etc
Calibration
Alignment
…
Detector Hits/Digis
Local Clustering
STT Tracking
Global Tracking
Software Trigger
Further Algorithms:
Hough transform,
Riemann tracker, …
Triplet Finder
Global scheme specifically designed for PANDA

## Slide 11: More (Online) Tracking Algorithms
Algorithm | Comments
Hough Transform, Yutie Liang | FPGA implementation
Hough Transform, Mohammad Al-Turany/Andreas Herten | GPU implementation
Non-Origin Trackfinder, Lia Lavezzi | Focused on offline, online application(?)
Triplet Finder, MCM | No isochrone info required, online
Track Segment Finder + Linker, Sean Dobbs | Template based
Fast Combinatorial Finder / Fitter, Sean Dobbs | Based on CLEO‘s SOLO
Forward Hough, Martin Galuska | Focused on offline, applicable for online
Riemann Tracker, Tobias Stockmanns | Focused on offline, online application(?)
Global Tracking in PandaRoot, Gianluigi Boca | Focused on offline
Neural networks pattern reco, Pablo Genova | Focused on offline, applicable for online
Riemann Tracker, Andreas Herten | GPU implementation
Triplet Finder, Andrew V. Adinetz | GPU implementation

## Slide 12: Track Information Storage / Algorithm Interplay
  Connection of hits to tracks
  Ideal storage for these connections?
  Desired parameters to store?
  Override old values? Store list?
  Parameters for assigned hits/tracks
    Unassigned
    Low quality – Veto value close to threshold
    Mid quality
    High quality – additional quality criterion passed
    Multi algorithm confirmed quality

## Slide 13: Triplet Finder

## Slide 14: Triplet Finder Concept
  Focus on mathematical simplicity  Fast and robust
  No isochrone information used  Does not require t0 or radius-drifttime calibration
  Can provide t0 seed for selected tracks (hit timestamp constraints, matching with other detectors)
  Three step operation:
    Identification of hit Triplets (or n-lets) around pivot straws
    3 point circle calculation: Origin + 2 Triplets
    Hit association via circle proximity

## Slide 15: STT Geometry in PandaRoot
Axial pivot straws indicated
in one sector (red)
Skewlet layers indicated
in one sector (orange)
Axial Straws:
Triplets are generated around pivot straws
Skewed Straws:
Half-Skewlets are generated per skewed double layer (analog to Triplets in the axial layers)
Half-Skewlets of oppositely skewed double layers above and below Skewlet layer are combined to (full) Skewlets  3D spatial information

## Slide 16: Triplet Finding in Axial Straws
  Pivot straw is checked for hit
  Surrounding straws are checked for hits
  Center of mass of fired straws is calculated (small number of combinations  suitable for lookup table)
Pivot straws

## Slide 17: Event Time Constraining
  t0 constraining concept for Triplets and tracks:
Pivot straws
t1
t2
t3
220 ns

## Slide 18: Triplet Finding in Axial Straws
  Once two triplets are found, calculate circle through origin
  Associate nearby hits with track candidate
Track Verification:
  Currently mix of curvature and number of associated hits
  Lots of room for improvement
Further possibilites:
  Distance sorting, Concurrent associations, Clutter veto, …
  Missing straw compensation: Pivot straw triggered by neighbor straws
  Weight hits within triplet according to timestamp
Interaction Point
Pivot straws
Pivot straws

## Slide 19: Triplet Finding in Axial Straws
Interaction Point
Pivot straws
Pivot straws
  Once two triplets are found, calculate circle through origin
  Associate nearby hits with track candidate
Track Verification:
  Currently mix of curvature and number of associated hits
  Lots of room for improvement
Further possibilites:
  Distance sorting, Concurrent associations, Clutter veto, …
  Missing straw compensation: Pivot straw triggered by neighbor straws
  Weight hits within triplet according to timestamp

## Slide 20: Triplet Finding in Axial Straws
Interaction Point
Pivot straws
Pivot straws
  Once two triplets are found, calculate circle through origin
  Associate nearby hits with track candidate
Track Verification:
  Currently mix of curvature and number of associated hits
  Lots of room for improvement
Further possibilites:
  Distance sorting, Concurrent associations, Clutter veto, …
  Missing straw compensation: Pivot straw triggered by neighbor straws
  Weight hits within triplet according to timestamp

## Slide 21: Triplet Finding in Axial Straws
Interaction Point
Pivot straws
Pivot straws
  Once two triplets are found, calculate circle through origin
  Associate nearby hits with track candidate
Track Verification:
  Currently mix of curvature and number of associated hits
  Lots of room for improvement
Further possibilites:
  Distance sorting, Concurrent associations, Clutter veto, …
  Missing straw compensation: Pivot straw triggered by neighbor straws
  Weight hits within triplet according to timestamp

## Slide 22: Triplet Finding in Axial Straws
Interaction Point
Pivot straws
Pivot straws
  Once two triplets are found, calculate circle through origin
  Associate nearby hits with track candidate
Track Verification:
  Currently mix of curvature and number of associated hits
  Lots of room for improvement
Further possibilites:
  Distance sorting, Concurrent associations, Clutter veto, …
  Missing straw compensation: Pivot straw triggered by neighbor straws
  Weight hits within triplet according to timestamp

## Slide 23: Triplet Finding in Skewed Straws: Skewlets
  Triplet search in individual skewed double layers
  Combination of adjacent double layers‘ Triplets to Skewlets
  Track matching in xy-projection
  Extraction of z-information

## Slide 24: Triplet Finding in Skewed Straws: Skewlets
  Triplet search in individual skewed double layers
  Combination of adjacent double layers‘ Triplets to Skewlets
  Track matching in xy-projection
  Extraction of z-information

## Slide 25: Triplet Finding in Skewed Straws: Skewlets
  Triplet search in individual skewed double layers
  Combination of adjacent double layers‘ Triplets to Skewlets
  Track matching in xy-projection
  Extraction of z-information

## Slide 26: Triplet Finding in Skewed Straws: Skewlets
  Triplet search in individual skewed double layers
  Combination of adjacent double layers‘ Triplets to Skewlets
  Track matching in xy-projection
  Extraction of z-information

## Slide 27: Triplet Finding in Skewed Straws: Skewlets
  Triplet search in individual skewed double layers
  Combination of adjacent double layers‘ Triplets to Skewlets
  Track matching in xy-projection
  Extraction of z-information

## Slide 28: Triplet Finding in Skewed Straws: Skewlets
  Triplet search in individual skewed double layers
  Combination of adjacent double layers‘ Triplets to Skewlets
  Track matching in xy-projection
  Extraction of z-information

## Slide 29: Triplet Finding in Skewed Straws: Skewlets
  Triplet search in individual skewed double layers
  Combination of adjacent double layers‘ Triplets to Skewlets
  Track matching in xy-projection
  Extraction of z-information

## Slide 30: Triplet Finding in Skewed Straws: Skewlets
  Triplet search in individual skewed double layers
  Combination of adjacent double layers‘ Triplets to Skewlets
  Track matching in xy-projection
  Extraction of z-information

## Slide 31: Triplet Finding in Skewed Straws: Skewlets
  Triplet search in individual skewed double layers
  Combination of adjacent double layers‘ Triplets to Skewlets
  Track matching in xy-projection
  Extraction of z-information

## Slide 32: Triplet Finding in Skewed Straws: Skewlets
  Triplet search in individual skewed double layers
  Combination of adjacent double layers‘ Triplets to Skewlets
  Track matching in xy-projection
  Extraction of z-information

## Slide 33: Monte Carlo Simulation

## Slide 34: Hitstream Display: 15 GeV/c DPM, 50 ns Mean Time
  Black circles: Early isochrone
  Blue circles: Early skewed isochrone
  Green circles: Close isochrone
  Red circles: Late isochrone
  Black dots: MVD hits
  Green dots: MVD hits r/z > 0.3
  Black+Red dots: Triplets/Skewlets
  Yellow tracks: Timed out track
  Blue tracks: Current track
XY-View
  DPM Benchmark: Realistic event rate and structure, continuous operation
Dual Parton Model (DPM): Standard pp background generator

## Slide 35: Monte Carlo Benchmarking
  Efficiency: Ratio of correctly reconstructed tracks vs. simulated tracks
  Purity: Quality of track finder output
  Resolution: Deviation of reconstructed observables from MC input for selected tracks (of secondary interest for a track finder  defer to track fitter)

## Slide 36: Monte Carlo Benchmarking
  Time-based simulation with 50 ns mean time between events
    Continuous stream of hits
    Realistic event overlaps
    Realistic selection of time windows for track finding
    BUT: Lots of information which is trivial in event based simulations, is harder to obtain in time based simulations
  Benchmark requires careful selection of „reconstructable“ events
  Two directions of analysis:
    Reconstructable Monte Carlo event input
    Complete track finder output

## Slide 38: Reconstruction Run Statistics (200 µs of Data)
Total reconstructed track count: 38246
Reached MC ID: 3917
MC Track Grand Total: 1968001
MC Track PDG Code too large: 4987
MC Track Non Prime: 1910598
MC Track Low Momentum: 25341
MC Track Low Pt Hit: 2738
MC Track Low BetaGamma: 5508
Secondary Tracks: 3582
MC Track missed STT: 8822
MC Track to be recoed: 9163
MC Track recoed (all): 6778
MC Track recoed (90): 4787
MC Track recoed (80): 5581
MC Track recoed (bad): 3295
MC Track not recoed: 2385
MC Match Good 90: 15314
MC Match Good 80: 21008
MC Match Bad: 17177
MC Tracks with NULL pointers in Reco: 61
MC Tracks with NULL pointers: 0
Crashes PDG Library
Prime: MC ID -1 and 0
< 60 MeV/c
< 0.4
> 2 cm
MC Tracks Found
Reconstructable MC Tracks

## Slide 39: Momentum Distribution – MC „Primes“

## Slide 40: Momentum Distribution – Reconstructable Tracks

## Slide 41: Momentum Distribution – Reconstructed Tracks

## Slide 42: Results: Positive Particles‘ pt (Full Output)
PRELIMINARY
Many low momentum recoil protons

## Slide 43: Results: Positive Particles‘ pt (80% Correct Hits)
PRELIMINARY

## Slide 44: Results: Positive Particles‘ pt (90% Correct Hits)
PRELIMINARY

## Slide 45: Results: Negative Particles‘ pt (Full Output)
PRELIMINARY

## Slide 46: Results: Negative Particles‘ pt (80% Correct Hits)
PRELIMINARY

## Slide 47: Results: Negative Particles‘ pt (90% Correct Hits)
PRELIMINARY

## Slide 48: Results: pt Resolution (Full Output)
PRELIMINARY

## Slide 49: Results: pt Resolution (80% Correct Hits)
PRELIMINARY

## Slide 50: Results: pt Resolution (90% Correct Hits)
PRELIMINARY

## Slide 51: Results: φ Resolution (Full Output)
PRELIMINARY

## Slide 52: Results: φ Resolution (80% Correct Hits)
PRELIMINARY

## Slide 53: Results: φ Resolution (90% Correct Hits)
Little Bumps
PRELIMINARY

## Slide 54: Bumps: Both Directions of Recurring Tracks

## Slide 55: Bumps: Both Directions of Recurring Tracks

## Slide 56: GPU Implementation
Andrew V. Adinetz, NVIDIA Application Lab (www.fz-juelich.de/ias/jsc/nvlab)
Max. Burst Size

## Slide 57: Outlook
Triplet Finder
  Further studies with actual signal instead of background  Efficiencies and purities (resolution interesting, but not primary figure of merit  Track fitter)
Online Tracking System
  Investigate algorithm interplay
  Investigate „special cases“  Track flags, i.e. duplicate, curler, …
  Investigate correlation between
    Efficiency / Resolution
    Track properties
    Observables at reconstruction time
   Online reconstruction quality control  Selection of best result from several algorithms
Requirements in PandaROOT
  Burst simulation in digitization  Realistic burst structure in online reconstruction
  Signal events embedded into background at selectable rates (e.g. minimum time between signal events)

## Slide 58: Summary
  Full online tracking system design/ideas/requirements advancing
  Proof of concept Triplet Finder tested with DPM input in time based simulations at realistic event rates
  Robust first-line algorithm independent of isochrone (t0) information and drifttime calibration
  First quantitative test results incoming
  Many (straightforward) tuning possibilites affecting efficiency, purity and robustness to be studied
Future
  Triplet Finder reconstruction tests with signal events
  Investigation of interplay with other algorithms
  Investigation of „special cases“ (e.g. duplicate, curler, kink tracks)  Flags useful?
  More accurate simulation of PANDA‘s event structure required
Thank you for your attention