## Slide 1
Weak-strong simulations of electron cloud effects from
the Inner Triplets of the Large Hadron Collider
Konstantinos Paraschou, Giovanni Iadarola, Lotta Mether
CERN, Geneva, Switzerland
Many thanks to: G. Rumolo, H. Bartosik, Y. Papaphilippou, F. Van der Veken
14th International Computational Accelerator Physics Conference 2nd October 2024

## Slide 2
Introduction and motivation
Description of simulation method
Simulation results:
  Validation
  Frequency map analysis
  Dynamic aperture
Outline

## Slide 3
Introduction and motivation
Description of simulation method
Simulation results:
  Validation
  Frequency map analysis
  Dynamic aperture
Outline

## Slide 4
Electron clouds
Electrons are introduced into the chamber (residual gas ionization / synchr. rad. + photoelectric effect)
Electrons are accelerated by passing bunches and impact on beam chamber, emitting more electrons.
  If conditions allow, electrons multiply
  exponentially!
Quadrupole:
[PyECLOUD simulation]

## Slide 5
Slow proton beam loss comes from:
Luminosity burn-off (inelastic p-p collisions).
Additional losses (Beam dynamics).
Motivation
Total loss rate (Fast Beam Current Transformer)
Luminosity (ATLAS + CMS)
Several configurations were tested. All observations point to the e-cloud forming in the Inner Triplet quadrupoles. (Final focusing quadrupoles)
Good news: HL-LHC Inner Triplet will have a-C coating to suppress e-cloud formation.
Can we simulate these losses?
(By looking for a reduction of dynamic aperture in particle tracking simulations)

## Slide 6
The Inner Triplet
Q1
Q2A
Q2B
Q3
Large Hadron
Collider
The Inner Triplets are complex and in ≈ 30 m :
Two beams present arriving at different times at each slice (w.r.t. to each other).
Rapidly changing closed orbit.
Rapidly changing betatron functions.
Many slices are necessary.

## Slide 7
The computational problem
Q1
Q2A
Q2B
Q3
E-cloud strongly depends on delay between two beams:
  Less e-cloud at locations of beam-beam long-range interactions
  Less e-cloud in drift spaces.
384 slices per triplet → 4 triplets, 1536 slices.
≈ 4GB per slice → ≈ 6 TB

## Slide 8
Introduction and motivation
Description of simulation method
Simulation results:
  Validation
  Frequency map analysis
  Dynamic aperture
Outline

## Slide 9
Strategy
[G. Iadarola, CERN-ACC-NOTE-2019-0033]
An e-cloud slice can be described by a scalar potential ϕ(x, y, ζ) in a thin-lens formalism.
Transport slices to same location.
Slices commute (only depend on x, y, ζ). They can be summed.
ζ refers to s – β0ct, the longitudinal distance from the reference particle
i
1
k
2
3
4
...
Transport through
segment
Transport through
e-cloud slice

## Slide 10
Approximations
i
1
k
2
3
4
...
(1st approximation):
Courant-Snyder parameterization
(2nd approximation):
Constant phase advance
(3rd approximation):
No longitudinal motion
Effective (lumped) e-cloud:
i
k
Combines all slices into one scalar potential.
Equation can be evaluated on a 3D grid, and treated as a single slice.

## Slide 11
Effective e-cloud
Non-linear time-dependent forces.
Forces become exceedingly non-linear at large amplitudes of oscillation.
Weak-strong simulations:
Assume e-cloud is in a steady state.
Map is constructed once in a “pre-processing stage”, and re-used during particle tracking.

## Slide 12
Pre-processing stage (weak-strong)
PyECLOUD simulations (CPU)
1st slice
2nd slice
3rd slice
Nth slice
Triplet Maps
Particle tracking stage
Frequency map
analysis
Xsuite simulations (GPU)
Dynamic aperture
Emittance growth
Simulation flow
~ 8 CPU hours per slice, easy to parallelize
Tracking time for 1 000 000 turns, 20 000 particles in A100 GPU:
LHC lattice : 5.7 hours
LHC lattice + beam-beam : 6.1 hours
LHC lattice + beam-beam + e-cloud : 7.0 hours
reduction from ~ TB to ~ GB in required memory per triplet

## Slide 13
Introduction and motivation
Description of simulation method
Simulation results:
  Validation
  Frequency map analysis
  Dynamic aperture
Outline

## Slide 14
Validation
Focus on Q3 quadrupole (right of interaction point 1): Q3R1.
64 slices, can fit in 1TB RAM computers.
Dynamic aperture simulations to test previous equation.
Good agreement.
Q1
Q2A
Q2B
Q3

## Slide 15
Frequency Map Analysis
Tracking over 100 000 turns, tune evaluated over:
  First 50 000 turns,
  Last 50 000 turns.
Difference in tune → tune is not constant and so trajectory is chaotic.
  E-cloud doesn’t cause a significant tune-shift (compared to beam-beam effects)
  Visible effect of e-cloud → increase of non-linearities.
Beam-beam effects
Beam-beam effects &
e-cloud (in 4 Inner Triplets)

## Slide 16
Dynamic aperture
Dynamic aperture over 1 000 000 turns, including the e-clouds in the 4 inner triplets (left and right of i.p. 1 and 5).
E-cloud in triplet scales favorably with higher intensity.
E-cloud effects can become as strong as beam-beam effects at low bunch intensities.
E-clouds are worse with larger Secondary Emission Yield (SEY).
SEY < 1.10 will be enough to mitigate the effect of e-cloud in the triplets.

## Slide 17
Dynamic aperture
Tune scan
Dynamic aperture over 1 000 000 turns,
including the e-clouds in the 4 inner triplets (left and right of i.p. 1 and 5). Simulations varying the working point.
E-cloud effects cause a reduction of dynamic aperture for all tunes.
The optimal working point remains similar.
Simulation parameters:
Bunch intensity = 1.2 1011 p/b
SEY = 1.30

## Slide 18
Thank you for your attention!
Konstantinos Paraschou
Conclusions
Region around Inner Triplets is complicated.
Electron cloud effects from the inner triplets in the LHC can be simulated.
Method was developed and benchmarked to be able to simulate effects in a sustainable manner, by reducing memory consumption.
Frequency Map Analysis:
  Increased chaoticity that goes deeper into the distribution of particles.
  No significant tune-shift effects
Dynamic aperture studies:
  Effect that can be at least as strong as beam-beam effects at low bunch intensities.
  Cannot be mitigated with a change in working point.
Strategy of HL-LHC upgrade project to coat the new inner triplets with amorphous carbon remains a good solution.

## Slide 19
Backup slides

## Slide 20
Beam parameters:
Bunch intensity = 1.2 1011 p/b
norm. emittance = 2 μm
r.m.s. bunch length = 0.09 m
Energy = 6.8 TeV
Surface parameters:
SEY = 1.30
2023 Optics with β* = 30 cm
Half-crossing angle : 160 μrad
Working point: Qx = 62.31
Qy = 60.32
Non-linearities to mitigate coherent instabilities: Q’ = 20
I_MO = 300 A
Residual uncorrected global linear coupling:
Re[C-] = 0.001
Simulation parameters

## Slide 21
Lie tranformations
Lie transformations are operators that describe the solution of Hamiltonian systems:
where
is the Poisson bracket.
Example:
Transport through element with Hamiltonian
Transport through element with Hamiltonian
Transport through element with Hamiltonian

## Slide 22
Lie transformations
i
j
k
: Hamiltonian of e-cloud
interaction for one slice
at location j
: Hamiltonian of transport
between location i and j
: Hamiltonian of transport
between location j and k
Step 1: use property

## Slide 23
Lie transformations
i
j
k
We have transported the e-cloud slice (without approximation).
We need to simplify
Step 2: use property

## Slide 24
Lie transformations – Courant-Snyder parameterization
Courant-Snyder parameterization (first approximation):
Constant phase advance (second approximation):
Transformation becomes:
Third approximation: longitudinal coordinate doesn’t change.

## Slide 25
Effective e-cloud
Equation is manageable in this form.
is defined on a 3D grid, we just need to reinterpolate based on the above equation.
i
1
k
2
3
4
...
1536 simulations each to:
Do electron cloud buildup,
Detailed bunch passage “pinch”.
Combine on-the-fly to same 4 files.