## Slide 1: Automation and AI integration at the CERN injectors
14th International Computational Accelerator Physics Conference Lufthansa Seeheim Conference Hotel 02. October 2024
A. Huschauer, V. Kain, M. Schenk, F. Velotti on behalf of the CERN accelerator community

## Slide 2
40+ years ago at the CERN ISR …
J. Gamble et al., 11th International Conference on High-Energy Accelerators, CERN, Geneva, July 1980

## Slide 3
40+ years ago at the CERN ISR …
J. Gamble et al., 11th International Conference on High-Energy Accelerators, CERN, Geneva, July 1980
Some things have largely remained the same
Need for automation: complex interlinked systems, maximising machine availability and beam quality, reducing beam setup times
Reproducibility challenges: magnetic hysteresis and eddy-current effects, external factors beyond our control
Challenge of convincing ourselves of need and feasibility for automation
Have come a long way
Advanced analysis, modelling, algorithms (& computing libraries)
Flexibility of DAQ, real-time processing, control system
Improved BI & logging: observables, amount of data / bandwidths
Computing power

## Slide 4: Introduction
Accelerator automation history (at CERN)
2018
    Optimisers, ML, …
    Typically on-demand
    Learn models if not available
    Infrastructure: Python & frameworks
2021 -
    Closing the loop: continuous control or auto-launch
    Infrastructure: server-based solutions
    Equipment: predictive maintenance, fault analysis, …
1980
    High-level parameter control
    Hierarchical structures
    Conditional sequencing of actions
Classical automation
Adding AI / ML
2006
    Reduce complexity through models high-level parameter models with hierarchies, settings generation
    Sequencers, watchdogs & SW interlocks, classic control
systematic exploitation of ML & AI
Notes: Recent years: addition of AI / ML to control room. However, not yet in a systematic manner.  EPA

## Slide 5: Contents
    Introduction
    Efficient Particle Accelerators
      Infrastructure
      Specific WPs
    Final remarks

## Slide 6: Contents
    Introduction
    Efficient Particle Accelerators
      Infrastructure
      Specific WPs
    Final remarks

## Slide 7: Efficient Particle Accelerators project
Efficiency Think Tank
Question coming up repeatedly at CERN end-of-year workshops ‘21 & ‘22
How to better exploit the accelerator complex? in terms of efficiency, reproducibility, flexibility, and performance
Efficiency Think Tank (ETT) in 2023
7 strategic recommendations

## Slide 8: Efficient Particle Accelerators project
From think-tank to project
Think tank Efficient Particle Accelerators (EPA) project
Approved in 2023 for a 5-year period
9 interlinked work packages (WP)
Think tank recommendations
Infrastructure evolution

## Slide 9: Efficient Particle Accelerators project
From think-tank to project
Think tank recommendations
Infrastructure evolution
Think tank Efficient Particle Accelerators (EPA) project
Approved in 2023 for a 5-year period
9 interlinked work packages (WP)
Evolving infrastructure is key to bringing AI / ML into operations

## Slide 10: Contents
    Introduction
    Efficient Particle Accelerators
      Infrastructure
      Specific WPs
    Final remarks

## Slide 11: Infrastructure
Frameworks & building blocks
Machine Learning Platform Deployment & inference of (ML) models
Service to store & share ML models with VC
Language agnostic
Available in control room
Acc-Py “accelerating Python”
Full integration of Python with control system
Online data acquisition, equipment access (set / get), app development, …
Python package index
Classical automation concepts
EPA: sequencer 2.0, equipment testing, settings management
Sequencer: programmatic execution of tasks
High-level parameter models
AccTesting
    UCAP Unified Controls Acquisition & Processing
Virtual device service
Event-based, online data transformations
Further evolution with EPA
    GeOFF Generic Optimisation Framework and Frontend
    geoff4ucap Framework for optimisation & control via UCAP
        Facilitate implementation of automatic control
        Exploit & expose features of control architecture
        Maintain uniformity across complex
    Auto-pilots & optimisers
Enabling automation with AI / ML

## Slide 12: Infrastructure
UCAP: Unified Controls Acquisition & Processing
Framework & service to implement and run online data processing pipelines
Pipelines can be chained and structured into hierarchies
Can combine data from (almost) any source
Plays a key role in realising various EPA objectives
Transform
Process incoming data
Java or Python
GPU support
Acquire
Subscribe to data sources
Group incoming data via EventBuilder (e.g. cycle stamp)
Can be specific cycle(s) or all
Publish
Publish results
Can be hardware “sets”
Can be stored in logging database

## Slide 13: Infrastructure
UCAP: Unified Controls Acquisition & Processing
Example UCAP hierarchy: active noise cancellation on the SPS slow-extracted spill
Beams affected by noise introduced through power converter ripple (50 Hz and harmonics)
BSI signal (intensity during SX)
SX spill analysis
Noise spectrum
Noise cancellation controller (GP model, GPU)
gain & phase (hardware “sets”)
Other input
Intensity performance analysis
UCAP BCT concentrator
Metadata
…
Dump time
Extracted intensity
…
Data
Model

## Slide 14: Infrastructure
GeOFF & geoff4ucap
Parameter optimisation & drift compensation problems are being tackled across the injector complex
Generic Optimisation Framework & Frontend (GeOFF)
  Python framework to unify optimisation approaches
  Standardised interfaces, tools for developers & docs
  GUI application that wraps everything together
  “Facilitate implementation of parameter optimisation task with primary focus on problem itself”
Initiated at CERN and since 2022 under development in collaboration with GSI
Since 2023 similar framework adopted for UCAP
  Server-based GeOFF
  Cover need for continuous controllers
or simulation …

## Slide 15: Contents
    Introduction
    Efficient Particle Accelerators
      Infrastructure
      Specific WPs
    Final remarks

## Slide 16: Efficient Particle Accelerators project
From think-tank to project
Think tank Efficient Particle Accelerators (EPA) project
Approved in 2023 for a 5-year period
9 interlinked work packages (WP)
Evolving infrastructure is key to bringing AI / ML into operations
Think tank recommendations
Infrastructure evolution

## Slide 17: Efficient Particle Accelerators project
Overview
Remove fixed supercycles by dynamically & algorithmically scheduling beams
Deterministic magnetic field control Will have positive impact on reproducibility for almost all beam dynamics processes
Automate & standardise beam preparation in injectors for LHC fills; Reduce impact on fixed target users and LHC turn-around time.
Automate parameter optimisation & compensate drifts
Automatic testing for “all” equipment to speed up hardware commissioning
Automation of equipment setup, fault analysis, and recovery; preparing the grounds for preventive maintenance

## Slide 18: Efficient Particle Accelerators project
Automatic testing for “all” equipment to speed up hardware commissioning
Automation of equipment setup, fault analysis, and recovery; preparing the grounds for preventive maintenance
Automate & standardise beam preparation in injectors for LHC fills; Reduce impact on fixed target users and LHC turn-around time.
Automate parameter optimisation & compensate drifts
Overview
Remove fixed supercycles by dynamically & algorithmically scheduling beams
Deterministic magnetic field control Will have positive impact on reproducibility for almost all beam dynamics processes

## Slide 19: EPA: specific WPs
Supercycle (SC): sequence of beam types / cycles played over and over
Programming SC is a constrained scheduling problem and impacts efficiency & OP resources Constraints: some beams cannot be adjacent, respect priorities, etc. Stats: SC change takes 2 - 25 min; 40 - 60 x / 24 h
Goal: schedule beams live and automatically based on user requests
  First version of scheduling algorithm ready to “fill-in the gaps”
  Operational test before end of Run 2024
Fully dynamic scheduling requires compensation of magnetic hysteresis and eddy-current effects
Dynamic beam scheduling
SPS
PS
PSB
Notes: multi-destination machines

## Slide 20: EPA: specific WPs
Hysteresis & eddy-current compensation
Feed-forward correction to provide reproducible magnetic fields
  Saving cost, energy, time ”MD1 de-Gauss” cycle, 3.6 s, 5 kWh, ~106 year -1
  Reproducible conditions (orbit, tunes, etc.)
  Flexibility: dynamic beam scheduling
PoC for main dipoles at SPS since 2023
To be extended to other multipoles and injectors (LEIR, PSB, PS)
MD1 cycles

## Slide 21: EPA: specific WPs
Model
  “B-Train” Online B-field measurement for SPS
    Parasitic to OP: abundant, but lacking variability
    Dedicated: explore different supercycle variations
  Lab
    More flexibility in data collection
    “Sensor fusion”: combining Hall probes & flux meter
  Challenges
    Securing adequate data variability
    Measurement accuracy, baseline drift, and noise
Integration
Hysteresis & eddy-current compensation
Data source
Supercycle changes

## Slide 22: EPA: specific WPs
Model
Integration
Data source
  Predict future based on past and future
  Two types of time-series models under study
    Physics-inspired models (e.g. PhyLSTM)
    Temporal Fusion Transformer Powerful, but data hungry and compute-intensive training
    Auto-regressive mode using past also under exploration important for multipoles where no online measurement available
  Challenges
    Achieving sub-Gauss accuracy: crucial at low beam energies
    Generalisability: capturing transitions between unseen cycles
    Data quality (e.g. noise)
Hysteresis & eddy-current compensation

## Slide 23: EPA: specific WPs
Model deployment, integration with controls infrastructure, and tests with beam
MD results
  Promising real-time corrections for eddy-current compensation (“orbit flattening”) and hysteresis at high energy (SX beam)
  Low-energy hysteresis corrections limited by data / prediction accuracy
Hysteresis & eddy-current compensation
Model
Integration
Data source
  2.5 s to calculate & apply correction (effectively: 800 ms for acquisition, prediction, postprocessing)
Eddy-current compensation
Prediction at high energy (SX beam)

## Slide 24: Efficient Particle Accelerators project
Automatic testing for “all” equipment to speed up hardware commissioning
Automation of equipment setup, fault analysis, and recovery; preparing the grounds for preventive maintenance
Deterministic magnetic field control Will have positive impact on reproducibility for almost all beam dynamics processes
Overview
Remove fixed supercycles by dynamically & algorithmically scheduling beams
Automate & standardise beam preparation in injectors for LHC fills; Reduce impact on fixed target users and LHC turn-around time.
Automate parameter optimisation & compensate drifts

## Slide 25: EPA: specific WPs
Goal: standardise LHC beam preparation and automate filling procedure
  Produce beams according to clearly defined specs
  Reduce turn-around: LHC fills vs fixed-target physics
  First test before end of Run 2024
  Full implementation during LS3 (2026 – 2029)
Key components
  Orchestration of tasks and execution of sequences across complex
  Continuous monitoring and quality assessment e.g. now in place for triple & double splittings
  Automatic parameter optimisation (if needed)
UCAP and sequencer play major role
Automated LHC beam preparation
PS double splitting Intensity vs phase

## Slide 26: EPA: specific WPs
Continuous trajectory corrections
  Auto-steering framework
    Goal: continuous transfer line trajectory corrections multiplexed, between machines & to experimental targets
  Classical methods and numerical optimisers combined objective with e.g. beam loss, position, etc.
  Based on UCAP and interfacing geoff4ucap
PS n-TOF
P2SPS
Various steering controllers in place
  SPS NA target intensity sharing and symmetries
  PS EAST & AD target steering
  Testing phase: PS n-TOF, PS2SPS
  Next: SPS2LHC, PS injection
PS EAST
SPS NA

## Slide 27: EPA: specific WPs
following TOF & EAST
following two MTEs
4th order resonant excitation and extraction over 5 consecutive turns
Lessons learnt: MTE beam optimisation
PS multi-turn extraction optimisation
  Goal: uniform intensity across beamlets
  3 parameters: TFBharmonic, TFBgain, QH
Issues
  Slow drifts: relatively easy to handle e.g. using Extremum Seeking (ES) or adaptive Bayesian optimisation
  Abrupt changes: supercycle switch a.o. hysteresis: generally big impact on reproducibility
Some challenges and transferable lessons
  Develop understanding of problem dynamics (MDs, simulations) reduce from 3D to 2D problem, build knowledge into model if possible
  Test prototypes in MDs, but move to operational conditions early on some issues only appear over longer time-scales…
  External factors and time dependencies can make it difficult to incorporate historical data
  Hyperparameter tuning particularly: exploration / exploitation during operations
  Sanity checks for controller inputs & provide monitoring

## Slide 28: Efficient Particle Accelerators project
Automate & standardise beam preparation in injectors for LHC fills; Reduce impact on fixed target users and LHC turn-around time.
Automate parameter optimisation & compensate drifts
Deterministic magnetic field control Will have positive impact on reproducibility for almost all beam dynamics processes
Overview
Remove fixed supercycles by dynamically & algorithmically scheduling beams
Automatic testing for “all” equipment to speed up hardware commissioning
Automation of equipment setup, fault analysis, and recovery; preparing the grounds for preventive maintenance

## Slide 29: EPA: specific WPs
Equipment automation
Smart equipment with context-awareness: beam parameters, machine state, etc.
  Automate setup, fault analysis, and recovery
  Pave the way towards preventive maintenance
Plans 2024 – 2026
  Pilot implementations of parts of a new equipment automation framework
  Examples
    Controlled SPS kicker vacuum interlock auto-resets
    Convolutional auto-encoder for SPS beam dump anomaly detection
    Kicker temperature forecasting
Main implementation: during LS3 (2026 – 2029)

## Slide 30: EPA: specific WPs
Equipment: anomalies and auto-resets
Auto-reset of SPS kicker following vacuum interlock
  Goal: correctly classify vacuum “spikes” to avoid unnecessary downtime
  Method: VAE trained on historical time-series data
  Auto-reset and automatic e-mail with diagnostics plots to experts
VAE for anomaly detection from vaccum pressure data
Detect anomalous SPS beam dump patterns
Convolutional AE: use reconstruction loss to identify anomalies (5 – 20 x higher)
Fault diagnostics: localisation of error
Potential early detection of kicker issues
anomalous
normal
“unseen” MKDH failures

## Slide 31: Contents
    Introduction
    Efficient Particle Accelerators
      Infrastructure
      Specific WPs
    Final remarks

## Slide 32: Final remarks
Automation of accelerator operation has come in stages over the past decades
Next push thanks to technological advances
Efficient Particle Accelerators project in place to
  transform how we run the existing accelerator complex
  gain experience how to design and run future machines
Infrastructure plays a crucial role (Python, UCAP, optimisation frameworks, MLP, …)
Exciting undertaking and rewarding investment
Thank you

## Slide 33: References
A. Huschauer, V. Kain, K. Papastergiou, F. Velotti, ETT report, 2023.
CERN Joint Accelerator Performance Workshop, Montreux, Switzerland, 2023.
CERN LHC Performance Workshop, Chamonix, France, 2024.
D. Anderson et al., “The AccTesting Framework: an extensible framework for accelerator commissioning and systematic testing”, ICALEPCS’13, California, 2013.
L. Cseppento, M. Buttner, “UCAP: A FRAMEWORK FOR ACCELERATOR CONTROLS DATA PROCESSING @ CERN”, ICALEPCS’21, China, 2021.
A. G. Wilson and R. P. Adams, “Gaussian Process Kernels for Pattern Discovery and Extrapolation”, PMLR 28(3):1067-1075, Georgia, 2013.
K. Iliakis et al., Longitudinal Beam Diagnostics and Phase Space Reconstruction in the LHC Using ML, 6th Inter-Experiment Machine Learning Workshop, CERN, Geneva, Switzerland, 2024.
HL-LHC commissioning long-term plan, Mar 2024.
A. Lu et al., First operational experience with data-driven hystersis compensation for the main dipole magnets of the CERN SPS, IPAC’24, Nashville, TN.

## Slide 34
Backup

## Slide 35: EPA: specific WPs
Mainly: triple and double splittings
  Continuous longitudinal beam monitoring
  … and evaluation of splitting qualities now in place
Launch parameter optimisation according to beam quality requirements
  Triple splitting
    3 parameter problem
    CNN + RL agents
  Double splittings
    Linear relation between intensity and cavity phase
    Solved with a PI controller
  Challenges: different dynamics along bunch train (beam loading) and for consecutive cycles
LHC beam preparation in the PS
Triple splitting RL agents
Double splitting Intensity vs phase
Continuous monitoring

## Slide 36: EPA: specific WPs
Equipment anomalies and resets
Kicker magnet temperature forecasting
  Kicker temperatures limit SPS high-intensity operation (beam-induced heating)
  Goal: create temperature forecast using online measurement, current machine operation and future planning
  Method: Light Gradient Boosting Machine and using beam-induced heating equation

## Slide 37: Examples using RL
Correct RF phase & voltage for uniform bunch splitting (LHC beams)
Multi-agent (SAC) & CNN for initial guess
Successful sim2real transfer
If things go wrong: degraded beam
PS
Achieve optimal injection into LEIR
RL state based on β-VAE-encoded Schottky spectra
Agent trained on data-driven dynamics model
If things go wrong: beam loss, activation, equipment trips
LINAC3 / LEIR
V. Kain, N. Madysa, B. Rodriguez
Adjust fine delays of SPS injection kicker
RL agent (PPO) trained on data-driven dynamics model
If things go wrong: beam loss, activation
PS to SPS
M. Remta, F. Velotti
A. Lasheen, J. Wulff
Steer electron beam in AWAKE line
Test-bed for different RL algorithms & sim2real transfer
Large improvements in sample efficiency (Meta RL)
If things go wrong: not critical
AWAKE
S. Hirlaender, V. Kain

## Slide 38: Other optimisation examples
Slow-extracted beam has 50 Hz & 100 Hz noise originating from quadrupole power converter ripple discussed at IPP, 17.11.23
Continuous controller & empty bucket channeling (EBC) find more details here
  Adaptive Bayesian optimisation (ABO) spatio-temporal Gaussian Process model
  Running on UCAP since start of physics ‘24 essential: UCAP node with GPU & Python
  Still ironing out a few issues bugs that only became apparent longer-term, EBC adjustments, strong cycle-by-cycle variations
  Interesting case to study algorithm improvements proximal biasing to reduce exploration spikes
SPS: spill noise compensation

## Slide 39
39
Goal: tune sextupole & octupole currents to minimise impact of resonances
Generic SkoptBayesian not flexible enough and performance bottleneck given # samples and no GPU
Use custom optimisers newly supported by GeOFF Bayesian optimisation implemented with BoTorch
  Pre-conditioned model based on historical data
  Use prior knowledge to improve sample efficiency
Next
  Additional machine studies
  Year-to-year transfer?
F. Asvesta, T. Prebibaj, G. Tangari
PSB: resonance compensation
Other optimisation examples