## Slide 1: beam line optimization for laser-accelerated ions

## Slide 2: AgenDa
1 The LIGHT experiment setup
2 Target normal sheath acceleration
3 Optimization model
4 SIS18 Injection
5 Conclusion and future development

## Slide 3: The light experiment setup
Injection point
Notes: Blue dot is the Z6 target chamber where laser accelerated ions are “produced” using the PHELIX laser
Aim is to feed laser accelerated ions into the SIS18 via the transfer channel (TC)
Reaching the TC the beam will still pass some transport/shaping elements like cavities or quadrupoles so there is some freedom in the choice (within some acceptance limits of the TC) of particle ensembles -> provided we can increase the transmission for example

## Slide 4: The light experiment setup (z6)
M. Metternich, Shaping of laser-accelerated ion beams for applications in high energy density physics (2023)
currently a high-fidelity Runge-Kutta fieldmap tracker is used
beam line setup is done manually or by using parameter sweeps
so far, no optimization scheme has been implemented for this experiment
other attempts use simplified, specialized and idealized models and limited parameters (e.g. quadrupole currents but fixed distances, drift distances but fixed permanent magnet field)
robustness and accuracy of the optimization point is rarely addressed
Notes: Solenoid acts as magnetic lens (similar to optic lenses) where the focus is controlled by the current (proportionally related to B-field)
Cavity uses a standing (TM) wave to accelerate (or decelerate) specific particles

## Slide 5: Beamline elements Cavity energy compression
https://www.gsi.de/work/forschung/appamml/plasmaphysikphelix/experimente/light

## Slide 6: AgenDa
1 The LIGHT experiment setup
2 Target normal sheath acceleration
3 Optimization model
4 SIS18 Injection
5 Conclusion and future development

## Slide 7: Target normal Sheath Acceleration
M. Roth, M. Schollmeier, CAS, 105170, (2016)
Notes: Laser pre-pulse generating plasma on target front (laser) side
  Laser intensity have since then (image) increased. ELI-NP 10^23-10^24 regime, PHELIX 2*10^21 W/cm^2
Electrons are accelerated by the laser main pulse into the target under divergence angle
Electrons leave rear side of the target where they create an electron “sheath” leading to a charge separation and electric field (TV/m regime)
This electric field accelerates the ions from the plasma surface
A lot of research going into laser parameters (pulse-shaping:pre ramps, polarization…) as well as targets to modify the characteristics of TNSA

## Slide 8: particle distribution
Kinetic energy in MeV

## Slide 9: AgenDa
1 The LIGHT experiment setup
2 Target normal sheath acceleration
3 Optimization model
4 SIS18 Injection
5 Conclusion and future development

## Slide 10: optimization model
TNSA particle
distribution
Parameter set:
dsol,1, i1, …
Envelope along
beamline
kinetic energy
deviation
Notes: This leads to a model with a (for the first step) fixed bunch input which can then be optimized wrt. its output using the parameters

## Slide 11: optimization model
TNSA particle
distribution
Parameter set:
dsol,1, i1, …
Envelope along
beamline
kinetic energy
deviation
, …
(loss)
Notes: We now define the output as a loss function
each output characteristic is weighted and they are all added together
gradients, linking the parameters to the loss function are computed automatically using autograd
optimizer then uses gradients to find a (local) minimum for the loss function in the parameter hyperspace

## Slide 12: optimization model
TNSA particle
distribution
Parameter set:
dsol,1, i1, …
Envelope along
beamline
kinetic energy
deviation
, …
Beamline model must be
back-propagatable!
(loss)
Notes: BUT the model has to be back-propagatable
this rules out pic simulations, and most models using field maps (to some degree) or inplace operations

## Slide 13: particle tracking using maps
First order map (TPS, truncated power series) for a hard-edge model of a solenoid
Transport map:
R
Notes: Mapping is done by ”mapping” an incoming particle to its respective output behind the element
In this case second order maps were used for the solenoid
All operations are vector/tensor operations (using einsum in pytorch this is only one line of code!) making this very fast and most importantly back-propagatable
One full simulation run (2 solenoid and 1 cavity) takes about 400 ms (depending on matrix fragmentation)

## Slide 14: Solenoid model
T =
R =
M
sparse, rank 3 tensor
F. Christoph Iselin, MAD Physical Methods Manual
https://mad8.web.cern.ch/doc/phys_guide.pdf
Notes: Mapping is done by ”mapping” an incoming particle to its respective output behind the element
In this case second order maps were used for the solenoid
All operations are vector/tensor operations (using einsum in pytorch this is only one line of code!) making this very fast and most importantly back-propagatable
One full simulation run (2 solenoid and 1 cavity) takes about 400 ms (depending on matrix fragmentation)

## Slide 15: Cavity model
similar to the solenoid model the cavity model is also divided into n segments
every segment provides a voltage “kick” of u/n where u is the cavity voltage
u
t

## Slide 16: Gradient based optimization
TNSA particle
distribution
Parameter set:
dsol,1, i1, …
Envelope along
beamline
kinetic energy
deviation
, …
(loss)
Notes: BUT the model has to be back-propagatable
this rules out pic simulations, and most models using field maps (to some degree) or inplace operations

## Slide 17: optimization problem
Define as optimization problem:
With the parameter vector:
Subject to:

## Slide 18
Particle distribution:
- 7 – 9 MeV protons
- 140 mrad initial divergence
Loss function:
Optimization using only solenoids
Transverse values and are calculated between element or drift segments
Optimizer quickly finds a minimum for the envelope by shifting the solenoid positions and adjusting the currents
Notes: 419 particles make it through

## Slide 19: kinetic energy distribution
Include cavity and include energy deviation to loss function
If left unchecked energy distribution remains wide which makes the transport down the line difficult or the injection into SIS18 unfeasable.
Solution:

## Slide 20: kinetic energy distribution
Notes: better/less energy deviation but slightly worse transmission – only 398

## Slide 21: Comparison to high fidelity model
Using a 9… 11 MeV particle ensemble of 1000 protons
140 mrad initial divergence
Parameters are solenoid currents, cavity voltage and phase, and distance between first solenoid and cavity, cavity and second solenoid
Distance between first solenoid and target is fixed at the technical minimum of about 4 cm
Notes: Every optimization showed that the solenoid should be as close as possible to the target which is 4 cm

## Slide 22: Comparison to high fidelity model
Using a 9… 11 MeV particle ensemble of 1000 protons
140 mrad initial divergence
Parameters are solenoid currents, cavity voltage and phase, and distance between first solenoid and cavity, cavity and second solenoid
Distance between first solenoid and target is fixed at the technical minimum of about 4 cm
 | i1 [kA] | i2 [kA] | d1 [m] | d2 [m] | ucav [MV] | Φcav [rad]
Parameters | 9.3 | 4 | 0.7 | 1.1 | 0.5 | 1.5

## Slide 23: Comparison to high fidelity model
predicted optimum
Possible errors due to:
solenoid model – 3rd order, spherical aberrations
geometric errors – exact solenoidal coil positions
the loss function also minimizes the energy spread
60 – 65 % transmission
65 – 70 % transmission
Notes: 3D transmission (contour) map generated with RK Tracker using parameter sweep
errors hint towards an error caused by deviations from the exact geometry of the components:
- solenoid fieldmaps are 500 mm long for a 300 mm solenoid
- exact position of the coil withing the solenoid can only be guessed, so was assumed to be centered within the housing
- optimizer minimizes for energy spread as well, not only transmission/beam size (this might be the most important point) meaning that this might be due to a trade-off between transmission and energy spread

## Slide 24: Comparison to high fidelity model
Using a 4… 6 MeV particle ensemble of 1000 protons
140 mrad initial divergence
Parameters are solenoid currents, cavity voltage and phase, and distance between first solenoid and cavity, cavity and second solenoid
Distance between first solenoid and target is fixed at the technical minimum of about 4 cm
 | i1 [kA] | i2 [kA] | d1 [m] | d2 [m] | ucav [MV] | Φcav [rad]
Parameters | 6.5 | 2.6 | 0.2* | 1.5 | 0.4 | 1.5
Notes: contrasted to the faster 9… 11 MeV bunch these particles travel slower and have a bigger longitudinal spread than when reaching the cavity. model tries to compensate by moving the cavity as close as possible to the source which is limited by the first solenoid
0.2 was chosen here because the fieldmap in the RK tracker is 500 mm long as opposed to the mapping method with 300 mm
All gradients x 1e5

## Slide 25: Comparison to high fidelity model
predicted optimum
45 – 50 % transmission
40 – 45 % transmission
overall model has a small current offset for the solenoid
can still predict optimal operating points with up to 5 – 10 % accuracy with regards to transmission
Notes: same procedure as before, parameter sweep now only over parameters of the second solenoid since these were shown to be most sensible towards transmission
current seems to have a constant offset, hinting at a systematic error

## Slide 26: AgenDa
1 The LIGHT experiment setup
2 Target normal sheath acceleration
3 Optimization model
4 SIS18 Injection
5 Conclusion and future development

## Slide 27: Back to TNSA – short recap
Kinetic energy in MeV
Notes: This is not a trivial question since the TNSA spectrum follows an exponential function meaning that low energy protons are vastly overrepresented
However they also show a much higher divergence angle making their focus more challenging
also the cavity is not designed for this energy, frequency and overall experiment geometry are rather optimized for 5-10 MeV protons: slow protons will “debunch” more longitudinally and will have a higher longitudinal spread, not optimal for the cavity frequency
-> there is a tradeoff between a higher particle density in lower energy regions and system compatibility

## Slide 28: SIS18 injection
1. Use optimizer to find optimal parameters to shape a beam for SIS18 injection
  Expand the loss function by desired characteristics
  optimize using reference beam (9 – 14 MeV)
2. Run high fidelity field tracker to check the transmission of viable particles
envelope
momentum
gradient at zmax
emittances
x’
x

## Slide 29: SIS18 injection
input bunch
output bunch @ zmax
simulation using 107 input particles over 1– 28 MeV and the beam line element parameters from the optimizer
SIS18 acceptance: energy spread cutoff: , h. emittance: , v. emittance:
energy spread cutoff

## Slide 30: SIS18 injection
input bunch
output bunch @ zmax
scaled up to a full TNSA spectrum this leads to a bunch in the mid range of 108 (after cutoff) that could be injected into SIS18
compared with simulations done by LIGHT group: 3.2 x 108 particles
goal is to increase this to 109 – 1010 particle range
energy spread cutoff
Notes: This can be improved by:
improving the element models to predict more accurate parameters for loss minima
compare to alternative elements such as quadrupole duplet or plasma lens
add elements such as a cavity (tradeoff between acceleration and phase rotation for wide energy spectra)
  first cavity to accelerate and perform minor phase rotation, second cavity only for energy compression (phase rotation)

## Slide 31: conclusion and outlook
inclusion of other elements such as quadrupole duplets or plasma lenses
benchmark and improve model w.r.t. accuracy and robustness (using PHELIX measurements for various TNSA distributions)
  shot to shot robustness for one specific optimized system
expand/couple loss function for additional beam features such as energy selection, emittance, target divergence…
map improvement by adding higher order maps, map training
Notes: If a valid model laser parameters to TNSA distribution is developed it could be incorporated into this optimization scheme (if it is back-propagatable like for example a neural network) allowing to also optimize laser parameters together with the actual beam line parameters

## Slide 32: ACKNOWLEDGEMENTS
Supervisor: Oliver Boine-Frankenheim
Co-Supervisor: Catalin Ticoș
This work is supported by the Deutsche Forschungsgemeinschaft (DFG, German Research Foundation) – Project-ID 499256822 – GRK 2891 'Nuclear Photonics'.

## Slide 33: Result after loss function expansion
Notes: Left side shows the model optimizing the beam envelope (as seen before)
But now the kinetic energy spread is also optimized as seen on the right side
So the optimization works but how valid are the optimization results

## Slide 34: Solenoid Acceptance
target
solenoid
ds + L/2
rs
beam

## Slide 35: Energy Filtering
solenoid
aperture
rs
ra
La
Ls
ld
Notes: Specific numbers from LIGHT experiment: Ls = 300 mm, rs = 20 mm, La = 550 mm, ra = 17.5 mm, ld = 1700 mm
This leads to fmin = 1.3 m and fmax = 15.1 m.
Using simulations energy band of 10… 11.9 MeV was determined since relation between kinetic energy and focal length cannot be (accurately) be calculated. Factor alpha is dependent on magnetic field and geometry.

## Slide 36
Notes: - transmission is more or less predetermined by the geometry and initial distribution
- solenoid can only select the specific energy interval

## Slide 37: Full spectrum analysis – Transmission map
S1
S2
C1

## Slide 38: Transmission and Emittance
Overall, this leads to a transmission (from target to aperture exit)
What about the emittance?

## Slide 39: Energy Filtering
aperture
solenoid

## Slide 40: Transmission and Emittance
Overall, this leads to a transmission (from target to aperture exit)
What about the emittance?
TK/SIS18 acceptance:
Notes: Transmission depending on considered distribution and specific energy interval. For the calculation above different intervals between 8 and 12 MeV were considered

## Slide 41: On Using Transport Map Segments
Consider a first order map for a hard-edge model of a solenoid

## Slide 42: On Using Transport Map Segments
Consider a first order map for a hard-edge model of a solenoid

## Slide 43: On Using Transport Map Segments
Matrix can be decomposed into two fringe segments (F) surrounding a homogenous section

## Slide 44: On Using Transport Map Segments
Now split the whole transport map M into to two segments, each with

## Slide 45: On Using Transport Map Segments
Now split the whole transport map R into to two segments, each with

## Slide 46: On Using Transport Map Segments
Matrices and multiply to unity, and the two matrices multiply to so in essence nothing changes.

## Slide 47: On Using Transport Map Segments
We only gain insight into intermediary phase space vector which has a debatable significance/accuracy. BUT…

## Slide 48: On Using Transport Map Segments
What if we increase the number of segments and then use the actual profile of the magnetic field
…
…
…

## Slide 49: On Using Transport Map Segments
…
…
…
Neighboring fringe field matrices now combine to small input fringe field matrices ,
where which means that for high segmentation we are essentially replacing the initial with a numerical derivative
Notes: Mapping essentially turns into parallel tracking where the only (good) approximation is the radial field. Same approximation is also used in the astra solenoid for example
Potential space charge calculation in between steps?

## Slide 50: On Using Transport Map Segments
Including the tensor for the second order adds chromatic effects for a solenoid map:
AND using pytorch all calculations are included on the computational graph which provides all
partial derivatives, from the input parameters (in this case solenoid currents and drift lengths) to
whatever output is required for the loss function (beam size, emittance…)
Additionally, the transport maps are already available for most basic elements and can also be expanded
to the desired order