## Slide 1: Simulation of quench protection systems of next‑generation superconducting magnets
M. Wozniak, J. Dular, E. Schnaubelt, E. Ravaioli and A. Verweij
CERN, Switzerland
3rd October 2024

## Slide 2: Motivation: quench of superconducting magnets
Quench: loss of superconductivity leads to thermal runaway
  Violent process: high voltage, temperature and thermal stress
  Usually accompanied by dissipation in the coolant of stored magnetic energy ( rapid boil-off)
R. Navarro, “Hundred years of Superconducting Materials”, Second International Conference of Energy Engineering (2010)
M. Bajko, et al., “Report of the task force on the incident of 19th September 2008 at the LHC” . Technical report, CERN (2009). https://cds.cern.ch/record/1168025
  Stored energy in each main dipole circuit of the LHC
  ~ 1 GJ = 250 kg of TNT

## Slide 3: Quench simulation Key Facts and Requirements
Multi-physics, -rate and –scale problem
  Interaction: circuit, power convert., leads, magnets, protection…
  Today: coupling of thermodynamics (heat diffusion equation) and magnetics (magneto[quasi]statics)
Highly nonlinear with sharp (~ discont.) transitions
Local phenomenon  true 3D simulations or clever reduced order models required
Inherently transient effect
Accelerator magnet projects often run over decades
  How to ensure reproducible and traceable simulations?
L. Bortot et al., "STEAM: A Hierarchical Cosimulation Framework for Superconducting Accelerator Magnet Circuits," in IEEE Trans. Appl. Supercond. (2018).

## Slide 4: Table of Contents
Finite Element Quench Simulator (FiQuS)
Integration of FiQuS into STEAM framework
  Parametric analysis
  Co-simulation with other tools of the STEAM framework
Reduced order models
(Outlook on) high-performance computing
Summary

## Slide 5: Table of Contents
Finite Element Quench Simulator (FiQuS)
Integration of FiQuS into STEAM framework
  Parametric analysis
  Co-simulation with other tools of the STEAM framework
Reduced order models
(Outlook on) high-performance computing
Summary

## Slide 6
2D Example for quadrupole MQXA
3D Example of a CCT magnet
3D Example of a NI HTS coil
3D Example of a SC filaments
2D Reduced Magnetic Vector Potential Formulation
2D AC loss map of LTS strand
3D Racetrack coils (HTS and LTS)
Finite Element Quench Simulator

## Slide 7: FiQuS as a tool
FiQuS is developed at CERN in TE-MPE-PE
FiQuS is part of software framework for STEAM
FiQuS is coded in Python and uses its libraries
FiQuS is based on Gmsh and GetDP
onelab.info

## Slide 8: FiQuS code structure
A. Vitrano et al., "An Open-Source Finite Element Quench Simulation Tool for Superconducting Magnets,“ IEEE Trans. Appl. (2023)

## Slide 9: FiQuS input file and run types
FiQuS uses a yaml based input file
  Tree structure of lists, lists of lists, dictionaries etc.
There are some common parts (general, run) and geometry specific sections (CCT, multipole, ...)
This file can also be generated from a dedicated model library via STEAM SDK (see later)
Follows typical FE steps: geometry, mesh, solve
And a run type entry: “run”  “type” that can be:
‘geometry_only’
‘mesh_only’
‘solve_only’
‘pp_only’
‘solve_with_pp‘
‘mesh_and_solve_with_pp’
‘start_from_yaml’

## Slide 10: FiQuS folder structure
‘geometry_only’
‘mesh_only’
‘solve_only’
‘pp_only’
‘solve_with_pp‘
‘mesh_and_solve_with_pp’
‘start_from_yaml’
Geometry_1
Mesh_1
Solution_1
Solution_2
Mesh_2
Solution_1
After completing each of 3 basic steps (geometry, mesh, solve), FiQuS saves its ‘state’ to files so a number of subsequent steps can be started from that point
From Geometry_1 a few meshes can be created (useful for mesh sensitivity) and for each mesh many solutions performed (e.g., with changed excitation).

## Slide 11: FiQuS geometry and mesh generation via Gmsh API
Examples from S. Atalay et al., "An open-source 3D FE quench simulation tool for no-insulation HTS pancake coils," Supercond. Sci. Technol. (2018)
API
API

## Slide 12: FiQuS programmatic generation of .pro
    .regions file
    (yaml based)
.pro template
  .pro for GetDP
FiQuS uses templating engine (Jinja2 for Python) and .pro template and .regions file to generate .pro files for GetDP
FiQuS
code
    .yaml input file
geometry generation logic
pass through materials and BC
info
tags numbering logic
FiQuS
code
Jinja2 engine
Variables in <<…>> get replaced with data from .regions file

## Slide 13: Table of Contents
Finite Element Quench Simulator (FiQuS)
Integration of FiQuS into STEAM framework
  Parametric analysis
  Co-simulation with other tools of the STEAM framework
Reduced order models
(Outlook on) high-performance computing
Summary

## Slide 14
Conductor
Magnet
Circuit
Co-operative simulation
Consecutive analysis
Parametric analysis
Dakota
Materials properties
COSIM
STEAM SDK
STEAM SDK
Component library
STEAM SDK
Conductor
Input files
Magnet
Circuit
Analysis
Parametric
Meas. config
Co-sim.
Meas. data
STEAM SDK
PyBBQ
LEDET
LEDET
ProteCCT
SIGMA
FiQuS
PSPICE
BBQ
XYCE
CHALLENGES
Commercial software is not easily available to all users and expensive
Comparison to
measurements
STEAM SDK
FiQuS does not stand alone – the STEAM framework
Conductor
Magnet
Circuit
Co-operative simulation
Consecutive analysis
Parametric analysis
Comparison to
measurements
Dakota***
STEAM SDK
Materials properties
COSIM
STEAM SDK
STEAM SDK
Component library
STEAM SDK
Conductor
Input files
Magnet
Circuit
Analysis
Parametric
Meas. config
Co-sim.
Meas. data
Some functionality is under active development
STEAM SDK
PyBBQ
LEDET
LEDET
ProteCCT
SIGMA*
FiQuS
PSPICE**
BBQ*
XYCE***
Software in green boxes is free to use
*COMSOL license needed. **Commercial circuit solver from Cadence Design Systems. ***Free tools from Sandia Labs.
FiQuS
NICQS

## Slide 15: Parametric Analysis via STEAM SDK
STEAM SDK allows (traceable!) looping over different input file entries
  For all tools, not just FiQuS
Example: different lengths in turn numbers of local critical current defect of a no-insulation coil
simulation_number | ... | Options_FiQuS.Pancake3D.solve.localDefects.jCritical.defectLength
1 | ... | 10.1
2 | ... | 10.2
3 | ... | 10.3
4 | ... | 10.4
5 | ... | 10.5
6 | ... | 10.6
7 | ... | 10.7
8 | ... | 10.8
9 | ... | 10.9
10 | ... | 11
STEAM SDK
Example from S. Atalay et al., "An open-source 3D FE quench simulation tool for no-insulation HTS pancake coils," Supercond. Sci. Technol. (2018)

## Slide 16: STEAM SDK coupling to DAKOTA
→ Coupling to Dakota benefits from text-based input files for models, virtually any input can be changed
M. Wozniak et al., "Quench Protection of the HL-LHC Hollow Electron Lens Superconducting Solenoid Magnets," IEEE Trans. Appl. (2022)
UQ
Multivariate Closed-Loop Optimization
UQ
M. Gorenflo, "Closed-Loop Optimization of a Lumped Model of the Main Dipole Circuit’s Energy Extraction Resistor," Master’s Thesis Philipps-University Marburg (2024)

## Slide 17
ROXIE files
Magnet input file (model data)
ROXIE
files parser
Conductor,
Geometry,
Circuit,
Mesh,
Solution,
Options,
data
STEAM SDK
SIGMA model
FiQuS
Gmsh API
+ GetDP
Comsol
compiler
Comsol model
SIGMA
FiQuS input file
.data
.iron
.mod
.cadata
.bhdata
.map2d
LEDET input file
LEDET
Java script
LEDET
COMSOL
Integration of STEAM tools, example for multipole magnet
FiQuS*
ROXIE

## Slide 18: Cooperative simulation (co-simulation)
part 1 of
complex
simulation
part 2 of
complex
simulation
Why?
Cooperative simulation are used when the needs of complex simulation exceed the capabilities of one software tool.
Software tool 1
Software tool 2
Data exchange
Cooperative simulation
How?
Co-simulations are performed with at least two tools and data exchange between them. Typically, iterations are needed to converge on a final solution.
Which tools can be used?
Data exchange, consistency and iterations are performed by:
STEAM SDK – Python Based Tool: cern.ch/steam
FiQuS – Finite Elements Tool: cern.ch/FiQuS
LEDET – Finite Difference Tool: cern.ch/LEDET

## Slide 19
ESC transient: PSPICE + LEDET
CCT magnet: FiQuS + LEDET
COSIM: Flexibility to deal with special geometries or scenarios
Magnet design courtesy
of Fusillo design team at CERN

## Slide 20: Table of Contents
Finite Element Quench Simulator (FiQuS)
Integration of FiQuS into STEAM framework
  Parametric analysis
  Co-simulation with other tools of the STEAM framework
Reduced order models
(Outlook on) high-performance computing
Summary

## Slide 21: Reduced Order Modelling of Superconducting Magnets
Magnets are multi-scale structures.
Magnetization and AC loss depends on currents at the small scales, which must be resolved accurately.
Examples:
Interfilament coupling currents in strands.
Interstrand coupling currents in cables.
Detailed magnet models are however too computationally expensive.
Solution: Reduced Order Modelling, with homogenization.

## Slide 22: Reduced Order Modelling of Superconducting Magnets
Phase 1 – Detailed model:
  Multifilamentary superconducting strand and cable models in transient conditions.
  Coupled Axial and Transverse currents (CATI) method:
    2D finite element model: fast and accurate.
    Relies on periodicity, not symmetry, and hence applies to deformed geometries.
    Implemented in , user-friendly interface with small input file.
Next steps:
Rutherford cable model with homogenized parameters from strand resolution (see Phase 2 next slide).
Extract impedance from transport current excitations, and its coupling with external field.
3D Rutherford cable
2D CATI solution
    3D composite strand
    2D CATI method solutions
[1] J. Dular et al., “Coupled Axial and Transverse Currents Method for Finite Element Modelling of Periodic Superconductors”, SUST (2024).

## Slide 23: Reduced Order Modelling of Superconducting Magnets
Phase 2 – Homogenized model:
  Reduced Order Hysteretic Magnetization (ROHM) model:
    Describes AC loss and magnetization of a strand or cable subject to external field.
    Inspired by the ferromagnetic hysteresis models [1], [2] and extended (for eddy and coupling currents).
Next steps:
Automate the parameter identification procedure.
Coupling with transport current excitations, and definition of homogenized impedance.
[1] Bergqvist, 1997. [2] Henrotte, 2006.
Rate-independent case
Rate-dependent case
[3] J. Dular et al., “Reduced Order Hysteretic Magnetization Model for Composite Superconductors”, https://arxiv.org/abs/2409.13653

## Slide 24: Table of Contents
Finite Element Quench Simulator (FiQuS)
Integration of FiQuS into STEAM framework
  Parametric analysis
  Co-simulation with other tools of the STEAM framework
Reduced order models
(Outlook on) high-performance computing
Summary

## Slide 25: HPC for speeding up FiQuS and STEAM
in time
(PinT)
Despite efficient modelling, quench simulation stays very computationally demanding
Further reduction of computational time to practical times is needed  HPC!
We consider(ed) domain decomposition....
in space on algebraic level allowing for black-box usage
Portable, Extensible Toolkit for Scientific Computation
HPDDM: high-performance unified framework for domain decomposition methods
https://parallel-in-time.org

## Slide 26: Some HPC-related results
PinT: adapted Parareal for transients in NI coils yields only speed-up of around 2 times [1]
  More intricate methods promise to perform better but require more fundamental numerical research [2]
[1] E. Schnaubelt et al., “Parallel-in-Time Integration of Transient Phenomena in No-Insulation Superconducting Coils Using Parareal”, SCEE’24 proceedings, accepted
[2] T. Baumann et al., “Adaptive time step selection for Spectral Deferred Correction”, Springer Numerical Algorithms, submitted
FE solver GetDP comes with (limited) MPI parallelization  speed-up around 8 times
  Limited parallel system assembly, parallel solution using MPI-parallel PETSc
  Scalability not ideal  next step: employ domain decomposition methods via PETSc/HPDDM
  Non-linear material fitting functions are expensive to assemble  (precompute) look-up table and interpolate?
Requirement: algorithms must be useable by non-experts in a (quasi-)black-box fashion!
Chart: FiQuS-Pancake3D: MPI GetDP
| 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256
new mat | 1 | 1.0794 | 2.0012 | 3.0808 | 4.0275 | 5.3051 | 7.675 | 7.8326 | 6.2244

## Slide 27: Table of Contents
Finite Element Quench Simulator (FiQuS)
Integration of FiQuS into STEAM framework
  Parametric analysis
  Co-simulation with other tools of the STEAM framework
Reduced order models
(Outlook on) high-performance computing
Summary

## Slide 28: Summary
Transient simulation tools are developed in the STEAM framework
Python is used as a ‘glue’ language in the tools and between them
Simple text files (YAML) are used as input files (with other files, CAD)
Text files simplify parametric simulation setup
Co-simulation is used with file-based data exchange
FiQuS code structure allows for modularity and repeatability
FiQuS is based on components capable of HPC, which is future work
Many developed features need validation with measurements

## Slide 29
Thank you for your attention

## Slide 30: CERNGetDP: Software Toolchain
Vanilla GetDP
⋮
cern.ch/cerngetdp
getdp.info
Basic Linear Algebra Subprograms
(vector addition, dot product, ...)
Dependencies
Message Passing Interface
(standard for parallel computing)
Portable, Extensible Toolkit for Scientific Computation
(linear system solver)
Usage of sophisticated open-source (FE) tools requires non-trivial computing environment.
  All fully automated on CERN IT-provided runners and FiQuS-managed VMs via CERN Openstack.
  This way, we can run FiQuS easily on any computing infrastructure we have to (including HPC/HTC).
STEAM Material Lib.
CERNGetDP
FiQuS C++ Functions
Linux binaries
Windows executables
Docker containers (fully functional & portable computing environment)
Singularity containers (easy & efficient deployment on HPC/HTC)