## Slide 1
J. Christmann, L. A. M. D’Angelo, and H. De Gersem
Institute for Accelerator Science and Electromagnetic Fields, TU Darmstadt
Efficient nonlinear Simulations Of Fast Corrector Magnets
PETRA IV Conceptual Design Report
Notes: .

## Slide 2
Introduction
Contents
1
2
3
4
5
Homogenization Technique
Linear Corrector Magnet Simulations
Nonlinear Simulations
Conclusion/Outlook

## Slide 3: Introduction
Circular accelerators need dipole magnets to correct orbit distortions
PETRA IV: ultra-low emittance synchrotron radiation source
Fast orbit feedback system, corrector magnets with frequencies in kHz range
Strong eddy currents  power losses, time delay, and field distortion
Simulation challenging due to small skin depths and laminated yoke
 Need for technique to simplify simulations
Introduction

## Slide 4
Introduction
Contents
1
2
3
4
5
Homogenization Technique
Linear Corrector Magnet Simulations
Nonlinear Simulations
Conclusion/Outlook

## Slide 5: Homogenization Technique
Magnetoquasistatic PDE:
Replace reluctivity and conductivity in the laminated yoke with spatially constant tensors
THeory
Skin depth
Stacking factor
P. Dular et al., 2003
L. Krählenbühl et al., 2004
H. De Gersem et al., 2012

## Slide 6: Homogenization Technique
Model specifics:
      Iron yoke: length = 40 mm, lamination thickness = 1.83 mm
      Copper beam pipe: thickness = 0.5 mm, length = 140 mm
      Coils: current = 10 A (peak), # turns = 250
      Frequency domain simulation via
Verification

## Slide 7: Homogenization technique
VErification
Multipole coeff. | Average rel. error
Dipole | 
Quadrupole | 
Sextupole | 
Multipole coeff. | Average rel. error
Dipole | 
Quadrupole | 
Sextupole | 
Eddy current losses well approximated
Aperture field well approximated
Simulation time is reduced from several hours to just a few minutes!
 After comparing to other techniques, we decided to use this technique to simulate the corrector magnets
Multipole Coefficients
Eddy current losses

## Slide 8
Introduction
Contents
1
2
3
4
5
Homogenization Technique
Linear Corrector Magnet Simulations
Nonlinear Simulations
Conclusion/Outlook

## Slide 9: Linear Corrector magnet Simulations
Eddy Current losses & Multipole Coefficients
At lower frequencies: , as expected from theory*
Lamination thickness only important at frequencies
Dipole field is attenuated due to eddy currents
Beam pipe  stronger attenuation at higher frequencies
* R. L. Stoll, The Analysis of Eddy Currents. 1974.
J. Lammeraner and M. Štafl, Eddy Currents. 1966.

## Slide 10: Linear Corrector magnet Simulations
Integrated Transfer function & Field Lag
Integrated transfer function and field lag (phase difference between current and aperture field) are of high interest for design of feedback control
We compute both from our simulations for different yoke materials, different lamination thicknesses, etc.

## Slide 11
Introduction
Contents
1
2
3
4
5
Homogenization Technique
Linear Corrector Magnet Simulations
Nonlinear Simulations
Conclusion/Outlook
Notes: Ok and now we want to move on to nonlinear simulations.

## Slide 12: Nonlinear Simulations
To incorporate non-linear -curves into simulations: combine homogenization technique and harmonic balance FEM (HBFEM)
HBFEM is a technique to approximate periodic solutions of nonlinear transient PDEs in frequency domain
Example: excitation current with 1st and 3rd harmonic, include field quantities up to 3rd harmonic
without DC Bias - Theory
S. Yamada and K. Bessho (1988)
H. De Gersem, H. Vande Sande, K. Hameyer (2001)
+ Homogenization

## Slide 13: Nonlinear SimulationS
without DC Bias - Theory

## Slide 14: Nonlinear Simulations
Without DC Bias - Verification
Simple inductor with laminated core, excitation current:
Compare results of HBFEM + homogenization (GetDP + Python) to transient CST simulation with individually resolved laminations
 Good agreement in magnetic flux density
 Larger differences in magnetic field strength
 Suspicion: differences in magnetic field strength are due to not having included enough harmonics

## Slide 15: Nonlinear Simulations
Without DC Bias - Verification
Include 5th harmonic in the analysis
 Still good agreement in magnetic flux density, large differences in magnetic field strength vanish
 Decent agreement in magnetic energy

## Slide 16: Nonlinear Simulations
Current signal of corrector magnet: DC current + oscillations  modify HBFEM method to include DC bias
    Again, we combine HBFEM with a homogenization technique
With DC BIas - Theory
differential reluctivity
magnetizing field strength
Homogenization
J. Gyselinck et al., 1999
chord reluctivity

## Slide 17: Nonlinear Simulations
With DC Bias - verification
Excitation current:
Comparison to transient CST simulation of toy model:
        Very good agreement in magnetic energy in the core
        Decent agreement in magnetic flux densities at individual points inside the core (average rel. error

## Slide 18: Nonlinear Simulations
Same magnet as before, lam. thickness
Excitation current for both coils:
Agreement in aperture field and magnetic energy in the yoke
Eddy current losses well approximated: with Hom. HBFEM vs. 1.32 W with CST  relative error
Higher order finite elements* to achieve good approximation of losses and energy
Application To C-Dipole
*J.P. Webb and B. Forghani, “Hierarchal Scalar and Vector Tetrahedra“, 1993

## Slide 19: Nonlinear Simulations
Application to C-Dipole
Compute eddy current losses up to  Scaling behavior as expected from theory*
 Good agreement with CST results up to
Reason for differences between Hom. HBFEM and CST: At higher frequencies, CST results are mesh-dependent, Hom. HBFEM results are stable
Hom. HBFEM reduces simulation time for nonlinear simulations in kilohertz range from days to hours
* R. L. Stoll, The Analysis of Eddy Currents. 1974.
J. Lammeraner and M. Štafl, Eddy Currents. 1966.
Hom. HBFEM Eddy Current Losses at | 
 | P (kW)
 | P (kW)

## Slide 20
Introduction
Contents
1
2
3
4
5
Homogenization Technique
Linear Corrector Magnet Simulations
Nonlinear Simulations
Conclusion/Outlook

## Slide 21: Conclusion/Outlook
Conclusion/Outlook
Verification of Homogenization
Good approximation of multipoles & power losses
Simulation time for linear simulations reduced from hours to minutes
  2. Application of Homogenization to Corrector
  Power losses, multipoles along axis
  Integrated transfer function & field lag
  Cross-talk with neighboring magnets
  Beam pipe material transition
3. Implementation & Verification of Hom. HBFEM
Toy model with and without DC bias
C-Dipole without DC bias up to 65 kHz
Simulation time for nonlinear simulations reduced from days to hours
  Application of Hom. HBFEM to Corrector

## Slide 22: references
[1] PETRA IV Conceptual Design Report.
[2] K. Wille, Physik der Teilchenbeschleuniger und Synchrotronstrahlungsquellen. Stuttgart, Germany: Teubner, 1992.
[3] P. Dular et al., “A 3-D Magnetic Vector Potential Formulation Taking Eddy Currents in Lamination Stacks Into Account,” IEEE Trans. Magn., vol. 39, no. 3, pp. 1424-1427, May 2003.
[4] L. Krähenbühl et al., “Homogenization of Lamination Stacks in Linear Magnetodynamics,” IEEE Trans. Magn., vol. 40, no. 2, pp. 912 - 915 Mar. 2004.
[5] H. De Gersem, S. Vanaverbeke, and G. Samaey, “Three-Dimensional-Two-Dimensional Coupled Model for Eddy Currents in Laminated Iron Cores,” IEEE. Trans. Magn., vol. 48, no. 2, pp.815 – 818, Feb. 2012.
[6] B. Podobedov et al., “Eddy Current Shielding by Electrically Thick Vacuum Chambers,” Proceedings of PAC09, Vancouver, BC, Canada, 2009.
[7] S. Yamada and K. Bessho, “Harmonic Field Calculation by the Combination of Finite Element Analysis and Harmonic Balance Method,” in IEEE Trans. Mag., vol.24, no. 6, pp. 2588-2590, Nov. 1988.
[8] H. De Gersem, H. Vande Sande, and K. Hameyer, “Strong Coupled Multi-Harmonic Finite Element Simulation Package”, COMPEL, vol. 20, no.2, pp. 335-546, June 2001.
[9] J. Gyselinck, L. Vandevelde, and J. Melebeek, “Calculation of Eddy Currents and Associated Losses in Electrical Steel Laminations,” in IEEE Trans. Mag., vol. 35, n. 3, May 1999
[10] J. P. Webb and B. Forghani, "Hierarchal scalar and vector tetrahedra," IEEE Trans. Magn., vol. 29, no. 2, pp. 1495-1498, Mar. 1993, doi: 10.1109/20.250686.
[11] R. L. Stoll, The Analysis of Eddy Currents. Oxford, U. K., Clarendon Press, 1974.
[12] J. Lammeraner and M. Štafl, Eddy Currents. Iliffe books, 1966.
References