## Slide 1: JuTrack, a Julia Package for Auto- Differentiation Application in Accelerator Modeling and Tracking
Jinyu Wan, Helena Alamprese, Joshua Keeney, Christian Ratcliff, Yue Hao, Michigan State University
Ji Qiang, Lawrence Berkeley National Laboratory

## Slide 2: Outline
Revisit of Auto Differentiation
JuTrack package
Benchmark and Preliminary Applications
  Optimization
  NL Dynamics
  Self-Fields

## Slide 3: Derivatives
Derivative is a linear operator that transforms f to f’.
Basic relations:
Fast evaluation of function ‘s derivative has wide applications
Linearity:
Product Rule:
Chain Rule:
Trend prediction
Function optimization
Function approximation
Parameter Sensitivity
Jacobian for Nonlinear BD
Newton ‘s method
Gradient Descent based
Hermite Interpolation
Rational Approximations?

## Slide 4: Methods for Obtaining Derivatives
Symbolic differentiation
  Complex combination of expressions
  Examples: Mathematica, Sympy (Python)
  Maybe impractical for a complex system.
Numerical Differentiation
  Approximation, depend on stepsize
  Round-off errors and truncation errors can
  be significant in ill-conditioned problems

## Slide 5: Auto-Differentiation
Method | Feature
Symbolic differentiation (SD) | Exact expression and most informative; excessive expression
Numerical differentiation (ND) | Work with black-box functions; Numerical error, step size dependence
Auto Differentiation (AD) | SD in algorithm/compiler, precise derivatives; Separate algorithm needed.
Auto-differentiation (AD) decompose calculations into elementary steps and use chain rule for the function compositions.
Consider
with
Reverse Differentiation
Forward Differentiation

## Slide 6: Forward AD
Accelerator community is familiar with the Forward AD(FAD) since the Differential algebra or Truncated Power Series has been introduced.
The process can be illustrated as dual number for first derivative of 1-D functions, with const as and variable as
More efficient when output dimension is much larger than that of input.
Can be extended to multi-variable and high orders.

## Slide 7: FAD example
Intermediate Vars. | Expressions | Values | Derivatives with respect to
 | , | 1.5 | 1.0
 | , | 0.5 | 0.0
 |  | 3.0 | 2.0
 |  | 0.1411 | -1.98
 |  | 1.6487 | 0.0
 |  | 1.3513 | 2.0
 |  | 1.4924 | 0.02
 |  | 2.0167 | 3.0118
Intermediate Vars. | Expressions | Values | 
 |  | 1.5 | 1.0
 |  | 0.5 | 0.0
 |  | 3.0 | 2.0
 |  | 0.1411 | -1.98
 |  | 1.6487 | 0.0
 |  | 1.3513 | 2.0
 |  | 1.4924 | 0.02
 |  | 2.0167 | 3.0118

## Slide 8: Reverse AD
Reverse AD (RAD) calculate the derivatives from the outer functions, which is the same order with calculation by hand, a reversed direction of function evaluation.
Main workhorse of ML using NN (Backpropagation)
More efficient when input dimension is much larger.
Reverse Differentiation
Value evaluation
Adjoints from
Wengert list [1964]

## Slide 9: RAD example
Intermediate Vars. | Expressions | Values | Adjoints
 |  | 1.5 | 3.0118
 |  | 0.5 | -13.7239
 |  | 3.0 | 1.5059
 |  | 0.1411 | 1.3513
 |  | 1.6487 | -2.8437
 |  | 1.3513 | 2.8437
 |  | 1.4924 | 1.3513
 |  | 2.0167 | 1.0
Intermediate Vars. | Expressions | Values | Adjoints
 |  | 1.5 | 3.0118
 |  | 0.5 | -13.7239
 |  | 3.0 | 1.5059
 |  | 0.1411 | 1.3513
 |  | 1.6487 | -2.8437
 |  | 1.3513 | 2.8437
 |  | 1.4924 | 1.3513
 |  | 2.0167 | 1.0
Adjoints from
Wengert list [1964]

## Slide 10: AD in Accelerators
TPSA implemented in many widely used code such as MADX-PTC and BMAD. It is a forward-AD with dimensions and orders.
  Each variable is represented by Vector
  Almost impossible to include large number tuning parameters
The new implementation GTPSA (@Laurent), allows different maximum order for different variables. Recently, a Julia interface (@ Matt) was developed.
Other general AD tools
  C++: Stan, Enzyme and CppAD …
  Python: PyTorch, mygrad+numpy, TensorFlow …
  Julia: Zygote.jl, Enzyme.jl and GTPSA.jl …

## Slide 11: JuTrack
JuTrack, an AD enabled beam dynamics tool. The goal is to make simulation results and Truncated Power Series Algebra (TPSA) coefficients differentiable w.r.t. the design parameters of the accelerator.
Physics code (Lattice, Collective Effects)
6-D symplectic tracking with dynamics coordinate,
and design parameters,
6-D Truncate Power Series,
Coefficients,
TPSA package
Simulation results,
AD
AD makes and possible!

## Slide 12: JuTrack (cont’d)
We have chosen Julia + TPSA + AD (Enzyme) modules to implement.
Julia (released in 2012) is a high-level, high-performance programming language designed for technical computing.
Performance:
Julia’s just-in-time (JIT) compilation using the LLVM framework allows it to approach or match the speed of C for many tasks
Ease of use:
Dynamic type with option of explicitly type declaration, e.g., f(x, y), f(x::Int64, y::Float64) and f(x::Int64, y) are all acceptable.
Multiple Dispatch. Allows functions to behave differently based on the type of arguments. E.g., track(ele::Quad) and track(ele::Bend)
Readable Syntax. Easy to understand
Enzyme is a powerful tool designed to perform AD of programs, specifically targeting the LLVM compiler infrastructure, such as C, C++, Rust, and Julia.
In many AD tools, the process of differentiating code occurs at a high level, before the code is optimized by the compiler.
Enzyme makes it much faster by working at LLVM level.

## Slide 13: JuTrack Status
Beam and lattice module
  create various accelerator elements and build lattice
  create beam with specific type of particles
  calculate optics and coupling (based on Edward Teng’s parameterization)
Truncated power series algebra (TPSA) module
  create TPS of arbitrary order
  do arithmetic of TPS, include + - * / sin exp log sqrt pow sinh
Tracking module
  symplectic integration for elements in particle accelerator.
  calculation of collective effects (still under development)
  parallel computing using multi-threading feature of Julia

## Slide 14: Modeling of Collective Effects
Space Charge and Beam-Beam Effects
  Soft Gaussian Model, Bassetti-Ershkin Formula with customized derivatives.
  Self-consistent approach, Grid-less kick [J. Qiang, PRAB 20, 014203 (2017)] :
Wake field, from the convolution of the Green functions.
The Faddeeva function has its derivative:
where

## Slide 15: JuTrack GUI
Optics Display
Beam Tracking

## Slide 16: Example of AD Particle Tracking
For a FODO cell with two parameters (k1 and k2), the tracking results and its derivatives can be expressed as
function f(k1, k2)
xin = [0.001 0.0001 0.0 0.0 0.0 0.0]
beam = Beam(xin) D1 = DRIFT("D1", 0.5)
Q1 = KQUAD("Q1", 1.0, k1, 0)
D2 = DRIFT("D2", 0.5)
Q2 = KQUAD("Q2", 1.0, k2, 0)
seq = [Q1, D1, Q2, D2]
linepass!(seq, xin)
return beam.r
end
k1 = 1.0
K2 = -1.0
Grad = jacobian(Forward, f, [k1, k2], Val(2))
 | x |  | y |  | z | 
 | -0.0031362 | -0.0020738 | 0.0 | 0.0 | 2.54465e-6 | 0.0
 | 8.37936e-5 | 0.00014908 | 0.0 | 0.0 | -8.04511e-8 | 0.0
 | -0.0031362 | -0.0020738 | 0.0 | 0.0 | 2.54465e-6 | 0.0
 | 8.37936e-5 | 0.00014908 | 0.0 | 0.0 | -8.04511e-8 | 0.0

## Slide 17: Example of TPSA
Instead of a specific initial condition, we track the TPSA wrt origin and use k1 and k2 as the parameter
function f(k1, k2)
x = CTPS(0.0, 1, 6, 2)
px = CTPS(0.0, 2, 6, 2)
y = CTPS(0.0, 3, 6, 2)
py = CTPS(0.0, 4, 6, 2) delta = CTPS(0.0, 5, 6, 2)
z = CTPS(0.0, 6, 6, 2)
xin = [x,px,y,py,z,delta]
D1 = DRIFT("D1", 0.5)
Q1 = KQUAD("Q1", 1.0, k1, 0)
D2 = DRIFT("D2", 0.5)
Q2 = KQUAD("Q2", 1.0, k2, 0)
seq = [Q1, D1, Q2, D2]
track!(seq, xin)
return xin[1].map
end
TPS coefficients for x:
[0.0, 0.8142086540076545, 0.6148743649232753, 0.0, 0.0, 0.0, 0.0, 0.0, 0.0, 0.0, 0.0, 6.77177969053929, 0.0, 0.0, 0.0, 0.0, 3.777328658722505, 0.0, 0.0, 0.0, 0.0, 0.0, 0.0, 0.0, 0.0, 0.0, 0.0, 0.0]
derivatives of the coeffecients w.r.t. k1 and k2:
w.r.t. k1, [-0.0, -0.7066709784430745, -0.27861605201268735, -0.0, -0.0, -0.0, -0.0, -0.0, -0.0, -0.0, -0.0, -2.2561205078968287, -0.0, -0.0, -0.0, -0.0, -0.4931722737026719, -0.0, -0.0, -0.0, -0.0, -0.0, -0.0, -0.0, -0.0, -0.0, -0.0, -0.0],
w.r.t. k2, [0.0, -4.445896312934257, -2.614025589841921, 0.0, 0.0, 0.0, 0.0, 0.0, 0.0, 0.0, 0.0, 7.313226768999287, 0.0, 0.0, 0.0, 0.0, 5.576041849897743, 0.0, 0.0, 0.0, 0.0, 0.0, 0.0, 0.0, 0.0, 0.0, 0.0, 0.0]

## Slide 18: A real-life example
EIC is an ongoing project of US DOE which adds a new electron ring and its injector to the existing RHIC complex.
We reads in the current ESR lattice of MADX.
MADX Tune: 50.0800, 46.1400
JuTrack Tune: 50.0800, 46.1398
The calculated optics agrees well with MADX

## Slide 19: Application in Optimization
In local scheme of crab-crossing, the phase advance between two crab cavities should be .
2.0000
2.0272
Method: optimize 7 quadrupoles located between CC4 and CC1 (Their original strength is 0)
Do a simple gradient descent optimization:

## Slide 20: Simplified phase adv. matching
Optimization goal:
The phase advance is optimized within 3 steps.
More work is needed to use the existing optimizer which support constrains.

## Slide 21: Application in Nonlinear Optimization
The nonlinear DA indicators are used for optimizing DA.
We use SPEAR3 lattice as an example to show gradient based optimization of 3rd order Nonlinear Driving terms using two sextupole families.
Use as a test.
Here we only tested a basic gradient descent algorithm. Reach minimum in 400 iterations. The function may be trapped in a local minimum.

## Slide 22: Application in Self-Fields
Number of slices:
4 4 8 4 4
4-D Gaussian distribution
Specie: proton
Normalized emittance: 1mm
Current: 200 A
Energy: 1 GeV
Evaluate/Benchmark the self-consistent space charge using the grid-less symplectic method. Calculate derivative of final emittance (normalized by the initial emittance) with respect to the design parameters.
Space charge kick occurs in the middle of each slice
AD: derivatives calculated with auto differentiation
FD: derivatives estimated with finite difference approximation.
Results also agree with the Ji Qiang’s earlier work.

## Slide 23: Summary
JuTrack is an on-going project for Auto-Differentiation enabled accelerator design and beam dynamics code.
JuTrack adopts the flexibility and high-performance Julia language and the modules from the community.
The code can be applied in
  Optimization of lattice
  Nonlinear Beam dynamics
  Dynamics of self fields and more …
We plan to test alternative TPSA/AD packages. We are looking forward to any form of collaboration on code developments and broader range of applications.