## Slide 1: Integration of magnetic measurement data in magnetic field simulations by BEM-based discrepancy modeling
Chair: Mariusz Wozniak
Melvin Liebsch (CERN)
Stephan Russenschuck (CERN)
Matthias Bonora (CERN)
Luisa F. Fleig (CERN, TU Darmstadt)
Jens Kaeske (CERN, KIT Karlsruhe)

## Slide 2: Agenda
The lifecycle of the accelerator magnet
Hybrid modeling (Newton to Kepler)
  Calibrated models
  Delta models
Integration in the life cycle management
Conclusion
Learning from data through the lens of models is a way to exploit structure in an otherwise intractable problem [1]
[1] K. Wilcox, Predictive data science for physical systems – from model reduction to scientific machine learning. ICIAM – international congress on industrial and applied mathematics. 2019

## Slide 3: Agenda
The lifecycle of the accelerator magnet
Hybrid modeling (Newton to Kepler)
  Calibrated models
  Delta models
Integration in the life cycle management
Conclusion
Learning from data through the lens of models is a way to exploit structure in an otherwise intractable problem [1]
[1] K. Wilcox, Predictive data science for physical systems – from model reduction to scientific machine learning. ICIAM – international congress on industrial and applied mathematics. 2019

## Slide 4: Accelerator magnet life cycle
Design
Report
Meas.
Report
Test
Report
Simulation
Data
Digital twin
Specs
CAD
Drawings
Document-based  Model-based
Principles of systems modeling
Coupled multi-physics optimization
Integration in virtual environment
Multiscale modeling
Quality assurance
Fault detection and correction procedures
Magnet alignment data
Magnet transfer function
State observation
Prediction
Maintenance
Calibrating material properties
Optimal experimental design
Virtual prototyping
Prototype manufacturing/testing
Series manufacturing
Magnet operation
Document based information exchange
Data management services: EDMS, EAM, NORMA, PLM
Product life cycle
Development life cycle
slow
fast
Communication frequency
Communication frequency depends on the application

## Slide 5: Challenges
Complex (non-linear) dynamic system
  Interplay of iron saturation, hysteresis and eddy currents
  Superconductor magnetization
  Temperature effects
Computational costs
  A complete 3D magnet simulation does not allow for fast predictions
Tough requirements for machine operation
  Field stability at 1 unit in 100 000
  Field quality at 1 unit in 10 000
Measurement data needs to be integrated in the numerical model to enable accurate predictions
Digital representation
a.k.a. numerical system model
data
1st principles
Hybrid models integrate first principle and data driven models in a joint architecture

## Slide 6: The field simulation software ROXIE
Developed for the design of the superconducting magnets for the LHC
The standard tool for the design of cos(θ) magnets
Features the calculation of 3D fields and iron magnetization
Based on the coupling of boundary and finite elements (BEM-FEM), see [4]
Routine for the Optimization of Magnet X-sections, Inverse Field Computation and Coil End Design
ROXIE default output
[4] S. Russenschuck, “ROXIE: Routine for the optimization of magnet X-sections, inverse field computation and coil end design.,” in 1st International ROXIE Users Meeting and Workshop, Geneva, Switzerland, CERN Yellow Reports: Conference Proceedings, 3 1998.

## Slide 7: Agenda
The lifecycle of the accelerator magnet
Hybrid modeling (Newton to Kepler)
  Calibrated models
  Delta models
Integration in the life cycle management
Conclusion
Learning from data through the lens of models is a way to exploit structure in an otherwise intractable problem [1]
[1] K. Wilcox, Predictive data science for physical systems – from model reduction to scientific machine learning. ICIAM – international congress on industrial and applied mathematics. 2019

## Slide 8: Hybrid modeling [5]
https://commons.wikimedia.org/wiki/File:Sir_Isaac_Newton_by_Sir_Godfrey_Kneller,_Bt.jpg
1st principle modeling
Machine learning (ML)
measurements
physics
Delta models
ML models
Model calibration
D
P
D
P
D
P
D
https://de.wikipedia.org/wiki/Johannes_Kepler#/media/Datei:Portrait_Confused_With_Johannes_Kepler_1610.jpg
[5] Rudolph M., Kurz S. and Rakitsch B. Hybrid modeling design patterns, Journal of Mathematics in Industry, 2024, DOI: 10.1186/s13362-024-00141-0
“Newtonian paradigm”
“Keplerian paradigm”

## Slide 9: Model calibration [6]
Digital twin
[6] L. Fleig, M. Liebsch, S. Russenschuck and S. Schöps, "Identification of B(H) Curves Using the Karhunen Loève Expansion," in IEEE Access, vol. 12, pp. 59441-59449, 2024, doi: 10.1109/ACCESS.2024.3393348
Material Specimen
Permeameter
H(B)-curve
Pattern recognition (KLE)
Magnet manufacturing QA
Resulting parameters
Calibration test campaign
Design of experiment (DOE)
optimal sensor placement
Design of a test campaign
D
P

## Slide 10: Delta models
ROXIE boundary integral equation for field evaluation
 | Greens function | 
 | Greens function | 
Data driven update
The discrepancy between measurement and simulation may not vanish after magnet calibration
The discrepancy drives the delta model
The delta model may be used to understand the origin of the discrepancy
The predictions of the updated model are matching our observations
D
P

## Slide 11: Delta models - Data driven model update
D
P
minimize
subject to:
 | Energy functional
 | Energy matrix
 | Observation operator
 | Observation matrix
 | Measurement data
 | Predicted measurements
 | Energy functional
 | Energy matrix
 | Observation operator
 | Observation matrix
 | Measurement data
 | Predicted measurements
Minimum energy solution
minimize
subject to:
Discretized on boundary mesh
Model update is obtained by quadratic programming
We use the python software for convex optimization “cvxopt”
Boundary mesh

## Slide 12: Example integrated field measurement
D
P
Quadrupole magnet on test bench
Rotating coil measurement system

## Slide 13: Example 3D field mapping [7]
Curved dipole magnet on test bench
Model update () by means of a linear Kálmán filter
 | Prior covariance matrix
 | Posterior covariance matrix
 | Observation matrix
 | Measurement covariance matrix
 | Measurement data
 | Prior covariance matrix
 | Posterior covariance matrix
 | Observation matrix
 | Measurement covariance matrix
 | Measurement data
[7] Liebsch, Melvin, Russenschuck, Stephan and Kurz, Stefan. "BEM-Based Magnetic Field Reconstruction by Ensemble Kálmán Filtering" Computational Methods in Applied Mathematics, vol. 23, no. 2, 2023, pp. 405-424. https://doi.org/10.1515/cmam-2022-0121

## Slide 14: Example 3D field mapping [7]
Curved dipole magnet on test bench
Measurement data, boundary mesh and model update
[7] Liebsch, Melvin, Russenschuck, Stephan and Kurz, Stefan. "BEM-Based Magnetic Field Reconstruction by Ensemble Kálmán Filtering" Computational Methods in Applied Mathematics, vol. 23, no. 2, 2023, pp. 405-424. https://doi.org/10.1515/cmam-2022-0121

## Slide 15: Example 3D field mapping [7]
Curved dipole magnet on test bench
Validating the field evaluation
[7] Liebsch, Melvin, Russenschuck, Stephan and Kurz, Stefan. "BEM-Based Magnetic Field Reconstruction by Ensemble Kálmán Filtering" Computational Methods in Applied Mathematics, vol. 23, no. 2, 2023, pp. 405-424. https://doi.org/10.1515/cmam-2022-0121

## Slide 16: Agenda
The lifecycle of the accelerator magnet
Hybrid modeling (Newton to Kepler)
  Calibrated models
  Delta models
Integration in the life cycle management
Conclusion
Learning from data through the lens of models is a way to exploit structure in an otherwise intractable problem [1]
[1] K. Wilcox, Predictive data science for physical systems – from model reduction to scientific machine learning. ICIAM – international congress on industrial and applied mathematics. 2019

## Slide 17: The ROXIE evaluator
The ROXIE evaluator is python package for the advanced post-processing and reverse engineering
We make extensive use of GMSH for mesh operations and shape functions
Performant C++ extensions are used for the BEM matrix assembly
The C++ code leverages on
vectorization (EigenC++)
parallelization (OpenMPI)
It features a Multi Level Fast Multipole Method (MLFMM) for accelerated field evaluation
The poetry packaging manager is used for platform independence and dependency tracking
https://github.com/MelvinLie/roxie_evaluator

## Slide 18: Integration
Gen.
All systems models must be:
Exchangeable
Versioned
Integratable
Application specific software for ROXIE
ROXIE API
ROXIE evaluator
The goal is to integrate our models in pyMBSE [8], a python toolbox for the self-contained multi model execution
Application Specific Software
Design Software
DAQ & Analysis Software
Numerical Models
Measurement Models
Magnets & Devices
Transducers & instrumentation
Model-Based Systems Engineering
System Models
Physical Objects
Gen.
Design Software
Model-Based Systems Engineering
[8] PyMBSE User Documentation, Accessed: Oct. 03, 2024. [Online]. Available: https://chart-magnum.github.io/pymbse-docs/intro.html

## Slide 19: Agenda
The lifecycle of the accelerator magnet
Hybrid modeling (Newton to Kepler)
  Calibrated models
  Delta models
Integration in the life cycle management
Conclusion
Learning from data through the lens of models is a way to exploit structure in an otherwise intractable problem [1]
[1] K. Wilcox, Predictive data science for physical systems – from model reduction to scientific machine learning. ICIAM – international congress on industrial and applied mathematics. 2019

## Slide 20: Conclusion
We use hybrid modeling to integrate magnetic measurement data in numerical field simulations
Model calibration techniques alone are sometimes not sufficient to find a match between measurements and simulations
Delta models are used to compensate for discrepancies
They can provide an indication of the cause of the differences
Our post-processing techniques leverage on boundary integral equations
We follow the principles of model-based systems engineering to integrate the numerical models and simulation data in the development and product lifecycle

## Slide 21: Magnet operation
  Requires rapid information exchange
Machine learning models*
D
*Example provided by A. Lu (PhD, BE-CSS-DSB)
Example: Hysteresis compensation for SPS dipole magnets
Neural network-based Time series modeling B(I)
Currently developed with SPS training data
=
+
=
+
Model order reduction (MOR) [5]
High fidelity model
Reduced order model (ROM)
: State vector, : Input vector, : ROM state
[5] Sorti, S., Petrone, C., Russenschuck, S., Braghin, F.: Data-driven simulation of transient ﬁelds in air-coil magnets for accelerators, Nuclear Instruments and Methods in Physics Research Section A, 2021
Digital twin
State observation
Prediction
Maintenance
Magnet operation

## Slide 22: Delta models – Example
Quadrupole magnet on test bench
Rotating coil measurement system
ROXIE boundary integral equation for field evaluation
 | Greens function | 
 | Greens function | 
Data driven update

## Slide 23: Delta models – BEM-based field reconstruction
The representation formula
 | Dirichlet data | „boundary potential“
 | Neumann data | „normal flux“
 | Greens function | 
 | Dirichlet data | „boundary potential“
 | Neumann data | „normal flux“
 | Greens function | 
Magnetostatics in
Magnetic scalar potential | 
Magnetic scalar potential | 
 Dirichlet and Neumann data are linearly dependent!
 Problem must be formulated in or !

## Slide 24: Delta models
D
P
The discrepancy between measurement and simulation may not vanish after magnet calibration
The discrepancy drives the delta model
The delta model may be used to understand the origin of the discrepancy
The predictions of the updated model are matching our observations

## Slide 25: What is in ROXIE?
Main ingredients:
Reduced vector potential formulation
→ Simplifies conductor modeling and mesh generation (line currents)
BEM-FEM coupling
  → No mesh for air/vacuum domain
→ Smoothing property towards approximation errors
Second order method
→ High accuracy FEM approximation
Main drawback:
Non-local BEM interactions
→ Loss of sparsity. Low rank approximations are needed for eﬀicient
computations (e.g. ACA, FMM).

## Slide 26: Example integrated field measurement
D
P
Quadrupole magnet on test bench
Rotating coil measurement system

## Slide 27: The digital twin [2]
Physical object
a.k.a. accelerator magnet
[2] Piascik, R., et al., Technology Area 12: Materials, Structures, Mechanical Systems, and Manufacturing Road Map. 2010, NASA Office of Chief Technologist.
Digital representation
a.k.a. numerical system model
Communication channel
Data
Measurements
and inputs
Information
Prediction
State observation
Geometry
model
Thermal
model
Electromagnetic
model
Mechanical
model
The digital twin requires multi-physical modeling
[3]
[3] M. Maciejewski, B. Auchmann, D. M. Araujo, G. Vallone, J. Leuthold and J. Smajic, "Model-Based System Engineering Framework for Superconducting Accelerator Magnet Design," in IEEE Transactions on Applied Superconductivity, vol. 33, no. 5, pp. 1-5, Aug. 2023, Art no. 4003105, doi: 10.1109/TASC.2023.3249647