## Slide 1: Simulation study of nanostructured copper photocathodes
Margarita Bulgacheva¹, Erion Gjonaj¹, Dmitry Bazyl²
¹ TEMF, Technische Universität Darmstadt, Darmstadt, Germany
² Deutsches Elektronen-Synchrotron, Hamburg, Germany
This work is funded by the German Ministry of Research (BMBF) under contract 005K2022

## Slide 2: Introduction
D. Bazyl, et al. “CW Operation of the European XFEL: SC-Gun Injector Optimization, S2E Calculations and SASE Performance.” (2021)
D. Bazyl, “Nanostructured photocathode RnD for CW photoinjector at DESY”, Deutsches Elektronen-Synchrotron (DESY), unpublished.
A Continuous Wave (CW) electron source is necessary for the future operation of the CW and High-Duty-Cycle EuXFEL.
DESY is currently developing a 1.6-cell superconducting radio-frequency (SRF) gun cavity, designed to operate at 1.3 GHz.
This gun can only be used with metal photocathodes due to construction (no load lock system).
It is necessary to design a copper photocathode with increased Quantum Efficiency (QE).

## Slide 3: Short theory of plasmonics
Periodic structure
Laser pulse
+
laser
Array of nanoholes

## Slide 4: Short theory of plasmonics
Periodic structure
Laser pulse
Surface Plasmon Polariton (SPP) modes
+
laser
Array of nanoholes
Single nanohole
E-field

## Slide 5: Short theory of plasmonics
Periodic structure
Laser pulse
Increased local absorption
+
Surface Plasmon Polariton (SPP) modes
laser
Array of nanoholes
Single nanohole
E-field
Single nanohole

## Slide 6: Short theory of plasmonics
Periodic structure
Laser pulse
Increased local absorption
Increased quantum efficiency (QE)
+
Surface Plasmon Polariton (SPP) modes

## Slide 7: Dispersion modeling
Reflectance R(ω) depends on the complex, frequency dependent permittivity of the cathode material.
New dispersion model for accurate simulation of the reflectance spectra:
44 data points [Johnson & Christy] 1000 data points
Fast relaxed vector fitting
(passive – no energy growth)
Notes: ?

## Slide 8: Simulation methods and accuracy estimation
3 different simulation models:
• FEM solver, Floquet (periodic) boundaries
• FEM solver, natural (E+H) boundaries
• FIT solver, natural (E+H) boundaries

## Slide 9: Simulation methods and accuracy estimation
3 different simulation models:
• FEM solver, Floquet (periodic) boundaries
• FEM solver, natural (E+H) boundaries
• FIT solver, natural (E+H) boundaries
Results deviation:
• Minimum reflectance < 0.5%
• SPP resonance frequency < 0.02%

## Slide 10: Geometrical optimization results
Shapes considered for optimization:
Parameter | Square | Round | Cone
Periodicity, nm | 751 | 756 | 768
Nanohole width, nm | 260 | 300 | 372
Nanohole depth, nm | 240 | 240 | 210
Reflectance, % | 1 | 0.26 | 0.14
Optimized geometrical parameters

## Slide 11: Local field enhancement
Electric field peaks may impact the transverse emittance of the electron beam.
Conical-type nanoholes yield the most uniform field, while achieving the same reflectance level.

## Slide 12: Effect of geometrical imperfections
Perfect array profile, σ = 0%
Notes: ?

## Slide 13: Effect of geometrical imperfections
Perfect array profile, σ = 0%
Imperfect array profile, σ = 20%
Notes: ?

## Slide 14: Effect of geometrical imperfections
Perfect array profile, σ = 0%
Imperfect array profile, σ = 20%
Notes: ?

## Slide 15: Beam dynamics
How to simulate photoemission from structured cathodes?
Most beam dynamics codes are suitable only for flat cathodes

## Slide 16: Beam dynamics
How to simulate photoemission from structured cathodes?
Most beam dynamics codes are suitable only for flat cathodes
CST simulation allows to use non-flat cathode geometry

## Slide 17: Beam dynamics
How to simulate photoemission from structured cathodes?
Most beam dynamics codes are suitable only for flat cathodes
CST simulation allows to use non-flat cathode geometry
No photoemission in Particle-in-Cell solver

## Slide 18: Beam dynamics
How to simulate photoemission from structured cathodes?
Most beam dynamics codes are suitable only for flat cathodes
CST simulation allows to use non-flat cathode geometry
No photoemission in Particle-in-Cell solver
Optically induced emission model in Tracking solver

## Slide 19: Beam dynamics
How to simulate photoemission from structured cathodes?
Most beam dynamics codes are suitable only for flat cathodes
CST simulation allows to use non-flat cathode geometry
No photoemission in Particle-in-Cell solver
Optically induced emission model in Tracking solver
How to generate time dependent optically emitted bunch distribution?

## Slide 20: Beam dynamics in the cathode vicinity
Optically induced emission model (given QE):
Sample structure (single nano-cone)
Use light source with given wavelength and power

## Slide 21: Beam dynamics in the cathode vicinity
Optically induced emission model (given QE):
Sample structure (single nano-cone)
Use light source with given wavelength and power
  Get sample distribution on the cathode
  Get emission angle distribution at the cathode
  Get emission current for given power

## Slide 22: Beam dynamics in the cathode vicinity
Optically induced emission model (given QE):
Sample structure (single nano-cone)
Use light source with given wavelength and power
  Get sample distribution on the cathode
  Get emission angle distribution at the cathode
  Get emission current for given power
Construct temporal current profile according to the laser pulse
Import particle data into E-static PIC solver as a particle interface

## Slide 23: Beam dynamics flat vs structured
Structured cathode
Single nano-cone simulation, no space charge
Periodic boundary conditions
Flat cathode

## Slide 24: Beam dynamics flat vs structured (short bunch)
Flat cathode
Structured cathode
Single nano-cone simulation, no space charge
Periodic boundary conditions
1000 times shorter bunch (0.18 ps)

## Slide 25: energy spread FOR A SINGLE NANO-CONE
Accelerating gradient is constant (≈50 MV/m)
Energy spread grows with the increase of the nanohole depth
Effect is more prominent with space charge simulation

## Slide 26: results
New dispersion model for accurate simulation based on Johnson & Christy data
Optimized cathodes for different nanohole geometries
Implemented optically induced emission model
Calculated preliminary beam dynamics for a single nano-cone
Estimated the effect of nano-cone depth on beam dynamics