## Slide 1
Gradient descent-based optimization of the acceleration field in sub-relativistic dielectric laser accelerators using the adjoint method
M. Konrad, U. Haeusler, C. Neureuter, R. Shiloh, P. Hommelhoff
Friedrich-Alexander-University Erlangen-Nürnberg (FAU)
manuel.l.konrad@fau.de

## Slide 2: Contents
Working principles of dielectric laser acceleration (DLA)
Experimental Results
Optimization of DLAs
  Step by step optimization
  Inverse design applied to DLAs
  Adjoint method for efficient gradient calculation
Optimization of sub-relativistic DLAs

## Slide 3: Particle accelerator concepts
UNILAC (120m)
SIS18 (216m)
Swiss Light Source, PSI (300 m)
XFEL, DESY (3.4 km)
Image credits: Paul Scherrer Institut
Image credits: Desy Photon Line
Image credits: D. Fehrenz, GSI/FAIR
Koichi Shimoda, Appl. Opt. 1, 33-35 (1962)
Lohmann, A., IBM Tech. Note 5, 169–182 (1962)
Mizuno et al., Nature 328, 45 (1987)
Image credits: S.Kraus, J.Litzel | Laserphysics | FAU Erlangen
For electrons!

## Slide 4: Why dielectric-based laser accelerators?
Fermilab
Dielectric materials and optical frequencies
Higher damage threshold than metallic cavities
Higher gradients and smaller, minituarized structures
Much stricter requirements on beam properties
Lower current
per channel
f=150 THz (λ=2 μm)
τ=6.6 fs
RR ~ kHz-MHz
>3 GV/m fields
Gradient >1 GeV/m
Physical aperture: ~200 nm
Emittance <100 pm rad (norm)
fA-pA
(in single channel, many are possible soon)
f=3 GHz
τ=333 ps
RR ~ Hz-kHz
<200 MV/m
25-50 MeV/m
~1cm
1 μm ~ 1 mm rad
nA-μA and larger
DLA
RF
Multi-channel DLA:
Zhao et al., Photonics Research 8 10,
1586-1598 (2020)
Laser
Laser
S-band
https://indico.cern.ch/event/448486/contributions/1108454/attachments/1189017/1725317/Lecture13CavitiesIII_2015.pdf

## Slide 5: DLA basics
Single sided grating unstable -> use dual sided grating -> stable channel in the center
Breuer, J., and Hommelhoff, P. Phys. Rev. Lett. 111, 134803 (2013).
Gratings hard to align -> dual pillar structure etched -> from silicon

## Slide 6: Operation principle
~620nm
TM-polarized
Depending on particles position:
Acceleration
Deceleration
Deflection
2
1
3
4
Proof of concept:
25 MeV/m: J. Breuer, P. Hommelhoff, PRL 111, 134803 (2013)
: 250MeV/m: Peralta, E. A., Soong, K., England, R. J., Colby, E. R., Wu, Z., Montazeri, B., ... & Byer, R. L. (2013). Nature, 503(7474), 91-94.
First spatial harmonic
1
2
3
4
0
Acceleration
Deceleration
2
3
4
1
Goal: generate a mode that allows momentum transfer from laser field to electrons
Use first order effect (efficient!)
Second order effects too power costly
Synchronicity condition:

## Slide 7
Chen et al., Proposal (1989)
Shiloh, et al., Opt. Express 29, 14403-14411 (2021)
Leedle, et al. CLEO, pp. FM3M-7 (2018)
Leedle, et al. Opt. Lett. 40, 4344-4347 (2018)
Yousefi et al., Opt. Lett. 44, 1520-1523 (2019)
Fishman et al., Nature Comm 14, 3687 (2023)
Black et al., PRAB 23, 114001 (2020)
Bonded silica gratings
Silicon pillar structures
Peralta et al. Nature 503, 91–94 (2013)
Koyama, K., et al. IPAC (2014)
Wei et al., Appl. Optics 56(29) (2017)
Wie et al., Physics of Plasmas 24.7 (2017)
Cesar et al., NIMA 909, 252-256 (2018)
Cesar et al., Optics Expr., 26(22), (2018)
Crisp et al., arXiv:2310.12384 (2023)
Top illumination
2013
2021
2015

## Slide 8
Chen et al., Proposal (1989)
Shiloh, et al., Opt. Express 29, 14403-14411 (2021)
Leedle, et al. CLEO, pp. FM3M-7 (2018)
Leedle, et al. Opt. Lett. 40, 4344-4347 (2018)
Yousefi et al., Opt. Lett. 44, 1520-1523 (2019)
Fishman et al., Nature Comm 14, 3687 (2023)
Black et al., PRAB 23, 114001 (2020)
Bonded silica gratings
Silicon pillar structures
Peralta et al. Nature 503, 91–94 (2013)
Koyama, K., et al. IPAC (2014)
Wei et al., Appl. Optics 56(29) (2017)
Wie et al., Physics of Plasmas 24.7 (2017)
Cesar et al., NIMA 909, 252-256 (2018)
Cesar et al., Optics Expr., 26(22), (2018)
Crisp et al., arXiv:2310.12384 (2023)
Top illumination
2013
2021
2015

## Slide 9
2013
2021
2015
Bonded silica gratings
Silicon pillar structures
Top illumination
Laser
e-
Leedle, et al. CLEO, pp. FM3M-7 (2018)
Leedle, et al. Opt. Lett. 40, 4344-4347 (2018)
Yousefi et al., Opt. Lett. 44, 1520-1523 (2019)
Fishman et al., Nature Comm 14, 3687 (2023)
Black et al., PRAB 23, 114001 (2020)
Peralta et al. Nature 503, 91–94 (2013)
Koyama, K., et al. IPAC (2014)
Wie et al., Physics of Plasmas 24.7 (2017)
Cesar et al., NIMA 909, 252-256 (2018)
Cesar et al., Optics Expr., 26(22), (2018)
Crisp et al., arXiv:2310.12384 (2023)
Laser
Laser
Red (accelerating) and blue (decelerating)
Ez
Laser
Side illumination
z
y
x
For reviews, see for example:
R. J. England et al., Rev. Mod. Phys. 86, 1337 (2014),
R. Shiloh et al., Adv. Opt. Phot. 14, 862 (2022)

## Slide 10: Acceleration structures
500 µm long, made of 733 pillar pairs
Tapered periodicity: from 619 nm to 717 nm due to starting energy of 28.4 keV
Pillar radii: 240nm x 225nm, 225nm wide channel
Macro-cells: from 5 µm to 22.5 µm (total of 26 segments)
Average design gradient: 22.7 MeV/m
Peak electric optical field: 600 MV/m (2.2 µJ pulse energy and 360 mW average power)
Laser pulse front tilting required in experiment
225nm
450nm
480nm
Top view
2 pillar height
139 – 237nm

## Slide 11
1mm

## Slide 12
11
200
300
400
500
Previous generation accelerating structure
EPeak = 600MV/m - 700MV/m
Design gradient: 22.7MeV/m
2µm
1mm
e-
Laser

## Slide 13
Maximum energy gain 12.3 keV
Total energy of 40.7 keV
43% energy gain
200m
300m
400m
T. Chlouba*, R. Shiloh*, S. Kraus*, L. Brückner*, J. Litzel, P. Hommelhoff, Nature, 622, 476 (2023)
500m
Similar results from Stanford/Darmstadt team:
Broaddus, Egenolf, …, Byer, Leedle, Solgaard, Phys. Rev. Lett. 132, 085001 (2024)
Laser on
Laser off
Simulation
4.5 keV
Simulation
Pillar distance
Energy gain (keV)
% of survived particles
Energy
1
0.5
0
6.6 keV
8.8 keV
11.9 keV

## Slide 14: Inverse design in the past and goals of Thesis
Initial Goal:
Implement particle tracking into the optimization routine
Design non-periodic large scale accelerators
Built upon:
Existing code from my Bachelor’s Thesis (Basic inverse design implementation)
Christian Neureuter’s Master’s Thesis (Inverse design of non-periodic structures)
Inverse design of single unit cells:
Hughes et al. Opt. Express 25, 15414-15427 (2017)
Urs Haeusler, Master’s Thesis
Sapra et al. Science 367, 79-83 (2020)
Inverse design of multiple unit cells:
Manuel Konrad, Bachelor‘s Thesis
Inverse design of non-periodic structures:
Christian Neureuter, Master‘s Thesis
Notes: But after rewriting the code (due to the need to clean up and due to needing

## Slide 15: Step by step optimization
Electron travels in one direction -> Optimization pillar by pillar based on previous acceleration of
However: Changes in pillars affect mode over multiple structure periods -> Mode propagates in BOTH directions -> Affects previously optimized cells as well!

## Slide 16: Step by step optimization
Next cell again off
Already optimized
Goal function
Pillar position
Parameters: Distance between pillars
Iterative approach will only result in an approximation of the design
Susceptible to dephasing problems if structure does not follow the design exactly

## Slide 17: Step by step optimization
Iterative approach will only result in an approximation the design
Susceptible to dephasing problems if structure does not follow the design exactly
Need to know response of whole system to parameter change
Optimize all pillars/parameters at the same time -> Gradient descent
-> Inverse design
Instead:

## Slide 18: Inverse design of DLAs
Built upon:
Existing code from my Bachelor’s Thesis (Basic inverse design implementation)
Christian Neureuter’s Master’s Thesis (Inverse design of non-periodic structures)
Inverse design of DLAs in Literature:
Hughes et al. Opt. Express 25, 15414-15427 (2017)
Sapra et al. Science 367, 79-83 (2020)
Inverse design of multi-pillar cells:
Mostly used to create complex patterns
Repetition of single periodic unit cells
Only one unit cell optimized
-> Dephasing in long structures
-> Equivalent to single repeating pillar
-> Not suited for sub-relativistic DLAs
Extended structures
Concatenation of different unit cells
All unit cells optimized in the same step
-> But: still periodic (Repetition of -> block of unit cells)
Extended structures
Concatenation of different unit cells
All unit cells optimized in the same step
-> Can change periodicity along the structure
-> Equivalent to single repeating pillar
Inverse design of non-periodic structures:
Extended structures
Not periodic: Open ends
-> Can change periodicity along -> the structure
-> Suited for sub-relativistic DLAs
Notes: But after rewriting the code (due to the need to clean up and due to needing

## Slide 19: Inverse design of DLAs
Computational design via optimizing a structure for a certain objective function
Objective function: Acceleration gradient inside the structure with
: Injection phase
Wanted: efficient way to calculate the gradient of the objective function for some parameter vector
Parameters: Pillar dimensions in x and y direction
Laser coming from the side
(side illumination)
Field evaluated here

## Slide 20: Adjoint method
Maxwell’s equations in frequency domain:
On a grid:
Gradient of G: with
Define second simulation with source term
-> Only one additional simulation necessary to calculate complete gradient!
Finite difference
Electric field
Source term
Contains structure
Forward simulation
Adjoint simulation

## Slide 21: Inverse design of DLAs
Built upon:
Existing code from my Bachelor’s Thesis (Basic inverse design implementation)
Christian Neureuter’s Master’s Thesis (Inverse design of non-periodic structures)
Inverse design of DLAs in Literature:
Hughes et al. Opt. Express 25, 15414-15427 (2017)
Sapra et al. Science 367, 79-83 (2020)
Inverse design of multi-pillar cells:
Mostly used to create complex patterns
Repetition of single periodic unit cells
Only one unit cell optimized
-> Dephasing in long structures
-> Equivalent to single repeating pillar
-> Not suited for sub-relativistic DLAs
Extended structures
Concatenation of different unit cells
All unit cells optimized in the same step
-> But: still periodic (Repetition of -> block of unit cells)
Extended structures
Concatenation of different unit cells
All unit cells optimized in the same step
-> Can change periodicity along the structure
-> Equivalent to single repeating pillar
Inverse design of non-periodic structures:
Extended structures
Not periodic: Open ends
-> Can change periodicity along -> the structure
-> Suited for sub-relativistic DLAs
Notes: But after rewriting the code (due to the need to clean up and due to needing

## Slide 22: Multi-pillar optimization
Side illuminated, dual pillar structures
Constant channel width of 225 nm
Optimization parameters: and of each pillar pair
Spacing between pillars chosen according to the synchronicity condition:

## Slide 23: Multi-pillar optimization
For multiple pillars: Acceleration should follow design curve
Gradient:
Objective function
of cell n
Design curve value assigned to cell n
Gradient of the objective function of cell n for each parameter in the parameter vector

## Slide 24
Forward simulation
Adjoint simulation
Python process
Lumerical FDTD process
Optimizer: SciPy’s SLSQP
Optimization result

## Slide 25: Difficulty of designing DLAs II
Goal function
Pillar position

## Slide 26: Optimization Results – Periodic structure
27 pillar pairs (54 parameters)
Periodic
Arbitrary design curve -> prove of concept
Optimization successful after ~ 100 Simulations
Deviations below 1%

## Slide 27: Inverse design of DLAs
Built upon:
Existing code from my Bachelor’s Thesis (Basic inverse design implementation)
Christian Neureuter’s Master’s Thesis (Inverse design of non-periodic structures)
Inverse design of DLAs in Literature:
Hughes et al. Opt. Express 25, 15414-15427 (2017)
Sapra et al. Science 367, 79-83 (2020)
Inverse design of multi-pillar cells:
Mostly used to create complex patterns
Repetition of single periodic unit cells
Only one unit cell optimized
-> Dephasing in long structures
-> Equivalent to single repeating pillar
-> Not suited for sub-relativistic DLAs
Extended structures
Concatenation of different unit cells
All unit cells optimized in the same step
-> But: still periodic (Repetition of -> block of unit cells)
Extended structures
Concatenation of different unit cells
All unit cells optimized in the same step
-> Can change periodicity along the structure
-> Equivalent to single repeating pillar
Inverse design of non-periodic structures:
Extended structures
Not periodic: Open ends
-> Can change periodicity along -> the structure
-> Suited for sub-relativistic DLAs
Notes: But after rewriting the code (due to the need to clean up and due to needing

## Slide 28: Optimization Results – Non-periodic structure
300 pillar pairs (600 parameters)
First and last 15 pillars ignored
Non-periodic -> tapered structure (period increases over length of structure)
Sloped design curve -> generally higher acceleration -> gradients possible for higher -> energies
Optimization successful only away from the edges
C. Neureuter‘s Master‘s thesis

## Slide 29: Conclusion and Outlook
Current status:
  Can efficiently optimize multi-pillar macro-cells
  Struggle with edge effects in the non-periodic case
Future work:
  Implement deflecting/focusing forces
  Particle tracking instead of evaluating first harmonic
  Implement alternating phase focusing
  Move to more complex structures -> more parameters

## Slide 30: Thank you for your attention!

## Slide 31: Backup: Calculation of
Apply chain rule:
Calculation of using finite difference methods:
The gradient of the structure matrix becomes
For every parameter, one additional finite difference calculation is necessary -> Calculation effort can be neglected for single pillar case
From Maxwell’s equations
b)
c)
d)
Permittivity distribution not analytical
Vector of individual

## Slide 32: Backup: Adjoint source
Derivative of the multi-pillar objective function
Corresponding source:
Error: Prefactor not applied to source -> flat source profile
Prefactor only applied after the simulation
if y inside cell
if y outside cell
Source term of adjoint simulation