## Slide 1: Radiochemistry Diagnostics at NIF
EMMI-JINA Workshop
Dawn Shaughnessy for the Radiochemistry Diagnostics Group
EMMI, GSI
10/13/2012

## Slide 2: Radiochemistry on NIF can be used both for diagnostics and measuring nuclear data
Tracer atoms are loaded into the capsule ablator or on the hohlraum
~ 1015 atoms
with target foils
Longest range – probes remaining shell.
  124Xe + n  123Xe + 2n
  Eth = 10.6 MeV 1.6 barn (14.5 MeV)
  124Xe + n  125Xe + γ
  low Eth 0.01 barn (1 MeV) 0.002 barn (5 MeV)
Intermediate range – probes inner shell.
  127I + d  127Xe + 2n, 79Br(d,2n)79Kr
  Eth = 4.2 MeV 0.4 barn (10 MeV)
Neutron flux at peak burn creates >106 atoms of reaction products from 1015 target atoms

## Slide 3: A sample NIF capsule with xenon doping for gas collection
For charged particle mix diagnostic reactions there must be a sample recovery tracer
For neutron reactions the detector can be its own tracer
In Be capsules, Xe is introduced via the sputtering gas; in CH capsules Xe is ion implanted
Xe doping via ion implantation has been demonstrated
DT ice
DT
CH ablator
CH
CH
DT
6 m
1x1015 atoms Xe-124
1x1015 atoms I-127

## Slide 4: Both gaseous and solid debris collection have been developed at NIF
Diagnostic Insertion Manipulator (DIM)
nose cone with Solid RadioChemistry (SRC) collectors
50 cm
Equatorial DIM
(90,78)
Sold RadioChemistry (SRC) Detectors (metal foil or graphite) are removed
post-shot & gamma counted
Polar DIM
(0,0)
10 m diameter NIF chamber
Radiochemical Analysis of Gaseous
Samples (RAGS)
Gas load from the chamber is pumped to the RAGS apparatus and collected in a removable bottle for gamma counting

## Slide 5: Radioactive Analysis of Gaseous Samples (RAGS) gaseous collection
T
T
T
NIF
chamber
(600m
3
)
Turbos
Gas
Puff
System
Xenon Cryogenic
Fractionation & Detector
System
Gas Pre-cleaner System
G
e
r
m
a
n
i
u
m
d
e
t
e
c
t
o
r
C
r
y
o
T
r
a
p
He flush
NIF
Target
Chamber
Noble
Cryo Prefilter
Getter
Getter
Getter
Getter
He flush
Removable Trap
Getter
Getter
RGA
Abort Tank
RGA
LaBr
LaBr
LaBr
LaBr
RGA
Noble Gas Mass Spectrometer
Cryo Collector
Tritium Processing System
Ge detector

## Slide 6: Xenon collection and detection cart
From pre-cleaner
Future cryo head with 2 coincident Ge detectors for in situ counting
Sample removal bottle for decay counting and noble gas mass spectrometry
Cu foam cryo head

## Slide 7: First RAGS xenon collection and gamma spectroscopy data
* Used 65% collection efficiency Target Chamber to RAGS Xe sample bottle
Gamma ray spectrum collected 4.5-5.5 hr post-shot on Germanium detector
NIF shot N120228-001-999 (Exploding Pusher)
123gI
t1/2=13.3 h
125gXe
t1/2=16.9 h
123gXe
t1/2=2.1 h
Production Ratios
124,126,128Xe(n,2n)123,125,127Xe
NXe-125 / NXe-123 = 1.22 ± 0.05
NXe-127 / NXe-123 = 1.24 ± 0.17
Normalized to 124:126:128 = 1:1:1
by scaling counting atom ratio with the target isotope fractions and assuming small n, contributions vs n,2n
Estimated atoms @Tzero *
NXe-123 ≈ NXe-125 = 2.1E6
NXe-127 ≈ 2E5
Minimum ~ factor of 2 lower
Maximum – not known

## Slide 8: Solid Radiochemistry (SRC) was developed by analyzing samples from various locations in the chamber
8
Chamber diameter is ~10 meters. Most of our samples were 1 to 5 cm in diameter.
50 cm
Polar Diagnostic Insertion Module (DIM)
Equatorial DIM
Disposable Debris Shield (DDS) + Final Optics Assembly
25-50 cm
8-10 cm
Equatorial DIM
DDS
DDS
DDS
7 m
Al Shields: covered Neutron Activation Diagnostic
Ta Collimators: part of x-ray diagnostic assembly
Glass DDS: covered the final optics assembly
Metal Disks: WRF housing
Glass Debris Catchers: mounted throughout the chamber
Drawing Not to Scale, Side View

## Slide 9
Structural contaminants and Au debris from the hohlraum were identified on all analyzed materials
Unique elemental signature – usually incorporated with Si and Cu
These sub-micron Au features contribute little in terms of mass collection but may be of interest in terms of chemical/geometric fractionation.
40 µm
40 µm
1 μm

## Slide 10: Several materials were fielded as shot ride-alongs to test their feasibility as collectors
Nb, Ta, V, Mo, Ti, Ag and graphite foil (Diameter 5 cm) were fielded using existing wedge range filter mounts that attach to the DIMs
Similar shots with plastic shell Ge-doped capsules, Au hohlraum, laser energy from 940 – 1300 kJ, 50 cm from TCC
Samples were evaluated for morphology changes, Au collection, Ge collection, surface melt, ablation depth, etc.
Sample
50 cm from TCC
DIM Snout
Preshot assembly
Postshot assembly
963 kJ TCC energy
Nb / Ta
V / Mo

## Slide 11: Surface morphology of pre-shot and post-shot disks indicate that the debris wind is not homogenous
10 µm
Pre-shot
Post-shot (0-0, Polar)
Post-shot (90-78, Equator)
The polar sample has a high density of craters and large splats.
The equatorial sample has less craters, which are smaller in diameter, and less large debris splats. There is a high density of very small (< 1µm) features on the disks.
Niobium

## Slide 12: Most of the Au target debris << 1 μm in diameter. Debris condensation needs to be modeled.
Notice the small Au features surrounding the sphere.
4 μm
100 nm
Darker particulates on the sphere are Al/Si

## Slide 13: Post-shot photos of collectors fielded on the new 4-mount bracket show differences in debris distribution
Distance between collector mid-point | 
Pos1, Pos 2 | 6.2 cm
Pos1, Pos 3 | 30 cm
Position 1 shows more gold debris than position 4

## Slide 14: First activated solid debris samples collected from NIF – 11/04/11
Tantalum - unpolished
Tantalum - polished
5 cm diameter
Stainless steel retaining ring
Experiment – determine surface finish effects on collection
Measurement of neutron activated Au from the hohlraum
Sample 196Au (from n,2n on 197Au) 198Au (from n,g on 197Au)
Polished Ta (3.28±0.06)E06 (1.50±0.06)E04
Unpolished Ta (1.72±0.04)E06 (7.00±6.00)E03
198/196Au Ratio (polished Ta): (4.28±1.71)E-03
182/180Ta Ratio (polished Ta): (7.97±0.04)E-02
Ta/Au Ratio: 18.61±7.53
181Ta(n,2n) and 181Ta(n,g)182Ta (collector self-activation)
197Au(n,2n)196Au and 197Au(n,g)198Au
(hohlraum debris)

## Slide 15: The gamma spectra from the first SRC collectors showed activated Ta and Au debris from the hohlraum
Chart: Channel
180Ta (8 hr)
Chart: Channel
196Au (6.2 d)
These spectra show both 181Ta(n,2n) (collector) and 197Au(n,2n) (hohlraum debris) activation
Gamma lines from 181Ta(n,g)182Ta and 197Au(n,g)198Au neutron capture were also present in the data
We regularly observe various neutron reactions on the collector material and from collected debris

## Slide 16: The gold SRC results open the door to hohlraum-mounted s(n,g) / Fn measurements
10-50% of 4π
0.2-1.0 g
(≈1.5-7.5 MAu)
(n,g) cross sections in the keV energy range are unknown and very difficult to model – SRC results show that the hohlraum could be used as a target for studying these reactions
These experiments can ride-along on other NIF shots and could be fielded regularly
Challenges include mounting fouls on the hohlraum; need for higher collection efficiency (collectors currently face the diagnostic windows)

## Slide 17: Summary
Collection of gas and solid debris has been established at NIF as a diagnostic
Radiochemical data from RAGS collection shows the possibility of measuring short-lived gaseous species
Solid debris radiochemistry shows that activation and neutron capture products are produced during a NIF shot
Nuclear reaction data can be measured using RAGS and SRC – increased SRC collection efficiency and capsule fabrication development are needed