## Slide 1: A high time resolution and high dynamic range ASIC for the micro vertex detector in the PANDA experiment
Hui Zhang, Toko Hirono, Ivan Peric
Karlsruhe Institute of Technology, ASIC and Detector Lab

## Slide 2: PANDA Micro Vertex Detector
The PANDA detector is composed of several subdetectors
The Micro Vertex Detector (MVD) is a tracking device for charged particles. It is the innermost sub-detector system of the target spectrometer
Main tasks of the MVD are:
  High vertex resolution for primary and secondary vertices of short-lived particles
  Improvement of momentum resolution
  Additional input for particle identification
High time resolution of 1ns RMS enables efficient track reconstruction and possibly particle identification by time of flight
Energy resolution in wide dynamic range 100ke with 100e noise for dE/dX measurements and particle identification
Pixel size: 80 µm x 80 µm
Chip size: 1 cm x 2 cm

## Slide 3: Chip Architecture
HVCMOS 180 nm technology with MPW run
Chip Size: ~ 5 mm x 5 mm
Pixel Matrix: 29 columns x 62 rows
Pixel Size: 50 µm x 165 µm
Configuration register
Readout Cell
End of Column
Synthesized Digital
Bias Block
Pads
End of Column
Synthesized Digital
+ Bias Block
Pads
Pixel Matrix
Configuration
+Hit Buffer
TDC

## Slide 4: HVCMOS Technology
HVCMOS Sensor, a new generation of particle detectors
Commercial technology, not expensive
The sensor and readout electronics in the same die
Use external negative bias voltage
Pixel is based on a deep n well with electronics inside, isolated against HV
Charge collection by drift
Substrates from 300Ωcm to ~20kΩcm
Good time resolution, detection efficiency and radiation tolerance
Can be thin
Radiation tolerant technology, further increased by special design
  Radiation tolerant PMOS transistors
  Deep submicron
  Guard Ring
  Shielding

## Slide 5: Pixel Electronics
Charge sensitive amplifier with variable gain
Feedback circuit
Two comparators
  Fast comparator: enable accurate time measurement
  Slow comparator: enable precise amplitude measurement
Amplifier
Sensor
Comparator
Th
BL
TDAC
Injection
EnInjection_row_i
RAM
Q(0:2)
4
RAM in
WrRAM(0:3)_row_i
Cinj
Bias resistance
Data transfer line
column control (in CRB)
-HV
1.8V
Hit buffer
Pixel
Offset
Disable=Q(3)
Disable
AnalogOut
row control (in CRB)
AlwaysEnB
Injection
AmpOut

## Slide 6: Pixel Electronics
The first stage is a standard folded cascode amplifier
  Implement variable gain
The second stage are the two source followers
  It provides fast time constant and voltage level shifting
  The bias current of the second source follower is smaller than that of the first
  The second source follower acts as a low pass filter
Each pixel has two comparators and two readout channels

## Slide 7: Readout control unit
h1
&
h2
L
&
h1
meoc
L
&
Ld column
Rd column
LdCol1
LdCol2
PD1
PD2
LdPix1
LdPix2
RdCol1
RdCol2
RdCol3
RdCol4
Rd column
Ld pixel
pd
DataOut
Serializer
Ld column
Rd Pixel
Ld pixel
Scan In
TS
TS2
Scan Out
Scan Out
Scan In
Rd column
m2
m1
EOC
Hit buffer
TDAC
RAM
TDC
TS3
TSCk
+
edge
row control (in pixel control reg)
column control (in pixel control reg)
EnB
From Pixel
RCU
RAM Wr
RAMIn<0:3>
Regulated
cascode
Hit Buffer, End of Column, Readout Control Unit

## Slide 8: Hit buffer
Hit buffer logic
  RAM cell
  4-bit Tune DAC
  Regulated cascode receiver
  Time to digital converter
  Main hit buffer logic
LE
RAM
Addr
ROM
TS1
Data Bus
LE
RAM
TS2
TDAC
RAM
+
EnB
RAM Wr
RAMIn<0:3>
Hit from pixel
LE
RAM
TS3
TDC
Main hit buffer logic

## Slide 9: Hit buffer
Main hit buffer
  Edge detector
  Priority logic
  Address ROM cells
  Time stamp RAM cells
S
R
LE
RAM
Addr
ROM
TS1
Data Bus
Scan Out
Scan In
RdPix
S
R
SR latch
1st hit flag
2nd hit flag
Enable*
LE
RAM
TS2
LdPix & !Hit
Priority Logic
Enable
RdInt
+
EnB
Hit
LE
RAM
TS3

## Slide 10: Time to Digital Converter
Time to digital converter
The hit time is measured by storing two time stamp values
Two time stamp counters run with the same period of 10ns and could be reset synchronously
0
1
2
3
4
5
6
7
Clk
Particle hit
HitSync
0
1
2
3
4
5
6
7
TS coarse
TS fine
time stretching circuit

## Slide 11: Time to Digital Converter
Our circuit
FF
Clk
hit
Ibig
Ismall
hit
hitSync
hit
hitSync
vcap
comp
comp
vcap
1
6
TS
coarse
TS
fine
Amplified
time
Amplified time = (
TDCfine
–
TDCcoarse
) x
Tclk
Clk
TS
coarse
0
1
2
3
4
5
6
7
0
1
2
3
4
5
6
7
TS
fine
Vth

## Slide 12: End of Column
Data for each event has 55 bits
  Coarse time stamp (20 bits TS1)
  Energy measurement (10 bits TS2)
  Fine time stamp (7 bits TS3)
  Row Address (10 bits)
  Column Address (8 bits)
The time stamp frequency: 100MHz
TS1 uses two 10-bit counters, one clocked with positive edge and the other with the negative edge
col
row
row
row
124 Hit buffers
EoC
Column control line 0
Row0
Row1
Row2
col
row
row
row
Hit buffers
EoC
Column control line 28
(…)
Config. reg block
Config. reg block

## Slide 13: Readout control unit
Readout block, data formatting block, time stamp counter, Phase locked loop
Readout block comprises a state machine
Data formatting block performs 8-bit to 10-bit conversion and transmits the data serially
Serializer is based on a binary tree, and transmits a bit on the rising and falling output clock edge
PLL input clock of 250 MHz and output clock of maximal 800 MHz
Maximal data rate: 1.6Gbps
Data formatting block
RCU
Readout block
Time stamp counter
Phase locked loop
State machine
Serializer

## Slide 14: Measurement system
Test system
Signal source for measurements is a test signal circuit – a capacitor placed in every pixel
The test circuit is calibrated with radioactive source

## Slide 15: Measurements
Pulse width measurement
The pulse width of slow signal is larger than the fast signal. The sigma value for slow channel is smaller, leading to significantly larger SNR.
Energy resolution with SNR>1000 possible, the maximum signal limited by the injection circuit
- For 32ke amplifier does not saturate, maximum signal limited by injection circuit
- The average ToT noise is about 48 ns for slow comparator. Its gain can be obtained by fit and it is 0.413 ns/e. If we divide the ToT by gain, we obtain the noise in electrons as 116 e.

## Slide 16: Measurements
Comparator response time and pulse width
The time of threshold crossing is smaller when measured ToT is larger. Exponential function has been fitted to the data and it is used for the time walk correction.
Time resolution <1ns should be possible

## Slide 17: Measurements
Threshold dispersion is <60e, both comparators can be tuned

## Slide 18: Outlook
Planned design improvements include:
  reduce detector capacitance, reduce noise
  optimize layout design
Next prototype (named MiniPANDA), with 80 μm x 80 μm pixel size has been completed.
  Uses two stage amplifier and one comparator
  Second amplifier improves energy resolution by TOT
  Uses deep p-well and isolated amplifier
  Test system ready, results soon
Following testing of the MiniPANDA ASIC, the full-size sensor will be designed.
2.5fF
25pA
10fF
200pA
20fF