## Slide 1: Status of MIMOSIS
MIMOSIS-1, 60µm thick
( )
?
M. Deveaux, GSI detector laboratory

## Slide 2
The Micro Vertex Detector (MVD) of CBM
Main requirements:
  ~5 µm spatial resolution.
  70 MHz/cm² (peak)
  0.5 cm from the beam axis.
  0.3-0.5% X0 In vacuum.
CBM Detector
CMOS MAPS
called MIMOSIS
DRD3 Week, CERN, 17 June 2024

## Slide 3
Size of MIMOSIS-1
Nominal acceptance
Target
-electrons are kicked out by beam from target.
-electrons form 90% of occupancy.
-electrons create highly non-uniform radiation field.
No Trigger signature => Continuous readout
“Slow extraction” of beam on target creates beam fluctuations.
Detector must handle significant rate peaks.
Beam intensity (SIS18-measured)
M. Deveaux, SQM 2017
Utrecht/Netherlands
Operation very close to the beam => Tolerate ions
Significant beam halo => Need to understand integrated radiation damage
Manage Single Event Effects up to highest LET (dE/dx >>104 m.i.p).
HI-physics is low momentum physics – Material budget really matters!
DRD3 Week, CERN, 17 June 2024
Requirements for sensors in fixed target HI-experiments.

## Slide 4
The operation principle of MAPS
Reset
+3.3V
+3.3V
Output
SiO2
SiO2
SiO2
N++
N++
N+
P+
P-
P+
Digital camera: ~1000 photons produce one electron each.
Particle detector: One particle produces ~1000 electrons.

## Slide 5
MAPS vs. Hybrid pixels
CMS @ LHC – Hybrid Pixel
~100 µm
~120 µm
Readout - chip
Hybrid:
0.5mm Si
equivalent
Pixel
Pixel
Pixel
MAPS:
~0.05 µm
Si equivalent
Multiple coulomb scattering:
Particle trajectory is manipulated by detector.
Angle scales with

## Slide 6: MIMOSIS – A sensor for CBM
MIMOSIS-0 (2018)
Demonstrate pixel concept.
Demonstrate zero suppression.
Demonstrate readout concept.
MIMOSIS-1 (2020)
Full dimension sensor
Add buffer structure.
SEE hardening 1/2
MIMOSIS-2.1 (Q2/2024)
On-chip pixel grouping.
Final pixels.
SEE hardening 2/2
All submissions:
Additional CE18 test structures to study specific design questions.
MIMOSIS-1, 60µm thick
MIMOSIS-1
MIMOSIS-3 (~2025)
Final sensor for mass production
In synergy with:
13th POS conference, Oxford, Sept 2023
Work in progress

## Slide 7
Micro Vertex Detector – Sensor requirements
 | PANDA MVD | MIMOSIS
Spatial resolution [µm] | 28 | 5-7
Material budget [X0/layer] | ~1% | 0.05%
Power [mW/cm²] | <800 | <100
Rate [MHz/cm²] | > 6 | 20
Ionizing dose [Mrad/10 years] | 10 | > 5 Mrad
Non-ion dose [neq/cm²/10 years] | ~ 1014 | ~3 x 1014
Operation temperature | Liquid cooled, 35°C | Air cooled? 15°C
Readout | Self-triggered, GBTx | Self-triggered, GBTx
Time binning | <10 ns | 5 µs
dE/dx | Yes | Somewhat*
Better than required
As required
Use strip information instead?

## Slide 8: The state of the art: MIMOSIS-1 (inspired by ALPIDE)
Size: 504 x 1024 pixels (27x30µm²), 5µs time binning
Full integrated: 20 MHz/cm² (80 MHz/cm² for 35µs), ~70mW/cm²
Fully depleted: >20V top bias
MIMOSIS-1, 60µm thick
p-stop
n-gap
standard
Standard
Rad. hard, candidate 1
Rad. hard, candidate 2
First proposed by W. Snoeys et al.
H. Pernegger et al., 2017 JINST 12 P06008
A
B
C
D
>20V HV top bias
Capacitor blocks HV
Back bias possible.
P-Well bias (ALPIDE) possible
Most likely Fully Depleted
MIMOSIS-1: 25 µm epitaxial layer. MIMOSIS-2.1: 25µm + 50µm epitaxial layer => stay tuned.
DRD3 Week, CERN, 17 June 2024

## Slide 9
Sensor performance: New and after 5 MRad + 1014neq/cm²
Best performing pixel: AC P-stop
Efficiency >99% (end of life-time).
Spatial resolution: ~6 µm
Dark rate (not shown, see backup):
  Marginal before irradiation.
  <10-6 after irradiation.
Short dimension
of 27x30µm² pixel.
Conclusion on sensor performance:
All pixels work excellent before irradiation.
Standard pixels show best spatial resolution. (see backup)
P-stop AC pixel most radiation hard, matches requirements of CBM.
13th POS conference, Oxford, Sept 2023
CBM
Plots: Curtesy CBM-MVD collaboration

## Slide 10
Test and integration work at GSI/Uni-Frankfurt
Test of bent ALICE and
65nm TPSCo prototypes:
The GSI ALICE group.
MIMOSIS-2 SEE tests with ~5 AMeV heavy ion beam.
Working bit-flip recovery.
No latch-up <50 MeV cm²/mg.
  (work in progress)
Test of differential rad. damage:
Issues finding common working point at differential rad. damage.
Effect saturates: Pre-condition by irradiating with ~1 MRad.
  (work in progress)
Integration :
Vacuum compatible detector stations with 0.3 - 0.5% X0.
High speed DAQ (CBM)
DRD3 Week, CERN, 17 June 2024

## Slide 11
How to get the data out?
Data-Buffer
01001010010
01001010110
01001011000
On-chip
Off-chip
ALPIDE Sensor.
~ 50 mW/cm²
Human hair (to scale)
~30µm
~30µm
14.5µm
Mimosis Pixel Logic Layout (106 Transistors)
Priority encoder

## Slide 12
MIMOSIS – Internal structure
Double column:
2 x 504 pixel
Common priority encoder
Region (64x):
Concentrated data from 8 double col.
Max. 100 hit pixel/frame
Super Region (16x):
Further data concentration
Elastic buffer:
Input 10.24 Gbps, output 2.4 Gbps.
Stores 80 MHz/cm² peaks for max 35µs.
Output:
1x, 2x, 4x or 8x 320 Mbps DDR SLVS.
GBTx compatible
MIMOSIS-data arrives with defined time stamp but a typical delay of few 10 µs due to buffers.

## Slide 13
Data format (slightly simplified)
Data words length: 16 bit
Meaning | 15 8 |  |  | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Pixel Data | Pixel Address (N-Pix) |  |  |  |  | N-Col |  |  | Pattern |  | 
Idle | FC | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0
Frame header | FC | 1 | 0 | Payload (N-Frame…) |  |  |  |  |  |  | 
Frame trailer | FC | 1 | 1 | Flags |  |  |  |  |  |  | 
Region header | FC | 0 | 1 |  | N-Region |  |  |  |  |  | 
Spare | FC | 0 | 0 | 0 |  |  |  |  |  |  | 
Spare | FC | 0 | 1 | 1 |  |  |  |  |  |  | 
V
O
V
O = Overflow flag, Pattern: Status of consecutive pixels
Highly efficient data format – mostly no post-compressing required.
Frame header (8 words) | Region header (1 word) | Pixel data (<100 words) | Region header (1 word) | Pixel data (<100 words) | Frame trailer (1 word) | Checksum (1 word) | Idle
Data train

## Slide 14
Readout chain (work in progress)
MIMOSIS-1, 60µm thick
GBTx
8x 320 Mbps
In vacuum
In air
Cri-Board (PXIe-board)
Green Cube
SCA
CROB
Slow control: I2C
clk (40 MHz)
5 Gbps (optical)
GBTx
GBTx
Common Readout Board
Common Readout Interface
See talk of D. Emschermann (tomorrow)
HV (+10V)
GND
VDD (1.8V)
VBB (-1V)

## Slide 15
Summary and conclusion
GSI, IPHC and Goethe University Frankfurt are developing MIMOSIS:
  Fully depleted, >1014neq/cm².
  5 µm spatial resolution.
  5 µs time binning.
  20 MHz/cm² (80 MHz/cm² peak).
  Proven tolerance to heavy ion impacts.
Sensor design far advanced, expect final sensor within 2 years.
MIMOSIS readout and FEE:
1x, 2x, 4x, 8x 320 Mbps DDR data links.
Compatible with GBTx/SCA and the CBM readout chain.
Voltages: 1.8V (power), GND, Pixel HV (10V, -1V)
Integration into the CBM standard readout system is in progress.
Thanks to:
IPHC, Uni-Frankfurt, GSI (CBM-MVD) collaboration:
Julio Andary1, Benedict Arnoldi-Meadows1, Ole Artz1, Jérôme Baudot2, Grégory Bertolone2, Auguste Besson2, Norbert Bialas1, Roma Bugiel2, Gilles Claus2, Claude Colledani2, Hasan Darwish1,2,3, Michael Deveaux3, Andrei Dorokhov2, Guy Dozière2, Ziad El Bitar2, Ingo Fröhlich1,3, Mathieu Goffe2, Fabian Hebermehl1, Abdelkader Himmi2, Christine Hu-Guo2, Kimmo Jaaskelainen2, Oliver Michael Keller6, Michal Koziel1, Franz Matejcek1, Jan Michel1, Frédéric Morel2, Christian Müntz1, Hung Pham2, Christian Joachim Schmidt3, Stefan Schreiber1, Matthieu Specht2, Dennis Spicker1, Joachim Stroth1,3,4, Isabelle Valin2, Yue Zhao2, Roland Weirich1 and Marc Winter2,5 1Goethe-Universität Frankfurt, Germany, 2Université de Strasbourg, CNRS, IPHC UMR 7178, Strasbourg, France 3GSI Helmholtzzentrum für Schwerionenforschung GmbH, 4Helmholtz Forschungsakademie Hessen für FAIR, 5IJCLab, UMR9012 – CNRS / Université Paris-Saclay / Université de Paris, France, 6 FIAR GmbH,Germany
ALICE@GSI: Silvia Masciocchi et al.
DRD3 Week, CERN, 17 June 2024