## Slide 1: Status of FAIR and Super-FRS .
Haik Simon – GSI Darmstadt

## Slide 2
FAIR Construction Site
April 2024
April 2024 – Shell construction Finished – Groundbreaking July 2017

## Slide 3
May 2022
FAIR Project Progress – Civil Construction
Construction Area South – Only TBI and landscaping missing
H.Simon - Halo Week '24

## Slide 4: Fair-28: Main Objectives - NUSTAR
Super-FRS
Increase in primary
beam intensity
10-100
Matched with acceptance
and selectivity of a versatile
Separator: Ion optics and instrumentation …
 Experiments
SIS100

## Slide 5: Super-FRS (@SIS18/SIS100) workhorse for NUSTAR
One of worlds most powerful
separators
for exotic nuclei
L prod.
D exc.
E* 13 MeV
Large acceptance
High rigidity, minimized losses
 Thick production targets
Most effective use of primary beam for experiments
Target
Ring Branch
High energy Branch
Technical Design Report:
H. Geissel, M. Winkler, H. Weick, et al. (2009)
Low energy
Branch with
Energy buncher
H. Simon – Halo Week ‘24

## Slide 6: Early Science Objective
FCC
commissioning
Start version taking beam from SIS18 via Super-FRS to the High Energy Branch
Beam intensity increase through optimized beam transport and transmission from SIS18

## Slide 7: HE Beam Transport Early Science (SIS18 – Super-FRS)
G0704A
G0702A
H0705A
K0617A
Super-FRS
SIS18
Installation start on 03.04.2024

## Slide 8: Super-FRS Target area (artists‘ view)
unreacted primary beam
wanted fragment beam
magnets
Preselection in
The pre-separator
allows to cope with
100-fold intensity from
SIS-100.
Technically challenging
Radiation area.

## Slide 9: Target area components
target
Q1a
Q1b
Q2
S1
D1
D2
D3
BC1
BC2
BC3
S2
iron and concrete shielding
Russian In-kind
contributions from
BINP (Novosibirsk)
IOFFE Institue (St Peterburg)
needed replacement !
Installation start of
lateral iron shielding started 05/2024 as scheduled

## Slide 10: Area of success: All target component entering production or running
7.5 t
3.6m
plug parts
Welding
test chamber 1:1 at Trident, Kanpur
Ex Russian In-kind: rad-hard Dipoles (2) and Multipoles (2) again in production (Buckley NZ, SigmaPhi F)
Ex Russian
vacuum system
Local cryogenics components
detectors
Again in production !

## Slide 11: Target Area -Remote handling and shielding
Target chamber
BC chambers
Pillow seal plugs
parking cell
Plugs parking cells
Hot and decay cell
Hot cell slider
pillow seals
E. Kozlova
Beam Plug interactions
hall
maintenance
Notes: Here, one can observe the target area beamline enclosed from the top.
The target area beamline is situated near the hot cell where plugs are periodically repaired, including target plugs and beam catcher plugs.
A total of 21 plugs will be required depending on the phase of the facility's life cycle.
To facilitate maintenance, storage of both fresh and activated plugs must be considered, given that the hot cell is in use.
The plugs are activated and can reach a dose rate of up to 7 Sv/h.

## Slide 12
Final Absorber Block
1:1 dummy
~ 300 kg
400 mm
Collaborative development,
optimization and technical implementation !
Cu
C
steel
motor
linear drive
absorber block
490 mm
graphite tile

## Slide 13: Area of success: 3 beam catchers in production
7.5 t
3.6m
3 full beam catchers (IK India; CMERI Durgapur)
chambers plus absorber plugs
In-kind contract not yet signed, but…
Indian manufacturer already awarded (Trident Auto Components, IN)
Planned end of design (FDR): June 2024
Planned end of delivery to FAIR: October 2025
Planned installation: Q2-Q4 2025
plug parts
Welding
test chamber 1:1 at Trident, Kanpur
3 special alignment supports
FAIR contract award: February 2023 (Fantini Sud, IT)
FDR = December 2023
Planned delivery: November 2024
Planned installation: Q1 2025

## Slide 14
Sc Magnets are key components:
Testing at CERN of sc magnets
Very successful tests @ CERN
Ion optical performance well achieved ! (99% done ,,,)
But:
magnet leaks at cold observed
H. Simon – Halo Week ‘24

## Slide 15: Superconducting Magnets Re-Entering Series Production after Prototype testing and repair
Similar activity with Elytt (Dipoles)
 entering series testing if running tests are successful
Technical issues
with thermal shield
brazing connections

Reworks and Design change was neccessary
Intense ollaboration with CERN to resolve the issue with manufacturers.

## Slide 16: Example: Magnet Supplies as part of the Building Local Cryogenics distribution system
FoS tests @ STF/GSI
Chart: Distance from supply, m
| 1.7649999999999999 | 8.0649999999999995
T | 5.3029 | 5.3236
P1 | 5.3025 | 5.3091 | 5.3269 | 5.3371 | 5.357
P2 | 5.3005 | 5.3014 | 5.3027 | 5.3037 | 5.3047 | 5.3065 | 5.3102 | 5.3116
M | 5.3119 | 5.3128 | 5.3137 | 5.3157 | 5.3196 | 5.3219 | 5.3234 | 5.325 | 5.3276 | 5.3333 | 5.3354 | 5.3374 | 5.3394 | 5.3432 | 5.3511 | 5.3526
R | 5.3015 | 5.3036 | 5.306 | 5.3112 | 5.3232 | 5.3309 | 5.3371 | 5.3452 | 5.3639 | 5.4464
H | 5.3036 | 5.3081 | 5.3141 | 5.3314 | 5.3823
L | 5.3009 | 5.3018 | 5.3024 | 5.303 | 5.3039 | 5.307 | 5.3721
G | 5.3024 | 5.3087
E | 5.3044 | 5.3093 | 5.3151 | 5.3219 | 5.3303 | 5.3415 | 5.3578 | 5.3894
Complex distribution system, long distances
Design in collaboration with WUST/Wroclaw
CDR phase just finished
Tender of FoS Branch-T running to be tested @GSI
Sharing of IK components
in Council 20240710-11

## Slide 17: Overall installation schedule – entering 3 dense years after a lot of stride
BB
May 2024 Dec 2025
Juni 2026
Oct 2026
Jan 2025 July 2026
Installation local cryogenics
control system ready for test operations
* starts with lateral iron shielding
cryo plant available
Installation start 6.5.2024
Many issues solved
But still some on the way !

## Slide 18
HISPEC
DESPEC
Super-FRS Exp.
1st NUSTAR
 R³B
All NUSTAR Experiments possible
(some in start versions @ FHF1)
Exception: ring experiments & MATS LASPEC @ Super-FRS
Prospects: First stage: High energy branch R3B/GLAD (and setup @ FHF1)
15m

## Slide 19: From R³B prototype to R³B precursor
Empty Cave with GLAD 2015/16

## Slide 20
R³B setup ready
to move to FAIR in 2025/6
Liquid - H2 target
(100%)
CALIFA (60-70%)
2528 detection units
CsI(Tl)-LAAPD
1.3 m3 and 2.5 tons
TRT Si based
Technically challenging still R&D ongoing based
e.g. ALPIDE pixel detectors
GLAD (100%)
Large aper. 80x100 cm
4,8 Tm ; 3,5 x7x4 m
50 tons first to move
NeuLAND (50-60%)
250x250 cm2
3000 BC408 + 6000
PMTs ; 32 tons
Tracking detectors (100%)
Silicon/ Plastics
Fibers 80x80 cm2, 500 mm MUSIC´s
MW´s 90x60 cm2 , 200 mm
3 m
Up to 15 m
2 m
ToF walls (100%)
Plastics walls 120x80 cm2
Plastics walls 84x60 cm2 (15 ps)
RPC system (protons)
H.Simon - Halo Week '24
Notes: 20

## Slide 21
R3B experiment
Reactions with Relativistic Radioactive Beams
30 m
2 m
HI Beams @ 500– 1000 A MeV
beam from SIS18/FRS
neutrons
protons
Moving date to be decided – Beam time retreat 20240711-12
Heavy fragments
© GSI/FAIR, Zeitrausch
Tracking detectors
Target + Si-Tracker + CALIFA
GLAD
Tracking detectors
Tracking detectors
NeuLAND
Notes: 21

## Slide 22: Thanks
Super-FRS project group and
www.gsi.de/superfrs
www.gsi.de/r3b www.r3b-nustar.de
collaboration

## Slide 24: FAIR beams (with suitable intensities)
Up to 20Tm beam rigdity  high energy coulomb excitation
@ 240 A MeV
 high energy ~1 A GeV
S. Bacca et al.
PRL 89 (2002) 052502 PRC 69 (2004) 057001
GSI
FAIR
ds/Efnn
[mb/MeV]
Thesis:
C. Lehr – D17 (2022)
6He@185 A MeV
 RIKEN campaign
© ANL
(1998)
Heavier systems !
clean separation
no charge states

## Slide 25: FAIR beams (with suitable intensities)
Phil. Trans. R. Soc. Lond.
A356 (1998) 2063
Not only 11Li but also
3LH forms presumably a halo system !
 1.57 A GeV threshold
A. Obertelli

## Slide 26: Summary
Instrumentation suitable for halo and dripline physics constructed and commissioned within Phase-0 experiments of the R³B experiments, examples presented (Nikhil, Stefanos, …)
FAIR facility enables exclusively dedicated program especially suited for energetic intense secondary beams in particular also for heavy nuclei (N=126)
Installation/(commissioning) schedule and scenario for NUSTAR experiments@FAIR presented  dedicated program during ramp up
"If you want to build a ship, don't drum up people to collect wood and don't assign them tasks and work, but rather teach them to long for the endless immensity of the sea." - Antoine de Saint Exupéry

## Slide 27
2015 - 2020
R3B in Cave C @ GSI  preparing for FAIR
Lola Cortina

## Slide 28
2020 - 2025
Lola Cortina
R3B in Cave C @ GSI  preparing for FAIR

## Slide 29: First 12C(p,2p) experiment @ 400AMeV - „R³B prototype setup“
H. Simon – Halo Week ‘24

## Slide 30: The 17Ne 2p halo quest (@500 AMeV)
CH2 target !
15O core
excitations
Rather small
2s² - contribution 35(3) %
 Suppressed halo

## Slide 31: 7H ↓ and 4n →
p(8He,pp)7H
61.3 AMeV
PRL90(2003)082501
PRL 99 (2007)
062502
12C(8He,7-5H 3H + x)13N
15.4 A MeV
EPJA 32
(2007) 261
2H(8He,3He )7H
42 A MeV
PRC81 (2010)
064606
Direct study is enabled by exclusive measurements
PRL 116 (2016) 052501
4n@100keV
600 A MeV, 35m
>60% 4n recog.
 NeuLAND.
Missing mass analysis
K. Kisamori et al.
4He(8He; 8B) @ 186 A MeV
M. Duerr et al.
8He(p,pa) @ 156 A MeV

## Slide 32: Neuland demonstrator @ RIKEN
NeuLAND demonstrator (40 cm depth with 4/30 double planes and 800 readout channels) at RIKEN 2014-2017, participation in various beam times
Several experiments performed and published (e.g. M. Duerr et al., Nature 606 (2022) 678)
NEBULA
NEULAND
SAMURAI
March 2015
4 double planes @ RIBF

## Slide 33: O-28 a first Landmark for fragment + 4n detection
Causallity cuts only 16% remaining background
e(3n)=2% e(4n)=0.4%
Very intense RIBF beams  detection efficiency is key !

## Slide 34: Novel Neutron Detector: NeuLAND
Fully active neutron detector based on
scintillators (calorimetry & tracking)
30 double planes
2 x 50 paddles each
5 x 5 x 250 cm³
RP408 / R8619ASSY
FPGA TDC readout
Previously < 50%
Previously <5% !
4n coincident four-momentum detection
Split detector + causality cuts could be added.
NIMA 1014 (2021) 165701
H.Simon - Halo Week '24

## Slide 35: Steady State Thermal Simulation Optimisation of Absorber Profile
950 K
300 K
modified material
l =15 W/m-K in center (c1-c3)
l =15 W/m-K, shaped better
fresh SGL R6650
Apply radiation damage only
in inner regions of spot (c1..c3)
Use Gaussian beam spot and 17 kW (1500 MeV/u 238U)
301 K
301 K
1504 K
2210 K
to copper heat sink
LS-DYNA
beam

## Slide 36: Example for status of major components: sc multiplets in series production
FoS SM
FoS LM
early science
(20 multiplets)
baseline
actual
ASG: 01/09/2021
First-of-Series Magnets readily prepared for tunnel installation
FoS SM
Beam pipe
Apperture
400 mm
Weigth:
Several 10 tons

## Slide 37: Replacement of ex-Russian in-kind components Status and challenges
FoS diagnostic cambers
early science
ex RU in-kind
FoS sc dip. chambers
nc dip. chambers
„closing all vacuum“ Q4
specs being rewritten
tender running
tender awarded
production completed
series sc dip. chambers Q3
local cryogenics
branch box
nc dipoles
sc branch dip. chambers
nc dip. wires
nc dip. supports
LC branch B transfer lines
new PolishIK
nc dip. chambers
some detectors (now in-house)
series diagn. chamb. Q2
LC warm gas pipes Q4
nc dipoles
nc dip. wires
nc dip. supports
All components on track to be ready for early science

## Slide 38: ... with direct applications
Development of a high precision nuclear clock: Promising candidate thorium-229
High-performance and scientific computing, big data, green IT, AI (host of Hessian AI)
Space radiation protection, unique facility for simulation, collaboration with ESA
Innovation in
Cancer Treatement
Tumor
harte Röntgenstrahlung
Eindringtiefe [cm]
18
2
6
10
14
50 %
100 %
0 %
Schädigung
Ionen-strahl
38

## Slide 39: FAIR in construction
First Runs expected 2026/27

## Slide 40: A new vertex tracker for R3B assembled for FAIR Phase-0 2022
Si microstrip vertex tracker assembled for 2022
FAIR Phase-0 beam time

## Slide 41
ALPIDE pixel detector station (area 100 cm2, position resolution 5 µm, rate up to 100 kHz)
Developed for MIPs, possibility to measure heavy ions is proved
Holding/mounting frame is developed, production started
Cooling carbon-fiber plate is developed and produced at CERN
Beam tests:
CERN, relativistic muons
FZ Jülich, deuterons @300 MeV, 800 MeV
and 1 GeV
Investigation of efficiency,
maximum trigger / data rate,
PID (via cluster size),
synchronous readout
of many detectors
MOSAIC FPGA readout boards
Cluster size and hit occupancy
measurements at Jülich
Si vertex detector developments
Courtesy: W. Korten
Measurements at FZ Jülich
Notes: Recent results from tests at CERN and Jülich

## Slide 42
From precursor to (almost) final
2018-2019
2020-2022
20 % detector setup
Stable beams
60-70 % detector setup
Fragmentation beams@ cave C
Fission beams @ cave C
Notes: 42

## Slide 43
Dec. 28th , 2006
First Beam 27Al10+ 345 MeV/u at RIBF-SRC
March, 2007
12th 86Kr31+ beam at 345 MeV/u several pnA.
13th First production of RI beams with 86Kr beam
23rd First successful acceleration of 238U86+
beam at 345 MeV/u and 0.002 pnA
27th First production of RI beams with 238U beam
May-June, 2007 (without ZDS)
with 238U beam at 345 MeV/u and 0.02 pnA max
May 16th-23th BigRIPS commissioning experiment
May 24th – June 3rd Search for new isotopes
End of June(a few days) detector testing
Nov. 2007 acceleration test with 86Kr beams, 30 pnA
(~1x108 pps)
TOF
DE
DE
History of RIBF commissioning
T. Kubo RIKEN / Separator Expert Meeting
Break at the facility !

## Slide 44
Z
A/Q
Z
A/Q
Z=46
Bρ: 7.438 Tm
Total dose: 3.6×1012
Total time: 25.4 hour
125Pd
Searching for new isotopes
May 2007
T. Kubo RIKEN

## Slide 45: R³B experiments in 2018/19
Modular and versatile experimental setup with unprecedented efficiency, acceptance, and resolution for kinematical complete measurements of reactions with high-energy radioactive beams  first experiments
2017-2018
2015
Cave C empty
2016 GLAD @ GSI
Cave refurbishment
2017
GLAD Installation
HTD detector commiss.
2018/19
GLAD + Big chamber
CALIFA and NeuLAND
Demonstrator
S444 Main detection system commissioning
S454 Studying the astrophysical reaction rate of C(alpha,gamma)
S473 Constraining energy‐density functionals and the density‐dependence of the symmetry energy (i)
Stable beams
Notes: 45

## Slide 46
R³B experiments in 2020/21
2021
+ LH2 +
CALIFA iPHOS
NeuLAND 12 DP
2020
CALIFA Barrel (P-39, Han-Bum Rhee)
NeuLAND 8 DP
SOFIA tracking detectors
R3BMusic
2022
+ Proton arm
behind GLAD
& LH2 target preparation
New Fiber
Detectors
S444 Detection system commissioning
S467 Single‐particle structure of neutron‐rich Ca isotopes
S455 Fission studies @R3B -  talk by Jose Luis Rodríguez-Sánchez
S515 Constraining energy‐density functionals and the density‐dependence of the symmetry energy (ii)
S494 Coulomb dissociation of ​16​O into ​12​C and ​4​He.
Notes: 46

## Slide 47
LH2 + FOOT + CALIFA + NeuLAND (13 DP) + Fiber tracking + Proton arm
behind GLAD
S522 First characterization of
Short-Range Correlations in exotic
nuclei at R3B (16C)
S509 Study of multi-neutron
configurations in atomic nuclei
& Dedicated field mapping for precision tracking
S494
S522
Neuland
TOFD
FIB
x, y
FIB
LH2
ROLU
RPC
FOOT x4
R3B
Music
FOOT x4
FOOT x 2
FOOT
VACUUM
AIR
14°
CALIFA
MW
MW
LOSS
GLAD
RPC & FIBER
TOFD
GLAD
Cocotier LH2 target FOOT Si-trackers
CALIFA calorimeter
Ended few weeks ago!
R³B experiments in 2022
Notes: For 2022 there are several important additions in preparation, most notably the FOOT Si detector array, which is an intermediate solution but increasing the efficiency for two-proton detection in (p,2p) reactions to 20-30% running at rates up to 10kHz.

## Slide 48: GSI FRS  FAIR Super-FRS (key parameters and enhancement)
1000 7500
Super-FRS
FRS

## Slide 49
FAIR-Phase 0 –
Start in 2018!
SIS 100
Super FRS
SIS18
UNILAC
100 m
HESR
CR
ESR
CRYRING
FRS
HITRAP
GSI and FAIR – The Facility
FAIR,
under construction
GSI, existing (upgraded to integrate with FAIR)
FAIR key features
intensity for wide range of ions
storage rings
antiproton beams
ESR, CRYRING, & HITRAP are part of the FAIR MSV
49

## Slide 50: 𝛬 hypernuclei @ R3B
Study of Hyperhalos, determination of binding energies and lifetimes
Program at R3B based on a new high-resolution pion tracker (TPC) , HYDRA, inside GLAD
 Halo properties can be probed

## Slide 51
Target area: remote handling in highly radioactive environment
Remote Handling of beamline inserts
(X and Y slits) using industrial robots
Automatic media board disconnection
Robot tools
Shielded Flask for transport
to hot cell for maintenance
Customized environment for handling of
activated materials

## Slide 52: Main components for early science aiming for Q4/2026
power converters
local cryogenics
sc short multiplets
production target
nc dipoles
beam catchers
nc multipoles
focal plane chambers
+
detectors
iron shielding
early science at R3B
early science
HISPEC DESPEC
Super-FRS Exp.
sc long multiplets
sc dipoles
power converters
Reduced scope, in line with building infrastructure
Major components in production

## Slide 53: Example: R³B at the High energy Branch of the Super-FRS
From Past experiments (FRS + ALADiN-LAND setup) to future (Super-FRS – R³B setup)
Evolutionary steps towards R³B setup
Why do we need FAIR beams (SIS-100 & Super-FRS)
Status of the new facility
R³B collaboration meeting
June 2022