## Slide 1: Counter Production Readiness Review (PRR) of MRPC2 Detector in CBM-TOF System
Kai Sun, Yi Wang, Ingo Deppner
Tsinghua University, Beijing, China
Notes: 】

## Slide 2: Outline
Introduction
Description of MRPC2
Material preparation of MRPC2
Production of MRPC2
QA ＆ QC
Performance of MRPC2

## Slide 3: Introduction of CBM-TOF Wall
The CBM-TOF wall is subdivided into two parts called the inner wall and the outer wall: Inner wall: charged particle fluxes range between 5 kHz/cm2 and 30 kHz/cm2. Outer wall: charged particle fluxes range between 0.1 kHz/cm2 and 5 kHz/cm2.
MRPC2 detectors belong to the outer wall and cover the area where the charged particle fluxes range between 1 kHz/cm2 and 5 kHz/cm2.

## Slide 4: Introduction of CBM-TOF Wall
Requirements of MRPC2(Yellow Region) in CBM-TOF Wall: Efficiency: > 95% Time Resolution: better than 80 ps Rate Capability: ＞ 5 kHz/cm2 Granularity: ＜ 30 cm2

## Slide 5: Description of MRPC2
Main design parameters of MRPC2
Honeycomb
Top PCB
Mylar
Carbon film glass
Glass*3
Carbon film glass
Mylar
Mid PCB
Mylar
Carbon film glass
Glass*3
Carbon film glass
Mylar
Bot PCB
Honeycomb
Section and structure view of MRPC2

## Slide 6: Material preparation of MRPC2
Material | Length /[mm] | Width /[mm] | Thickness /[mm] | Amount | Others
Low-resistive glass | 330±0.2 | 276±0.2 | 0.7±0.02 | 10 | 
Carbon film | 324±0.5 | 270±0.5 | 0.005 | 4 | 
TOP PCB | 360±0.2 | 338±0.2 | 0.8±0.05 | 1 | 
Mid PCB | 360±0.2 | 338±0.2 | 0.8±0.05 | 1 | 
Bot PCB | 360±0.2 | 338±0.2 | 1.6±0.05 | 1 | 
Honeycomb board | 333±1 | 310±1 | 6±0.2 | 2 | 
Mylar | 340±0.2 | 286±0.2 | 0.25±0.02 | 8 | 
Carbon film tape | 50 | 50 | 0.13±0.2 | / | 
A type fix block | 23±0.2 | 10±0.2 | 4±0.05 | 4 | 3D-Print
B type fix block | 14±0.2 | 10±0.2 | 4±0.05 | 2 | 3D-Print
Pad Spacer | Φ=4 | Φ=4 | 0.25±0.005 | 448 | Made of Mylar
M2.5 Screws | 40 | 2.5 | / | 32 | 
M4 Screws | 40 | 4 | / | 16 | 
Protection resistor | / | / | / | 128 | 0603
Fix pin | 19 | Φ=0.6 | / | 100 | 
2×9 signal pin | / | / | / | 16 | 

## Slide 7: Material preparation of MRPC2

## Slide 8: Material preparation workflow
Low resistive glass
  Clean
  Spray carbon film
  Glue pad spacer
PCB
  Soldering 2×9 signal pin
  Soldering protection resistor
Mylar
  Slotted for high voltage
Honeycomb
High voltage lines
Other fix pin and fix blocks
Spray machine
Cleaning glass
  Spray carbon film

## Slide 9: Production of MRPC2
Glue the honeycomb panel on the PCB
HV connection
Test of gap thickness

## Slide 10: QA ＆ QC
Dimensional inspection of key materials

## Slide 11: QA ＆ QC
Other inspections
Low resistive glass
  Dark current smaller than 80nA under ±6000 V (spot test for each batch of glass)
Uniformity of the detector gas gap
  directly observing gap with a digital microscope
Signal connection
  Use a multimeter to test circuit connection
HV test and cosmic test for MRPC2 produced
MRPC gap image

## Slide 12: Performance of MRPC2
  Efficiency distribution of an MRPC2 at mTOF
Time resolution of MRPC2 at mTOF

## Slide 13
The first batch of mass production of
75 MRPC2 has started.
Thank you!
yiwang@mail.tsinghua.edu.cn