## Slide 1: Hit Triplet Finding in the PANDA-STT
Marius C. Mertens1
Sean Dobbs2, Jim Ritman1, Peter Wintz1
1 Forschungszentrum Jülich
2 Northwestern University

## Slide 2: Outline
  Part I  Focus on Tracking
    Triplet Finding and Tracking in Axial Straws
    STT Geometry in PandaRoot
    Track Verification
    Hitstream Display
    Triplet Finding in Skewed straws: Skewlets
    Summary/Outlook I
  Part II  Focus on OnlineManager/Implementation
    Triplet / Skewlet Finding Overview
    Implementation in OnlineManager
    Track/Hit Quality Criteria
    Output to Hitstream Display
    Summary/Outlook II

## Slide 3: Triplet Finding in Axial Straws
  Basic properties:
    Finds tracks originating from the interaction point
    Works in xy projection
    No isochrone information used  Does not require t0 or isochrone-drifttime calibration
  Results:
    Track candidates
    Associated hits
    t0 seed for selected tracks (hit timestamp constraints, matching with other detectors)
  Carried out in three steps:
    Identification of hit triplets (or n-lets) around pivot cells
    3 point circle calculation: Origin + 2 Triplets
    Hit association via circle proximity

## Slide 4: STT Geometry in PandaRoot
Axial pivot cells indicated
in one sector

## Slide 5: Triplet Finding in Axial Straws
  Pivot cell is checked for hit
  Surrounding straws are checked for hits
  Center of mass of fired straws is calculated (small number of combinations  suitable for lookup table)

## Slide 6: Triplet Finding in Axial Straws
  Once two triplets are found, calculate circle through origin
  Associate nearby hits with track candidate
Track Verification:
  Currently mix of curvature and associated hits
  Lots of room for improvement
Further possibilites:
  Distance sorting, Concurrent associations, Clutter veto, …
  Missing straw compensation: Pivot Straw triggered by neighbor straws
  Weight hits according to timestamp
  Improved Triplet merging
Interaction Point

## Slide 7: Hitstream Display: 15 GeV/c DPM, 50 ns mean time
  Black circles: Early isochrone
  Blue circles: Early skewed isochrone
  Green circles: Close isochrone
  Red circles: Late isochrone
  Black dots: MVD hits
  Green dots: MVD hits r/z > 0.3
  Black+Red dots: Triplets/Skewlets
  Yellow tracks: Vetoed
  Blue tracks: Accepted
XY-View
RZ-View

## Slide 8: Triplet Finding in Skewed Straws: Skewlets
Skewlet layers indicated
in one sector

## Slide 9: Triplet Finding in Skewed Straws: Skewlets
  Triplet search in individual skewed double layers
  Combination of adjacent double layers‘ Triplets to Skewlets
  Track matching in xy-projection
  Extraction of z-information

## Slide 10: Interlude Summary/Outlook
Part I
  Proof of concept Triplet Finder tested with DPM input
  Robust first-line algorithm independent of isochrone (t0) information and drifttime calibration
  Visual inspection yields promising results
  Many (straightforward) tuning possibilites affecting efficiency, purity and robustness
Part II
  Implementation within OnlineManager  Sean‘s talk
  Triplet Finder runs as compiled code and uses OnlineManager‘s data flow
  Animated visualization in HitstreamDisplay
Outlook:
  Implementation of hit association quality property
  Merge with canonical PandaRoot tools
  Long term goal: Track-to-event association

## Slide 11: Part II

## Slide 12: Outline
  Part I  Focus on Tracking
    Triplet Finding and Tracking in Axial Straws
    STT Geometry in PandaRoot
    Track Verification
    Hitstream Display
    Triplet Finding in Skewed straws: Skewlets
    Summary/Outlook I
  Part II  Focus on OnlineManager/Implementation
    Triplet / Skewlet Finding Overview
    Implementation in OnlineManager
    Track/Hit Quality Criteria
    Output to Hitstream Display
    Summary/Outlook II

## Slide 13: STT Geometry in PandaRoot
Axial pivot cells indicated
in one sector (red)
Skewlet layer indicated
in one sector (orange)

## Slide 14: Continuous Online Tracking: Status Sep. 2012
Sorting:
Arrival Time

Hit Time
Detector Hits
Detector Hits
Detector Hits
Cluster Finding
Hit Building
Digi
Reco
Hitstream Display
Digi/Reco

## Slide 15: Continuous Online Tracking in OnlineManager
Hits
Tracklets
Tracks
Events
Sorting:
Arrival Time 
Hit Time
Detector Hits
Detector Hits
Detector Hits
Hitstream
Display
Time Ordered Simulation
Functor Based Reader
PndOnlineManager
Cluster Finding
Hit Building
Reconstruction Algorithms
(FairTask)
Triplet
Finder

## Slide 16: Track/Hit Quality Criteria
Possible Extensions in Track Quality Measurement
  Hit distance to track order should correspond to hit timestamp
  Add extrapolations to other detectors
  Concurrent hit association / clutter criterion
  …
Implementation Sketch
  Hits are assigned to tracks with their quality measure
  Algorithms access and update the quality measure (may also reject processing if quality is already marked as very good)
  Same principle: Association of tracks to events

## Slide 17: Output to Hitstream Display
Analysis / Track Finding Part
  OnlineManager provides hits
  Triplet Finder processes hits and generates Triplet lists
  Track candidates are sent to OnlineManager
Visualization Part
  OnlineManager provides OnlineTracks
  Display Macro has functions to draw the different objects stored in the lists for display

## Slide 18: Hitstream Display: 15 GeV/c DPM, 50 ns mean time
  Black circles: Early isochrone
  Blue circles: Early skewed isochrone
  Green circles: Close isochrone
  Red circles: Late isochrone
  Black dots: MVD hits
  Green dots: MVD hits r/z > 0.3
  Black+Red dots: Triplets/Skewlets
  Yellow tracks: Vetoed
  Blue tracks: Accepted
XY-View
RZ-View

## Slide 19: Summary/Outlook
Part I
  Proof of concept Triplet Finder tested with DPM input
  Robust first-line algorithm independent of isochrone (t0) information and drifttime calibration
  Visual inspection yields promising results
  Many (straightforward) tuning possibilites affecting efficiency, purity and robustness
Part II
  Implementation within OnlineManager  Sean‘s talk
  Triplet Finder runs as compiled code and uses OnlineManager‘s data flow
  Animated visualization in HitstreamDisplay
Outlook:
  Implementation of hit association quality property
  Merge with canonical PandaRoot tools
  Long term goal: Track-to-event association
Thank you for your attention