## Slide 1: A DIRC-like TOF at STCF
R&D、beam test and future plan
Xuesen Lin On behalf of PID colleagues at STCF , USTC
1
Notes: Hello everyone, I’m honored here to introduce the progress of the development of PID of STCF detector. This report focus on R&D, beam test and future plan of the DTOF.

## Slide 2: Content
DTOF (DIRC-like TOF) @STCF: requirements
R&D: design ,reconstruction , simulation performance and cosmic ray test
Beam test @ CERN: experiment setup, result
Future plan: BTOF R&D and BTOF beam test preparation
2
Notes: I list the content here. The report contains of the requirement of PID for STCF. The R&D including the Design, reconstruction, simulation performance and cosmicray test. Afterwards, the beam test of a 1/3 prototype was conducted in CERN T9 last summer.And I ‘ll show you the experiment setup and result. Final I would talk about the Barrel DTOF, which we call BTOF R&D and the beam test preparation.

## Slide 3: DTOF@STCF: requirements
01
3

## Slide 4: STCF introduction
Super tau charm factory (STCF) in China
Maximum luminosity: >0.5×1035 cm-2s-1
Energy range: Ecm = 2-7 GeV
High luminosity frontier，focus on charm bottom quark and precise measurement of SM
The momenta of STCF final state particles
Endcap PID detector requirements
>4σ 𝜋/Κ separation power at p≤2 GeV/c
Compact structure, thickness<20 cm
Low material budget (<0.3 X0)
A polar angle coverage of 21°-36°
A DIRC detector !
Notes: STCF, short for super tao charm facility, is a high luminosity frontier collider, focus on charm, bottom quark and precise measurement of SM. The maximum luminosity is ~ 10^35, energy range from 2-7GeV/c. Here’s the momentum distribution of the STCF final states particles, and you can see that almost every charged particle momentum < 2GeV, that is , we need to separate the particle , especially Pi K below 2 GeV. What’s more we want it to be more compact and lower material budget, so we choose the DIRC detector as the endcap PID detector.

## Slide 5: DTOF requirement
4σ 𝜋/Κ separation power at p≤2 GeV/c
Total time resolution
ps
DTOF intrinsic time resolution
ps
40 ps
An approximate estimation
Length of Flight ~ 1500mm
Time of Flight (TOF) ~ 5 ns
Length of Propagation ~ 0.5 m~1 m
Time of Propagation (TOP) ~ 3ns
for π/K @ 2GeV/c ~ 120 ps
~ 200ps
Need 50ps time resolution in total
Length of Flight
Length of
Propagation
Lateral
Top&bottom
Front&back
Absorber here
Notes: The basic design schematic picture lies on the left. Here is the one side of the endcap, consists of 4 quadrant parts.And each part consists of a piece of radiator, MCP-PMT coupled on the large edge of radiator, and electronics.The end of the radiator should be painted with absorber to avoid the confusion of the photons. The Length of flight is ~ 1.5 m and length of propagation ~ 0.5-1 m. The TOF difference ~ 120 ps for 2 GeV/c Pi K, and if add the TOP together , the difference ~ 200ps , much looser for the detector requirement for separation. T0 on STCF ~ 40 ps.

## Slide 6: (DIRC-like TOF) DTOF R&D
Design: detector & electronics ,reconstruction and cosmic ray test
02
6

## Slide 7: DTOF design
Apply matting paint to the sides of the radiator
Unit：mm
Radiator
Heraeus Suprasil 312 synthetic fused silica
  High purity, transparency>99%@200 nm
  High radiation tolerance
  Thickness=15 mm, area ≈ 0.56 m2
Surface roughness
  Front&Back RMS <1 nm (0.75 nm）
  Lateral Surfaces RMS~5nm
Thickness=15±0.1 mm, Tmax-Tmin<25 μm
Fused silica used in the cosmic-ray test
Precise parameter of the radiator
Notes: We use heraues suprasil 312 synthetic fused silica. Below is the requirement of the parameters. It has a high purity transparency , and according to Panda data, it can tolerate high radiation.The surface roughness important because we want it to be very smooth to keep Cherenkov angle information. The radiator size is listed on the right.Here is the radiator we use in the cosmic ray test. My colleague was putting absorber on the side

## Slide 8: DTOF design
MCP-PMT
Hamamatsu R10754
  Sensitive area, 23×23 mm2
  4×4 pixels, 5.5×5.5 mm2 each
  spectral response range, 200-850 nm
  Quantum efficiency, ~25%@λ=400 nm
  Transit time spread(TTS):~28ps
Coupled to radiator by EJ550 silicon grease
σ = 33 ps
Recoiling electrons
Laser (width=60 ps) test performance
PMT coupled to radiator
(cosmic ray test prototype)
Hamamatsu R10754
MCP-PMT time resolution after calibration
(including system error ~ 19 ps)
Notes: MCP-PMT we use it a Hamamatsu type. The parameters show here. It contains 16 pads, and each has an area of 5.5*5.5 mm2. .The time resolution of the MCP-PMT ~ 28ps . The systematic calibration of all MCP-PMT is finished and you can that the average time resolution ~ 35ps. MCP-PMT coupled to radiator by EJ550 silicon grease.

## Slide 9: DTOF design
Flexible adapter board×21
Data collect board×2
MCP-PMT×42
Clock&Trigger distribute board×1
Front-end readout board ×21
Electronics
  Time precision 10 ps
  Record TOA (Time of Arrival) and TOT (Time over threshold) of PMT
  Dead time < 10ns
Notes: Here’s the electronics structure , we have a TDC electronics , which can record TOA and TOT of PMT signal. The dead time ~ 10ns. MCP-PMT coupled to flexible adapter board and FEE finally to the Data collect board. We have a clock trigger distribution board.The total time resolution of electronics ~ 10 ps

## Slide 10: Basic conception of reconstruction
What does pattern look like?
  Photons propagate like “water wave”
Reconstruction concept
  Calculate the photon propagation vector using hit point and the channel information
Cherenkov ring propagation in radiator
Absorber on the end side
Cherenkov ring for π/p at 4GeV/c at beam test
Notes: Now I ‘ll introduce the basics of the reconstruction. When a charged particle comes through radiator, the photons propagate like “water wave”. Some photons cannot hit the PMT channel, and will get absorbed at the end of radiator.Finally you can get the hit pattern like this. You can see that the pattern can be primarily used to separate particles. And combine the position information and the time informantion, we can do the separation much better.

## Slide 11: Basic conception of reconstruction
Reconstruction concept
  How to get Δz?
  Using reflective index to deduct the TOP
  Use average refractive index to reconstruct time=>Evaluate time performance
  Divide the index to make a hit pattern=>Fast imaging algorithm
c
Δy
Δz
Z
Y
Track ,
Quartz plate
Photon detector
Δx
Δy
X
Y
Photon detector
Track
Quartz plate
photon
Imaging-based likelihood analysis for the STCF DTOF detector
Notes: Here ‘s the reconstruction conception. Since we know the track information about its hit position and direction and the photon hit channel, We already know the all parameters except deltzZ here. By some mathematic calculation, you can get DeltaZ in this equation. And instantly all the information about the photon propagation vector and emission time. If you use average refractivity index to reconstruct the hit time, you will get a time performance evaluation. On the other hand, if you divide the index, you can calculate the hit pattern. More details please view the article below.

## Slide 12: Previous R&D
Previous R&D
  Reach a total 50 ps time resolution at almost every point
  Below 2 GeV/c, almost all polar angle could reach 4σ separation power for particle
separation power
Nσ = [erfc-1(2ηmis) - erfc-1(2εid)]
σtotal or σdet (ps)
Time resolution@2GeV/c
σtotal <50 ps, σDTOF <30 ps
Geant4 Simulation
Notes: Now here’s the result of previous R&D, we reach a total 50 ps time resolution at all the phase point of phi and theta @2GeV for PiK. And below 2GeV, almost all polar angle could reach 4 sigma separation.

## Slide 13: Cosmic ray test and result
Trigger
2 × Trackers
T0
DTOF
Lead brick
2 × Trackers
Trigger
Z
X
Y
Trigger counters
  Plastic scintillator + PMT, 220 × 220 mm2
  Coincidence of two trigger counters
Trackers
  4 × MicroMegas, 150×150 mm2
  Efficiency ~90%, σpos < 200 μm
Reference time detector (T0)
  180×180×10 mm3 fused silica
  4 × MCP-PMT，Φ = 10 mm
  σT0 ≈ 20 ps
5 cm lead absorber
  Remove soft muons (p < 200 MeV/c)
Front-end readout board
Radiator
(in dark box)
>1.5 m
Cosmic ray test of a full-sized DTOF detector prototype for the STCF experiment
Notes: We perform a cosmic ray test for the whole size DTOF prototype to test its time performance. The cosmic ray platform consists of 2 triggers, 4 trackers, a reference time detector~20ps and a lead absorber.

## Slide 14: Cosmic ray test and result
Central area
Detection efficiency = 99.4%
Single photon, σSPE = ≈ 59 ps
Single track, σDTOF = ≈ 21 ps
DATA
Central
Central area
Peripheral area
DATA
Central
Single photon
(after selection)
DATA
Central
Single track
Signals
Recoiling electrons
DATA
Central
BKG: δ-electrons, scattering photons and dark noise, et al.
Single photon
(before selection)
Notes: And the result of the cosmicray test : we get 38 photons on average, and this is the single photon time distribution. You can see there’s some tails, and we use a selected algorithm to cut the tail, and get a 62 ps time resolution for single photon, average them afterwards , a 29 ps time resolution for single track could be achieved.the Npe ~ 20. Detection effieciency ~ 99%,.

## Slide 15: Summary of cosmic-ray test
A Geant4-based simulation has been done to check the experimental results.
The experimental DATA are consistent with the MC results.
The time resolution of the DTOF prototype is ~22 ps, which meets the performance requirements of the DTOF detector (σDTOF < 30 ps).
Test areas |  |  | Central area | Peripheral area
Number of photon electrons |  | DATA | 20.6 | 17.8
 |  | MC | 20.3 | 17.6
Time resolution of the DTOF prototype | DATA | Single photon | 59 ps | 60 ps
 |  | Single track | 21 ps | 22 ps
 | MC | Single photon | 54 ps | 57 ps
 |  | Single track | 18 ps | 22 ps
Central area
Peripheral area
Notes: We also do the G4 simulation on the cosmic ray test. Here’s the result you can see that the

## Slide 16: Beam test at CERN PS-T9
Setup and result
03
16
16

## Slide 17: Beam test setup
A 1/3 prototype
  PMT x 14，channel x 224
  Using 4 GeV/c /P (~2GeV/c /K)to evaluate DTOF separation performance
  Some channels are malfunctional
T0 detector
  Time resolution ~ 44ps
  Distance ~ 8m, provide separation information
Tracker
  Position and direction
Fused silica (radiator)
MCP-PMT
Electronics
cabinet
radiator
DTOF
T0
Tracker
T0
Tracker
DTOF
Tracker
T0
Micromegas
Micromegas
Reference point:
1450mm to DTOF
Hit point:
Applied matting painting
1/3 prototype detector and mechanical structure

## Slide 18: Beam test setup
A 1/3 prototype
  PMT x 14，channel x 224
  Using 4 GeV/c /P (~2GeV/c /K)to evaluate DTOF separation performance
  Some channels are malfunctional
T0 detector
  Time resolution ~ 44ps
  Distance ~ 8m, provide separation information
Tracker
  Position and direction
DTOF
T0
Tracker
T0 performance @ 4GeV/c
T0
Tracker
DTOF
Tracker
T0
Micromegas
Micromegas
Reference point:
1450mm to DTOF
Hit point:

## Slide 19: Beam test setup
DTOF
T0
Tracker
Tracker space resolution σ~323um
Beam hit size ~ 2cm
A 1/3 prototype
  PMT x 14，channel x 224
  Using 4 GeV/c /P (~2GeV/c /K)to evaluate DTOF separation performance
  Some channels are malfunctional
T0 detector
  Time resolution ~ 44ps
  Distance ~ 8m, provide separation information
Tracker
  Position and direction
T0
Tracker
DTOF
Tracker
T0
Micromegas
Micromegas
Reference point:
1450mm to DTOF
Hit point:

## Slide 20: Data analysis
Test point
  Mark the vertical and horizontal angle are zero at normal incidence
Test point
3 GeV,normal incidence
4 GeV,normal incidence
5 GeV,normal incidence
4 GeV, = 30 deg
4 GeV, = 22 deg , y = 66mm
Test point
3 GeV,normal incidence
4 GeV,normal incidence
5 GeV,normal incidence
Typical hit pattern
Electronics channel malfunction
Vertical Axis,
Horizontal Axis,
1/3 prototype schematic
Axis y
Axis x

## Slide 21: Data analysis-alignment-Kullback-Leibler Divergence
KL divergence alignment
  KL divergence
    Evaluate discrepancy between 2 distributions
    Non negative
  Minimum of KL divergence point is the alignment point
hit pattern from
beam test | fast pattern algorithm
4GeV/c 30 deg
Scanning &
alignment point

## Slide 22: Result and simulation
Separation power reach ~4 σ below 4 GeV/c momentum
Test point | Separation/σ | Npe
3 GeV/c normal | 5.9 | 31.7
4 GeV/c normal | 4.4 | 40.6
5 GeV/c normal | 2.7 | 41.2
4 GeV/c | 3.98 | 28.3
4 GeV/c y=+66mm | 3.93 | 31.6
Test point | Separation/σ | Npe
3 GeV/c normal | 5.9 | 31.7
4 GeV/c normal | 4.4 | 40.6
5 GeV/c normal | 2.7 | 41.2
 | 3.98 | 28.3
 | 3.93 | 31.6
Include secondary particles
Number of Photo-electrons detected ~ 40.6 @ 4 GeV/c normal incidence
Separation power ~4.4 σ @ 4 GeV/c normal incidence

p
1.7%|98.3%
98.4%|1.6%

## Slide 23: Result and simulation
Simulation set up
  MCP-PMT response
  4 GeV /p from
  Wavelength:280-600 nm
  Two 8mm thickness aluminum shell to simulate black box
  Surface roughness
  main ~ 1 nm , lateral~ 20 nm
  Track hit point ~ 2D
  Gaus (mean=0, sigma=14 mm)
Hit x-y@sim
PMT response Time distribution
Geant4 simulation
Hit pattern

## Slide 24: Result and simulation
Simulation for Separation power of Pi/P
1.4%|98.6%
98.5%|1.5%
Simulation Separation power ~4.8 σ @ 4GeV/c normal incidence
Number of Photons ~ 45
Simulation result
  The number of photons ~ 45
  Separation power ~ 4.8σ
  Consists well with beam test
  More simulation is ongoing for other test points

p

## Slide 25: Future plan for barrel PID using DTOF
Consists of 12 modules of Barrel DTOF (BTOF)
Meet the STCF requirement < 2GeV/c, but need to be optimized
Plan to do beam test Oct. 2025 @ CERN PS-T9
1350mm
860mm
MCP-PMT

## Slide 26: Conclusion
DIRC-like TOF at STCF focuses on separation of hadron whose momentum below 2GeV/c
A reconstruction method was developed
Simulation shows the DTOF could meet the requirements of STCF(4σ@2 GeV/c /K)
Cosmic ray test was made and the result shows that the intrinsic time resolution < 25 ps
Beam test indicates that the separation power ~ 4σ @ 4GeV/c /p which equivalent to 2GeV/c /K
More to do on barrel DTOF ……

## Slide 27: Thank you！
ds1997@mail.ustc.edu.cn

## Slide 29
Horizontal angle = -3.8 deg | KL divergence = 0.58
= -3.8 deg | KL = 0.58

## Slide 30
Horizontal angle = -2.2 deg | KL divergence = 0.46
KL = 0.46
= -2.2 deg | KL = 0.46

## Slide 31
Horizontal angle = -0.59 deg | KL divergence = 0.24
KL = 0.24
= -0.59 deg | KL = 0.24

## Slide 32
Horizontal angle = 1.01 deg | KL divergence = 0.29
KL = 0.29
= -1.01 deg | KL = 0.29

## Slide 33
Horizontal angle = 2.6 deg | KL divergence = 0.43
KL = 0.43
= 2.6 deg | KL = 0.43

## Slide 34
Horizontal angle = 4.2 deg | KL divergence = 0.64
KL = 0.64
= 4.2deg | KL = 0.64

## Slide 35: Surface roughness
Sim-30nm
Sim-50nm
Sim-20nm

## Slide 36
ParticleType/L=1450mm | TOF/DeltaTOF:ps | Beta
Pi@2GeV | 4839.6 | 0.9975
K@2GeV | 4967.9 | 0.9709
TOF Difference Pi/K@2GeV | 128.3 | 
Pi@4GeV | 4848.4 | 0.9994
P@4GeV | 4981.4 | 0.9736
TOF Difference Pi/P@4GeV | 133.0 | 

## Slide 37
实验数据
图案生成算法数据
x=(-2.5,2.5)
y=(-2.5,2.5)
thetaX=0.5
thetaY=1.5
x=(-2.5,2.5)
y=(-2.5,2.5)

## Slide 38
Before selection
DATA
Signals
Recoiling electrons
BKG: δ-electrons, scattering photons and dark noise, et al.
SPE signals of one track
DT1 , DT2 , … , DTN
Calculated DTmax , DTmin and DTmean
DTmax -DTmin<ΔT ？
Output DT1 , DT2 , … , DTN
And DTmean
(DTmax -DTmean)×w<DTmean -DTmin ？
Eliminate DTmin
Eliminate DTmax
YES
YES
NO
NO
After selection
DATA
σ = 62 ps
ΔT = 200 ps
w = 1.3
Two parameters, Δt and w

## Slide 39
Radiator shape (4, 12, 24 sectors)
Absorber or mirror
Radiator thickness (10, 15, 20 mm)
Some conclusions
Thick radiator increases material, and thin radiator degreases performance  a right thickness is better
Large area radiator reduces the number of lateral reflections, causing less hit map’s overlaps and better π/K separation power
Adding mirror on the top surface will increase Np.e., but cause more overlaps on the photon hit maps. As results, no obvious performance improvement and great attenuation of MCP-PMT’s lifetime  Reducing the misidentification of photon paths is more important than increasing the number of photons
Optimal design: Large area (4 sectors)，15 mm radiator, with absorber on top and button surfaces

## Slide 41
roughness/nm | Reflectivity
0 | 1
5 | 0.99
10 | 0.95
15 | 0.89
20 | 0.81
25 | 0.72
30 | 0.63
Roughness /nm | Reflectivity
0 | 1
1 | 0.999
2 | 0.998
3 | 0.995
preliminary

## Slide 42: T0探测器性能分析
T0
  180×180×10 mm3 fused silica
  4 R3809U single channel MCP-PMT
T0
ST0
TOP
Timing reconstruction principle
Photon TOP
  Reconstructed like DTOF出
Photon detected timeST0
T0 reconstruction：；Multiple photons：
，evaluate Timing performance（when Np.e.=2）
TOP重建值分布
σ = 20.3 ps
T0diff

## Slide 43
Cherenkov photons are uniformly distributed in phiC and transportation dimension!
2D likelihood:
Project the channel into the R-PhiC phase district
Divide the channel into multiple cells，calculate the propagation vector for different cells, and area ~ intensity

## Slide 45: Prototype Test with laser input
Average measurement precision of 672 channels is 6.19 ps
Single photon time resolutions of DTOF prototype before and after corrections
Notes: Finally, We tests performance of the electronics system. the time resolution of 672 channels is shown in the figure, the total timing accuracy of electronics, including the uncertainty of clock distribution, is less than 15ps, and most of them are between 5-8ps. And we tested the MCPPMT single photon signal, The figure on the right shows the single-photon timing resolution after TOT and temperature calibration of 672 channels. It can be seen that after correction, the single-photon resolution is concentrated in the range of 32-37ps, which is is consistent with the typical Transit Time Spread (TTS) value of MCPPMT itself.We can conclude that the performance of the DTOF electronics system meets the requirements we set out at the beginning of the design.

## Slide 46: Performance Summary
 | value
Channel number | 672
Time resolution of electronics | < 10 ps
Single-photon time resolution | 34.5 ps (Contribution of MCP-PMT is about 32 ps)
Signal timing method | Leading edge timing + FPGA-based TDC + TOT correction
Measurement Dead time | < 10 ns
DAQ transmission bandwidth | ~ 6 GB/s
Maximum event rate | < 400 kHz/ch
Power consumption | 600 mW/ch
Notes: This is the overall performance of the DTOF electronics system