## Slide 1: Super-FRS DAQ for detectors and diagnostics

## Slide 2: Super-FRS detectors
Super-FRS is an experiment
Super-FRS is a machine
Super-FRS is a beam line
all is true
some of the instrumentation is for beam line, some for experiments
2 worlds of DAQ:
  SFRS ACC DAQ (2.4.6.3.1.1) see talk of Andreas this afternoon
  SFRS EXP DAQ (2.4.6.3.1.2) this talk

## Slide 3: Super-FRS detector suit – beam line
Standard BEA detectors:
  usually for beam characterization focal plane per focal plane
  intensity monitoring
   all readout in ACC network, all integrated in control system
  more this afternoon

## Slide 4: Super-FRS “experiment”
Goal of the identify/ion optic characterisatio
need event by event readout -> mean full emitance measurement
need event by event redout for identification
 identficiation need at least 2 focal planes
x/y x2 and tof and Q(Z)


## Slide 6: Detector main types, experiement side
Tracking detectors (X/Y for each plan, often 2 per focal plane)
time of flight  plastics (scintillator detectors)
DE: Ionization chambers (MUSIC)

## Slide 7: Detector main types, experiement side
Tracking detectors (X/Y for each plan, often 2 per focal plane)
developed by Helsinki
“drift chamber” with a GEM stack
position event by event,
rate up to 1e6pps,
<300 um resolution
Li to U ions

## Slide 8: Detector main types, experiement side
Tracking detectors (X/Y for each plan, often 2 per focal plane)
time of flight  plastics
DE: Ionization chambers (MUSIC)
Time of flight in spectrometer: 100 ns
Light propagation time in plastic: 20 cm/ns
 up 2 ns
Difference in time of flight for ions <50 ps

## Slide 9: Detector main types, experiement side
Tracking detectors (X/Y for each plan, often 2 per focal plane)
time of flight  plastics
DE: Ionization chambers (MUSIC)
  DE  amount of electrons add correction from
  velocity  gives the Z
  In practice measure Q, but if energy high enough Q=Z

## Slide 10: Conclusion
Tof give velocity
TPC give position/angle
MUSIC gives DE
  MUSIC+ TOF  give Z
  Br = bg . A/Q  TOF give bg
  Ion optic tells us:
  Br = Br0(1-(x4-Mx2)/D)
  position measurement we get the Br of the particule
  A/q is know, Z=Q at high energy  A/Q

## Slide 11: Example

## Slide 12: Full identifciation

## Slide 13: Early science configuration
Super-FRS: should have data reduction
FMF2, 2 TPC, 1 plastic
 up 1e6 particle per second
FHF1, 2 TPC, 1 plastic,
1 MUSIC
1e3 particle per second

## Slide 14: DAQ request
Need to correlate event per event for a given focal plane
Need to measure between focal planes event per event
Need to correlate with DAQ of experiment

## Slide 15: DAQ for experiment
Use NUSTAR DAQ (TDR 2016)
Evolution of MBS (currently two branches, MBS from EE and DRASI from Goeteborg)
FRS operation today: mostly VME crates, readout with MVLC or PCI from EE
   allows time stamped synchronous readout
   allows easy integration of asynchronous reaoudt with time stamp
  time stamp protocol, general is WR (VETAR/PEXAR modules from EE)
   local time stamp from trigger/logic module derived from WR (ratatime)
DESPEC uses MBS, similar hardware + “full readout system” TRD from Daresbury
R3B similar hardware, similar DAQ, with more complex front end (some asynchronous)

## Slide 16: Example of event

## Slide 17: Example of DAQ for experiment and FRS
DAQ 2020

## Slide 18: Main point - conclusion
Super-FRS will have high performance tracking detectors permiting event per event tracking on serval focal planes  needed for experiments
Those detectors are readout in the “complex” DAQ of NUSTAR
higher order optical correction need to be implemented and will require precise position/angle/beam envelop at several focal planes
all magnets controls are on the ACO network
 Need way to talk to each other