## Slide 1: The Scintillation Tile Hodoscope (SciTil)
1
Motivation
  Event timing/ event building/ software trigger
  Conversion detection
  Charged particle TOF (relative timing)
Requirements, Simulations
Prototype
Mechanics
Work packages
C.Schwarz
on behalf of the SiPM Group at GSI
(given by A. Sanchez Lorente, HIM, Mainz)
SciTil
SiPM workshop EU(HP3) 16. Feb. 2013, Vienna

## Slide 2: Panda Detector
2
PANDA interaction rate:
Average 20MHz
Peak 50-100MHz
Endcap
Barrel
endcap disc DIRC
barrel DIRC
Beam
barrel SciTil
FW end cap disc SciTil
BW end cap disc SciTil

## Slide 3: Event timing
3
Time between successive events are not equally spaced
but follow a exponential distribution : avg ~ 10 ns
On this time scale : all data collected to form data package
63% most likely below
average

## Slide 4: Event timing
4
Klaus Götzen,Influence of Particle Timing on Event Building
PANDA collaboration meeting March 2011, GSI
Events 1,2,3,4,5,6,7,8... for 50Mhz interaction rate with 6 tracks
t0
ti , σt

## Slide 5
5
Fast detector assigns
accurate time stamps
to tracks.

## Slide 6: Conversion detection
6
DIRC
EMC
1%
17%
SciTil
Conversion of gammas within the DIRC
can be detected with the SciTil

## Slide 7: Relative timing
7
TOF
TOF
PANDA has no start detector
SciTil important for relative timing and PID

## Slide 8: Scintillator Material
8
For subnanosecond timing: timing on first arriving photon
→ Time resolution depends on number of photons.
Time spread of first photon (RMS) for many events ~1/N
tD=2.2 ns
Pure exponential:
Unfortunately
→ not so simple...
Simulation

## Slide 9
9
Rise time comparable to wanted time resolution
→ Additional smearing of first photon
Rise time + exponential:
tD=2.2 ns
tR=0.9 ns
Time spread of first photon (RMS) for many events ~1/sqrt(N)
BC-408
Simulation
BC-408: 100 ps
100 photons

## Slide 10
30 x 30 x 5 mm3 → 115 photons
20 x 20 x 5 mm3 → 180 photons

## Slide 11: Slitrani simulations
11
Stefano Casasso, University of Turin
Summerstudent program GSI 2010
20 x 20 x 5mm3
Simulations agree
with above rough estimates

## Slide 12: Prototype
12
BC408
20 x 20 x 5 mm3
Hamamatsu SiPM
S10931-050P
S10362-33-050C
Photonique
Fast amplifier 611
Readout
NINO + HADES TRB

## Slide 13
13
SciTil
GSI, CERN DIRC prototype beam times
---> SciTil time resolution of 600ps :(

## Slide 14
14
Timing resolution of 3 detectors
Measure t1-t2, t1-t3, t2-t3 , t1→ s212 s213 s223 s21
And subtract 2s2electr. → s2'12 s2'13 s2'23
1
2
3
CFD
NIM-ECL
TDC
Stop
Start
s21 = s2electr.
s2'12 + s2'13 - s2'23 = (s21 + s22 )+ (s21 + s23 ) - (s22 + s23 )
= 2 s21
For 4 detectors each s2 can be determined several times
→ error bars

## Slide 16
16
Calibration of QDC spectra with PicoQuant laser to count photons
Bias off

## Slide 17
17
2
Fast
AMP611

## Slide 18
18
Time resolution including electronic time jitter
We see the right number of photons

## Slide 19
19
Electronic time
Resolution
(FTA820/CFD/ NIM-ECL converter)
90Sr source, results corrected for electronic time resolution
High gain
AMP604
most promising

## Slide 20
20
Scintillator Tile Detector Geometry
Low material budget :1% radiation length
Four tiles arranged with their SiPMs for densest packing:
A quad module with a R&D PCB based on 8-channel readout ASIC and a data transfer chip.
Supermodule : (3X30) 90 quad modules on top of a DIRC bar box.
Entire SciTil half barrel composed of 8 super-modules
DIRC
SciTil
Notes: 20
20
Einfachen hyperkernennen hingegen lassen sie doppelhyperkernen nur ersten durch den elektromagnetischen
Zerfall ihren angeregten zuständen und wenn dern kern den grundzustand erreicht hat, durch
Den mesonischen und nicht mesonischen zerfall ihre geladenen zerfallsprodukte.
Letztendlich durch hadronischen Zerfall.
Hadronische und mesonische Zerfälle:meist nur Grundzustand

## Slide 21: Mechanics
21
Readout at two positions
more photons
less light path fluctuations
larger detection efficiency
Quad module
With electronics
8 ch. ASIC
data transfer IC

## Slide 22
22
Super-module = 90 quad modules
16 super modules
outside of DIRC barrel
3 x 30 quads
Total
5760 SciTils
Cooled by dry air
Radial thickness
1.8 cm

## Slide 23
23

## Slide 24
Simulation within the PANDARoot Framework
Raw MC information :
UrQMD generator :300 events, mult ~ 10 particles/event
PndDrcBarPoints
PndScitPoints
An event takes place at a certain to . The generated particles travel for some time with a certain velocity v before they hit a timing detector.
Each particle creates a signal at wall clock time ti. Assuming that the track length s can be provided the time of origin t0,i is equal to ti – s/v .
Uncertainties can be assumed gaussian, so these values are distributed around event to with a total time resolution σt .
Hit Position corresponds to the center
point of each scintillating tile in the submodule
Time is smeared by the expected resolution of the detector ~ 100ps
Notes: 24
Der polarwinkel theta.
Der nachweiss des antihyperon und seine assoziierten kaonen erfolgt unter dem winkelbereich von 0-45grad.
2. Geschieht zwischen 45-90
3. Wird bei ruckswartswinkeln nachgewiesen wo der hadronische untergrund geringer ist.

## Slide 25
Ideal Hit Information
PndBoxGenerator ~3000 p events
P = 1 GeV/c, theta = 70 ° , phi = 40°
Smearing of MC time t by a
TMath::Gauss (t0 + s/v, σt = 100ps)
Notes: 25
Einfachen hyperkernennen hingegen lassen sie doppelhyperkernen nur ersten durch den elektromagnetischen
Zerfall ihren angeregten zuständen und wenn dern kern den grundzustand erreicht hat, durch
Den mesonischen und nicht mesonischen zerfall ihre geladenen zerfallsprodukte.
Letztendlich durch hadronischen Zerfall.
Hadronische und mesonische Zerfälle:meist nur Grundzustand

## Slide 26: TODO : Real reconstruction Hit Collection
Light output of scintillator :
Time resolution depends on
number of photons
Signal response of a SiPM
has to be accordingly parametrized.
t0
ti , σt
PndSciTHit.h Hit Position corresponds to the center
point of each scintillating tile in the submodule
Time : precise timestamp (after Amp. and Disc.) is generated
for each valid hit.
Notes: 26
Der polarwinkel theta.
Der nachweiss des antihyperon und seine assoziierten kaonen erfolgt unter dem winkelbereich von 0-45grad.
2. Geschieht zwischen 45-90
3. Wird bei ruckswartswinkeln nachgewiesen wo der hadronische untergrund geringer ist.

## Slide 27: Work Packages
27

## Slide 28: Summary
28
SciTil for
  Event timing/ conversion detection/ relative time
Prototype works
  AMP604 pre-amps give right time resolution
  Number of photons agrees with estimates
A simple ( only Scintillator tile, no electronic) geometry detector based on the Scintillator tile hodoscope detector proposal has been implemented within the Pandaroot Framework
A more complex hit reconstruction including R&D is in progress