## Slide 1: STS Readout Developments Final Boards for STS Integration: STS-ROB, RPOB, FPOB
J. Lehnert, R. Kapell, P. Semeniuk
46th CBM Collaboration Meeting
Tue. 21.10.2025
S
T
S

## Slide 2: From CROB to STS-ROB
STS Readout Chain
1752 FEB8 with 8 SMX ASICs
  1-5 uplinks 320 Mbps uplinks (9.4-47 MHits/s/link; 73-367 kHits/s/channel)
  common clock and downlink
576 ROB3
  data aggregation from 40 uplinks ( 1-5 FEB8 )
76 CRI (8 ROB3 each)
  data readout, controls, TFC
Common Readout Board (CROB)
full required ROB3 functionality for STS
in use since 2018 (mCBM and test setups)
  up to 7 boards in mSTS
  also mMUCH, mTRD1D, (mTRD2D), mMVD
Irradiation at 1st STS station
Rad. Hard GBTX and VTRX
STS-ROB
FEB8_1/2
CRI1
CROB
mSTS Data Rates
significantly smaller form factor
https://arxiv.org/abs/2505.20517
mSTS Reconstructed Space Points
O(kGy)

## Slide 3: STS-ROB Design
STS Readout Board
same GBTX/VL functionality as CROB
size: 201 mm x 36 mm (CROB: 208 mm x 199 mm)
powering: FEAST_MP off-board
commissioning: configuration and monitoring off-board
hardwired configuration pins
re-arrangement of GBTX/VL locations
FEE connector: 200pin
  Samtec SEAF-20-05.0-S-10-2-A-K-TR
  elinks required for STS, MVD
  custom pinout
STS-ROB PCB
14 layer design
components on top and bottom layer
5 inner signal layers
  impedance controlled (100 ohm differential)
elinks between master(25), slave GBTX(17) and FEE connector
Assembled STS-ROB
Assembled STS-ROB with VTXx and FMC
Inner Signal Layer
FMC_11111
FMCs
addon board for various FEE connectivity
  ZIF connectors for each FEB8
first type FMC_11111 ( 5 x FEB8_1) - used for full FEE connectivity tests
7 types in total (no readout cable crossing)
  FMC_11111
  FMC_122 and FMC_221
  FMC_1112 and FMC_2111
  FMC_5(t) and FMC_5(b)
FMC_122 PCB (Top)
Layout: R.Pursch (GSI/EE)
Slave GBTX
Master GBTX
Slave GBTX
GBT SCA
VTRX
VTTX
FEE Conn.
for
FMC
LV In
readout cables
LC fibers

## Slide 4: STS-ROB Testing
STS-ROB Testing and Characterization
extensive evaluation of operational functionality and data transmission
focus on features modified wrt CROB
  layout related
optimization of selected components
Powerup/Startup/Reset
Efuse Configuration
Onboard LV Filtering
External Power Supply
voltage drops
operational V range
stability
Signal Integrity
Transmission Error Rates
SCA Monitoring
STS-ROB Testing
ROB Temperature Monitoring no active cooling
VDDRx/VDDTx Inductances
FEE Clock
FEE Downlink
Elinks
Optical
links
Startup: 1.5V and var.ious ResetB settings
Operation at var. VDD
Addon Board for
Commisioning
I2C
efusing
monitoring
No relevant issues observed

## Slide 5: STS-ROB Integration
Power Dissipation and Temperature (Uncooled!)
GBTX ASIC with Cooling Interface and Thermal Pad
STS-ROB Mechanical Mount
Side View of STS-ROB Unit with Mech. Mount, FMC and VTXx
STS-ROB Unit
Mechanical Mount and Cooling
STS-ROB PCB screwed to mechanical support fin
  components towards fin
interface with thermal pads to all power dissipating devices
  structured surface to accommodate height differences
dissipated power ~5W  factor 4 lower than on FEB8 fin
mechanics designs: O. Vasiliev (GSI/DTL)

## Slide 6: FPOB and RPOB Powering
Frontend Board Powering
8 FEB8 per FPOB
1 x 2.4V and 1x 3.0V FEAST_MP per FEB8
LDOs on FEB for 1.2V and 1.8V
each FEB8 and its FEAST_MP on corresponding sensor bias potential up to +/- 250V
used in mSTS
Powering for STS Frontend Boards and Readout Boards
radiation tolerant FEAST_MP (CERN) DCDC converter
  custom CBM form factor
installed on dedicated Powering Board (PoB)
Readout Board Powering
1 x 1.5V FEAST_MP per ROB
1 x 2.5V FEAST_MP per 2 ROB
1 LV channel per 3 ROB
4 ROB per RPOB
short (4-8cm) LV cables
all RPOB and ROB on common GND
FEAST_MP
CBM form factor
Assembled FPOB
Assembled RPOB
FPOB Internal Layer: Thick Traces
FPOB Internal Layer: Split Planes
RPOB with FEAST_MP and L-Cooling Fin
(3D printed mockup)
Schematics
FEAST_MP Unit
FPOB with Sumida LV cables to FEBs
FPOB Isolation Test 500V
8 LV ch. IN
2 LV ch. IN

## Slide 7: The ROB/POB Stack
1.4 m
2.3 m
1.0 m
C-Frame
STS Box with
20 C-frames
ROB/POB Stack (Top or Bottom)
FPOBs
ROB/RPOB
Units:
4 x ROB
1 x RPOB
Backend Inteface: LC Fibers to CRI & LV IN
Frontend Inteface: Readout Cables & LV Cables
ROB-FPOB
Overlap
Unified Cooling Plate
STS-ROB on ROB/POB Stack
ROB mounted on top or bottom of fin
  only one ROB version (no symmetric twin needed)
ROB-FMC with ZIF connectors on top/bottom
  two cable types (same/opposite side contacts)

## Slide 8: Status
components for full STS readout and powering developed, built, tested
  STS-ROB, RPOBs, FPOBs, FMC_11111 (FMC_122 in the next days)
sufficient boards available for integration of first C-Frame
when mechanics components available
  characterization of cooling performance
  assembly of first ROB/POB stack
some additional characterization work
  extended BER tests
Rev.2 with minor modifications
  mostly optimizations for series assembly and testing
Production Readiness Review for STS-ROB and RPOB, FPOB
  successfully done last Thu. 16.10.25
  https://indico.gsi.de/event/23248/
ROB and POB devices
for first C-frame