## Slide 1: CBM DCS Detector Control System OVerVIEW
Peter Zumbruch, GSI
Oct 21, 2025

## Slide 2: Project Lead
Min Li, IMP CAS
  Among others Development of Control System of CEE (next talk)
Peter Zumbruch
  HADES controls

## Slide 3: Purpose & Objectives
Ensure the proper and safe operation of the experiment
  but excluding human safety, interlocks, emergency shutdown systems, safety instrumented systems (SIL)
    Task of DSS Detector Safety System
Deliver a modular, scalable, distributed, DCS on basis of EPICS, (Experimental Physics and Industrial Control System) across multiple detector units
Ensure each detector must be able to run stand-alone for testing or fallback, incl. Alarm and Archive
Each detector's distributed DCS is integrated into the hierarchy of the Experiment Control System (ECS) below the Control Agents, alongside the Readout Controls system
Replace existing local solutions by common, maintainable solutions
  If feasible take local solutions into account and integrate
Leverage and integrate building blocks of the existing external DCS‘s where feasible (e.g. ACC)
Enable real-time monitoring, control, and data exchange with other industry PLC based systems (Magnet, Cryo, Gas)
Persistantly store data and thus enable DAQ and Analysis to perform (online) usage of DCS data
Provide intuitive operator HMIs via EPICS tools and/or web-based Applications
Maintainability and wide knowledge base via comprehensive documentation, open-source, training, and long-term support

## Slide 4: Modular, Scalable, Distributed ...
Expected no. of Process Variables » 105 (HADES) up to O(107)
EPICS, proven at many sites as mature tool,
  long-term, open-source, large collaboration, big players (e.g. ESS, ITER)
Containerization / Virtual Machines
Detector focussed segration of DCS networks
Configuration Database driven
  automatic and reproducible, template based
    IOC setup
  tag based data-settings

## Slide 5: Scope
SCA + DCA
DCS
Gateway
DAQ
…
,
DAQ
DAQ
DAQ
DAQ
DAQ
DAQ
DAQ
DAQ
DAQ
DAQ
IOC
“per detector“
(time-series)
Database
Performance
Database
Configuration
TOF
FSD
BMON
MVD
STS
TRD
RICH
MUCH
Common
Magnet
DAQ
Other Clients
Aggregation
GUI/HMI
Analysis
EPICS IOC development for Detectors
Integration interfaces between EPICS and higher ECS
  Sub-detector Status
  Sub-detector Tasks
  Automatic configuration & setup
  database setup for performant data storage (archiver) and retrieval
Communication layers to PLCs (OPC UA, Modbus, MQTT)
Task/signal survey and control-logic mapping
Containerization and orchestration of all services
  based on configuration databases local to the detector
Security, archiving, alarm, and data-aggregation subsystems
Segregated, subdived Network architecture
HMI/GUI development (support) for sub-detectors
(time-series)
Database
TARGET
Status request / direct access
CA/PVA
State machine
ECS
TIG

## Slide 6: make use of experience at CEE ...
See next Talk:
  DCS CEE, M.Li, IMP
    https://indico.gsi.de/event/20881/contributions/93864/
(Slides from previous presentation 2024)

## Slide 7: CEE … evaluate what can be used, adopted
After
  getting the status quo and needs of the detector systems
    during CBM DCS Workshop April 2025
    Detailed survey
But not forgetting/ignoring the existing local built-up expertise and work

## Slide 8: Status quo The survey
Stakeholder contacts
DCS Workshop April 2025
Survey

## Slide 9: Stakeholders
External DCS Provider:
  GSI Accelerator
  CBM ECS System
PLC Vendors:
  Magnet Control System
  Gas Control Systems (Mladen, GSI ACC)
End Users/Operators:
  CBM groups
  CBM Analysis
  DAQ/Fles
Hardware / IT support
  CBM / GSI IT Hardware experts
    e.g. D.Emschermann as contact ?
Project Leader:
  Min Li (IMP, CAS)
  Peter Zumbruch (GSI)
Subproject Contact Persons
  BMON – J.Pietraszko, GSI
  Target – NN (P.Dahm,?)
  Magnet – NN (P.Senger,?)
  MVD – C.Müntz, IKF
  STS – D.Gutierrez Menendez
  RICH – C.Pauly (Wuppertal), F.Hollfoth (Gießen)
  MUCH
    GEM – NN (A.Dubey)
    Straw - NN
  TOF – E.Rubio, Heidelberg
  TRD – D.Schledt, Münster
  DAQ/FLES (DAQ coordinator)
  FSD – NN (P.Chaloupka, ?)

## Slide 10: Status quo The survey
Sent to known contacts
Quite complicated to fill out
Next to evaluate and combine with detector system reports from DCS Workshop

## Slide 11: Timeline & Milestones
Project Kickoff
  assign leaders
  define scope
Contacts, Task & Signal Survey
  Ongoing, send out,
Survey evaluation including timing request
  Until CM 2025/Lanzhou
Existing CEE DCS Evaluation
Design consideration of data sources/sinks
  e.g. Archiver Data Base / DAQ resources / grafana
Choice of Pilot detector
  small and/or mature
EPICS Architecture & Interface Design Consolidation
Code Infrastructure setup (gitlab)
Hardware platforms choice & procurement
Hardware setup
  including network hierarchy
parallel per System, continously integrating
  IOC Development/Configuration per Unit
  HMI/GUI Development
  System Integration & Testing
  Documentation & Training
  Final Deployment
  Post-Deployment Review
Interface consolidation to external Users/ECS/DCS/CS

## Slide 12: Database
First Project (M.Li et al.)
  setup timebased high-performance database prototype
DCS
Gateway
,
Database
Configuration
GUI/HMI
Analysis
Status request / direct access
CA/PVA
State machine
(time-series)
Database
DAQ
DAQ
DAQ
DAQ
DAQ
IOC

## Slide 13: DCS Working Group Session
Going into Details …
Getting in contact with the IMP Team
Status, Feedback, plans, ...
Wednesday 15:00 – 18:00
  https://indico.gsi.de/event/20881/contributions/93946/
  666 Meeting Room, 6th floor, No. 6 Building, IMP

## Slide 14: Upcoming talks
IMP
  Introduction to DCS of CEE
  Related Activities of IMP Group
STS
  Needs on Controls

## Slide 15: Upcoming talks
IMP
  Introduction to DCS of CEE
  Related Activities of IMP Group
STS
  Needs on Controls
Thank you.

## Slide 17: Addendum

## Slide 18: Deliverables
EPICS-based control system per unit
External DCS interface
PLC communication layer
Operator HMIs (CSS/Phoebus)
Task/signal survey docs
Training materials & manuals
Aggregated status reports to higher ECS tiers
keyword triggered automatic configuration setup
persistant database (configuration and archive)
  efficient data retrieval for HMI, Clients, DAQ and Analysis
Access control
Network segregation via EPICS gateways, per Detector system
Data archiving
Alarm handling
Data aggregation
Stand-alone operation capability
Containerization (e.g., podman, singularity)
Orchestration (e.g., Kubernetes)

## Slide 19: Risks & Mitigation
Risk | Mitigation
Incompatibility with external DCSs | Early evaluation & prototyping
PLC communication delays | Proven protocol bridges & rigorous testing
Resource bottlenecks per unit | Dedicated subproject leaders
Scalability challenges | Container orchestration & auto-scaling policies
Data volume overload | Shared and modularized archiving backend & optimized queries

## Slide 20: Success Criteria
Reliable, real-time control across all units
Seamless integration with external DCS and PLCs
Operator satisfaction with HMIs & alarms
Independent operation of each detector
Stable performance with 10 million+ PV load
Complete documentation, training, maintainability plan
Notes: https://copilot.microsoft.com/shares/i97mDTLZBVQxszfTqqbSc