## Slide 1
RDMA-based Data Transmission System Prototype
  Yuqiao Zhang , Min Li, Kai Zhou, Kejie You, Han Zhang
  Institute of Modern Physics（IMP）
  October 21, 2025

## Slide 2
CONTENTS
Introduction of RDMA Data Transmission System
Preliminary Application of the System
Software update & optimization
Conclusion

## Slide 3
Why We Choose RDMA Technology
CEE: CSR External-Target Experiment, it will be the first-large nulclear physics experimental device at HIRFL-CSR, heavy-ion collisions
The experimental requirement for real-time data transmission throughput is > 5 GB/s.
The network communication is implemented using the TCP/IP infrastructure
Notes: As you can see, the CEE network architecture adopts a three-layer structure. Some relevant communication protocols used, such as EPICS CA and ZeroMQ, are built on the TCP/IP nfrastructure, so the TCP is the cornerstone of CEE network communication.

## Slide 4
Traditional TCP solutions : cross-machine data-copy, kernel scheduling jitter, and tail latency.
Infiniband/RDMA has become the "standard component" in HPC and large-scale science.
Many institutions choose RDMA as a performance boost solution for their next-gen data transmission systems.
Why We Choose RDMA Technology
ESRF’s RASHPA framework
FELIX-RDMA
STARLIGHT Transmission Architecture
Notes: Computer and electronic communication tech is getting better all the time, when we comes to high-throughput data transmission, the old TCP protocol starts having problems and bottlenecks.
For reference, a lot of major research institutions choose RDMA as a performance boost solution for their next-gen data transmission systems, And Infiniband/RDMA basically becomes a "standard part" now for HPC and large-scale science projects

## Slide 5
Design of RDMA Data Transmission System
Composed of control path and data path;
control path handles low-frequency kernel operations, data path managing high-frequency transmission
Basic data flow
Control path and Data path
Notes: So because of this, we designed and built a prototype RDMA data transmission system for handling the growth of data transmission in the future.
The basic idea behind the design is this: the network card does direct DMA to the pre-registered memory of the process, and moves data directly.
The system uses a two-channel structure: RDMA for the data side and TCP/HTTP for the control side. The control side handles low-frequency operations, while the data side takes care of high-frequency ones.

## Slide 6
Design of RDMA Data Transmission System
Combined with network communication models, the system architecture is designed in layers
System Layering
Kernel Bypass
Programmed I/O, Doorbell, Memory Mapping, DMA
Basic System Structure
Notes: Building on the classic network model, we designed the transport system's layered structure.The user-mode subsystem is on top. It handles interactions between upper apps and lower hardware.The kernel-mode subsystem is Linux's RDMA kernel framework and NIC drivers , let apps access devices via Verbs.
We also use Programmed I/O, Doorbell, Memory Mapping, DMA and other mechanisms to bypass the kernel for data movement.
As for Application basic sysytem structure, We split the user-mode app into six functional modules that work together. They cover the full process from data acquisition to high-speed transmission.

## Slide 7
The sender node connects to the accelerator network to acquire PVs and transmit it to the CEE DCS
Data Transmission Test
Configuration | Sender/Receiver
CPU | Core i7-10700
Thread/Core | 8 cores / 16 threads
Memory | 16GB
Memory frequency | DDR4 2667MHz
Operating system | Ubuntu64 20.04
Network Card | M2890-2QSFP200G
Driver | MLNX_OFED_LINUX-5.8-3.0.7.0
Transmission medium | Optical fiber
EPICS base | 7.0.4.1
Pylon | 5.0.12
one sender and one receiver node with identical hardware and software conditions
Notes: Once we designed and built the system, we ran initial tests to check the systems’ performance advantages.
2 servers were connected(one on as sender the accelerator network, the other as receiver on the CEE DCS network) via optical fibers , we conduct cross-network PV data transmission situiation.

## Slide 8
Conduct preliminary tests to compare the data transmission performance of RDMA and traditional TCP transmission systems.
Three performance metrics: Latency, Throughput, and CPU Utilization.
4KB
2KB
1KB
512Byte
256Byte
128Byte
64Byte
8KB
16KB
32KB
64KB
128KB
Data Transmission Test
Avergae Latency comparison
Notes: Set the RDMA data transmission system as the experimental group and the TCP one as the control group. We compared them across three performance metrics: latency, throughput, and CPU utilization.

## Slide 9
Three performance metrics: Latency, Throughput, and CPU Utilization.
Throughput comparison
Average CPU utilization comparison
RDMA reduced latency by 96.3%, increased throughput by 95.1%, and lowered CPU utilization by 85.6% compared to TCP.
Data Transmission Test
μavg: overall average improvement, the interval [i,j]: the range of lengths for the data packets,
Q: the test value of RoCE, P: the test value of TCP, N: the number of different packet lengths.
Notes: We used an "average performance improvement rate" formula to calculate the overall average improvement for each performance metric. After transmitting over 100,000 data packets and analyzing the results, we found that:
RDMA reduced latency by 96.3%, increased throughput by 95.1%, and lowered CPU utilization by 85.6% compared to TCP.
This initially proves the system’s performance advantages over traditional network transmission protocols.

## Slide 10
CONTENTS
Introduction of RDMA Data Transmission System
Preliminary Application of the System
Software update & optimization
Conclusion

## Slide 11
Imaging System for the Laser Wakefield Electron Accelerator at SIOM
Real-Time Image Acquisition & Transmission: Integrates camera control and real-time high-bandwidth acquisition for fast image transmission
Trasnmission Pipeline
FRAME_META
GUI of the Imaging System
Notes: We’ve applied this system to the "X-ray Imaging System" project in collaboration with Shanghai Institute of Optics and Fine Mechanics. To achieve real-time camera control image acquisition and transmission.
Based on the control and data path design I’ve illustrated before, we built a transmission pipeline using a pair of lock-free ring buffers in the memory registration area.
And custom transport layer protocol header (FRAME_META) includes meta info like data source ID, sequence number, data index and timestamp. The client parses and converts data using the header to ensure accurate storage.

## Slide 12
Imaging System for the Laser Wakefield Electron Accelerator at SIOM
microsecond-level latency dispersion
stable transmission pipeline
stable latency distribution
The results show this system has industrial stability and feasibility.
Notes: We evaluated server-side RDMA send “post-to-completion” batch latency under a unified methodology.
Looking at each camera stream, we saw this: at the 2Hz trigger frequency, all data streams had a steady rhythm and microsecond-level dispersion. The transmission pipeline stayed stable too, this shows the RDMA stack is nowhere near its capacity limit under this configuration and load.

## Slide 13
CONTENTS
Introduction of RDMA Data Transmission System
Preliminary Application of the System
Future Work
Conclusion

## Slide 14
Future Work
Implementation of the FPGA-RDMA transmission model and apply it to the general data transmission
FPGA-RDMA data flow
FPGA-RDMA basic architecture
Notes: The construction of a "hardware acceleration + protocol optimization" dual-driven technology system has been launched, to implement a universal FPGA-RDMA data acquisition and transmission framework for detectors, which is planned to be applied to the data acquisition system of the next-generation particle detector.

## Slide 15
CONTENTS
Introduction of RDMA Data Transmission System
Preliminary Application of the System
Future Work
Conclusion

## Slide 16
Conclusion
A RDMA-based Data Transmission System Prototype was designed and implemented. Compared with the traditional TCP transmission mode, its performance advantages were verified.
It was applied to the X-ray imaging system of the laser accelerator, realizing stable parallel processing of pipeline tasks and verifying its industrial reliability and applicability in large-scale physical experiments.
Implement a universal FPGA-RDMA data acquisition and transmission framework for detectors.

## Slide 17
Thank You Very Much !