## Slide 1
RBAC @ GSI
Current State & Outlook

## Slide 2
RBAC : Role-Based Access Control
  CERNs developed solution for providing a sufficient level of device access security
  Fully integrated into the CMW RDA library
  Originally deployed at LHC, but used widely nowadays
Motivation behind RBAC *:
  Protects against human mistakes
    A well meaning person from doing wrong thing at the wrong time
    An ignorant person from doing anything at anytime
  Can be deployed anywhere in the Controls Infrastructure
  Aims to enhance the overall Machine Safety
  Provides Authentication (A1) and Authorization (A2) services
  Does not prevent hackers from doing damage
What is RBAC
* taken from CERN Presentation slides

## Slide 3
Architecture
Authentication
  User can be authenticated with password or location
  RBAC Server returns a token containing a list of associated roles
Authorization:
  Application sends token to CMW (FESA) when connecting
  FESA verifies token signature once and uses the credentials for every subsequent request
  CMW checks access map to authorize a request

## Slide 4
User Perspective

## Slide 5
Database
  Database is available but, mostly, empty
  Will be filled gradually when use-cases are defined
Server
  Source code adopted for GSI and is up and running
  Connects to ACC LDAP
    Controls Account required for personal authentication
Client
  JAVA and C++ clients are available at GSI
    Will be integrated into new FESA and YOCTO based devices
Summary
  Technically RBAC components are available and can be used
  First simple Use-Cases are in elaboration
Components and state @ GSI

## Slide 6
Definition of a basic Roles and Rule Concept for the operation (ongoing)
  Can and will be refined in the future
  Input from Operations group is required
Step-by-Step integration into the operation
  Understanding the actual GSI needs and use cases
  Identify and address technical shortcomings
  Refining of the Rule concept
  Definition of responsibilities
  etc.
Next Steps

## Slide 7
Questions ?