## Slide 1
G. GIRAUDO - D. ORECCHINI
Beam-Target line for PANDA – GSI – 4 February 2013
Central Trackers assembly sequence
and Interface with cross-pipe - draft proposal -

## Slide 2
ASSEMBLY SEQUENCE
Beam-Target line for PANDA – GSI – 4 February 2013
Preliminary work in a Clean Dedicated Area
  Auxiliary Support Structure + Dummy Rails Aligned
  (Survey Service Assistance)
G. GIRAUDO - D. ORECCHINI

## Slide 3
ASSEMBLY SEQUENCE
Beam-Target line for PANDA – GSI – 4 February 2013
G. GIRAUDO - D. ORECCHINI
Preliminary work in a clean Dedicated area
  Auxiliary Support Structure + Dummy Rails Aligned
  (Survey Service Assistance)
  Central Frame on Rails

## Slide 4
ASSEMBLY SEQUENCE
Beam-Target line for PANDA – GSI – 4 February 2013
G. GIRAUDO - D. ORECCHINI
Preliminary work in a clean Dedicated area
  Auxiliary Support Structure + Dummy Rails Aligned
  (Survey Service Assistance)
  Central Frame on Rails
  Clamps Open

## Slide 5
ASSEMBLY SEQUENCE
Beam-Target line for PANDA – GSI – 4 February 2013
G. GIRAUDO - D. ORECCHINI
Preliminary work in a clean Dedicated area
  Auxiliary Support Structure + Dummy Rails Aligned
  (Survey Service Assistance)
  Central Frame on Rails
  Clamps Open
  Cross Pipe Mounting and Alignments

## Slide 6
ASSEMBLY SEQUENCE
Beam-Target line for PANDA – GSI – 4 February 2013
G. GIRAUDO - D. ORECCHINI
Preliminary work in a clean Dedicated area
  Auxiliary Support Structure + Dummy Rails Aligned
  (Survey Service Assistance)
  Central Frame on Rails
  Clamps Open
  Cross Pipe Mounting and Alignments
  Clamps Close

## Slide 7
Beam-Target line for PANDA – GSI – 4 February 2013
ASSEMBLY SEQUENCE
Cross Pipe – CF Interfaces (existing design)
Clamping Sleeve must be integrated with the Target Arm
Clearance Sleeve/CF  CRITICAL
Relative Orientation, Coaxiality  CRITICAL
Position of the horizontal pipe  CRITICAL
New Solution must be evaluated
G. GIRAUDO - D. ORECCHINI

## Slide 8
Beam-Target line for PANDA – GSI – 4 February 2013
ASSEMBLY SEQUENCE
G. GIRAUDO - D. ORECCHINI
Preliminary work in a clean Dedicated area
  Auxiliary Support Structure + Dummy Rails Aligned
  (Survey Service Assistance)
  Central Frame on Rails
  Clamps Open
  Cross Pipe Mounting and Alignments
  Clamps Close
  MVD & MVD’s cooling + electronics assembly
GBT set Fixed on Flange & CF

## Slide 9
Beam-Target line for PANDA – GSI – 4 February 2013
Manufacturing tolerances
  Assembly tolerances
    0.8 mm clearance between beam pipe and disks
ASSEMBLY SEQUENCE
G. GIRAUDO - D. ORECCHINI

## Slide 10
Beam-Target line for PANDA – GSI – 4 February 2013
ASSEMBLY SEQUENCE
G. GIRAUDO - D. ORECCHINI
Preliminary work in a clean Dedicated area
  Auxiliary Support Structure + Dummy Rails Aligned
  (Survey Service Assistance)
  Central Frame on Rails
  Clamps Open
  Cross Pipe Mounting and Alignments
  Clamps Close
  MVD & MVD’s cooling + electronics assembly
  STT & STT’s electronics assembly

## Slide 11
Beam-Target line for PANDA – GSI – 4 February 2013
ASSEMBLY SEQUENCE
ADDITIONAL SUSPENSION MUST BE ADDED Auxiliary support structure must be extended
G. GIRAUDO - D. ORECCHINI
Preliminary work in a clean Dedicated area
  Auxiliary Support Structure + Dummy Rails Aligned
  (Survey Service Assistance)
  Central Frame on Rails
  Clamps Open
  Cross Pipe Mounting and Alignments
  Clamps Close
  MVD & MVD’s cooling + electronics assembly
  STT & STT’s electronics assembly
  Beam Pipe Upstream Sector (DC-DC Converters)

## Slide 12
Beam-Target line for PANDA – GSI – 4 February 2013
ASSEMBLY SEQUENCE
READY TO MOVE TO THE SERVICE PLATFORM
G. GIRAUDO - D. ORECCHINI

## Slide 13
Beam-Target line for PANDA – GSI – 4 February 2013
ASSEMBLY SEQUENCE
CENTRAL TRACKING SYSTEM SLIDES IN
G. GIRAUDO - D. ORECCHINI

## Slide 14
Beam-Target line for PANDA – GSI – 4 February 2013
G. GIRAUDO - D. ORECCHINI
SUMMARY
The clamping sleeves must be integrated with the Target Arms
  Tolerances (geometry, manufacturing & assembly)
MVD assembly – Possible problem with Beam Arm
  Tolerances (geometry, manufacturing & assembly)
  Beam Pipe Upstream Sector act as DC-DC Converters holder
  Beam Pipe Upstream Sector (DC-DC Converters) must be suspended during assembly and handling
    Interaction with End-Cap EMC during assembly

## Slide 15
Beam-Target line for PANDA – GSI – 4 February 2013
ASSEMBLY SEQUENCE
G. GIRAUDO - D. ORECCHINI
Beam Pipe sector as a whole

## Slide 16
Beam-Target line for PANDA – GSI – 4 February 2013
G. GIRAUDO - D. ORECCHINI
ASSEMBLY SEQUENCE
Whole MVD assembled
2840

## Slide 17
Beam-Target line for PANDA – GSI – 4 February 2013
G. GIRAUDO - D. ORECCHINI
ASSEMBLY SEQUENCE
Upstream pipe sector: (Preliminary) welded support for electronics
Support for cooling pipe still missing

## Slide 18
Beam-Target line for PANDA – GSI – 4 February 2013
G. GIRAUDO - D. ORECCHINI