## Slide 1: Online Tracking Overview & Triplet Finder Status
Marius C. Mertens1,2
Sean Dobbs3, Jim Ritman1, Peter Wintz1
1 Forschungszentrum Jülich
2 Justus-Liebig-Universität Gießen
3 Northwestern University, Evanston

## Slide 2: Outline
  Continuous Online Tracking Overview
  Online Manager Status (Sean Dobbs)
  Triplet Finder Status
  Key Topics for Future Investigations

## Slide 3: PANDA Operating Conditions
  Gap estimate:
    Barrier Bucket: 80% Filling
    HESR length: 575 m
    Antiproton velocity: c
    Revolution time: 2000 ns
    Gap: 400 ns
    Fill/Gap ratio may vary
  Events per revolution  Burst:
    2·107/s·2 µs = 40

## Slide 4: Continuous Online Tracking: Motivation/Concept
  Similar topology of signal and background  No simple criteria with high suppression potential
  Quasi-continuous high-rate operation of PANDA  Overlapping events, stateless pattern recognition started upon simple criteria may process redundant time windows
  Most channel selections require tracking information

## Slide 5: Continuous Online Tracking
Online Tracking
Tracks
Information Merging:
PID, etc
Calibration
Alignment
…
Detector Hits/Digis
Local Clustering
STT Tracking
Global Tracking
Software Trigger
Triplet Finder
Hough Transform
…

## Slide 6: Online Manager Status
  New/faster interface to simulation data implemented
  Fully operational for algorithm testing  Triplet Finder benchmarks
  Under construction:
    Output to ROOT tree
    Event reconstruction
  Release to public as soon as ROOT file output is implemented
Big thanks to Sean for his developments!

## Slide 7: Triplet Finding in Axial Straws
  Find Triplets within pivot straws  Calculate center of mass around pivot straw and adjacent straws with hits
  Once two Triplets are found, calculate circle through origin
  Associate nearby hits with track candidate
Interaction Point
Pivot straws
Pivot straws

## Slide 8: Triplet Finder Status
  First quantitative test with 15 GeV/c DPM
    Full burst processing: 2000 ns
    Animated display in finer granularity: 5 ns
  Raw data results:
Total reconstructed track count: 100179
Reached MC ID: 5130
Reconstructable MC track count: 10679
MC Tracks reconstructed: 5993
Reco Status Good: 13790
Reco Status Bad: 86389
Secondary Tracks: 475
  Results:
    > 50% reconstruction efficiency
    Δφ: < 100 mrad
    Δpt: < 10% (below 450 MeV/c)

## Slide 9: Hitstream Display: 15 GeV/c DPM, 50 ns Mean Time
  Black circles: Early isochrone
  Blue circles: Early skewed isochrone
  Green circles: Close isochrone
  Red circles: Late isochrone
  Black dots: MVD hits
  Green dots: MVD hits r/z > 0.3
  Black+Red dots: Triplets/Skewlets
  Yellow tracks: Vetoed
  Blue tracks: Accepted
XY-View
  DPM Benchmark: > 50% of primary tracks in the STT reconstructed by basic triplet finder
Dual Parton Model (DPM): Standard pp background generator

## Slide 10: Triplet Finder Status
  t0 constraining concept for Triplets and tracks:
Pivot straws
t1
t2
t3
220 ns

## Slide 11: Future Investigations: Fit/Finder Quality
  Association of hits to tracks  Design questions
    Ideal storage for these associations?
    Desired parameters to store?
    Override old values? Store list?
  Parameters for assigned hits/tracks:
    Unassigned
    Bad Hit – Clutter, Noise, etc.
    Low Quality – veto value close to threshold
    Mid Quality
    High Quality – additional quality criterion passed
    Multi Algorithm Confirmed Quality

## Slide 12: More (Online) Tracking Algorithms
Algorithm | Comments
Hough Transform, Yutie Liang | FPGA implementation
Hough Transform, Mohammad Al-Turany/Andreas Herten | GPU implementation
Non-Origin Trackfinder, Lia Lavezzi | Focused on offline, online application(?)
Triplet Finder, MCM | No isochrone info required
Track Segment Finder + Linker, Sean Dobbs | Template based
Fast Combinatorial Finder / Fitter, Sean Dobbs | Based on CLEO‘s SOLO
Forward Hough, Martin Galuska | Focused on offline, applicable for online
Riemann Tracker, Tobias Stockmanns | Focused on offline, online application(?)
Global Tracking in PandaRoot, Gianluigi Boca | Focused on offline
Neural networks pattern reco, Pablo Genova | Focused on offline, applicable for online
Rieman Tracker, Andreas Herten | GPU implementation
Other developments?

## Slide 13: Summary/Outlook
  Online Manager: Implementation of canonical ROOT interface
  Quantitative Triplet Finder benchmark (DPM): > 50% reconstructed tracks
Outlook
  Development of track finder quality bookkeeping
  Currently missed tracks:
    Characteristics need to be investigated
    Triplet Finder adaptions
    Additional algorithms for reconstruction
  Triplet finder resolution:
    Enough for certain selections?
    Other algorithms with higher resolution at momenta > 450 Mev/c?
Thank you for your attention