## Slide 1: COSY/HESR stochastic cooling system developments
06.03.2025 I Rolf Stassen
+ RF-systems

## Slide 2: Cosy status
Most components still installed
Drying of water channels inside magnets started (dipoles finished)
Drying of cavities water channels will start very soon
Beam pipes filled with nitrogen
Dismantling of HESR components (one cavity, one pickup and one kicker) partly started.
Power supplies switched off since more than one year
2MeV electron cooler: SF6 gas was pumped out and safely stored
100keV electron cooler: operated until last COSY runs, great interest from GSI SYS group
BPM: Electronics successful updated with Instrumentation Technology Libera Hadron (accuracy ~ 100µm), Liberas back to GSI
Short summary

## Slide 3: Stochastic cooling system cosy
Pickup and kicker design including λ/4-structures were based on AA-design from CERN (many, many thanks to all the CERN colleagues for their great support).
Changes:
  two band system (1-1.8 GHz, 1.8-3 GHz) instead of three
  Redesign of structures and combiner-boards (single loop instead of double loop, optimized electrodes for COSY beam
  Plunging system based on stepper-motors
  New design of active RF-components
  Smallest group 25cm with progr. delay-lines outside the tanks to cover the whole momentum range (1.5 – 3.7GeV/c)
AD 24 double loops
Lars Thorndahl:
Sum pickup performance comparison between a possible future COSY pickup tank with
48 single loops and the present AD tank with 24 double loops. 2 GeV/c, betaparticle=0.9
COSY tank with 48 AD
single loops

## Slide 4: First stochastic cooling at cosy
First observation of vertical stochastic cooling at COSY twenty-eight years ago.
Vertical beam profiles were measured with EDDA experiment.
Cooling only with band I (1 -1.8) GHz
Gain and phase not optimized at that time
No beam losses

## Slide 5: Stochastic Cooling in the COSY-11 Experiment (September 1998)
Experiment located in one arc -> dispersion, due to energy-loss, beam is shifted from the target
Transverse and Longitudinal Cooling switched ON, energy-loss compensated
Cycle length one hour
Counting rate becomes nearly constant when cooling is ON
System prepared for supercycle (two different energies)

## Slide 6: Experiment with closable storage cell
Transvers cooling very effective to cool halo particles -> reduction of background
Halo particles cooled within 30 sec (total particle number: 1E9)
Start transvers cooling
30 sec

## Slide 7: PU as precise measurement tool
Fractional part of tune, tune spread
Chromaticity (very helpful during commissioning of extraction at higher momenta)
Longitudinal Schottky spectra for monitoring the momentum distribution during the experiment
Estimation of target-thickness (mean energy loss)
Change of emittance during cooling
Optimization of extracted beam

## Slide 8: Longitudinal Cooling Methods tested at COSY
Filter cooling:
TOF cooling:
PK  0
PK  0
Sum
Pickup
Sum
Kicker
Pre
Amp
900
Phase Shifter
Notch Filter
+
+
+
_
Power
Amp
variable delay
Sum
Pickup
Sum
Kicker
Pre
Amp
900
Phase Shifter
+
+
+
_
Power
Amp
1800
Phase Shifter
Filter Cooling:
  Notch Filter discriminates between particles with different momenta. Optimum: no mixing from PU to Ki
TOF Cooling:
  Uses mixing from PU to Ki to discriminate between particles with different momenta.
open connection

## Slide 9: ToF cooling very sensitive against delay change
Initial momentum spread heated to p/p  1  10-3 (rms)
Center frequency moves towards an equilibrium value during cooling that depends on the delay setting
Delay: + 7.5 mm
Delay: adjusted

## Slide 10: Electron cooling with transverse stochastic pre-cooling
Studies electron cooling together with stochastic cooling: simultaneous cooling not possible, but transvers stochastic pre-cooling significantly improves electron cooling

## Slide 11: Cooling of thick targets with the aid of a barrier bucket cavity
Chart: Frequency / GHz
Counting rate
Beam current
Cooling,bb on
Cooling,bb off
The mean energy loss was also compensated by the RF as well, but no
stochastic cooling was visible
and the counting rate was significantly
influenced by the short bunch length
Longitudinal Schottky spectra 1000th harmonics
Initial distribution
After 160s without cooling and barrier bucket
After 160s with stochastic cooling
After 160s with cooling and barrier bucket
Advantage for the experiment:
Quasi dc-beam
Higher duty-cycle

## Slide 12: Polarization life-time with stochastic cooling
Polarisation measured with vertical stochastic cooling on/off and a cycle-length of 30 min.
SC off:
P = 0.75 +/- 0.005
SC on:
P = 0.753 +/- 0.006
Stochastic cooling can be used to achieve long spin coherence times necessary for EDM measurements
First estimations (H. Stockhorst) taking into account the small kicker fields during cooling confirmed the experimental results. Assumption: no spin-resonance condition by kicker fields

## Slide 13: Old stochastic cooling system
Except horizontal pickup, all tanks outside COSY
Reuse at CERN AD checked and rejected
Reuse in RESR/COSY possible but a lot repair needed
  5-phase motors no longer available
  Maintenance of cold head needed
  Some connections to electrodes lost
  Amplifier no longer available
Band 1: 1 – 1.8 GHz, Band 2: 1.8 – 3 GHz
Kicker horizontal | Band 1 | 8,4 Ohm |  |  | Band 2 | 6,26 Ohm |  | 
right | 10,9 | 9,2 | 10,1 | 9,7 | Mohm | 6,60 | 6,5 | 7
left | 8,9 | 8,8 | 9,5 | 10,8 | 7 | 6,7 | 6,7 | 6,4
Kicker vertical |  |  |  |  |  |  |  | 
top | 9,7 | 9,6 | 8,7 | 9,3 | 6,7 | 7,6 | 8,5 | 6,7
down | 8,6 | 9,3 | 9,1 | 9,5 | 7 | 8,3 | 6,7 | 6,7
Pickup V Tank1 |  |  |  |  |  |  |  | 
top | 9 | 20 | 15,8 | 12,3 | 10,1 | 6,6 | 9,5 | 20,2
down |  |  |  |  |  |  |  | 

## Slide 14: SC from cosy to hesr
One reason of SC downtime: motor-driven plunging
Aperture COSY: 140mm, HESR: 90mm
=> Fixed structures for HESR
Printed loop structures – slot-ring structures
h = 12.5 mm
aperture = 90 mm

## Slide 15: Slot ring couplers
Self-supporting structure
No plunging
All three cooling planes with same structures
No aperture reduction
8x50 Ω electrodes for broadband operation
90mm

## Slide 16: Test tank with lambda/4 printed loop structures and slot ring structures
Chart: longitudinal: red slot-coupler, blue lambda/4
Chart: vertical sidebands: red slot-coupler, blue lambda/4

## Slide 17: Pickup tests at COSY
Chart: Slot coupler: red vertical, blue horizontal
Chart: longitudinal parts in vertical transvers signal
Structure vertical moved: 3mm
Structure vertical moved: 4mm
Betatron sidebands measured with the same structure (vertical tune close to 3.5 -> bandoverlap)
16 rings in test-tank cooled down to 30K:
Beta-functions at TP1: Horizontal 5.2 m
Vertical 14 m

## Slide 18: Different slot-ring developments
HESR 4-6 GHz slot-ring coupler with 12 electrodes and first combiner in the structure
(only prototype, replaced by one PU and one KI for lower beta)
2–4 GHz
1-2 GHz
0.4 – 0.8 GHz

## Slide 19: Cooling at nuclotron Dubna
Pickup: 16 rings
Kicker: 16 rings
Filter cooling with optical
Notch-Filter
Ions: D+
Intensity: 2E9
Cooling time: 480s
Initial dp/p: 0.55x10-3
Final dp/p: 0.25x10-3
March 2013

## Slide 20: Developments: Notch-filter
Started with thick foam-filled coax-line: notch-depth only 20dB, dispersion to high
Using air-filled coax-lines: dispersion better, but not notch-depth
Optical notch filter: first only long optical delay line, later whole filter optical (higher notch-depths, no dispersion -> lower momentum spreads possible)
Most changes over the years

## Slide 21: active control of fibre length
Pilot signal added to PU signal
parallel transfer through both optical paths
Phase comparison after band pass filter
Control of adjustable delay line
(Amplitude control by new optical attenuator with included power meters)
HESR: h~ 0.06; Dp/p ~ 2E-5 => Df/f ~ 1E-6 Higher slope of notches required Fibre: 30 ps/km/°C; Dt < 2ps => Temp-control < 0.16°C or
=> phase control circuit with pilot signal
Single mode fiber have a high temperature coefficient

## Slide 22: First measurements with simple control loop
Chart: Date

## Slide 23: Adjustable optical delay-lines
A. Kononov, N. Shurkhno: A precise opto-mechanical free
space delay line with a delay range of 0-700 ps and a resolution of 1 fs and an optical step delay with a delay range of 0-127.5 ns and 0.5 ns step. Thus, the total delay
range of the OPDM is 128 ns. Device is temperature and attenuation compensated.
Laser light trough air space will be reflected 6 times by two prism before coupled back into a 50µm multi-mode fiber. One prism motorized to set up the right delay.
(very sensitive, very expensive, impracticel)

## Slide 24: New Installations at vertical Pickup-station
1. HESR Pickup-tank
FCT
Space for
BPM tests
Rogowski
coils
Installation of first HESR Pickup-tank into COSY (end of 2015)

## Slide 25: Kicker section during summer-shutdown 2016

## Slide 26: HESR stochastic cooling tested in COSY
Together with original PANDA jet target
Chart: Particle number 1-2 *1010
Schottky signal of 1500th harmonics with
stochastic cooling, barrier bucket and target.

## Slide 27: Hollow fiber lines
Transmission line between PU and KI
Advantage:
High speed: 99.9% c0
Low temperature coefficient
Easy to handle compared to air-filled coax lines
But:
Sometimes amplitude and phase changes
High losses at transition to FC/APC (not useful for notch-filter)
Zero-span Sweep-time: 2 sec
Longitudinal cooling-rate with hollow fiber line and air-filled coax line
Change in amplitude: 1dB, in phase: 10°

## Slide 28: HESR stochastic cooling
7 tanks fabricated:
  Main-system (=0.92): 2 Pickup, 3 Kicker
  Low beta system (=0.77): 1 Pickup, 1 Kicker
Low noise amplifier, programmable delay lines, power amplifier already installed at tanks.
Optimizes optical delay lines for notch-filter and system delay
Software developments for a fully automated system adjustment.
Order of transmission line (optical hollow fiber line) freezed
One Pickup and one Kicker installed and tested in COSY
Status

## Slide 29: Cosy cavities
Acceleration/deceleration
  Broadband cavity with VitroPerm cores, water cooled
  One gap, two tanks in push-pull mode driven by tube amplifier
  Tube amplifier does not reach the required RF power anymore, that’s the reason why we used one HESR cavity for the last year of COSY operation

## Slide 30: Cosy cavities
Barrier-bucket
  Similar design but only one gap one tank (test cavity for HESR)
  Vppmax = +/- 200V, limited by solid state amplifier
  Not optimized for solid state amplifier
  Operated in experiments since years
  Used amplifier now in operation for SIS100 KO-exciter tests.

## Slide 31: HESR cavities
Two equal cavities
Forced air cooled
Optimized for solid state amplifier
Can be used for acceleration/deceleration and barrier bucket operation
Left side
Difference 20% BB, f0=488.7kHz,
8,4 kVpp
Right side
Acceleration:
U (t) = Û sin (ωt)
Û ~ 3kV,
430kHz - 1.6MHz

## Slide 32: RESR/cosy possible changes in HESR
Only one cavity needed in HESR for acceleration and barrier-bucket. The other one can be used in RESR/COSY (constraint: aperture limited to 90mm)
One kicker and one pickup of the main HESR stochastic cooling system can be used in RESR/COSY (constraint: aperture limited to 90mm)
No accumulation in HESR
Thank you