## Slide 1
Yannik Zobus*, Udo Eisenbarth, Zsuzsanna Major, and Vincent Bagnoud
an open-source optical simulation framework
*y.zobus@gsi.de

## Slide 2: outline
Introduction THRILL / OPOSSUM
Overview OPOSSUM
OPOSSUM Ecosystem
Simulation examples
Outlook / User Feedback

## Slide 3: Technology for High-Repetition- Rate Intense Laser Laboratories
EU-funded project under the HORIZON-INFRA-2022-TECH-01 call (01/2023-12/2026)
Goal: Bringing high-energy high-repetition-rate (HEHRR) lasers to the next level
Bottleneck technologies
  high-energy actively cooled amplification
  scaling by beam combining
  real-time wavefront control
  capabilities for large optical components in academic environment
  system modeling
Output: Towards conceptual designs for lasers at FAIR and Eu-XFEL
liquid-cooled glass module
Pseudo-Active Mirror Disk Amplifier (Amplitude)
ELIAS coating chamber

## Slide 4
Modern high-intensity laser systems become more sophisticated & complex
Rigorous planning is crucial to make systems sustainable
Full-scale modeling of these systems, ideally creating a “digital twin” is necessary!
However, existing modeling solutions are
Proprietary (closed source):
  Hard / impossible to extend, expensive
Self-written codes:
  Often „single-use“ during a thesis
  Not well maintained, mostly non-compatible with other codes
Targeting specific problems
Open Source
General
solution
Custom code integration
Design once,
model often
Rust: fast,
memory safe
Our Approach: OPOSSUM OPen-source Optics Simulation System and Unified Modeler
Open source, accessible for all
Decouple system design from modeling: setup design once, model/analyze in numerous ways
Platform for custom-code integration
Extensible to specific needs
Holistic simulation of large-scale laser facilities
Modern backend, written in Rust for high maintainability, memory safety
OPOSSUM - Introduction

## Slide 5
Modern high-intensity laser systems become more sophisticated & complex
Rigorous planning is crucial to make systems sustainable
Full-scale modeling of these systems, ideally creating a “digital twin” is necessary!
However, existing modeling solutions are
Proprietary (closed source):
  Hard / impossible to extend, expensive
Self-written codes:
  Often „single-use“ during a thesis
  Not well maintained, mostly non-compatible with other codes
Targeting specific problems
OPOSSUM - Introduction
https://git.gsi.de/phelix/rust/opossum
Our Approach: OPOSSUM OPen-source Optics Simulation System and Unified Modeler
Open source, accessible for all
Decouple system design from modeling: setup design once, model/analyze in numerous ways
Platform for custom-code integration
Extensible to specific needs
Holistic simulation of large-scale laser facilities
Modern backend, written in Rust for high maintainability, memory safety

## Slide 6: Simulation Principle
Example flow graph
Model arbitrary optical systems as (acyclic) directed graphs
“Light" flowing as data between nodes
Complex system, consisting of similarly complex sub-systems
Optics (lenses, mirrors, setups, custom code…) as nodes
Nodes can store an internal status, e.g. population inversion
Intuitive node positioning/alignment in 3D space
Different analyzer modes

## Slide 7: Nodes
Nodes are the building blocks of the optical system
A node holds one or multiple optical interfaces
An optical interface consists of:
  A geometrical surface: e.g., plane, sphere, cylinder…
  An aperture
  A coating: e.g., Fresnel, ideal-AR, specified reflectivity
  Laser-induced damage threshold (LIDT) information
Refractive indices after a surface can be handled via:
  Constant value
  Sellmeier equations
E.g. Lens
Aperture
Radius
Coating
n1
n2

## Slide 8: Nodes – Node types
Generic nodes:
Spherical / cylindrical / paraxial lens
Flat / spherical / oap mirror
Wedge
Ideal filter
Reflective grating
Ideal beam splitter

## Slide 9: Nodes – Node types
FF Spot diagram
0
x in µm
10
-10
0
y in µm
10
-10
Wavefront
0
x in mm
2
-4
-2
4
0
y in mm
2
-4
-2
4
-15
wavefront error in mλ
-10
-5
FF Fluence
0
10
x in µm
-10
0
y in µm
10
-10
20
fluence in kJ/cm²
40
100
80
60
Detector nodes:
Energy
Wavefront
Spot diagram
Spectrum
Fluence
Spectrum
1050
wavelength in nm
1060
1040
0
20
50
spectrum in arb. u.

## Slide 10: Nodes – Node types
Special nodes:
Source:
  Energy / fluence distribution: uniform, 2D Gaussian
  Position distribution: hexapolar, Fibonacci, .etc
  Shape: ellipse, rectangle
  Spectrum: Gaussian, single lines
Spectrum
1050
wavelength in nm
1060
1040
0
20
50
spectrum in arb. u.
Rectangular shape
0
x in mm
20
-20
-20
20
0
10
-10
y in mm
Hexapolar positioning
0
x in mm
50
-50
-40
40
0
20
-20
y in mm
General 2D Gaussian
0
x in mm
20
-20
-20
20
0
10
-10
y in mm
fluence in J/cm²
0.2
0.1

## Slide 11: Nodes – Node types
Special nodes:
Source:
  Energy / fluence distribution: uniform, 2D Gaussian
  Position distribution: hexapolar, Fibonacci, .etc
  Shape: ellipse, rectangle
  Spectrum: Gaussian, single lines
Nodegroup
  Allows grouping of nodes / subsystems
  Infinite nesting possible (groups in groups …)

## Slide 12: Nodes – Node types
Special nodes:
Source:
  Energy / fluence distribution: uniform, 2D Gaussian
  Position distribution: hexapolar, Fibonacci, .etc
  Shape: ellipse, rectangle
  Spectrum: Gaussian, single lines
Nodegroup
  Allows grouping of nodes / subsystems
  Infinite nesting possible (groups in groups …)
Reference nodes
  Effective re-using of nodes
  Considers internal status
Example: Double-pass amplifier
Beam splitter (BS)
Active medium (AM)
λ/4
Mirror (M)
BS
AM
λ/4
M
Ref λ/4,
Inv.
Ref AM,
Inv.
Ref BS,
Inv.
Flow-graph:

## Slide 13: Node Geometry / Positioning
„Conventional“ approach (ZEMAX, Code V, OSLO,…)
  Using absolute coordinates
  Using coordinate breaks
OPOSSUM approach
  Use relative positioning through calculation of an optical axis
  Most optical systems easy to model
  Absolute positioning still possible
  Needs to check for inconsistencies
non flexible (but sometimes necessary)
may cause headaches for complex designs
How to define a node position in 3D space?

## Slide 14: Node Geometry / Positioning
y
z
S
Position first node (typ. source) absolutely in 3D space

## Slide 15: Node Geometry / Positioning
y
z
S
100 mm
Position first node (typ. source) absolutely in 3D space
Define relative distance to next node along the current optical axis

## Slide 16: Node Geometry / Positioning
y
z
S
Position first node (typ. source) absolutely in 3D space
Define relative distance to next node along the current optical axis
Define local orientation of node (tilt, decenter of anchor point)
Define relative distance to next node along the current optical axis
100 mm
Repeat

## Slide 17: Analyze your optical setup
Simple energy analyzer
  Energy flow between nodes
  Rudimentary but very fast
Sequential ray-tracing analyzer:
  Rays propagate from node to node guided along a topologically sorted flow-graph
  Parameters such as fluence, energy, wavefront accessible via detector nodes
Semi-sequential ghost-focus / LIDT analyzer
  Rays propagate similar to ray-tracing analyzer but can bounce off of surfaces
  Iterative for- and backward propagation
  Report for optics on which the fluence exceeds LIDT
Node 1
Node 2
Node 3
E1
E2
E3
Node 1
Node 2
Node 3
Rays1
Rays2
Rays3
Node 1
Node 2
Node 3
Node 1
Node 2
Node 3
Iteration 1: forward
Iteration 2: backward
Iteration 3: forward…

## Slide 18: Reports
Reports are generated as HTML to be viewed in a web browser
Format is analyzer dependent
Example: ghost focus analyzer
  Global plot
  LIDT-specific data  damaged optic  information about origin of damaging beam  fluence values on optic

## Slide 19: outline
Introduction THRILL / OPOSSUM
Overview OPOSSUM
OPOSSUM Ecosystem
Simulation examples
Outlook / User Feedback