## Slide 2
Status Report About Activities In Juelich
Peter Wintz (IKP - FZ Jülich)
XLV – PANDA Collaboration Meeting, June-25, 2013

## Slide 3
STT layout
  Geometry update / gas distribution
  Online tracking ( Marius)
STT construction (WPs)
  Straw mass production
  Hexagon sector setup
  Readout electronics ( Jacek/Greg)
COSY-beam tests
New to the group: Artur Cebulla, a.cebulla@fz-juelich.de
Outline Juelich Activities

## Slide 4
Reminder: straws are close-packed with ~20µm gaps
Pressurized straw diameter defines layout dimensions
  Depends on strip winding / glue layer, slight differences each delivery (LAMINA)
Precise diameter measurement neccess. for final new tubes, results this Sep.
  Method approved, ~1-2µm precision (by Artur Cebulla)
  Measure diam. vs overpressure & long-term (setting time)
  Change (prelim.): 10.10  10.14(5) mm (incl. 20µm gap)
  Small change in radial STT dimension (~1.3mm)
    Few mm safety margin in layout still left
  Re-calculation of all straw positions (in Sep./Oct.)
    CAD & text file for MC input (Artur/Peter)
    Mechanical frame adaption
STT Geometry Update
R  1.3 mm
STT x-y view, change of radial dimensions by larger straw diameter

## Slide 5
1
2
3a
3b
4a
4b
Per semi-barrel: 12 gas supply lines, 212 gas pipes (in-/outlet)
Optimisation of gas distribution scheme, parallel lines access. from outside
Arrangement of 4 parallel gas lines per hexagon sector, if one failures
  still 3d tracking possible with momentum reso. in each sector
  still 3d-online track recognition possible
  similar number of straws per gas line,
  #205, 196, 190, 142
  different gas flows possible
No hints for serious gas failures
(leakage) from COSY-STT (4yrs in vacuum)
Proposal! open for discussions
STT Gas Distribution Lines
Hexagon sector with 4 parallel gas lines: 1, 2, 3(a+b), 4(a+b)

## Slide 6
STT layout must fullfill PANDA specific reco requirements
  offline: full simulation & analysis of benchmark channels done
  online: track & event reconstruction in continuous data stream
Online: proof by time-distributed event simulation (DPM)
  STT stand-alone tracking, based on axial zones
  STT hits w/o external timing (t0)
  hit triplets method seems to work
    hit triplet: ~1mm precision (cms-x,y)
    single straw: ~3mm
    isochrone: ~ 150µm, only with t0
STT Online Reconstruction
 Marius‘ talk
Time-distributed event simulation (DPM) and track reco based on hit triplets

## Slide 7
Straw mass production and layer modules
Electronic readout system
Mechanical frame system: STT (+ central support frame)
Hexagon sector setup (pre-comissioning)
Gas system
HV system
Slow control system (DCS)
STT final setup and comissioning
Partners in Germany, Italy, Poland, Romania, ..
STT Construction WPs

## Slide 8
Straw productions in Juelich (100% WP)
Pilot mass production run done at end 2012/13
  Unexpected leakage  tests, new specific. of film tubes (winding/glue)
  Replacement order (LAMINA), first 5000 straws delivered this June
  Re-definition of production quality criteria, assurance tests, ..
Final straw mass production starts this Sep.
  Preps done: all materials, mounting tools & techniques
  Needs 3-4 years, including >> 50% spare straws
  First task: precise measure of pressurized (p=2 bar) straw diameter
    No change of inner tube diameter, same end plugs
    New CAD drawings for straw modules (skew angle, side bands, ..)
    Pending: new reference (groove) plate for straw layer gluing
Straw Production Status

## Slide 9
Ideal pre-commissioning of full STT design (mechanics & electronics)
Mechanical setup issues
  Precision measurement of straw positions (3d-gauge)
  Alignment structures (connecting tubes, frame-straw module connect.)
  Mechanical frame adaption, final mounting scheme
Electronic readout system
  800 straw channels
  Final mounting scheme, cooling
Ready in 2014/ 2015, beam tests in 2015
In addition: existing straw prototype detector
setups for ongoing beam tests
STT Hexagon Sector Setup
STT hexagon sector, 1.5m length

## Slide 10
2 Concepts to measure drift time + signal amplitude (for dE/dx)
TDR fully approved, ECE evaluation & recommendation: “.. following both electronics options is a wise approach ..“
  Amplitude sampling: LE-Time + Q
      Frontend amplifier + FADC (240MHz)
      Status: sr ~ 150 µm, (dE/dx) < 10% measured, ~7% feasible at PANDA
      Pending: High-rate FPGA pulse analysis and readout, final amplifiers
  Amplitude by time-over-threshold*: LE-Time + ToT(Q)
      Frontend ASIC chip + Time-Readout-Boards
      Status: first in-beam tests sucessfull, analysis ongoing
      Pending: full ToT  dE/dx calibration, analysis, >4 beam momenta, larger straw setups equipped with RO (few 100 straws, inclined to beam)
STT Readout
*ToT used for PID at ATLAS- TRT & HADES-MDC

## Slide 11
50mV threshold
25mV threshold
dQ/Q resolution ~ 10%
Charge (pC) vs ToT (ns)
Time (ns)
Time over Threshold (ns) 
ASIC testversion with analog out, first in-beam test 2012 ( Jacek)
Next ASIC version in production: 100 chips 8 ch, few param. optimisations
Calibration of ToT  dE/dx with 55Fe-source and beam protons
    need >4 different beam momenta to get ToT  dE/dx relation and resolution
Time-Over-Threshold Method
Pulse
integral
ToT
(25mV)
ToT
(50mV)
Beam on straws, TRB readout
backgrd
55Fe-signals
220(110)e-/200µm, pulse
integral + ToT measuremt
15mV thresh.
diff z-positions

## Slide 12
Accessible dE/dx-range: ~10mips with proton/deuteron beams ~ 0.6-3 GeV/c
Straw prototype setups for readout tests in COSY beam area (Big Karl)
Pileups (trigger + straws) during last beam test (Dec-12)
    multiple beam/triggers within 300ns, delayed straw hit times possible
    next time: cleaner setup (multiplicity veto, lower intensities for checks, ..)
COSY Beam Tests
2 Straw setups, beam coming from the back (Big Karl area)
Scint. trigger
Straw signals
(ASIC analog out, yellow, blue, purple)
300ns
1000 ns

## Slide 13
Well prepared to start straw production in Sep. this year
Beam straw tests at COSY ongoing for high-rate measurements
Hexagon sector setup ideal for pre-commissioning (mechanics/electr.)
Followed by dedicated beam tests at COSY in 2015
Summary