## Slide 1
M. Tiemens, M. Kavatsyuk
KVI, University of Groningen
EMC Front-End Electronics
for the Preassembly

## Slide 2
Feature Extraction: (developed at KVI)
Stage I:
  Base-line follower
  Pulse detection
  Pile-up detection (output waveforms)
  Time-stamp at maximum
Stage II:
  Precise time
  Precise energy
-25 °C
EMC Volume
LAAPD’s
Preamplifier
Digitizer
SADC
FPGA
Online pulse-data processing;
Feature Extraction
Data Concentrator
Calibration
Merge data from 2 photo-sensors
Optical Link
Hit data
SADC clock sync. signals
slow control
SODANET
Compute Node
Data Concentration:
(developed at KVI)
  Time ordering data from all inputs
  Pile-up recovery (to be implemented)
Readout for Electromagnetic Calorimeter

## Slide 3
HUB
HUB
HUB
HUB
SODANET
source
slow
control
slow
control
slow
control
slow
control
slow
control
DC
Burst building network (BBN)
DC
DC
DC
FEE
FEE
FEE
FEE
SODANET Topology

## Slide 4
EMC Volume
Digitizer
SADC
FPGA
Online pulse-data processing;
Feature Extraction
(developed by P. Marciniewski)
Digitizer prototype v2
Forward End Cap:
Average hit rate of 350 kHz -> ~ 2.2 Gbps
Required channel density reached
Radiation hardness is being studied
EMC Digitizer
- Data rates

## Slide 5
EMC Volume
Digitizer
SADC
FPGA
Online pulse-data processing;
Feature Extraction
(developed by P. Marciniewski)
Digitizer prototype v2
TOO EXPENSIVE
Redesign required:
Replace Virtex 6 with Kintex 7 FPGA
New board expected ready next year
EMC Digitizer
- Data rates

## Slide 6
Ready to use & fully functional with existing test readout (EMC only, no external triggers)
Tests with PROTO192 on-going
Common tests with other subsystems
Online event building
Possibility of external triggering
Development of SODA source, time-distribution network (SODANET) and new data concentrator is on-going
Once done, hopefully end of summer
EMC Digitizer
- Passive cooling & readout

## Slide 7
Required functionality (EMC):
  Time-distribution functionality
  Separation of the hit-data and slow-control streams
  Combine information from two photo-sensors, reading out same crystal
    Identification and correction of a nuclear counter effect
  Energy calibration
  Time-ordering of the data
  Pile-up recovery
Data Concentrator
- Functionality

## Slide 8
Current implementation:
  Hardware: WASA data concentrator
    Functional
    EMC only
Desired implementation:
  Hardware: TRBv3 Board
    Combined readout for: EMC, STT, MVD, DIRC
    Ready by end of summer
Data Concentrator
- Implementation

## Slide 9
Advantages:
  Different configurations of readout system possible
Disadvantages:
  Low optical fibre speed (max 3 Gbps)
Low speed/EMC hit-rate
(<60 kHz/crystal):
  1 SODANET IO (TRB main board)
  1 link to CN (TRB main board)
  24 links to digitizers (piggyback boards)
High speed (expected at normal operation at HESR):
  1 SODANET IO (TRB main board)
  6 links to CN (piggyback boards)
  18 links to digitizers
  (piggyback boards)
Possible TRB configurations for the End Cap:
TRB as a Data Concentrator

## Slide 10
Preamps
Digitizers
DC
TRB Boards
To time-ordering network/ Compute Nodes
# Input channels: 6941×2
# Digitizers: 217
# TRB boards: 9
# Fibres to CN: 9
Interface to DAQ
- Low rate

## Slide 11
Preamps
Digitizers
DC
TRB Boards
To time-ordering network/ Compute Nodes
# Input channels: 6941×2
# Digitizers: 217
# TRB boards: 12
# Fibres to CN: 72
Interface to DAQ
- High rate

## Slide 12
Summary
  Digitizers:
        Board which fulfils EMC requirements is functional (can be ordered for interested parties)
        First prototype of passive-cooling crate is functional: optimization is on-going
        Redesign is required to reduce costs
  Data concentrator:
        Existing version (based on WASA hardware) is functional; works for EMC only
        TRB board is under development
              Allows to combine data of different subsystems
              Flexible configuration for readout of the EMC forward end cap with few Compute Nodes:
                Complete end cap readout at low rates (<60 kHz/crystal)
                Partial end cap readout at high rates