## Slide 1: Data Supply
Operator School 2025
D. Ondreka, SYS 31.10.2025

## Slide 2: Have you ever asked yourself…
How does the control system know
  how an accelerator is supposed to work?
  what a synchrotron cycle is?
  which knobs are needed to tune a machine?
  the properties of all devices?
If I change a parameter in ParamModi:
  What happens behind the scenes?
  How can I know which devices are affected?
  What is a parameter anyway?
  How can I inspect old and new values?
?

## Slide 3: What is ‘Data Supply’?
Accelerator can only work if
  all devices have consistent set values
  the timing system provides the right events
  required beam parameters can be specified
  required operation modes can be selected
  the right knobs for tuning are available
That’s what ‘Data Supply’ is about!
Core feature: machine model
  Abstraction in terms of physics parameters
  Relations to hardware set values
  Representation of operation modes
SIS18 Model Statistics | 
#Devices | ~150
#Parameters | ~1500
#Input Parameters | ~200
#Hardware Parameters | ~350
#Rules | ~1700

## Slide 4: Machine modeling using LSA
LSA: Framework for accelerator modeling
  Invented by CERN, co-developed by CERN/GSI
Data-driven system with 3-tier architecture
  LSA-DB: storage for input and output data
  LSA-Server: calculations and data access
  Applications: management of data
Generic structures for modeling
  Tables for machine specific data (e.g. optics)
  Tables for device data (e.g. calibrations, limits)
  Object model for description of accelerators
  Interface for definition of physics algorithms
Change injection tunes
Calculate tune ramp
Function from scalar
Calculate quadrupole strengths
Optics data
Calculate quadrupole current
Calibration data
Calculate set value
Proper format
Physics
Hardware
Algo- rithms
Data

## Slide 5: LSA in a nutshell
Spatial partitioning of facility
  Particle transfers (=timing groups)
  Accelerator zones
Accelerator represented via parameters
  Linked to logical or physical devices
  Organized in hierarchy from physics to hardware
Cycles organized in contexts
  Basic unit: beam process for particle transfer
  Grouping into chains and sub-chains
Values represented as settings
  Value of parameter in beam process
  HW settings get sent to devices (set-values)
Calculations implemented as rules
  Java code mostly written by physics experts
  Calculate child from parents and data in LSA-DB
SIS18BEAM/QH
SIS18BEAM/QV
SIS18BEAM/BRHO
LOGICAL.GS01QS1F/KL
LOGICAL.GS01QS2D/KL
LOGICAL.GS01QS1F/BL
LOGICAL.GS01QS2D/BL
GS01QS1F/Setting#current
GS01QS2D/Setting#current
Physics
Hardware
Setting of tune parameter | 
Parameter | SIS18BEAM/QH
Beam process | P.SIS18.RING_INJECTION
Value | Constant function = 4.28
LSA DB
MADX
Java code
QH
KL
INJECTION
RAMP
EXTRACTION
RESET
INIT

## Slide 6: SIS18 Cycle
Cycle represented as chain
  Comprises several particle transfers
    Ring, cooler, beamline sections
  Partitioned into in beam processes
    Types and number depend on particle transfer
  Display with chain viewer
    ParamModi: context menu on chain name
    Displays timing events also
BEAM_IN
BEAM_OUT
BP boundary
Timing event
SIS18 dipole current and beam processes

## Slide 7: Hierarchy and Trim: An Example
What happens if we change injection tune?
  ParamModi sends changed value to LSA-server
  LSA-server calculates new values along hierarchy
  Let’s join it on the journey!
How do I know the parameter?
  Go to ‘Expert Mode’ (Menu ‘Extras’)
  Find the input field by its label ‘Hor. tune QH (Inj.)’
    Linked to parameter ‘SIS18BEAM/QH_END_S’
    Linked to injection beam process
Open hierarchy viewer on trim tab
  Select parameter and click ‘Hierarchy’
  How to find parameter?
    Select all ‘Parameter Groups’
    Select all ‘Type Groups’
    Use ‘Filter’ field, e.g. ‘*QH_END’
ParamModi: Expert Mode (SIS18: Modi/Injection)
ParamModi: open hierarchy on trim tab

## Slide 8: Tune Trim: Hierarchy
Quadrupoles
Tunes: Scalar to Functions
Bumpers

## Slide 9: Tune Trim: Scalar to Functions
Scalar input must be converted to function
  Tune function required when there is beam
  Tunes constant during ramp  change in PRE
INJ
RAMP
PRE
BUN
EXT
POST
INIT
RESET
Input value for QH at injection
Values for QH at beam process boundaries
INJ
RAMP
PRE
BUN
EXT
POST
INIT
RESET
Function for QH from injection to extraction
INJ
RAMP
PRE
BUN
EXT
POST
Function of difference DQH to theory tune (QH = 4.29)
INJ
RAMP
PRE
BUN
EXT
POST

## Slide 10: Tune Trim: Quadrupole Strengths
Accelerator physics comes in:
  Quadrupole strengths depend on both tunes
  Generally requires ion optical simulations
  Linear approximation used in model
LSA DB
MADX
Java code
QH
KL
Quadrupole strength changes in beam process PRE_EXTRACTION
Coefficients for linear approximation of strength change

## Slide 11: Tune Trim: Strength to Current
Independent calculations per quadrupole
  Integral field: strength x rigidity
  Current: calibration curve look-up
Strength (K1L): DK1L + theory strength
Calibration curve
Quadrupole current (I)
Integral field (B1L)
x BRHO
Calibration look-up
Rigidity (BRHO)

## Slide 12: Tune Trim: Current to Voltage
Power converters need current and voltage
  Inductive contribution from current change
  Eddy current contribution
Current change (IDOT): numerical differentiation
Load voltage prediction (U)
Eddy current contribution to voltage (UEDDY)
Eddy current model
U = R∙I + L(I) ∙dI/dt + Ueddy
Inductance curve

## Slide 13: Tune Trim: Set Values
Ramped SCUs need quadratic polynomials
  Polynomial fit of values on time grid
  Extraction of coefficients into set value parameters
  Sent to SCU for resident chains
Current polynomial (I_POLYNOMIAL) and current (I)
Current set value Setting#coeffArrCurr (RAMP)

## Slide 14: Model: Interface to Machine
Model provides general access to settings
  Modifications not limited to ParamModi
  Programmatic access to all levels of the hierarchy
  Modification of time functions possible
Applications using model in routine operation
  Benno Application (C. Heßler/OPE): beamline steering and focusing
  Device Automator (W. Geithner/DEC): parameter scanning
Interfaces used for machine experiments
  Java API: standard used by CS applications
  Python bridge: experimental ( S. Appel/APH)
Benno Application
Device Automator Application
Java code for executing the tune trim just discussed
LOCO-based ORM measurement (Java app, steerer function trims)
Courtesy of D. Vilsmeier

## Slide 15: Thank you for your attention!
Looks like accelerator modeling is an art…
SIS18
ESR
CRYRING
SIS100
Courtesy A. Schaller
Special thanks go to the great FAIR Data Supply team: Peter Gerhard, Holger Liebermann, Ingrid Kraus, Sergey Litvinov, Michael Kelnhofer, Christoph Hessler, Raphael Müller, Andreas Schaller, Jonas Pforr, Jutta Fitzek, Hanno Hüther, and others