## Slide 1: SUPER-FRS DAQ workshop MUSIC
17. Nov. 2025
David Urner

## Slide 2: Overall setup
foil motor(s)
VME crate
controller:MVLC
MDPP32 ADC/TDC
low voltage PS
high volt. PS 400V+
Preamp
data
low voltage supl
high voltage supl+
pulser
amplify. setting
USB3
MBS DAQ computer
NUSTAR network
Voltage Supply
6kV
400V
low voltage
USB
Detector cathode
foil motor controller
power
end
switch
ACC network
modules:
1 MVLC
2(FMF1), 3(FHF1) MDPP32
low vol PS (?)
high vol PS (?)
white rabbit (?) VETAR
ENV3
VULOMB
TRIVA

## Slide 3: MUSIC detector signals
Control
  control preamplifier, via NUSTAR network
    amplification level
    pulser signals
  both signals are supplied by the VME crate controller and can be set via MBS commands, integration in SFRS device control still needed
  control stripper foil motors via Acc. network
    communication via acc network
    FESA classes are written (Cosylab) and first tests are made
      these classes can access all needed commands on the motor controller
      Integration into SFRS device control still needed, to realise a move in/out with necessary checks
      Connection to ELSA to inform main control room about status still needs to be made

## Slide 4: Trigger
We expect a trigger signal as input to MUSIC
  a self trigger is possible for commissioning
  MUSIC will select a window
    readout will then start some 1µs before the trigger signal (buffer on the ADC)
    readout will be in the order of 8µs to get the full drift time
  MDPP module has an
    ADC section, which will provide a signal height corresponding to the amount of charge on the pad
    TDC (CF) will provide the time of the signal
  The system is multi-hit capable, that means during an event several hits per channel can be read out.

## Slide 5: Signal Readout
Setup of the MVLC (crate controller)
  we are currently setting the MVLC using the MESYTEC provided software
  It is possible to Send and receive commands/info to the controller via MBS
  A script needs to be written, that can do the setup
  Potentially one might want a user interface to control the setup (rather than editing the script by hand)
Timing information:
  So far we are undecided whether we will use
    DAQ Bus to connect all devices (ToF, position, MUSIC,…) of one focal plane
    Each system is receiving an independent white rabbit time stamp
    I prefer the bus, and I would encourage to get a formal decision on this point asap.

## Slide 6: Physical Position of the systems
Readout cable routing:
  The readout cables go from the dome via a mobile cable handler leading the cable to the top of the big diagnostic chamber.
  from there they need to go to the VME crate
  cable charakteristics:
    We are using shielded bipolar cables.
    There are a total of 96 channels for FHF1 and 64 channels for FMF1
    We tested the cables up to 8m length
      This would require the VME crate to be in the tunnel!
    We should determine the shortest possible route to the VME crate outside the tunnel
      With the upgraded pre-amplifier we can then try to test the cables (or find other cable types), which would allow us to place the VME crate outside of the tunnel.

## Slide 7: Physical Position of the systems
Foil motor controller small (ca 15cm x 10cm x 10cm).
  We know that we can transport the power over 8m.
  If possible we would like to position the controller outside of the tunnel
    we still need to do tests with longer cables

## Slide 8: Final thoughts
July 25 run issues:
  version of VETRA firmware introduced synchronisation issues
    needs to be looked into by EEL
  Some issues with compatibility between DRASI and MBS versions of lmd files
    Do we have a clear definition on the format of mdl.