## Slide 1
Automation of GSI key beam manipulations with AI methods
Sabrina Appel (APH)
(Team: APH, Super-FRS, CERN, TUDa, PLUS Salzburg)

## Slide 2: FAIR/GSI
2
S. Appel - APH
Automation and optimization with Python:
Beam steering and focusing (TK, X2)
Multi-turn injection loss minimization (SIS18)
Closed-orbit correction for non-standard optics (SIS18)
Slow extraction loss minimization (SIS18)
Beam steering and focusing (FRS/S-FRS)
Methods of interests of automation:
Numerical + Bayesian optimization (BO)
Physics-information or Multi-Fidelity BO
Multi-Objective optimization with BO
Data-driven model predictive control (MPC) and reinforcement learning (RL)
Goal: Tools for automating key beam manipulations to support control room operators.
EURO-LABS finances scientific staff member + 2 staff member from APH
Several TUDa Master and PhD students (with TUDa funding)
One Master student from Paris Lodron Universität Salzburg
Collaboration with CCPS, TUDa and CERN
Notes: Methods of interests of automation:
Numerical + Bayesian optimization (BO)
  Uses only measurements; needs sufficient iterations
Physics-information or Multi-Fidelity BO
  Combines data and simulation; fewer iterations
Multi-Objective optimization with BO
  Optimizes competing goals; explores trade-offs
Data-driven model predictive control (MPC) and reinforcement learning (RL)
  Learns control via interaction; model-based variants reduce data needs
  Efficient at runtime after learning system behavior

## Slide 3: GSI: Python Bridge
One key ingredient: Python bridge to GSI Control System (software and hardware)
The Python access to FESA is most meaningfully used for retrieving data from beam diagnostic devices, while changes to settings (e.g., for magnets) should be handled via LSA.
1https://wiki.gsi.de/BEPHY/PythonBridge,
2https://git.gsi.de/scripting-tools/pjlsa_gsipro,
3https://www-acc.gsi.de/wiki/FESA/PythonCmwRda,
4https://gitlab.cern.ch/acc-co/devops/python/prototypes/pyda
pjlsa
pyrda3
FESA
LSA
Ported existing CERN solution to GSI
Python bridge will be maintained by APH (new software engineer, starting today) + “GSI Acc-Py“
(ACO/SYS)
(BEA)
D. Ondreka. MT, 2025

## Slide 4: GeOFF at GSI
Python-based framework
lists, configures and runs optimization problems
standardized interfaces and adapters for various packages via Common Optimization Interfaces
Optimization problems formulated as environment (classes) (allow optimization of very complex problems)
Class contains logic for live plotting, data logging, and communication with LSA, FESA and the Device Access system
Quick adaptation of code and on-the-fly during shifts: This is made easy due to flexibility of the framework.
GeOFF Development/Distribution/Maintenance (P. Madysa, APH, EU funded)
Madysa, Appel et al. arXiv, 2506.03796
https://doi.org/10.1016/j.softx.2025.102335
Additional ingredient: Generic Optimization Frontend & Framework (GeOFF) GeOFF is a widely used framework for deploying automation at CERN

## Slide 5: Automation of MIT adjustment and optimization
1
5
2
4
3
+ 4 TK Steers (+ 2 Quads)
Usually is MTI optimized manually with varying success
Idea: Automated optimization of MTI
  with numerical optimizer (BOBYQA) + ML
  by using GeOFF and python bridge
  Aim: low loss injection over many turns
  Bounds and constraints for parameters can be included
Variables controlled by the numerical optimizer

## Slide 6: Automation of Multi-Turn Injection
150 iterations required, which took about 30 minutes. (depending on cycle time, LSA reaction time, and averaging)
1 iteration = median of 3 evaluations (to reduce variance)
gray area = initialization phase of algorithm.
Loss could be reduced from 30 % to 12 %
Usually, MTI is optimized manually, with varying success
Using nine optimization parameters.
(correction of loss calculation to earlier publications)
successful use of numerical optimizer BOBYQA
CON: algorithm's internal model not reusable
S. Appel, P. Madysa,

## Slide 7: GeOFF GUI at GSI (1. June 2025)
P. Madysa , L. Dingeldein, S. Appel
GUI – Easy to Use
Optimization context fully described by environment
Custom live plotting
  Tested multiple options for usability
Workflow
Select:
  LSA context
  Problem environment (e.g., SIS injection)
  Algorithm
    Configure if needed
Start/Stop optimization
Machine learning and numerical automation via intuitive GUI for operators

## Slide 8: Bayesian optimization: Simulation results
Comparison of different acquisition functions
various BO kernels and acquisition functions studied
combine multiple answers to make BO more general
Hedging algorithm prefers most exploitative answer
S. Appel, P. Madysa, C. Reinwald

## Slide 9: Multi Objective Bayesian Optimization
Competing goals: maximize number of injections, minimize loss
dependence of gain factor on loss
BO with hypervolume-based optimization drives efficient PA-front improvement
Achieves similar or better results in a fraction of the time of genetic algorithms
Prior art (up to 10 hours):
Simulation with genetic algorithms
Measurements with MOBO
Optimization of injector beam line is missing
https://ax.dev/tutorials/multiobjective_optimization.html
S. Appel, P. Madysa

## Slide 10: Multi-Fidelity Bayesian Optimization
Towards to a Digital Twin
GP model
Acquisition funciton
Simulation
Machine
experiment
Parameters space
Fidelity space
x
s
s<1
s=1
MFBO combines
  low-fidelity simulations (fast but approximate, s <1) and
  high-fidelity experiments (accurate but expensive, s=1).
to optimize black box functions via BO
Method
Optimization problem:
Joint Gaussian Process model over
reduces costly machine interactions
measurements for validating predictions.
useful when machine evaluation is time-consuming
S. Appel, P. Madysa, H. Alsmeier, R. Findeisen, S. Hirt, E. Lenz, M. Pfefferkorn

## Slide 11: X2 beam line optimization
cooperation with CCPS lab of TU Darmstadt
custom algorithms implemented by domain experts without prior knowledge
here: combination of BO & Extremum Seeking

## Slide 12: Summary and Outlook
Acknowledgements
Supported by EURO-LABS (EU Horizon programme)
Collaboration with CERN, TUDa, PLUS Salzburg
Outlook
Using Geoff for PUMA experiment at CERN (TUDA)
Possible use also at KIT and GANIL (EU)
Super-FRS and SIS100 commissioning methods
Geoff Development, Project URLs
Geoff enables rapid, automated tuning
Open-source framework for accelerator
Recent paper in SoftwareX
https://gitlab.cern.ch/geoff
https://github.com/geoff-project
https://cernml.docs.cern.ch
Advanced Techniques
SIS18 injection losses reduced 45\% → 15\%
Multi-objective BO
Multi-fidelity BO → Towards to a digital twin

## Slide 13: Geoff Paper Published in SoftwareX
https://doi.org/10.1016/j.softx.2025.102335
Team: S. Appel, P. Madysa, V. Kain, M. Schenk

## Slide 14: Introduction:
Automation:
Acceleration of manual tuning (which can take days)
→ mathematical optimization → AI
Accelerator optimization:
Performed live on the machine using mathematical optimizers and AI.
Tuning of a large number of parameters with limited online measurements, while incorporating prior knowledge from previous measurements, physical simulations, and domain expertise.
R- Roussel et al., Phys. Rev. Accel. Beams 27, 084801 (2024)
Accelerator surrogates and ML:
From simple regression models to artificial neural networks
Training from real machine or/and simulation data
Goal: Fast, invertible models for analysis/optimization
1-2 interaction
‘Model-based ML’
on FPGAs
> 1e6 interaction
Evolution/numerical optimization
Accelerator adjusting
Today: partly manually
SIS18 + FRS adjustment
hours up to days
< 100 interaction
‘Model-based ML’
Extremum Seeking
Real time
During cycle
RF control
Milliseconds
Control
Cycle by cycle
Noise control
Seconds/Minutes
Challenges: Long setup times, safety constraints, external conditions, and feedback systems.

## Slide 15: FRS (FRagment Separator) and Super-FRS
Production and investigation of nuclear structure of exotic nuclei.
characteristics of the high-resolution magnetic spectrometer FRS, exotic nuclei can be produced, separated, identified and eventually stored in a storage ring
Super-FRS increas of acceptance and complexity (about 4 times more magnets), Gain factors of 1000 (12C) and 7500 (132Sn) can be reached.
Super-FRS layout:
Automation of operational tasks essential for Super-FRS

## Slide 16: FRS: Automated online steering
steerer
dipol
Hor. foucs quad
Ver. Foucs quad
grids
target
Objective Functions: Offset or distance to the beam target using to two grids in front of the target
Proof of principle:
All the required systems for automation have been verified.
Online beam steering in 50 iteration and took 18 minutes.
As a first step toward a possible full automation, we started with beam steering.

## Slide 17: FRS 1st order: tune quadrupoles
Proof of principle at FRS:
Steer beams at the target
Tune quadrupoles to focus the beam (central spot upright)
  Numerical optimization (BOBYQA)
  TPC Data analysis
    with unsupervised clustering
    or more sophisticated (inner and outer spots)
Automated measurement of misalignments (method validation for Super-FRS commissioning)
Tune sextupoles to remove focal plane tilt and “banana”-deformation
Evaluation of beam spot slope
Change quadrupole strengths
Schematic illustration of FRS Dispersive Focus area

## Slide 18: Optimization of separator optics with primary beam
TPC Data analysis
U91+
U90+
U92+
Dispersion
Different tilt,
a_center ≠ 0:
Different distance:
focus tilt
Different heights
Twiss parameters  1st order transfer matrix
2nd order deformations  sextupole errors
Central spot (2024):
  x-Twiss parameters
  Non-dispersive 1st order x-transfer matrix
Charge states after target (outer spots, 2025):
  Dispersive transfer matrix elements of 1st and 2nd order
Goal: Bring the spectra as close as possible to desired 1st order parameters
Using charge states = more deduced optical properties (Difficult for humans to interpret and optimize)
2024
2025
Individual particle tracking detectors + charge states:
-> Lots of information from x-x’ spectra at dispersive focal plane
Team: S. Appel, M. Bajzek, E. Kazantseva, P. Madysa, S. Pietri, H. Weick, D. Kallendorf