## Slide 1: FRS Machine Run 12th July 2025: Method testing for S-FRS:
Ion-Optical Optimization
Quadrupole axes measurements
D. Kallendorf, Z. Brencic, J. Wirtz, M. Bajzek, S. Appel, P. Madysa, J. H. Hetzel, H. Weick, S. Pietri, E. Kazantseva

## Slide 2: Reminder: Fragment Separator FRS
-2% | 
-1% | 
Ref | 
+1% | 
+2% | 
-2% | 
-1% | 
Ref | 
+1% | 
+2% | 
S2
Separated by dispersion
Focus
Angle independent of momentum
Focus independent of momentum
No distortion

## Slide 3: Experimental Setup: Expected case
Diagnostic Mode: Use target to generate charge states of primary beam Beam: 650MeV/u U, TA: 113mg Be + Sci1
TPCs (experimental DAQ) measure phase space

## Slide 4: What you might see instead:
Bad S2 phase space (simulation)
Consequences:
No x-separation of spots
Emittance growth
Solution
Optimization based on detector data
Improve machine knowledge
Imperfect model
Reason:

## Slide 5: Optimization

## Slide 6: Parameter Extraction
Clustering
Identify linear distortions (red) Quadrupoles
Identify non-linear distortions (blue)  Sextupoles

## Slide 7: Results
Ion-Optical Optimization
Python FRS magnet control ✔
Python FRS-DAQ readout ✔
Numerical online optimization at the dispersive focal plane ✔
Automatic evaluation of multiple charge-state spots ✔
Optimization of momentum dependent component ✔
Include transmission X
Optimization of sextupoles X

## Slide 8: FRS Misalignments measurements
Goal: deduce quadrupole misalignments by quadrupole scan
Procedure: turn off as many magnets as possible, turn on quadrupoles one by one, vary K1L, measure phase space at S2 and S4 to reconstruct misalignments
pjlsa was used to set up magnets automatically
Result evaluation is in progress (PhD student Z. Brencic)
D3
D4
S2
S3
S4
Q31
Q32
Q41
Q43
Q42

## Slide 9: FRS Misalignment measurements
Trigger at S4 sci led to cutting part of beam  need more thorough analysis to reconstruct misalignments of Q31 and Q32
2 approaches to test:
  evaluate only mean beam position/angle changes
  single particle dynamics